## Slide 1
CS162
Section 8

## Slide 2
Administrivia
Spring Break: It was last week!
Project 3 design doc: Due on Tuesday (4/8) !!
You’re done with nachos. Hooray! Read and understand the source for project 3 ASAP, as it is the same source for project 4.
Do not, do not, do not, do NOT: post, solicit, sell, flagrantly display, or indecently expose your code from projects 1 and 2 to the public.

## Slide 3
QUIZ TIME

## Slide 4: Five Layers Summary
Lower three layers implemented everywhere
Top two layers implemented only at hosts
Logically, layers interacts with peer’s corresponding layer
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Host A
Host B
Router

## Slide 5: The Internet Hourglass
Data Link
Physical
Applications
The Hourglass Model
Waist
There is just one network-layer protocol, IP
The “narrow waist” facilitates interoperability
SMTP
HTTP
NTP
DNS
TCP
UDP
IP
Ethernet
SONET
802.11
Transport
Fiber
Copper
Radio

## Slide 6: Implications of Hourglass
Single Internet-layer module (IP):
Allows arbitrary networks to interoperate
  Any network technology that supports IP can exchange packets
Allows applications to function on all networks
  Applications that can run on IP can use any network
Supports simultaneous innovations above and below IP
  But changing IP itself, i.e., IPv6 is very complicated and slow

## Slide 7: TCP: Transport Control Protocol
Reliable, in-order, and at most once delivery
  Packets don’t necessarily have to be sent in order, and they don’t necessarily have to arrive in order.
  Packets must be delivered to the application (top layer) in order.
Stream oriented: messages can be of arbitrary length
Provides congestion and flow control

## Slide 8: Reliable Transfer
Retransmit missing packets
  Numbering of packets and ACKs
Do this efficiently
  Keep transmitting whenever possible
  Detect missing packets and retransmit quickly
Two schemes
  Stop & Wait
  Sliding Window (Go-back-n and Selective Repeat)

## Slide 9: Detecting Packet Loss?
Timeouts
  Sender timeouts on not receiving ACK
Missing ACKs
  Receiver ACKs each packet
  Sender detects a missing packet when seeing a gap in the sequence of ACKs
  Need to be careful! Packets and ACKs might be reordered
NACK: Negative ACK
  Receiver sends a NACK specifying a packet it is missing

## Slide 10: Stop & Wait w/o Errors
Send; wait for ack; repeat
RTT: Round Trip Time (RTT): time it takes a packet to travel from sender to receiver and back
  One-way latency (d): one way delay from sender and receiver
ACK 1
Time
Sender
Receiver
1
2
ACK 2
3
RTT
RTT
RTT = 2*d
(if latency is
symmetric)
d

## Slide 11: Stop & Wait w/o Errors
How many packets can you send?
1 packet / RTT
Throughput: number of bits delivered to receiver per sec
ACK 1
Time
Sender
Receiver
1
2
ACK 2
3
RTT
RTT

## Slide 12: Stop & Wait w/o Errors
Say, RTT = 100ms
1 packet = 1500 bytes
Throughput = 1500*8bits/0.1s = 120 Kbps
ACK 1
Time
Sender
Receiver
1
2
ACK 2
3
RTT
RTT
Throughput doesn’t depend on the network capacity → even if capacity is 1Gbps, we can only send 120 Kbps!

## Slide 13: Stop & Wait with Errors
If a loss wait for a retransmission timeout and retransmit
Slow w/o errors. Even SLOWER with errors! Timeouts take a long time.
ACK 1
Time
Sender
Receiver
1
RTT
timeout
1

## Slide 14: Sliding Window
window = set of adjacent sequence numbers
The size of the set is the window size
Assume window size is n
Let A be the last ACK’d packet of sender without gap; then window of sender = {A+1, A+2, …, A+n}
Sender can send packets in its window
Let B be the last received packet without gap by receiver, then window of receiver = {B+1,…, B+n}
Receiver can accept out of sequence, if in window

## Slide 15: Sliding Window w/o Errors
Throughput = W*packet_size/RTT
Time
Window size (W) = 3 packets
Sender
Receiver
1
{1}
2
{1, 2}
3
{1, 2, 3}
4
{2, 3, 4}
5
{3, 4, 5}
Unacked packets
in sender’s window
Out-o-seq packets
in receiver’s window
{}
6
{4, 5, 6}
.
.
.
.
.
.
{}
{}

## Slide 16: Example: Sliding Window w/o Errors
Assume
  Link capacity, C = 1Gbps
  Latency between end-hosts, RTT = 80ms
  packet_length = 1000 bytes
What is the window size W to match link’s capacity, C?
Solution
  We want Throughput = C in the optimal case (max out our capacity)
  Throughput = W*packet_size/RTT
  C = W*packet_size/RTT
  W = C*RTT/packet_size = 109bps*80*10-3s/(8000b) = 104 packets
Window size ~ Bandwidth (Capacity), delay (RTT/2)

## Slide 17: Sliding Window with Errors
Two approaches
  Go-Back-n (GBN)
  Selective Repeat (SR)
In the absence of errors they behave identically
Go-Back-n (GBN)
  Transmit up to n unacknowledged packets
  If timeout for ACK(k), retransmit k, k+1, …
  Typically uses NACKs instead of ACKs
    Recall, NACK specifies first in-sequence packet missed by receiver

## Slide 18: Selective Repeat (SR)
Sender: transmit up to n unacknowledged packets
Receiver: indicate packet k is missing (by ACKing packet k+1)
Assume packet k is lost
Sender: retransmit packet k (either immediately or after a timeout)

## Slide 19: SR Example with Errors
Time
Sender
Receiver
1
2
3
4
5
6
4
7
Window size (W) = 3 packets
{1}
{1, 2}
{1, 2, 3}
{2, 3, 4}
{3, 4, 5}
{4, 5, 6}
{4,5,6}
{7}
Unacked packets
in sender’s window
ACK 5
ACK 6
No timeout, so resend immediately
Do you see why packet 7 can’t be sent along with 4? (Hint: think about the window size)