## Slide 1: CS 61C: Great Ideas in Computer Architecture Introduction to Machine Language
Randy H. Katz
http://inst.eecs.Berkeley.edu/~cs61c/fa13

## Slide 2: New-School Machine Structures (It’s a bit more complicated!)
Parallel Requests
  Assigned to computer
  e.g., Search “Katz”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates @ one time
Programming Languages
Smart Phone
Warehouse Scale Computer
Software Hardware
Harness Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory (Cache)
Input/Output
Computer
Cache Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0
Today’s Lecture

## Slide 3: Levels of Representation/Interpretation
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
High Level Language Program (e.g., C)
Assembly Language Program (e.g., MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g., block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Architecture Implementation
Anything can be represented as a number, i.e., data or instructions
Logic Circuit Description (Circuit Schematic Diagrams)

## Slide 4: Pointers and Strings in C
char *p; # p is a pointer to a character
char x[] = “Randy Katz”; # x points to a literal string
p = x; # p points to the same place as x
p = &x[0]; # same as p = x
Cannot write x = “Randy Katz”;
Strings are not a primitive type in C (but character arrays are)
Element/character at a time processing possible, but whole string processing requires special routines
R A N D Y sp K A T Z 0
0 1 2 3 4 5 6 7 8 9 10
P
X
Notes: a[b] – Array subscript
*a -- Indirection ("object pointed to by a")
&a -- Reference ("address of a")
p = &x[0] is the same as “p gets the address of the 0th element pointed to by x

## Slide 5: Agenda
Machine Language
Administrivia
Operands
Technology Break
Decisions
And in Conclusion …

## Slide 6: Agenda
Machine Language
Administrivia
Operands
Technology Break
Decisions
And in Conclusion …

## Slide 7: The Language a Computer Understands
Word a computer understands: instruction
Vocabulary of all words a computer understands: instruction set (aka instruction set architecture or ISA)
Different computers may have different vocabularies (i.e., different ISAs)
  iPhone not same as Macbook
Or the same vocabulary (i.e., same ISA)
  iPhone and iPad computers have same instruction set

## Slide 8: The Language a Computer Understands
Why not all the same? Why not all different? What might be pros and cons?

## Slide 9: The Language a Computer Understands
Why not all the same? Why not all different? What might be pros and cons?
  Single ISA (to rule them all):
    Leverage common compilers, operating systems, etc.
    BUT fairly easy to retarget these for different ISAs (e.g., Linux, gcc)
  Multiple ISAs:
    Specialized instructions for specialized applications
    Different tradeoffs in resources used (e.g., functionality, memory demands, complexity, power consumption, etc.)
    Competition and innovation is good, especially in emerging environments (e.g., mobile devices)

## Slide 10: MIPS: Instruction Set for CS 61C
MIPS is a real-world ISA (see www.mips.com)
  Standard instruction set for networking equipment
  Was also used in original Nintendo-64!
Elegant example of a Reduced Instruction Set Computer (RISC) instruction set
Invented by John Hennessy @ Stanford
  Why not Berkeley/Sun RISC invented by Dave Patterson? Ask him!

## Slide 11: RISC Design Principles
Basic RISC principle: “A simpler CPU (the hardware that interprets machine language) is a faster CPU” (CPU  Core)
Focus of the RISC design is reduction of the number and complexity of instructions in the ISA
A number of the more common strategies include:
  Fixed instruction length, generally a single word; Simplifies process of fetching instructions from memory
  Simplified addressing modes; Simplifies process of fetching operands from memory
  Fewer and simpler instructions in the instruction set; Simplifies process of executing instructions
  Only load and store instructions access memory; E.g., no add memory to register, add memory to memory, etc.
  Let the compiler do it. Use a good compiler to break complex high-level language statements into a number of simple assembly language statements

## Slide 12: Mainstream ISAs
ARM (Advanced RISC Machine) is most popular RISC
  In every smart phone-like device (e.g., iPhone, iPad, iPod, …)
Intel 80x86 is another popular ISA and is used in Macbook and PCs (Core i3, Core i5, Core i7, …)
  x86 is a Complex Instruction Set Computer (CISC)
  20x ARM sold vs. 80x86 (i.e., 5 billion vs. 0.3 billion)

## Slide 13: MIPS Green Card

## Slide 14: MIPS Green Card

## Slide 15: Inspired by the IBM 360 “Green Card”

## Slide 16: MIPS Instructions
Every computer does arithmetic
Instruct a computer to do addition:
add a, b, c
  Add b to c and put sum into a
3 operands: 2 sources + 1 destination for sum
One operation per MIPS instruction
How do you write the same operation in C?

## Slide 17: Guess More MIPS instructions
Subtract c from b and put difference in a?
Multiply b by c and put product in a?
Divide b by c and put quotient in a?

## Slide 18: Guess More MIPS instructions
Subtract c from b and put difference in a?
sub a, b, c
Multiply b by c and put product in a?
mul a, b, c
Divide b by c and put quotient in a? div a, b, c

## Slide 19: Guess More MIPS instructions
C operator &: c & b with result in a?
and a, b, c
C operator |: c | b with result in a?
or a, b, c
C operator <<: b << c with result in a?
sll a, b, c
C operator >>: b >> c with result in a? srl a, b, c

## Slide 20: Guess More MIPS instructions
C operator &: c & b with result in a?
and a, b, c
C operator |: c | b with result in a?
or a, b, c
C operator <<: b << c with result in a?
sll a, b, c
C operator >>: b >> c with result in a? srl a, b, c

## Slide 21: Example Instructions
MIPS instructions are inflexible, rigid:
  Just one arithmetic operation per instruction
  Always with three operands
How write this C expression in MIPS?
  a = b + c + d + e

## Slide 22: Example Instructions
MIPS instructions are inflexible, rigid:
  Just one arithmetic operation per instruction
  Always with three operands
How write this C expression in MIPS?
  a = b + c + d + e
  add t1, d, e
  add t2, c, t1
  add a, b, t2

## Slide 23: Comments in MIPS
Can add comments to MIPS instruction by putting # that continues to end of line of text
add a, b, c # b + c is placed in a
add a, a, d # b + c + d is now in a
add a, a, e # b + c + d + e is in a
Are extremely useful!

## Slide 24: C to MIPS
What is MIPS code that performs same as?
        a = b + c; add a, b, c
        d = a – e; sub d, a, e
What is MIPS code that performs same as?
        f = (g + h) – (i + j);
        add t1, i, j
        add t2, g, h
        sub f, t2, t1
Notes: add a, b, c
sub d, a, e
add t0,g,h # temporary variable t0 contains g + h
# Although the next operation is subtract, we need to calculate the sum of i and j before we can subtract.
add t1,i,j # temporary variable t1 contains i + j
# Thus, the second instruction places the sum of i and j in another temporary variable created by the compiler, called t1:
code:sub f,t0,t1 # f gets t0 – t1, which is (g + h) – (i + j)
# Finally, the subtract instruction subtracts the second sum from the first and places the difference in the variable f, completing the compiled

## Slide 25: C to MIPS
What is MIPS code that performs same as?
        a = b + c; add a, b, c
        d = a – e; sub d, a, e
What is MIPS code that performs same as?
        f = (g + h) – (i + j);
        add t1, i, j
        add t2, g, h
        sub f, t2, t1
Notes: add a, b, c
sub d, a, e
add t0,g,h # temporary variable t0 contains g + h
# Although the next operation is subtract, we need to calculate the sum of i and j before we can subtract.
add t1,i,j # temporary variable t1 contains i + j
# Thus, the second instruction places the sum of i and j in another temporary variable created by the compiler, called t1:
code:sub f,t0,t1 # f gets t0 – t1, which is (g + h) – (i + j)
# Finally, the subtract instruction subtracts the second sum from the first and places the difference in the variable f, completing the compiled

## Slide 26
C, Python, MIPS
MIPS, Python, C
MIPS, C, Python
Python, MIPS, C
☐
☐
☐
☐
For a given function, which programming language likely takes the most lines of code? (most to least)
Notes: VertLeftWhiteCheck1
B: Print 4 …because ints in this system are 4-bytes long and the actual address increments by 4 even though it appears to only incrememt 1.

## Slide 27
C, Python, MIPS
MIPS, Python, C
MIPS, C, Python
Python, MIPS, C
☐
☐
☐
☐
For a given function, which programming language likely takes the most lines of code? (most to least)
Notes: VertLeftWhiteCheck1
B: Print 4 …because ints in this system are 4-bytes long and the actual address increments by 4 even though it appears to only incrememt 1.

## Slide 28: Agenda
Machine Language
Administrivia
Operands
Technology Break
Decisions
And in Conclusion …

## Slide 29: Administrivia
This week in lab and homework:
  HW #2 due Sunday
  Lab #3 EC2 to be posted soon

## Slide 30: CS61c in the News

## Slide 31: Agenda
Machine Language
Administrivia
Operands
Technology Break
Decisions
Summary

## Slide 32: Computer Hardware Operands
High-Level Programming languages: could have millions of variables
Instruction sets have fixed, smaller number
Called registers
  “Bricks” of computer hardware
  Fastest way to store data in computer hardware
  Visible to (the “assembly language”) programmer
MIPS Instruction Set has 32 registers

## Slide 33: Why Just 32 Registers?
RISC Design Principle: Smaller is faster
  But you can be too small …
Hardware would likely be slower with 64, 128, or 256 registers
32 is enough for compiler to translate typical C programs, and not run out of registers very often
  ARM instruction set has only 16 registers
  May be faster, but compiler may run out of registers too often (aka “spilling registers to memory”)

## Slide 34: Names of MIPS Registers
For registers that hold programmer variables:
$s0, $s1, $s2, …
For registers that hold temporary variables:
$t0, $t1, $t2, …
Notes: add $so, $s1, $s2
add $t0, $s3, $s4
sub $s0, $s0, $t0

## Slide 35: Names of MIPS Registers
Suppose variables f, g, h, i, and j are assigned to the registers $s0, $s1, $s2, $s3, and $s4, respectively. What is MIPS for
f = (g + h) – (i + j);
add $t1, $s3, $s4
add $t2, $s1, $s2
sub $s0, $t2, $t1
Notes: add $so, $s1, $s2
add $t0, $s3, $s4
sub $s0, $s0, $t0
Talk about conventions

## Slide 36: Names of MIPS Registers
Suppose variables f, g, h, i, and j are assigned to the registers $s0, $s1, $s2, $s3, and $s4, respectively. What is MIPS for
f = (g + h) – (i + j);
add $t1, $s3, $s4
add $t2, $s1, $s2
sub $s0, $t2, $t1
Notes: add $so, $s1, $s2
add $t0, $s3, $s4
sub $s0, $s0, $t0
Talk about conventions

## Slide 37: Size of Registers
Bit is the atom of Computer Hardware: contains either 0 or 1
  True “alphabet” of computer hardware is 0, 1
  Will eventually express MIPS instructions as combinations of 0s and 1s (in Machine Language)
MIPS registers are 32 bits wide
MIPS calls this quantity a word
  Some computers use 16-bit or 64-bit wide words
  E.g., Intel 80x86, MIPS64

## Slide 38: Data Structures vs. Simple Variables
In addition to registers, a computer also has memory that holds millions / billions of words
Memory is a single dimension array, starting at 0
To access memory, need an address (like an array index)
But MIPS instructions only operate on registers!
Solution: instructions specialized to transfer words (data) between memory and registers
Called data transfer instructions
0
1
2
3
…

## Slide 39: Transfer from Memory to Register
MIPS instruction: Load Word, abbreviated lw
Assume A is an array of 100 words, variables g and h map to registers $s1 and $s2, the starting address/base address of the array A is in $s3
int A[100];
g = h + A[3];
Becomes:
lw $t0,3($s3) # Temp reg $t0 gets A[3]
add $s1,$s2,$t0 # g = h + A[3]

## Slide 40: Memory Addresses are in Bytes
0
1
2
3
…
Lots of data is smaller than 32 bits, but rarely smaller than 8 bits – works fine if everything is a multiple of 8 bits
8 bit item is called a byte
(1 word = 4 bytes)
Memory addresses are really in bytes, not words
Word addresses are 4 bytes apart
  Word address is same as leftmost byte
0
4
8
12
…
1
5
9
13
…
2
6
10
14
…
3
7
11
15
…
Addr of lowest byte in word is addr of word

## Slide 41: Transfer from Memory to Register
MIPS instruction: Load Word, abbreviated lw
Assume A is an array of 100 words, variables g and h map to registers $s1 and $s2, the starting address/base address of the array A is in $s3
g = h + A[3];
Becomes:
lw $t0, 3($s3) # Temp reg $t0 gets A[3]
add $s1,$s2,$t0 # g = h + A[3]
12
Notes: Re]lace 8 with 32 on lw

## Slide 42: Transfer from Register to Memory
MIPS instruction: Store Word, abbreviated sw
Assume A is an array of 100 words, variables g and h map to registers $s1 and $s2, the starting address, or base address, of the array A is in $s3
A[10] = h + A[3];
Turns into
lw $t0,12($s3) # Temp reg $t0 gets A[3]
add $t0,$s2,$t0 # t0 = h + A[3]
# A[10] = h + A[3]
Notes: Add
sw $t0, 40($s3) # Stores h+A[3] into A[10]

## Slide 43: Transfer from Register to Memory
MIPS instruction: Store Word, abbreviated sw
Assume A is an array of 100 words, variables g and h map to registers $s1 and $s2, the starting address, or base address, of the array A is in $s3
A[10] = h + A[3];
Turns into
lw $t0,12($s3) # Temp reg $t0 gets A[3]
add $t0,$s2,$t0 # t0 = h + A[3]
sw $t0,40($s3) # A[10] = h + A[3]
Notes: Add
sw $t0, 40($s3) # Stores h+A[3] into A[10]

## Slide 44: Speed of Registers vs. Memory
Given that
  Registers: 32 words (128 Bytes)
  Memory: Billions of bytes (2 GB to 8 GB on laptop)
and the RISC principle is…
  Smaller is faster
How much faster are registers than memory??
About 100-500 times faster!

## Slide 45
Can byte address 8GB with a MIPS word
imm must be a multiple of 4 for
lw $t0,imm($s0) to be valid
If MIPS halved the number of registers
available, it would be twice as fast
add $t0,$t1,4($t2) is valid MIPS
☐
☐
☐
☐
Which of the following is TRUE?
Notes: VertLeftWhiteCheck1
B: Print 4 …because ints in this system are 4-bytes long and the actual address increments by 4 even though it appears to only incrememt 1.

## Slide 46
Can byte address 8GB with a MIPS word
imm must be a multiple of 4 for
lw $t0,imm($s0) to be valid
If MIPS halved the number of registers
available, it would be twice as fast
add $t0,$t1,4($t2) is valid MIPS
☐
☐
☐
☐
Which of the following is TRUE? NONE!
Notes: VertLeftWhiteCheck1
B: Print 4 …because ints in this system are 4-bytes long and the actual address increments by 4 even though it appears to only incrememt 1.

## Slide 47: And In Conclusion …
Computer words and vocabulary are called instructions and instruction set respectively
MIPS is example RISC instruction set in this class
Rigid format: one operation, two source operands, one destination
  add, sub, mul, div, and, or, sll, srl
  lw, sw to move data to/from registers from/to memory
Simple mappings from arithmetic expressions, array access, if-then-else in C to MIPS instructions