## Slide 1: CS 61C: Great Ideas in Computer Architecture More MIPS Machine Language
Instructor:
Randy H. Katz
http://inst.eecs.Berkeley.edu/~cs61c/fa12

## Slide 2: New-School Machine Structures (It’s a bit more complicated!)
Parallel Requests
  Assigned to computer
  e.g., Search “Katz”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates @ one time
Programming Languages
Smart Phone
Warehouse Scale Computer
Software Hardware
Harness Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory (Cache)
Input/Output
Computer
Cache Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0
Today’s Lecture

## Slide 3: Big Idea #1: Levels of Representation/Interpretation
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
High Level Language Program (e.g., C)
Assembly Language Program (e.g., MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g., block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation
Anything can be represented as a number, i.e., data or instructions

## Slide 4: Review
Computer words and vocabulary are called instructions and instruction set respectively
MIPS is example RISC instruction set in this class
Rigid format: 1 operation, 2 source operands, 1 destination
  add, sub, mul, div, and, or, sll, srl
  lw, sw to move data to/from registers from/to memory
Simple mappings from arithmetic expressions, array access, if-then-else in C to MIPS instructions

## Slide 5: Agenda
Decisions
Strings
Administrivia
String Copy Example
Technology Break
Functions
MIPS register allocation convention
Memory Heap
And in Conclusion, …

## Slide 6: Agenda
Decisions
Strings
Administrivia
String Copy Example
Technology Break
Functions
MIPS register allocation convention
Memory Heap
And in Conclusion, …

## Slide 7: Computer Decision Making
Based on computation, do something different
In programming languages: if-statement
  Sometimes combined with gotos and labels
MIPS: if-statement instruction is
beq register1,register2,L1
means go to statement labeled L1 if value in register1 = value in register2
(otherwise, go to next statement)
beq stands for branch if equal
Other instruction: bne for branch if not equal

## Slide 8: Example If Statement
Assuming translations below, compile if block
f → $s0 g → $s1 h → $s2
i → $s3 j → $s4
if (i == j) bne $s3,$s4,Exit
f = g + h; add $s0,$s1,$s2
Exit:
May need to negate branch condition

## Slide 9: Example If Statement
Assuming translations below, compile if block
f → $s0 g → $s1 h → $s2
i → $s3 j → $s4
if (i == j) bne $s3,$s4,Exit
f = g + h; add $s0,$s1,$s2
Exit:
May need to negate branch condition

## Slide 10: Types of Branches
Branch – change of control flow
Conditional Branch – change control flow depending on outcome of comparison
  branch if equal (beq) or branch if not equal (bne)
Unconditional Branch – always branch
  a MIPS instruction for this: jump (j)

## Slide 11: Making Decisions in C or Java
if (i == j)
f = g + h;
else
f = g – h;
If false, skip over “then” part to “else” part => use conditional branch bne
Otherwise, (its true) do “then” part and skip over “else” part => use unconditional branch j

## Slide 12: Making Decisions in MIPS
Assuming translations below, compile
f → $s0 g → $s1 h → $s2
i → $s3 j → $s4
if (i == j) bne $s3,$s4,Else
f = g + h; add $s0,$s1,$s2
else j Exit
f = g – h; Else: sub $s0,$s1,$s2
Exit:

## Slide 13: Making Decisions in MIPS
Assuming translations below, compile
f → $s0 g → $s1 h → $s2
i → $s3 j → $s4
if (i == j) bne $s3,$s4,Else
f = g + h; add $s0,$s1,$s2
else j Exit
f = g – h; Else: sub $s0,$s1,$s2
Exit:

## Slide 14
Can make a loop with j
Can make a loop with beq
Can always return from a function call with j
Can make an unconditional branch from a
conditional branch instruction
☐
☐
☐
☐
Which of the following is FALSE?
Notes: VertLeftWhiteCheck1
B: Print 4 …because ints in this system are 4-bytes long and the actual address increments by 4 even though it appears to only incrememt 1.

## Slide 15
Can make a loop with j
Can make a loop with beq
Can always return from a function call with j
Can make an unconditional branch from a
conditional branch instruction
☐
☐
☐
☐
Which of the following is FALSE?
Notes: VertLeftWhiteCheck1
B: Print 4 …because ints in this system are 4-bytes long and the actual address increments by 4 even though it appears to only incrememt 1.

## Slide 16: Agenda
Decisions
Strings
Administrivia
String Copy Example
Technology Break
Functions
MIPS register allocation convention
Memory Heap
And in Conclusion, …

## Slide 17: Strings: C vs. Java
Recall: a string is just a long sequence of characters (i.e., array of chars)
C: 8-bit ASCII, define strings with end of string character NUL (0 in ASCII)
Java: 16-bit Unicode, first entry gives length of string

## Slide 18: Strings
“Cal” in ASCII in C; How many bytes?
Using 1 integer per byte, what does it look like?
Notes: Thus, the
string “Cal” is represented in C by the following 4 bytes, shown as decimal numbers:
67, 97, 108, 0.

## Slide 19: Strings
“Cal” in ASCII in C; How many bytes?
Using 1 integer per byte, what does it look like?
Notes: Thus, the
string “Cal” is represented in C by the following 4 bytes, shown as decimal numbers:
67, 97, 108, 0.

## Slide 20: Strings
“Cal” in Unicode in Java; How many bytes?
Using 1 integer per byte, what does it look like? (For Latin alphabet, 1st byte is 0, 2nd byte is ASCII)
Notes: Thus, the
string “Cal” is represented in C by the following 10 bytes, shown as decimal numbers:
0, 0, 0, 3, 0, 67, 0, 97, 0, 108
(32 bit word contains string length)

## Slide 21: Strings
“Cal” in Unicode in Java; How many bytes?
Using 1 integer per byte, what does it look like? (For Latin alphabet, 1st byte is 0, 2nd byte is ASCII)
Notes: Thus, the
string “Cal” is represented in C by the following 10 bytes, shown as decimal numbers:
0, 0, 0, 3, 0, 67, 0, 97, 0, 108
(32 bit word contains string length)

## Slide 22: Support for Characters and Strings
Load a word, use andi to isolate byte
lw $s0,0($s1)
andi $s0,$s0,255 # Zero everything but last 8 bits
RISC Design Principle: “Make the Common Case Fast”—Many programs use text: MIPS has load byte instruction (lb)
lb $s0,0($s1)
Also store byte instruction (sb)

## Slide 23: Support for Characters and Strings
Load a word, use andi to isolate half of word
lw $s0,0($s1)
andi $s0,$s0,65535 # Zero everything but last 16 bits
RISC Design Principle #3: “Make the Common Case Fast”—Many programs use text, MIPS has load halfword instruction (lh)
lh $s0,0($s1)
Also store halfword instruction (sh)

## Slide 24: Endianess
MIPS is Big Endian
  Most-significant byte at least address of a word
  c.f. Little Endian: least-significant byte at least address
Big Endian: address of most significant byte = word address (xx00 = “Big End” of word): IBM 360/370, MIPS, Sparc
Little Endian: address of least significant byte = word address (xx00 = “Little End” of word): Intel 80x86
Can only tell if access same data with load/store byte and load/store word
msb
lsb
3 2 1 0
little endian byte 0
0 1 2 3
big endian byte 0

## Slide 25: Agenda
Decisions
Strings
Administrivia
String Copy Example
Technology Break
Functions
MIPS register allocation convention
Memory Heap
And in Conclusion, …

## Slide 26: Administrivia
This week in lab and homework:
  Lab #3 EC2
  HW #3 Posted
  Project #1 posted

## Slide 27: CS61c In the News

## Slide 28: Agenda
Decisions
Strings
Administrivia
String Copy Example
Functions
Technology Break
MIPS register allocation convention
Memory Heap
And in Conclusion, …

## Slide 29: Fast String Copy Code in C
Copy x[] to y[]
char *p, *q;
p = &x[0]; /* p = x */
/* set p to address of 1st char of x */
q = &y[0]; /* q = y also OK */
/* set q to address of 1st char of y */
while((*q++ = *p++) != ‘\0’) ;

## Slide 30: Fast String Copy in MIPS Assembly
Get addresses of x and y into $s1, $s2
p and q are assigned to these registers
# $t1 = &p (BA), q @ &p + 4
# $s1 = p
# $s2 = q
Loop: # $t2 = *p
# *q = $t2
# p = p + 1
# q = q + 1
# if *p == 0, go to Exit
j Loop # go to Loop
Exit: # N characters => N*6 + 3 instructions
P
Q
BA
BA+4

## Slide 31: Fast String Copy in MIPS Assembly
Get addresses of x and y into $s1, $s2
p and q are assigned to these registers
lw $t1, Base Address (e.g., BA)
# $s1 = p
# $s2 = q
Loop: # $t2 = *p
# *q = $t2
# p = p + 1
# q = q + 1
# if *p == 0, go to Exit
j Loop # go to Loop
Exit: # N characters => N*6 + 3 instructions
P
Q
BA
BA+4
Student Roulette?

## Slide 32: Fast String Copy in MIPS Assembly
Get addresses of x and y into $s1, $s2
p and q are assigned to these registers
lw $t1, Base Address (e.g., BA)
lw $s1,0($t1) # $s1 = p
# $s2 = q
Loop: # $t2 = *p
# *q = $t2
# p = p + 1
# q = q + 1
# if *p == 0, go to Exit
j Loop # go to Loop
Exit: # N characters => N*6 + 3 instructions
P
Q
BA
BA+4
Student Roulette?

## Slide 33: Fast String Copy in MIPS Assembly
Get addresses of x and y into $s1, $s2
p and q are assigned to these registers
lw $t1, Base Address (e.g., BA)
lw $s1,0($t1) # $s1 = p
lw $s2,4($t1) # $s2 = q
Loop: # $t2 = *p
# *q = $t2
# p = p + 1
# q = q + 1
# if *p == 0, go to Exit
j Loop # go to Loop
Exit: # N characters => N*6 + 3 instructions
P
Q
BA
BA+4
Student Roulette?

## Slide 34: Fast String Copy in MIPS Assembly
Get addresses of x and y into $s1, $s2
p and q are assigned to these registers
lw $t1, Base Address (e.g., BA)
lw $s1,0($t1) # $s1 = p
lw $s2,4($t1) # $s2 = q
Loop: lb $t2,0($s1) # $t2 = *p
# *q = $t2
# p = p + 1
# q = q + 1
# if *p == 0, go to Exit
j Loop # go to Loop
Exit: # N characters => N*6 + 3 instructions
P
Q
BA
BA+4
Student Roulette?

## Slide 35: Fast String Copy in MIPS Assembly
Get addresses of x and y into $s1, $s2
p and q are assigned to these registers
lw $t1, Base Address (e.g., BA)
lw $s1,0($t1) # $s1 = p
lw $s2,4($t1) # $s2 = q
Loop: lb $t2,0($s1) # $t2 = *p
sb $t2,0($s2) # *q = $t2
# p = p + 1
# q = q + 1
# if *p == 0, go to Exit
j Loop # go to Loop
Exit: # N characters => N*6 + 3 instructions
P
Q
BA
BA+4
Student Roulette?

## Slide 36: Fast String Copy in MIPS Assembly
Get addresses of x and y into $s1, $s2
p and q are assigned to these registers
lw $t1, Base Address (e.g., BA)
lw $s1,0($t1) # $s1 = p
lw $s2,4($t1) # $s2 = q
Loop: lb $t2,0($s1) # $t2 = *p
sb $t2,0($s2) # *q = $t2
addi $s1,$s1,1 # p = p + 1
# q = q + 1
# if *p == 0, go to Exit
j Loop # go to Loop
Exit: # N characters => N*6 + 3 instructions
P
Q
BA
BA+4
Student Roulette?

## Slide 37: Fast String Copy in MIPS Assembly
Get addresses of x and y into $s1, $s2
p and q are assigned to these registers
lw $t1, Base Address (e.g., BA)
lw $s1,0($t1) # $s1 = p
lw $s2,4($t1) # $s2 = q
Loop: lb $t2,0($s1) # $t2 = *p
sb $t2,0($s2) # *q = $t2
addi $s1,$s1,1 # p = p + 1
addi $s2,$s2,1 # q = q + 1
# if *p == 0, go to Exit
j Loop # go to Loop
Exit: # N characters => N*6 + 3 instructions
P
Q
BA
BA+4
Student Roulette?

## Slide 38: Fast String Copy in MIPS Assembly
Get addresses of x and y into $s1, $s2
p and q are assigned to these registers
lw $t1, Base Address (e.g., BA)
lw $s1,0($t1) # $s1 = p
lw $s2,4($t1) # $s2 = q
Loop: lb $t2,0($s1) # $t2 = *p
sb $t2,0($s2) # *q = $t2
addi $s1,$s1,1 # p = p + 1
addi $s2,$s2,1 # q = q + 1
beq $t2,$zero,Exit # if *p == 0, go to Exit
j Loop # go to Loop
Exit: # N characters => N*6 + 3 instructions
P
Q
BA
BA+4
Student Roulette?

## Slide 39
$s1 corresponds to p
$s1 corresponds to q
$s1 corresponds to *p
$t1 corresponds to p
☐
☐
☐
☐
Which statement is TRUE?
lw $t1, Base Address (e.g., BA)
lw $s1,0($t1) # $s1 = p
lw $s2,4($t1) # $s2 = q
Loop: lb $t2,0($s1) # $t2 = *p
sb $t2,0($s2) # *q = $t2
addi $s1,$s1,1 # p = p + 1
addi $s2,$s2,1 # q = q + 1
beq $t2,$zero,Exit # if *p == 0, go to Exit
j Loop # go to Loop
Exit:
char *p, *q;
p = &x[0]; q = &y[0];
while((*q++ = *p++) != ‘\0’) ;
Notes: VertLeftWhiteCheck1
Answer: B s1 corresponds to p,
($s2 corresponds to q)
($t1 corresponds to &x[0])
*p lb/sb $t2,0($s1) = value in $t2 at right point …because ints in this system are 4-bytes long and the actual address increments by 4 even though it appears to only incrememt 1.

## Slide 40
$s1 corresponds to p
$s1 corresponds to q
$s1 corresponds to *p
$t1 corresponds to p
☐
☐
☐
☐
Which statement is TRUE?
lw $t1, Base Address (e.g., BA)
lw $s1,0($t1) # $s1 = p
lw $s2,4($t1) # $s2 = q
Loop: lb $t2,0($s1) # $t2 = *p
sb $t2,0($s2) # *q = $t2
addi $s1,$s1,1 # p = p + 1
addi $s2,$s2,1 # q = q + 1
beq $t2,$zero,Exit # if *p == 0, go to Exit
j Loop # go to Loop
Exit:
char *p, *q;
p = &x[0]; q = &y[0];
while((*q++ = *p++) != ‘\0’) ;
Notes: VertLeftWhiteCheck1
Answer: B s1 corresponds to p,
($s2 corresponds to q)
($t1 corresponds to &x[0])
*p lb/sb $t2,0($s1) = value in $t2 at right point …because ints in this system are 4-bytes long and the actual address increments by 4 even though it appears to only incrememt 1.

## Slide 41: Assembler Pseudo-instructions
Register $zero always contains 0
Can use “pseudo-instruction” in assembly language to make it programming easier
Example
clear $rt
Implemented as:
add $rt, $zero, $zero

## Slide 42: More Pseudo-Instructions

## Slide 43: Assembler Pseudo-instructions
See http://en.wikipedia.org/wiki/MIPS_architecture
Load Address (asm temp regs): $at = Label Address
la $at, LabelAddr
Implemented as:
lui $at, LabelAddr[31:16];
ori $at, $at, LabelAddr[15:0]

## Slide 44: Agenda
Decisions
Strings
Administrivia
String Copy Example
Technology Break
Functions
MIPS register allocation convention
Memory Heap
And in Conclusion, …

## Slide 45: Agenda
Decisions
Strings
Administrivia
String Copy Example
Technology Break
Functions
MIPS register allocation convention
Memory Heap
And in Conclusion, …

## Slide 46: Six Fundamental Steps in Calling a Function
Put parameters in a place where function can access them
Transfer control to function
Acquire (local) storage resources needed for function
Perform desired task of the function
Put result value in a place where calling program can access it and restore any registers you used
Return control to point of origin, since a function can be called from several points in a program

## Slide 47: MIPS Function Call Conventions
Registers way faster than memory, so use registers
$a0–$a3: four argument registers to pass parameters
$v0–$v1: two value registers to return values
$ra: one return address register to return to the point of origin
(7 + $zero +$at of 32, 23 left!)

## Slide 48: MIPS Registers Assembly Language Conventions
$t0-$t9: 10 x temporaries (intermediates)
$s0-$s7: 8 x “saved” temporaries (program variables)
18 registers
32 – (18 + 9) = 5 left

## Slide 49: MIPS Function Call Instructions
Invoke function: jump and link instruction (jal)
  “link” means form an address or link that points to calling site to allow function to return to proper address
  Jumps to address and simultaneously saves the address of following instruction in register $ra
  jal ProcedureAddress
Return from function: jump register instruction (jr)
  Unconditional jump to address specified in register
  jr $ra

## Slide 50: Notes on Functions
Calling program (caller) puts parameters into registers $a0-$a3 and uses jal X to invoke X (callee)
Must have register in computer with address of currently executing instruction
  Instead of Instruction Address Register (better name), historically called Program Counter (PC)
  It’s a program’s counter; it doesn’t count programs!
jr $ra puts address inside $ra into PC
What value does jal X place into $ra? ????
Student Roulette?

## Slide 51: Notes on Functions
Calling program (caller) puts parameters into registers $a0-$a3 and uses jal X to invoke X (callee)
Must have register in computer with address of currently executing instruction
  Instead of Instruction Address Register (better name), historically called Program Counter (PC)
  It’s a program’s counter, it doesn’t count programs!
jr $ra puts address inside $ra into PC
What value does jal X place into $ra? Next PC
PC + 4

## Slide 52: Where Save Old Registers Values to Restore Them After Function Call
Need a place to place old values before call function, restore them when return, and delete
Ideal is stack: last-in-first-out queue (e.g., stack of plates)
  Push: placing data onto stack
  Pop: removing data from stack
Stack in memory, so need register to point to it
$sp is the stack pointer in MIPS
Convention is grow from high to low addresses
  Push decrements $sp, Pop increments $sp
(28 out of 32, 4 left!)

## Slide 53: Example
int leaf_example (int g, int h, int i, int j)
{
int f;
f = (g + h) – (i + j);
return f;
}
Parameter variables g, h, i, and j in argument registers $a0, $a1, $a2, and $a3, and f in $s0
Assume need one temporary register $t0

## Slide 54: Stack Before, During, After Function
Need to save old values of $s0 and $t0
Contents of $s0
Contents of $t0

## Slide 55: MIPS Code for leaf_example
leaf_example:
# adjust stack for 2 int items
# save $t0 for use afterwards
# save $s0 for use afterwards
# f = g + h
# t0 = i + j
# return value (g + h) – (i + j)
# restore $s0 for caller
# restore $t0 for caller
# delete 2 items from stack
# jump back to calling routine
Notes: addi $sp,$sp,-8 # adjust stack for 2 items
sw $t0, 4($sp) # save $t0 for use afterwards
sw $s0, 0($sp) # save $s0 for use afterwards
add $s0,$a0,$a1 # f = g + h
add $t0,$a2,$a3 # t0 = i + j
sub $v0,$s0,$t0 # return value (g + h) – (i + j)
lw $s0, 0($sp) # restore register $s0 for caller
lw $t0, 4($sp) # restore register $t0 for caller
addi $sp,$sp,8 # adjust stack to delete 2 items
jr $ra # jump back to calling routine

## Slide 56: MIPS Code for leaf_example
leaf_example:
addi $sp,$sp,-8 # adjust stack for 2 int items
# save $t0 for use afterwards
# save $s0 for use afterwards
# f = g + h
# $t0 = i + j
# return value (g + h) – (i + j)
# restore register $s0 for caller
# restore register $t0 for caller
# adjust stack to delete 2 items
# jump back to calling routine

## Slide 57: MIPS Code for leaf_example
leaf_example:
addi $sp,$sp,-8 # adjust stack for 2 int items
sw $t0, 4($sp) # save $t0 for use afterwards
# save $s0 for use afterwards
# f = g + h
# $t0 = i + j
# return value (g + h) – (i + j)
# restore register $s0 for caller
# restore register $t0 for caller
# adjust stack to delete 2 items
# jump back to calling routine

## Slide 58: MIPS Code for leaf_example
leaf_example:
addi $sp,$sp,-8 # adjust stack for 2 int items
sw $t0, 4($sp) # save $t0 for use afterwards
sw $s0, 0($sp) # save $s0 for use afterwards
# f = g + h
# $t0 = i + j
# return value (g + h) – (i + j)
# restore register $s0 for caller
# restore register $t0 for caller
# adjust stack to delete 2 items
# jump back to calling routine

## Slide 59: MIPS Code for leaf_example
leaf_example:
addi $sp,$sp,-8 # adjust stack for 2 int items
sw $t0, 4($sp) # save $t0 for use afterwards
sw $s0, 0($sp) # save $s0 for use afterwards
add $s0,$a0,$a1 # f = g + h
# $t0 = i + j
# return value (g + h) – (i + j)
# restore register $s0 for caller
# restore register $t0 for caller
# adjust stack to delete 2 items
# jump back to calling routine

## Slide 60: MIPS Code for leaf_example
leaf_example:
addi $sp,$sp,-8 # adjust stack for 2 int items
sw $t0, 4($sp) # save $t0 for use afterwards
sw $s0, 0($sp) # save $s0 for use afterwards
add $s0,$a0,$a1 # f = g + h
add $t0,$a2,$a3 # $t0 = i + j
# return value (g + h) – (i + j)
# restore register $s0 for caller
# restore register $t0 for caller
# adjust stack to delete 2 items
# jump back to calling routine

## Slide 61: MIPS Code for leaf_example
leaf_example:
addi $sp,$sp,-8 # adjust stack for 2 int items
sw $t0, 4($sp) # save $t0 for use afterwards
sw $s0, 0($sp) # save $s0 for use afterwards
add $s0,$a0,$a1 # f = g + h
add $t0,$a2,$a3 # $t0 = i + j
sub $v0,$s0,$t0 # return value (g + h) – (i + j)
# restore register $s0 for caller
# restore register $t0 for caller
# adjust stack to delete 2 items
# jump back to calling routine

## Slide 62: MIPS Code for leaf_example
leaf_example:
addi $sp,$sp,-8 # adjust stack for 2 int items
sw $t0, 4($sp) # save $t0 for use afterwards
sw $s0, 0($sp) # save $s0 for use afterwards
add $s0,$a0,$a1 # f = g + h
add $t0,$a2,$a3 # t0 = i + j
sub $v0,$s0,$t0 # return value (g + h) – (i + j)
lw $s0, 0($sp) # restore register $s0 for caller
# restore register $t0 for caller
# adjust stack to delete 2 items
# jump back to calling routine

## Slide 63: MIPS Code for leaf_example
leaf_example:
addi $sp,$sp,-8 # adjust stack for 2 int items
sw $t0, 4($sp) # save $t0 for use afterwards
sw $s0, 0($sp) # save $s0 for use afterwards
add $s0,$a0,$a1 # f = g + h
add $t0,$a2,$a3 # $t0 = i + j
sub $v0,$s0,$t0 # return value (g + h) – (i + j)
lw $s0, 0($sp) # restore register $s0 for caller
lw $t0, 4($sp) # restore register $t0 for caller
# adjust stack to delete 2 items
# jump back to calling routine

## Slide 64: MIPS Code for leaf_example
leaf_example:
addi $sp,$sp,-8 # adjust stack for 2 int items
sw $t0, 4($sp) # save $t0 for use afterwards
sw $s0, 0($sp) # save $s0 for use afterwards
add $s0,$a0,$a1 # f = g + h
add $t0,$a2,$a3 # $t0 = i + j
sub $v0,$s0,$t0 # return value (g + h) – (i + j)
lw $s0, 0($sp) # restore register $s0 for caller
lw $t0, 4($sp) # restore register $t0 for caller
addi $sp,$sp,8 # adjust stack to delete 2 items
# jump back to calling routine
Student Roulette?

## Slide 65: MIPS Code for leaf_example
leaf_example:
addi $sp,$sp,-8 # adjust stack for 2 int items
sw $t0, 4($sp) # save $t0 for use afterwards
sw $s0, 0($sp) # save $s0 for use afterwards
add $s0,$a0,$a1 # f = g + h
add $t0,$a2,$a3 # $t0 = i + j
sub $v0,$s0,$t0 # return value (g + h) – (i + j)
lw $s0, 0($sp) # restore register $s0 for caller
lw $t0, 4($sp) # restore register $t0 for caller
addi $sp,$sp,8 # adjust stack to delete 2 items
jr $ra # jump back to calling routine

## Slide 66
Print 4
a.out will crash
None of the above
Print -4
☐
☐
☐
☐
What will the printf output?
static int *p;
int leaf (int g, int h, int i, int j)
{
int f; p = &f;
f = (g + h) – (i + j);
return f;
}
int main(void) { int x;
x = leaf(1,2,3,4);
x = leaf(3,4,1,2);
…
printf(”%d\n”,*p);
}
Notes: VertLeftWhiteCheck1
B: Print 4 …because ints in this system are 4-bytes long and the actual address increments by 4 even though it appears to only incrememt 1.

## Slide 67
Print 4
a.out will crash
None of the above
Print -4
☐
☐
☐
☐
What will the printf output?
static int *p;
int leaf (int g, int h, int i, int j)
{
int f; p = &f;
f = (g + h) – (i + j);
return f;
}
int main(void) { int x;
x = leaf(1,2,3,4);
x = leaf(3,4,1,2);
…
printf(”%d\n”,*p);
}
Notes: VertLeftWhiteCheck1
B: Print 4 …because ints in this system are 4-bytes long and the actual address increments by 4 even though it appears to only incrememt 1.

## Slide 68: And in Conclusion, …
C is function oriented; code reuse via functions
  Jump and link (jal) invokes, jump register (jr $ra) returns
  Registers $a0-$a3 for arguments, $v0-$v1 for return values
Stack for spilling registers, nested function calls, C local (automatic) variables