## Slide 1: CS 61C: Great Ideas in Computer Architecture Everything is a Number
Instructor:
Randy H. Katz
http://inst.eecs.Berkeley.edu/~cs61c/fa13

## Slide 2: New-School Machine Structures (It’s a bit more complicated!)
Parallel Requests
  Assigned to computer
  e.g., Search “Katz”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates @ one time
Programming Languages
Smart Phone
Warehouse Scale Computer
Software Hardware
Harness Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory (Cache)
Input/Output
Computer
Cache Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0
Today’s Lecture

## Slide 3: Big Idea #1: Levels of Representation/Interpretation
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
High Level Language Program (e.g., C)
Assembly Language Program (e.g., MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g., block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation
Anything can be represented as a number, i.e., data or instructions
We are here!

## Slide 4: Review
C is function oriented; code reuse via functions
  Jump and link (jal) invokes, jump register (jr $ra) returns
  Registers $a0-$a3 for arguments, $v0-$v1 for return values
Stack for spilling registers, nested function calls, C local (automatic) variables

## Slide 5: Agenda
Memory Heap
Everything is a Number
Administrivia
Overflow and Real Numbers
Technology Break
Instructions as Numbers
Assembly Language to Machine Language
And in Conclusion, …

## Slide 6: Agenda
Memory Heap
Everything is a Number
Administrivia
Overflow and Real Numbers
Technology Break
Instructions as Numbers
Assembly Language to Machine Language
And in Conclusion, …

## Slide 7: What If a Function Calls a Function? Recursive Function Calls?
Would clobber values in $a0 to $a1 and $ra
What is the solution?
Notes: Save $ra on the stack

## Slide 8: Allocating Space on Stack
C has two storage classes: automatic and static
  Automatic variables are local to function and discarded when function exits.
  Static variables exist across exits from and entries to procedures
Use stack for automatic (local) variables that don’t fit in registers
Procedure frame or activation record: segment of stack with saved registers and local variables
Some MIPS compilers use a frame pointer ($fp) to point to first word of frame
(29 of 32, 3 left!)

## Slide 9: Stack Before, During, After Call

## Slide 10: Recursive Function Factorial
int fact (int n)
{
if (n < 1) return (1);
else return (n * fact(n-1));
}

## Slide 11: Recursive Function Factorial
Fact: # adjust stack for 2 items
addi $sp,$sp,-8
# save return address
sw $ra, 4($sp) # save argument n
sw $a0, 0($sp) # test for n < 1
slti $t0,$a0,1
# if n >= 1, go to L1
beq $t0,$zero,L1 # Then part (n==1) return 1
addi $v0,$zero,1 # pop 2 items off stack
addi $sp,$sp,8 # return to caller
jr $ra
L1:
# Else part (n >= 1) # arg. gets (n – 1)
addi $a0,$a0,-1 # call fact with (n – 1)
jal fact
# return from jal: restore n
lw $a0, 0($sp) # restore return address
lw $ra, 4($sp) # adjust sp to pop 2 items
addi $sp, $sp,8 # return n * fact (n – 1)
mul $v0,$a0,$v0 # return to the caller
jr $ra
mul is a pseudo instruction

## Slide 12: Optimized Function Convention
To reduce expensive loads and stores from spilling and restoring registers, MIPS divides registers into two categories:
Preserved across function call
  Caller can rely on values being unchanged
  $ra, $sp, $gp, $fp, “saved registers” $s0- $s7
Not preserved across function call
  Caller cannot rely on values being unchanged
  Return value registers $v0,$v1, Argument registers $a0-$a3, “temporary registers” $t0-$t9

## Slide 13: Where is the Stack in Memory?
MIPS convention
Stack starts in high memory and grows down
  Hexadecimal (base 16) : 7fff fffchex
MIPS programs (text segment) in low end
  0040 0000hex
Static data segment (constants and other static variables) above text for static variables
  MIPS convention global pointer ($gp) points to static
  (30 of 32, 2 left! – will see when talk about OS)
Heap above static for data structures that grow and shrink ; grows up to high addresses

## Slide 14: MIPS Memory Allocation

## Slide 15: Register Allocation and Numbering

## Slide 16
jal saves PC+1 in $ra
The callee can use temporary registers ($ti) without saving and restoring them
The caller can rely on save registers ($si) without fear of callee changing them
MIPS uses jal to invoke a function and jr to return from a function
☐
☐
☐
☐
Which statement is FALSE?
Notes: VertLeftWhiteCheck1
B: Print It saves PC+4 …because ints in this system are 4-bytes long and the actual address increments by 4 even though it appears to only incrememt 1.

## Slide 17
jal saves PC+1 in $ra
The callee can use temporary registers ($ti) without saving and restoring them
The caller can rely on save registers ($si) without fear of callee changing them
MIPS uses jal to invoke a function and jr to return from a function
☐
☐
☐
☐
Which statement is FALSE?
Notes: VertLeftWhiteCheck1
B: Print It saves PC+4 …because ints in this system are 4-bytes long and the actual address increments by 4 even though it appears to only incrememt 1.

## Slide 18: Agenda
Memory Heap
Everything is a Number
Administrivia
Overflow and Real Numbers
Technology Break
Instructions as Numbers
Assembly Language to Machine Language
Summary

## Slide 19: Key Concepts
Inside computers, everything is a number
But everything is of a fixed size
  8-bit bytes, 16-bit half words, 32-bit words, 64-bit double words, …
Integer and floating point operations can lead to results too big to store within their representations: overflow/underflow

## Slide 20: Number Representation
Value of i-th digit is d × Basei where i starts at 0 and increases from right to left:
12310 = 110 x 10102 + 210 x 10101 + 310 x 10100
= 1x10010 + 2x1010 + 3x110 = 10010 + 2010 + 310
= 12310
Binary (Base 2), Hexadecimal (Base 16), Decimal (Base 10) different ways to represent an integer
  We use 1two, 5ten, 10hex to be clearer (vs. 12, 48, 510, 1016 )

## Slide 21: Number Representation
Hexadecimal digits: 0,1,2,3,4,5,6,7,8,9,A,B,C,D,E,F
FFFhex = 15tenx 16ten2 + 15tenx 16ten1 + 15tenx 16ten0 = 3840ten + 240ten + 15ten = 4095ten
1111 1111 1111two = FFFhex = 4095ten
May put blanks every group of binary, octal, or hexadecimal digits to make it easier to parse, like commas in decimal

## Slide 22: Signed and Unsigned Integers
C, C++, and Java have signed integers, e.g., 7, -255:
  int x, y, z;
C, C++ also have unsigned integers, which are used for addresses
32-bit word can represent 232 binary numbers
Unsigned integers in 32 bit word represent 0 to 232-1 (4,294,967,295)

## Slide 23: Unsigned Integers
0000 0000 0000 0000 0000 0000 0000 0000two = 0ten
0000 0000 0000 0000 0000 0000 0000 0001two = 1ten
0000 0000 0000 0000 0000 0000 0000 0010two = 2ten
... ...
0111 1111 1111 1111 1111 1111 1111 1101two = 2,147,483,645ten
0111 1111 1111 1111 1111 1111 1111 1110two = 2,147,483,646ten
0111 1111 1111 1111 1111 1111 1111 1111two = 2,147,483,647ten
1000 0000 0000 0000 0000 0000 0000 0000two = 2,147,483,648ten
1000 0000 0000 0000 0000 0000 0000 0001two = 2,147,483,649ten
1000 0000 0000 0000 0000 0000 0000 0010two = 2,147,483,650ten
... ...
1111 1111 1111 1111 1111 1111 1111 1101two = 4,294,967,293ten
1111 1111 1111 1111 1111 1111 1111 1110two = 4,294,967,294ten
1111 1111 1111 1111 1111 1111 1111 1111two = 4,294,967,295ten

## Slide 24: Signed Integers and Two’s Complement Representation
Signed integers in C; want ½ numbers <0, want ½ numbers >0, and want one 0
Two’s complement treats 0 as positive, so 32-bit word represents 232 integers from -231 (–2,147,483,648) to 231-1 (2,147,483,647)
  Note: one negative number with no positive version
  Book lists some other options, all of which are worse
  Every computers uses two’s complement today
Most significant bit (leftmost) is the sign bit, since 0 means positive (including 0), 1 means negative
  Bit 31 is most significant, bit 0 is least significant

## Slide 25: Two’s Complement Integers
0000 0000 0000 0000 0000 0000 0000 0000two = 0ten
0000 0000 0000 0000 0000 0000 0000 0001two = 1ten
0000 0000 0000 0000 0000 0000 0000 0010two = 2ten
... ...
0111 1111 1111 1111 1111 1111 1111 1101two = 2,147,483,645ten
0111 1111 1111 1111 1111 1111 1111 1110two = 2,147,483,646ten
0111 1111 1111 1111 1111 1111 1111 1111two = 2,147,483,647ten
1000 0000 0000 0000 0000 0000 0000 0000two = –2,147,483,648ten
1000 0000 0000 0000 0000 0000 0000 0001two = –2,147,483,647ten
1000 0000 0000 0000 0000 0000 0000 0010two = –2,147,483,646ten
... ...
1111 1111 1111 1111 1111 1111 1111 1101two = –3ten
1111 1111 1111 1111 1111 1111 1111 1110two = –2ten
1111 1111 1111 1111 1111 1111 1111 1111two = –1ten
Sign Bit

## Slide 26: Twos Complement Examples
Assume for simplicity 4 bit width, -8 to +7 represented
0011
0010
3
+2
5
0101
0011
1110
3
+ (-2)
1
1 0001
0111
0001
7
+1
-8
1000
Overflow!
1101
1110
-3
+ (-2)
-5
1 1011
1000
1111
-8
+ (-1)
+7
1 0111
Underflow!
Carry into MSB =
Carry Out MSB
Carry into MSB =
Carry Out MSB

## Slide 27
0 to +31
-16 to +15
-15 to +16
-32 to +31
☐
☐
☐
☐
Suppose we had a 5 bit word. What integers can be represented in two’s complement?
Notes: VertLeftWhiteCheck1
B: Print 4 …because ints in this system are 4-bytes long and the actual address increments by 4 even though it appears to only incrememt 1.

## Slide 28
0 to +31
-16 to +15
-15 to +16
-32 to +31
☐
☐
☐
☐
Suppose we had a 5 bit word. What integers can be represented in two’s complement?
Notes: VertLeftWhiteCheck1
B: Print 4 …because ints in this system are 4-bytes long and the actual address increments by 4 even though it appears to only incrememt 1.

## Slide 29: MIPS Logical Instructions
Logical operations | C operators | Java operators | MIPS instructions
Bit-by-bit AND | & | & | and
Bit-by-bit OR | ¦ | ¦ | or
Bit-by-bit NOT | ~ | ~ | nor
Shift left | << | << | sll
Shift right | >> | >>> | srl
Useful to operate on fields of bits within a word
  e.g., characters within a word (8 bits)
Operations to pack /unpack bits into words
Called logical operations

## Slide 30: Bit-by-bit Definition
Operation | Input | Input | Output
AND | 0 | 0 | 0
AND | 0 | 1 | 0
AND | 1 | 0 | 0
AND | 1 | 1 | 1
OR | 0 | 0 | 0
OR | 0 | 1 | 1
OR | 1 | 0 | 1
OR | 1 | 1 | 1
NOR | 0 | 0 | 1
NOR | 0 | 1 | 0
NOR | 1 | 0 | 0
NOR | 1 | 1 | 0

## Slide 31: Examples
If register $t2 contains
0000 0000 0000 0000 0000 1101 1100 0000two
And register $t1 contains
0000 0000 0000 0000 0011 1100 0000 0000two
What is value of $t0 after:
and $t0,$t1,$t2 # reg $t0 = reg $t1 & reg $t2
Notes: and $t0,$t1,$t2 # reg $t0 = reg $t1 & reg $t2
the value of register $t0 would be
0000 0000 0000 0000 0000 1100 0000 0000two
Called a mask
or $t0,$t1,$t2 # reg $t0 = reg $t1 | reg $t2
is this value in register $t0:
0000 0000 0000 0000 0011 1101 1100 0000two
has the value 0, the result of the MIPS instruction
nor $t0,$t1,$zero # reg $t0 = ~ (reg $t1 | 0)
is this value in register $t0:
1111 1111 1111 1111 1100 0011 1111 1111two

## Slide 32: Examples
If register $t2 contains
0000 0000 0000 0000 0000 1101 1100 0000two
And register $t1 contains
0000 0000 0000 0000 0011 1100 0000 0000two
What is value of $t0 after:
and $t0,$t1,$t2 # reg $t0 = reg $t1 & reg $t2
0000 0000 0000 0000 0000 1100 0000 0000two
Notes: and $t0,$t1,$t2 # reg $t0 = reg $t1 & reg $t2
the value of register $t0 would be
0000 0000 0000 0000 0000 1100 0000 0000two
Called a mask
or $t0,$t1,$t2 # reg $t0 = reg $t1 | reg $t2
is this value in register $t0:
0000 0000 0000 0000 0011 1101 1100 0000two
has the value 0, the result of the MIPS instruction
nor $t0,$t1,$zero # reg $t0 = ~ (reg $t1 | 0)
is this value in register $t0:
1111 1111 1111 1111 1100 0011 1111 1111two

## Slide 33: Examples
If register $t2 contains
0000 0000 0000 0000 0000 1101 1100 0000two
And register $t1 contains
0000 0000 0000 0000 0011 1100 0000 0000two
What is value of $t0 after:
or $t0,$t1,$t2 # reg $t0 = reg $t1 | reg $t2
Notes: or $t0,$t1,$t2 # reg $t0 = reg $t1 | reg $t2
is this value in register $t0:
0000 0000 0000 0000 0011 1101 1100 0000two
has the value 0, the result of the MIPS instruction
nor $t0,$t1,$zero # reg $t0 = ~ (reg $t1 | 0)
is this value in register $t0:
1111 1111 1111 1111 1100 0011 1111 1111two

## Slide 34: Examples
If register $t2 contains
0000 0000 0000 0000 0000 1101 1100 0000two
And register $t1 contains
0000 0000 0000 0000 0011 1100 0000 0000two
What is value of $t0 after:
or $t0,$t1,$t2 # reg $t0 = reg $t1 | reg $t2
0000 0000 0000 0000 0011 1101 1100 0000two
Notes: or $t0,$t1,$t2 # reg $t0 = reg $t1 | reg $t2
is this value in register $t0:
0000 0000 0000 0000 0011 1101 1100 0000two
has the value 0, the result of the MIPS instruction
nor $t0,$t1,$zero # reg $t0 = ~ (reg $t1 | 0)
is this value in register $t0:
1111 1111 1111 1111 1100 0011 1111 1111two

## Slide 35: Examples
If register $t2 contains
0000 0000 0000 0000 0000 1101 1100 0000two
And register $t1 contains
0000 0000 0000 0000 0011 1100 0000 0000two
What is value of $t0 after:
nor $t0,$t1,$zero # reg $t0 = ~ (reg $t1 | 0)
Notes: and $t0,$t1,$t2 # reg $t0 = reg $t1 & reg $t2
the value of register $t0 would be
0000 0000 0000 0000 0000 1100 0000 0000two
Called a mask
or $t0,$t1,$t2 # reg $t0 = reg $t1 | reg $t2
is this value in register $t0:
0000 0000 0000 0000 0011 1101 1100 0000two
has the value 0, the result of the MIPS instruction
nor $t0,$t1,$zero # reg $t0 = ~ (reg $t1 | 0)
is this value in register $t0:
1111 1111 1111 1111 1100 0011 1111 1111two

## Slide 36: Examples
If register $t2 contains
0000 0000 0000 0000 0000 1101 1100 0000two
And register $t1 contains
0000 0000 0000 0000 0011 1100 0000 0000two
What is value of $t0 after:
nor $t0,$t1,$zero # reg $t0 = ~ (reg $t1 | 0)
1111 1111 1111 1111 1100 0011 1111 1111two
Notes: has the value 0, the result of the MIPS instruction
nor $t0,$t1,$zero # reg $t0 = ~ (reg $t1 | 0)
is this value in register $t0:
1111 1111 1111 1111 1100 0011 1111 1111two

## Slide 37: Shifting
Shift left logical moves n bits to the left (insert 0s into empty bits)
  Same as multiplying by 2n for two’s complement number
For example, if register $s0 contained
0000 0000 0000 0000 0000 0000 0000 1001two= 9ten
If executed sll $s0, $s0, 4, result is:
0000 0000 0000 0000 0000 0000 1001 0000two= 144ten
And 9ten × 2ten4 = 9ten × 16ten = 144ten
Shift right logical moves n bits to the right (insert 0s into empty bits)
  NOT same as dividing by 2n (negative numbers fail)
Notes: -2
0010  1101 + 1  1110

## Slide 38: Shifting
Shift right arithmetic moves n bits to the right (insert high order sign bit into empty bits)
For example, if register $s0 contained
  0000 0000 0000 0000 0000 0000 0001 1001two= 25ten
If executed sra $s0, $s0, 4, result is:
Notes: -2
0010  1101 + 1  1110

## Slide 39: Shifting
Shift right arithmetic moves n bits to the right (insert high order sign bit into empty bits)
For example, if register $s0 contained
  0000 0000 0000 0000 0000 0000 0001 1001two= 25ten
If executed sra $s0, $s0, 4, result is:
0000 0000 0000 0000 0000 0000 0000 0001two= 1ten
Notes: -2
0010  1101 + 1  1110

## Slide 40: Shifting
Shift right arithmetic moves n bits to the right (insert high order sign bit into empty bits)
For example, if register $s0 contained
  1111 1111 1111 1111 1111 1111 1110 0111two= -25ten
If executed sra $s0, $s0, 4, result is:
Notes: \

## Slide 41: Shifting
Shift right arithmetic moves n bits to the right (insert high order sign bit into empty bits)
For example, if register $s0 contained
  1111 1111 1111 1111 1111 1111 1110 0111two= -25ten
If executed sra $s0, $s0, 4, result is:
1111 1111 1111 1111 1111 1111 1111 1110two= -2ten
  Unfortunately, this is NOT same as dividing by 2n
    Fails for odd negative numbers
    C arithmetic semantics is that division should round towards 0
Notes: \

## Slide 42: Impact of Signed and Unsigned Integers on Instruction Sets
What (if any) instructions affected?
  Load word, store word?
  branch equal, branch not equal?
  and, or, sll, srl?
  add, sub, mult, div?
  slti (set less than immediate)?

## Slide 43
The previous statement has it backwards: && and || logical ops, & and | are branches
They are redundant and mean the same thing: && and || are simply inherited from the programming language B, the predecessor of C
Logical operations AND and OR do & and | while conditional branches do && and ||
☐
☐
☐
C provides two sets of operators for AND (& and &&) and two sets of operators for OR (| and ||) while MIPS doesn’t. Why?
Notes: VertLeftWhiteCheck1
B: Print 4 …because ints in this system are 4-bytes long and the actual address increments by 4 even though it appears to only incrememt 1.

## Slide 44
The previous statement has it backwards: && and || logical ops, & and | are branches
They are redundant and mean the same thing: && and || are simply inherited from the programming language B, the predecessor of C
Logical operations AND and OR do & and | while conditional branches do && and ||
☐
☐
☐
C provides two sets of operators for AND (& and &&) and two sets of operators for OR (| and ||) while MIPS doesn’t. Why?
Notes: VertLeftWhiteCheck1
B: Print 4 …because ints in this system are 4-bytes long and the actual address increments by 4 even though it appears to only incrememt 1.

## Slide 45: Peer Instruction Answer
C provides two sets of operators for AND (& and &&) and two sets of operators for OR (| and ||) while MIPS doesn’t. Why?
Logical operations AND and OR implement & and | while conditional branches implement && and ||
Reason:
e.g., && is logical and: true && true is true and everything else is false
& is bitwise and: e.g., (1010two & 1000two) = 1000two

## Slide 46: Agenda
Memory Heap
Everything is a Number
Administrivia
Overflow and Real Numbers
Instructions as Numbers
Technology Break
Assembly Language to Machine Language
And in Conclusion, …

## Slide 47: Administrivia
HW #3 Due Sunday @ 11:59:59
Project #1 Part 1 Due Sunday @ 11:59:59
Midterm on the horizon:
  10/17 (4 weeks), 6-9 PM
  It’s going to be completely multiple choice!

## Slide 48: “And in Conclusion, …”
Program can interpret binary number as unsigned integer, two’s complement signed integer, floating point number, ASCII characters, Unicode characters, …
Integers have largest positive and largest negative numbers, but represent all in between
  Two’s comp. weirdness is one extra negative numInteger and floating point operations can lead to results too big to store within their representations: overflow/underflow
Floating point is an approximation of reals
Everything is a (binary) number in a computer
  Instructions and data; stored program concept