## Slide 1: CS 61C: Great Ideas in Computer Architecture Moore’s Law, Components
Instructor:
Randy H. Katz
http://inst.eecs.Berkeley.edu/~cs61c/fa13

## Slide 2: New-School Machine Structures (It’s a bit more complicated!)
Parallel Requests
  Assigned to computer
  e.g., Search “Katz”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates @ one time
Programming Languages
Smart Phone
Warehouse Scale Computer
Software Hardware
Harness Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory (Cache)
Input/Output
Computer
Cache Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0
Today’s Lecture

## Slide 3: Agenda
Review
Moore’s Law
Administrivia
ARM and MIPS
Technology Break
Components of a Computer

## Slide 4: Agenda
Review
Moore’s Law
Administrivia
ARM and MIPS
Technology Break
Components of a Computer

## Slide 5: Review
Assemblers can enhance machine instruction set to help assembly-language programmer
Translate from text that easy for programmers to understand into code that machine executes efficiently: Compilers, Assemblers
Linkers allow separate translation of modules
Interpreters for debugging, but slow execution
Hybrid (Java): Compiler + Interpreter to try to get best of both
Compiler Optimization to relieve programmer

## Slide 6: Agenda
Review
Moore’s Law
Administrivia
ARM and MIPS
Technology Break
Components of a Computer

## Slide 7: Technology Cost over Time: What does Improving Technology Look Like?
Cost
$
Time
A
B
C
D

## Slide 8: Technology Cost over Time
Cost
$
Time
C

## Slide 9: Technology Cost over Time Successive Generations
Cost
$
Time
Technology Generation 1
Technology Generation 2
Technology Generation 3
Technology Generation 2
How Can Tech Gen 2 Replace Tech Gen 1?

## Slide 10: Five Components of a Computer
Control
Datapath
Memory
Input
Output
Notes: That is, any computer, no matter how primitive or advance, can be divided into five parts:
1. The input devices bring the data from the outside world into the computer.
2. These data are kept in the computer’s memory until ...
3. The datapath request and process them.
4. The operation of the datapath is controlled by the computer’s controller.
All the work done by the computer will NOT do us any good unless we can get the data back to the outside world.
5. Getting the data back to the outside world is the job of the output devices.
The most COMMON way to connect these 5 components together is to use a network of busses.

## Slide 11: Components of a Computer
Processor
Control
Datapath
PC
Registers
Arithmetic & Logic Unit
(ALU)
Memory
Input
Output
Bytes
Enable?
Read/Write
Address
Write Data
ReadData
Processor-Memory Interface
I/O-Memory Interfaces

## Slide 12: Reality Check: Typical MIPS Chip Die Photograph
Integer
Control and
Datapath
Performance
Enhancing
On-Chip
Memory
(iCache +
dCache)
Floating Pt
Control and
Datapath
Protection- oriented
Virtual
Memory
Support

## Slide 13: Types of Memory
Volatile (needs power to hold state)
Static RAM (SRAM), built from bistables that use local positive feedback to hold value
Dynamic RAM (DRAM), holds values on capacitors that must be periodically refreshed
Non-Volatile (holds state without power)
Read-Only Memory (ROM) – holds fixed contents
Magnetic memory – Core, plus newer MRAM
Flash memory – can be written only 10,000’s times

## Slide 14: Early Read-Only Memory Technologies
Punched cards, From early 1700s through Jaquard Loom, Babbage, and then IBM
Punched paper tape, instruction stream in Harvard Mk 1
IBM Card Capacitor ROS
IBM Balanced Capacitor ROS
Diode Matrix, EDSAC-2 µcode store

## Slide 15: Early Read/Write Memory Technologies
Williams Tube, Manchester Mark 1, 1947
Babbage, 1800s: Digits stored on mechanical wheels
Mercury Delay Line, Univac 1, 1951

## Slide 16: Core Memory
Core memory was first large scale reliable main memory
  invented by Forrester in late 40s/early 50s at MIT for Whirlwind project
Bits stored as magnetization polarity on small ferrite cores threaded onto two-dimensional grid of wires
Coincident current pulses on X and Y wires would write cell and also sense original state (destructive reads)
DEC PDP-8/E Board,
4K words x 12 bits, (1968)
Robust, non-volatile storage
Used on space shuttle computers until recently
Cores threaded onto wires by hand (25 billion a year at peak production)
Core access time ~ 1ms
Notes: Early machines had things like mercury delay lines (jse)
Photo from David Gesswein djg@pdp8.net

## Slide 17: One-Transistor Dynamic RAM [Dennard, IBM]
TiN top electrode (VREF)
Ta2O5 dielectric
W bottom
electrode
poly
word
line
access transistor
1-T DRAM Cell
word
bit
access transistor
Storage
capacitor (FET gate, trench, stack)
VREF
  Intel formed to exploit market for semiconductor memory
First commercial DRAM was Intel 1103, held 1Kb in 1970

## Slide 18: Modern DRAM Structure
[Samsung, sub-70nm DRAM, 2004]

## Slide 19: DRAM Packaging (Laptops/Desktops/Servers)
DIMM (Dual Inline Memory Module) contains multiple chips with clock/control/address signals connected in parallel (sometimes need buffers to drive signals to all chips)
Data pins work together to return wide word (e.g., 64-bit data bus using 16x4-bit parts)
Address lines multiplexed row/column address
Clock and control signals
Data bus
(4b,8b,16b,32b)
DRAM chip
~12
~7

## Slide 20: Reality Check: Samsung LPDDR2 4Gb DRAM Chip (May 2013)

## Slide 21: DRAM Packaging, Mobile Devices
[ Apple A4 package cross-section, iFixit 2010 ]
Two stacked DRAM die
Processor plus logic die
[ Apple A4 package on circuit board]

## Slide 22: Moore’s Law
“The complexity for minimum component costs has increased at a rate of roughly a factor of two per year. …That means by 1975, the number of components per integrated circuit for minimum cost will be 65,000.” (from 50 in 1965)
“Integrated circuits will lead to such wonders as home computers--or at least terminals connected to a central computer--automatic controls for automobiles, and personal portable communications equipment. The electronic wristwatch needs only a display to be feasible today.”
Gordon Moore, “Cramming more components onto integrated circuits,” Electronics, Volume 38, Number 8, April 19, 1965

## Slide 23: Moore’s Law
Predicts: 2X Transistors / chip every 2 years
Gordon Moore Intel Cofounder B.S. Cal 1950!
# of transistors on an integrated circuit (IC)
Year

## Slide 24: Memory Chip Size
4x in 3 years
2x in 3 years
Growth in memory capacity slowing

## Slide 25: End of Moore’s Law?
It’s also a law of investment in equipment as well as increasing volume of integrated circuits that need more transistors per chip
Exponential growth cannot last forever
More transistors/chip will end during your careers
  2022?
  (When) will something replace it?

## Slide 26: Technology Trends: Uniprocessor Performance (SPECint)
Improvements in processor performance have slowed
Why?

## Slide 27: Limits to Performance: Faster Means More Power
P = CV2f

## Slide 28: P = C V2 f
Power is proportional to Capacitance * Voltage2 * Frequency of switching
What is the effect on power consumption of:
  “Simpler” implementation (fewer transistors)?
  Smaller implementation (shrunk down design)?
  Reduced voltage?
  Increased clock frequency?

## Slide 29: Doing Nothing Well—NOT!
Traditional processors consume about two thirds as much power at idle (doing nothing) as they do at peak
Higher performance (server class) processors approaching 300 W at peak
Implications for battery life?

## Slide 30: Computer Technology: Growing, But More Slowly
Processor
  Speed 2x / 1.5 years (since ’85-’05) [slowing!]
  Now +2 cores / 2 years
  When you graduate: 3-4 GHz, 6-8 Cores in client, 10-14 in server
Memory (DRAM)
  Capacity: 2x / 2 years (since ’96) [slowing!]
  Now 2X/3-4 years
  When you graduate: 8-16 GigaBytes
Disk
  Capacity: 2x / 1 year (since ’97)
  250X size last decade
  When you graduate: 6-12 TeraBytes
Network
  Core: 2x every 2 years
  Access: 100-1000 mbps from home, 1-10 mbps cellular

## Slide 31: Internet Connection Bandwidth Over Time
50% annualized growth rate per year

## Slide 32: Internet Connection Bandwidth Over Time

## Slide 33: Internet Connection Bandwidth Over Time

## Slide 34: Agenda
Review
Moore’s Law
Administrivia
ARM and MIPS
Technology Break
Components of a Computer

## Slide 35: Administrivia
Lab #5, HW #4, Project #2-1 posted
Midterm on the horizon:
  No discussion during exam week
  TA Review: TBD
  Exam: Th, 10/17, 6-9 PM, 1 Pimentel, 10 Evans, 155 Dwinelle
  Small number of special consideration cases, due to class conflicts, etc.—contact me

## Slide 36: Agenda
Review
Moore’s Law
Administrivia
Components of a Computer
Technology Break
Components of a Computer

## Slide 37: Computer Eras: Mainframe 1950s-60s
  “Big Iron”: IBM, UNIVAC, … build $1M computers for businesses => COBOL, Fortran, timesharing OS
Processor (CPU)
I/O
Memory

## Slide 38: ARM Architecture
http://en.wikipedia.org/wiki/ARM_architecture

## Slide 39: The ARM Inside the iPhone

## Slide 40: Flash Card Quiz
How many ARM processors in an iPhone?
One
Two
More than two, less than eight
At least eight

## Slide 41: Flash Card Quiz
How many ARM processors in an iPhone?
One
Two
More than two, less than eight
At least eight

## Slide 42: iPhone Innards
1 GHz ARM Cortex A8
You will learn about multiple processors, data level parallelism, caches in 61C
I/O
I/O
I/O
Processor
Memory
Many different ARM implementations inside a single system!

## Slide 43: Flash Card Quiz
Which of following statements is true?
Need a different compiled version of C “strlen” for each ARM core in an iPhone
All processors in an iPhone execute the ARM ISA
Different ARM cores are optimized for the I/O device they control
Every ARM core can access all the memory in an iPhone

## Slide 44: Flash Card Quiz
Which of following statements is true?
Need a different compiled version of C “strlen” for each ARM core in an iPhone
All processors in an iPhone execute the ARM ISA
Different ARM cores are optimized for the I/O device they control
Every ARM core can access all the memory in an iPhone

## Slide 45: Example MIPS Block Diagram

## Slide 46: A MIPS Family (Toshiba)

## Slide 47: Agenda
Review
Moore’s Law
Administrivia
ARM and MIPS
Technology Break
Components of a Computer

## Slide 48: Agenda
Review
Moore’s Law
Administrivia
ARM and MIPS
Technology Break
Components of a Computer

## Slide 49: Components of a Computer
Processor
Control
Datapath
PC
Registers
Arithmetic & Logic Unit
(ALU)
Memory
Bytes
Enable?
Read/Write
Address
Write Data
ReadData
Processor-Memory Interface

## Slide 50: The Processor
Processor (CPU): the active part of the computer, which does all the work (data manipulation and decision-making)
  Datapath: portion of the processor which contains hardware necessary to perform operations required by the processor (“the brawn”)
  Control: portion of the processor (also in hardware) which tells the datapath what needs to be done (“the brain”)

## Slide 51: Phases of Instruction Execution
Can break up the process of “executing an instruction” into stages or phases, and then connect the phases to create the whole datapath
  Smaller phases are easier to reason about and design
  Easy to optimize (change) one phase without touching the others

## Slide 52: Project 2 Warning
You are going to write a simulator in C for MIPS, implementing these 5 phases of execution

## Slide 53: Stages of the Datapath : Overview
Problem: a single, atomic block which “executes an instruction” (performs all necessary operations beginning with fetching the instruction) would be too bulky and inefficient
Solution: break up the process of “executing an instruction” into stages or phases, and then connect the phases to create the whole datapath
  Smaller phases are easier to design
  Easy to optimize (change) one phase without touching the others

## Slide 54: Phases of the Datapath (1/5)
There is a wide variety of MIPS instructions: so what general steps do they have in common?
Phase 1: Instruction Fetch
  No matter what the instruction, the 32-bit instruction word must first be fetched from memory (the cache-memory hierarchy)
  Also, this is where we Increment PC (that is, PC = PC + 4, to point to the next instruction: byte addressing so + 4)
Simulator: Instruction = Memory[PC]; PC+=4;

## Slide 55: Phases of the Datapath (2/5)
Phase 2: Instruction Decode
  Upon fetching the instruction, we next gather data from the fields (decode all necessary instruction data)
  First, read the opcode to determine instruction type and field lengths
  Second, read in data from all necessary registers
    For add, read two registers
    For addi, read one register
    For jal, no reads necessary

## Slide 56: Simulator for Decode Phase
Register1 = Register[rsfield];
Register2 = Register[rtfield];
if (opcode == 0) …
else if (opcode >5 && opcode <10) …
else if (opcode …) …
else if (opcode …) …
Better C statement for chained if statements?

## Slide 57: Phases of the Datapath (3/5)
Phase 3: ALU (Arithmetic-Logic Unit)
  Real work of most instructions is done here: arithmetic (+, -, *, /), shifting, logic (&, |), comparisons (slt)
  What about loads and stores?
    lw $t0, 40($t1)
    Address we are accessing in memory = the value in $t1 PLUS the value 40
    So we do this addition in this stage
Simulator: Result = Register1 op Register2; Address = Register1 + Addressfield

## Slide 58: Phases of the Datapath (4/5)
Phase 4: Memory Access
  Actually only the load and store instructions do anything during this phase; the others remain idle during this phase or skip it all together
  Since these instructions have a unique step, we need this extra phase to account for them
  (As a result of the cache system, this phase is expected to be fast: talk about next week)
Simulator: Register[rtfield] = Memory[Address] or Memory[Address] = Register[rtfield]

## Slide 59: Phases of the Datapath (5/5)
Phase 5: Register Write
  Most instructions write the result of some computation into a register
  E.g.,: arithmetic, logical, shifts, loads, slt
  What about stores, branches, jumps?
    Don’t write anything into a register at the end
    These remain idle during this fifth phase or skip it all together
Simulator: Register[rdfield] = Result

## Slide 60: Instruction Level Parallelism
P 1
Instr 1
IF
ID
ALU
MEM
WR
P 2
P 3
P 4
P 5
P 6
P 7
P 8
P 9
P 10
P 11
P 12
Instr 2
IF
ID
ALU
MEM
WR
IF
ID
ALU
MEM
WR
Instr 2
Instr 3
IF
ID
ALU
MEM
WR
IF
ID
ALU
MEM
WR
Instr 4
IF
ID
ALU
MEM
WR
Instr 5
IF
ID
ALU
MEM
WR
Instr 6
IF
ID
ALU
MEM
WR
Instr 7
IF
ID
ALU
MEM
WR
Instr 8

## Slide 61: Laptop Innards

## Slide 62: Server Internals

## Slide 63: Server Internals
Google Server
Notes: Most companies buy servers from the likes of Dell, Hewlett-Packard, IBM, or Sun Microsystems. But Google, which has hundreds of thousands of servers and considers running them part of its core expertise, designs and builds its own. Ben Jai, who designed many of Google's servers, unveiled a modern Google server before the hungry eyes of a technically sophisticated audience.
Google's big surprise: each server has its own 12-volt battery to supply power if there's a problem with the main source of electricity. The company also revealed for the first time that since 2005, its data centers have been composed of standard shipping containers--each with 1,160 servers and a power consumption that can reach 250 kilowatts.
It may sound geeky, but a number of attendees--the kind of folks who run data centers packed with thousands of servers for a living--were surprised not only by Google's built-in battery approach, but by the fact that the company has kept it secret for years. Jai said in an interview that Google has been using the design since 2005 and now is in its sixth or seventh generation of design.
Read more: http://news.cnet.com/8301-1001_3-10209580-92.html#ixzz0yo8bhTOH

## Slide 64: And in Conclusion, …
Key Technology Trends and Limitations
  Transistor doubling BUT power constraints and latency considerations limit performance improvement
  (Single Processor) computers are about as fast as they are likely to get, exploit parallelism to go faster
Five Components of a Computer
  Processor/Control + Datapath
  Memory
  Input/Output: Human interface/KB + Mouse, Display, Storage … evolving to speech, audio, video
Architectural Family: One Instruction Set, Many Implementations