## Slide 1: CS 61C: Great Ideas in Computer Architecture Performance and Caches
Instructor:
Randy H. Katz
http://inst.eecs.Berkeley.edu/~cs61c/fa13

## Slide 2: New-School Machine Structures (It’s a bit more complicated!)
Parallel Requests
  Assigned to computer
  e.g., Search “Katz”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates @ one time
Programming Languages
Smart Phone
Warehouse Scale Computer
Software Hardware
Harness Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory (Cache)
Input/Output
Computer
Cache Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0
How do we know?

## Slide 3: Agenda
Defining Performance
Administrivia
Memory Hierarchy
Technology Break
Direct Mapped Caches
And in Conclusion ...

## Slide 4: Agenda
Defining Performance
Administrivia
Memory Hierarchy
Technology Break
Direct Mapped Caches
And in Conclusion …

## Slide 5: What is Performance?
Latency (or response time or execution time)
  Time to complete one task
Bandwidth (or throughput)
  Tasks completed per unit time

## Slide 6: Cloud Performance: Why Application Latency Matters
Key figure of merit: application responsiveness
  Longer the delay, the fewer the user clicks, the less the user happiness, and the lower the revenue per user

## Slide 7: Defining CPU Performance
What does it mean to say X is faster than Y?
Ferrari vs. School Bus?
2013 Ferrari 599 GTB
  2 passengers, 11.1 secs in quarter mile
2013 Type D school bus
  54 passengers, quarter mile time?
http://www.youtube.com/watch?v=KwyCoQuhUNA
Response Time/Latency: e.g., time to travel ¼ mile
Throughput/Bandwidth: e.g., passenger-mi in 1 hour

## Slide 8: Defining Relative CPU Performance
PerformanceX = 1/Program Execution TimeX
PerformanceX > PerformanceY => 1/Execution TimeX > 1/Execution Timey => Execution TimeY > Execution TimeX
Computer X is N times faster than Computer Y PerformanceX / PerformanceY = N or Execution TimeY / Execution TimeX = N
Bus is to Ferrari as 12 is to 11.1: Ferrari is 1.08 times faster than the bus!

## Slide 9: Measuring CPU Performance
Computers use a clock to determine when events takes place within hardware
Clock cycles: discrete time intervals
  aka clocks, cycles, clock periods, clock ticks
Clock rate or clock frequency: clock cycles per second (inverse of clock cycle time)
3 GigaHertz clock rate => clock cycle time = 1/(3x109) seconds clock cycle time = 333 picoseconds (ps)

## Slide 10: CPU Performance Factors
To distinguish between processor time and I/O, CPU time is time spent in processor
CPU Time/Program = Clock Cycles/Program x Clock Cycle Time
Or CPU Time/Program = Clock Cycles/Program ÷ Clock Rate

## Slide 11: CPU Performance Factors
But a program executes instructions
CPU Time/Program = Clock Cycles/Program x Clock Cycle Time = Instructions/Program x Average Clock Cycles/Instruction x Clock Cycle Time
1st term called Instruction Count
2nd term abbreviated CPI for average Clock Cycles Per Instruction
3rd term is 1 / Clock rate

## Slide 12: Restating Performance Equation
Time = Seconds Program Instructions Clock cycles Seconds Program Instruction Clock Cycle
×
×
=

## Slide 13: What Affects Each Component? Instruction Count, CPI, Clock Rate
Hardware or software component? | Affects What?
Algorithm | 
Programming Language | 
Compiler | 
Instruction Set Architecture | 
Notes: Algorithm Instruction count, possibly CPI
The algorithm determines the number of source program instructions executed and hence the number of processor instructions executed. The algorithm may also affect the CPI, by
favoring slower or faster instructions. For example, if the algorithm uses more floating-point operations, it will tend to have a higher CPI.
Programming language
Instruction count, CPI
The programming language certainly affects the instruction count, since statements in the language are translated to processor
instructions, which determine instruction count. The language mayalso affect the CPI because of its features; for example, a language
with heavy support for data abstraction (e.g., Java) will require indirect calls, which will use higher CPI instructions.
Compiler
Instruction count, CPI
The efficiency of the compiler affects both the instruction count and average cycles per instruction, since the compiler determines
the translation of the source language instructions into computer instructions. The compiler’s role can be very complex and affect
the CPI in complex ways.
Instruction set
architecture
Instruction count, clock rate, CPI
The instruction set architecture affects all three a
ts of CPU performance, since it affects the instructions needed for a
function, the cost in cycles of each instruction, and the overall clock rate of the processor

## Slide 14: What Affects Each Component? Instruction Count, CPI, Clock Rate
Hardware or software component? | Affects What?
Algorithm | Instruction Count, CPI
Programming Language | Instruction Count, CPI
Compiler | Instruction Count, CPI
Instruction Set Architecture | Instruction Count, Clock Rate, CPI
Notes: Algorithm Instruction count, possibly CPI
The algorithm determines the number of source program instructions executed and hence the number of processor instructions executed. The algorithm may also affect the CPI, by
favoring slower or faster instructions. For example, if the algorithm uses more floating-point operations, it will tend to have a higher CPI.
Programming language
Instruction count, CPI
The programming language certainly affects the instruction count, since statements in the language are translated to processor
instructions, which determine instruction count. The language mayalso affect the CPI because of its features; for example, a language
with heavy support for data abstraction (e.g., Java) will require indirect calls, which will use higher CPI instructions.
Compiler
Instruction count, CPI
The efficiency of the compiler affects both the instruction count and average cycles per instruction, since the compiler determines
the translation of the source language instructions into computer instructions. The compiler’s role can be very complex and affect
the CPI in complex ways.
Instruction set
architecture
Instruction count, clock rate, CPI
The instruction set architecture affects all three aspects of CPU performance, since it affects the instructions needed for a
function, the cost in cycles of each instruction, and the overall clock rate of the processor

## Slide 15
Computer A is ≈4.0 times faster than B
Computer B is ≈1.7 times faster than A
Computer B is ≈3.4 times faster than A
Computer A is ≈1.2 times faster than B
☐
☐
☐
☐
Computer A clock cycle time 250 ps, CPIA = 2
Computer B clock cycle time 500 ps, CPIB = 1.2
Assume A and B have same instruction set
Which statement is true?
Notes: VertLeftWhiteCheck1
Answer: Computer A is ≈1.2 times faster than B

## Slide 16
Computer A is ≈4.0 times faster than B
Computer B is ≈1.7 times faster than A
Computer B is ≈3.4 times faster than A
Computer A is ≈1.2 times faster than B
☐
☐
☐
☐
Computer A clock cycle time 250 ps, CPIA = 2
Computer B clock cycle time 500 ps, CPIB = 1.2
Assume A and B have same instruction set
Which statement is true?
Notes: VertLeftWhiteCheck1
Answer: Computer A is ≈1.2 times faster than B
2 x 250 = 500 ps per instruction … 0.002 instructions per ps
1.2 x 500 = 600 ps per instruction … 0.0016 instructions per ps
A is to B as 1.2 is to 1

## Slide 17: Workload and Benchmark
Workload: Set of programs run on a computer
  Actual collection of applications run or made from real programs to approximate such a mix
  Specifies both programs and relative frequencies
Benchmark: Program selected for use in comparing computer performance
  Benchmarks form a workload
  Usually standardized so that many use them

## Slide 18: SPEC (System Performance Evaluation Cooperative)
Computer Vendor cooperative for benchmarks, started in 1989
SPECCPU2006
  12 Integer Programs
  17 Floating-Point Programs
Often turn into number where bigger is faster
SPECratio: reference execution time on old reference computer divide by execution time on new computer to get an effective speed-up

## Slide 19: SPECINT2006 on AMD Barcelona
Description | Instruc-tion Count (B) | CPI | Clock cycle time (ps) | Execu-tion Time (s) | Refer-ence Time (s) | SPEC-ratio
Interpreted string processing | 2,118 | 0.75 | 400 | 637 | 9,770 | 15.3
Block-sorting compression | 2,389 | 0.85 | 400 | 817 | 9,650 | 11.8
GNU C compiler | 1,050 | 1.72 | 400 | 724 | 8,050 | 11.1
Combinatorial optimization | 336 | 10.0 | 400 | 1,345 | 9,120 | 6.8
Go game | 1,658 | 1.09 | 400 | 721 | 10,490 | 14.6
Search gene sequence | 2,783 | 0.80 | 400 | 890 | 9,330 | 10.5
Chess game | 2,176 | 0.96 | 400 | 837 | 12,100 | 14.5
Quantum computer simulation | 1,623 | 1.61 | 400 | 1,047 | 20,720 | 19.8
Video compression | 3,102 | 0.80 | 400 | 993 | 22,130 | 22.3
Discrete event simulation library | 587 | 2.94 | 400 | 690 | 6,250 | 9.1
Games/path finding | 1,082 | 1.79 | 400 | 773 | 7,020 | 9.1
XML parsing | 1,058 | 2.70 | 400 | 1,143 | 6,900 | 6.0

## Slide 20: Summarizing Performance …
Flashcard Quiz: Which system is faster?
System
Rate (Task 1)
Rate (Task 2)
A
10
20
B
20
10
System A
System B
Same performance
Unanswerable question!

## Slide 21: … Depends Who’s Selling
System
Rate (Task 1)
Rate (Task 2)
A
10
20
B
20
10
Average
15
15
Average throughput
System
Rate (Task 1)
Rate (Task 2)
A
0.50
2.00
B
1.00
1.00
Average
1.25
1.00
Throughput relative to B
System
Rate (Task 1)
Rate (Task 2)
A
1.00
1.00
B
2.00
0.50
Average
1.00
1.25
Throughput relative to A

## Slide 22: Summarizing SPEC Performance
Varies from 6x to 22x faster than reference computer
Geometric mean of ratios: N-th root of product of N ratios
  Geometric Mean gives same relative answer no matter what computer is used as reference
Geometric Mean for Barcelona is 11.7

## Slide 23: Agenda
Defining Performance
Administrivia
Memory Hierarchy
Technology Break
Direct Mapped Caches
And in Conclusion …

## Slide 24: Administrivia
Lab #5, Homework #4, Project #2-1 (it’s not too difficult)
Very high percentage of Project #1-2 submitted by Sunday deadline (approximately 97% of the class); 99% by Tuesday deadline … Excellent work!
Midterm, 17 October, 6-9 PM

## Slide 25: Agenda
Defining Performance
Administrivia
Memory Hierarchy
Technology Break
Direct Mapped Caches
And in Conclusion ...

## Slide 26: Big Idea: Memory Hierarchy
Processor
Size of memory at each level
Increasing distance from processor, decreasing speed
Level 1
Level 2
Level n
Level 3
. . .
Inner
Outer
Levels in memory hierarchy
As we move to outer levels the latency goes up and price per bit goes down. Why?

## Slide 27: Library Analogy
Writing a report based on books on reserve
  E.g., works of J.D. Salinger
Go to library to get reserved book and place on desk in library
If need more, check them out and keep on desk
  But don’t return earlier books since might need them
You hope this collection of ~10 books on desk enough to write report, despite 10 being only 0.00001% of books in UC Berkeley libraries

## Slide 28: Principle of Locality
Principle of Locality: Programs access small portion of address space at any instant of time
What program structures lead to locality in instruction accesses?

## Slide 29: Cache Philosophy
Programmer-invisible hardware mechanism to give illusion of speed of fastest memory with size of largest memory
  Works fine even if programmer has no idea what a cache is
  However, performance-oriented programmers today sometimes “reverse engineer” cache design to design data structures to match cache
  We’ll do that in Project 3

## Slide 30: Memory Access without Cache
Load word instruction: lw $t0,0($t1)
$t1 contains 1022ten, Memory[1022] = 99
  Processor issues address 1022ten to Memory
  Memory reads word at address 1022ten (99)
  Memory sends 99 to Processor
  Processor loads 99 into register $t0

## Slide 31: Memory Access with Cache
Load word instruction: lw $t0,0($t1)
$t1 contains 1022ten, Memory[1022] = 99
With cache (similar to a hash)
  Processor issues address 1022ten to Cache
  Cache checks to see if has copy of data at address 1022ten
    2a. If finds a match (Hit): cache reads 99, sends to processor
    2b. No match (Miss): cache sends address 1022 to Memory
      Memory reads 99 at address 1022ten
      Memory sends 99 to Cache
      Cache replaces word with new 99
      Cache sends 99 to processor
  Processor loads 99 into register $t0

## Slide 32: Cache “Tags”
Need way to tell if have copy of location in memory so that can decide on hit or miss
On cache miss, put memory address of block in “tag address” of cache block
  1022 placed in tag next to data from memory (99)
Tag | Data
252 | 12
1022 | 99
131 | 7
2041 | 20
From earlier
instructions

## Slide 33: Anatomy of a 16 Byte Cache, 4 Byte Block
Operations:
  Cache Hit
  Cache Miss
  Refill cache from memory
Cache needs Address Tags to decide if Processor Address is a Cache Hit or Cache Miss
  Compares all 4 tags
Processor
32-bit
Address
32-bit
Data
Cache
32-bit
Address
32-bit
Data
Memory
1022
99
252
7
20
12
131
2041

## Slide 34: Cache Requirements
Tag | Data
252 | 12
1022 | 99
131 | 7
2041 | 20
Tag | Data
252 | 12
1022 | 99
511 | 11
2041 | 20
Suppose processor now requests location 511, which contains 11?
Doesn’t match any cache block, so must “evict” one resident block to make room
  Which block to evict?
Replace “victim” with new memory block at address 511

## Slide 35: Block Must be Aligned in Memory
Word blocks are aligned, so binary address of all words in cache always ends in 00two
How to take advantage of this to save hardware and energy?
Don’t need to compare last 2 bits of 32-bit byte address (comparator can be narrower)
=> Don’t need to store last 2 bits of 32-bit byte address in Cache Tag (Tag can be narrower)

## Slide 36: Anatomy of a 32B Cache, 8B Block
Blocks must be aligned in pairs, otherwise could get same word twice in cache
Tags only have even-numbered words
Last 3 bits of address always 000two
Tags, comparators can be narrower
Can get hit for either word in block
Processor
32-bit
Address
32-bit
Data
Cache
32-bit
Address
32-bit
Data
Memory
1022
99
252
42
1947
12
130
2040
1000
7
20
-10

## Slide 37: Big Idea: Locality
Temporal Locality (locality in time)
  Go back to same book on desktop multiple times
  If a memory location is referenced, then it will tend to be referenced again soon
Spatial Locality (locality in space)
  When go to book shelf, pick up multiple books on J.D. Salinger since library stores related books together
  If a memory location is referenced, the locations with nearby addresses will tend to be referenced soon
Notes: How does the memory hierarchy work? Well it is rather simple, at least in principle.
In order to take advantage of the temporal locality, that is the locality in time, the memory hierarchy will keep those more recently accessed data items closer to the processor because chances are (points to the principle), the processor will access them again soon.
In order to take advantage of the spatial locality, not ONLY do we move the item that has just been accessed to the upper level, but we ALSO move the data items that are adjacent to it.
+1 = 15 min. (X:55)

## Slide 38: Principle of Locality
Principle of Locality: Programs access small portion of address space at any instant of time
What program structures lead to temporal and spatial locality in instruction accesses?
In data accesses?

## Slide 39: Common Cache Optimizations
Reduce tag overhead by having larger blocks
  E.g., 2 words, 4 words, 8 words
Separate caches for instructions and data
  Double bandwidth, don’t interfere with each other
Bigger caches (but access time could get bigger than one clock cycle if too big)
Divide cache into multiple sets, only search inside one set => saves comparators, energy
  If as many sets as blocks, then only 1 comparator (aka Direct-Mapped Cache)
  But may increase Miss Rate

## Slide 40: Hardware Cost of Cache
Need to compare every tag to the Processor address
Comparators are expensive
Optimization: 2 sets => ½ comparators
1 Address bit selects which set
40
Processor
32-bit
Address
Tag
Data
32-bit
Data
Cache
32-bit
Address
32-bit
Data
Memory
Tag
Data
Set 0
Set 1

## Slide 41: Processor Address Fields used by Cache Controller
Block Offset: Byte address within block
Set Index: Selects which set
Tag: Remaining portion of processor address
Size of Index = log2 (number of sets)
Size of Tag = Address size – Size of Index – log2 (number of bytes/block)
Block offset
Set Index
Tag
Processor Address (32-bits total)
Notes: For class handout

## Slide 42: What is limit to number of sets?
Can save more comparators if have more than 2 sets
Limit: As Many Sets as Cache Blocks – only needs one comparator!
Called “Direct-Mapped” Design
Block offset
Index
Tag

## Slide 43: One More Detail: Valid Bit
When start a new program, cache does not have valid information for this program
Need an indicator whether this tag entry is valid for this program
Add a “valid bit” to the cache tag entry
  0 => cache miss, even if by chance, address = tag
  1 => cache hit, if processor address = tag

## Slide 44: Agenda
Defining Performance
Administrivia
Memory Hierarchy
Technology Break
Direct Mapped Caches
And in Conclusion …

## Slide 45: Agenda
Defining Performance
Administrivia
Memory Hierarchy
Technology Break
Direct Mapped Caches
And in Conclusion …

## Slide 46: Direct-Mapped Cache Example
One word blocks, cache size = 1K words (or 4KB)
20
Tag
10
Index
Data
Index
Tag
Valid
0
1
2
.
.
.
1021
1022
1023
31 30 . . . 13 12 11 . . . 2 1 0
Block offset
What kind of locality are we taking advantage of?
20
Data
32
Hit
Valid bit ensures something useful in cache for this index
Compare Tag with upper part of Address to see if a Hit
Read data from cache instead of memory if a Hit
Comparator
Notes: Let’s use a specific example with realistic numbers: assume we have a 1 K word (4Kbyte) direct mapped cache with block size equals to 4 bytes (1 word).
In other words, each block associated with the cache tag will have 4 bytes in it (Row 1).
With Block Size equals to 4 bytes, the 2 least significant bits of the address will be used as byte select within the cache block.
Since the cache size is 1K word, the upper 32 minus 10+2 bits, or 20 bits of the address will be stored as cache tag.
The rest of the (10) address bits in the middle, that is bit 2 through 11, will be used as Cache Index to select the proper cache entry
Temporal!

## Slide 47: Cache Terms
Hit rate: fraction of access that hit in the cache
Miss rate: 1 – Hit rate
Miss penalty: time to replace a block from lower level in memory hierarchy to cache
Hit time: time to access cache memory (including tag comparison)
Abbreviation: “$” = cache (A Berkeley innovation!)

## Slide 48: Mapping a 6-bit Memory Address
In example, block size is 4 bytes/1 word (it could be multi-word)
Memory and cache blocks are the same size, unit of transfer between memory and cache
# Memory blocks >> # Cache blocks
  16 Memory blocks/16 words/64 bytes/6 bits to address all bytes
  4 Cache blocks, 4 bytes (1 word) per block
  4 Memory blocks map to each cache block
Byte within block: low order two bits, ignore! (nothing smaller than a block)
Memory block to cache block, aka index: middle two bits
Which memory block is in a given cache block, aka tag: top two bits
0
5
1
Byte Offset Within Block (e.g., Word)
2
3
Block Within $
Index
4
Mem Block Within $ Block
Tag

## Slide 49: Caching: A Simple First Example
00
01
10
11
Cache
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
Main Memory
Tag
Data
Q: Is the mem block in cache?
Compare the cache tag to the high-order 2 memory address bits to tell if the memory block is in the cache (provided valid bit is set)
Valid
One word blocks.
Two low-order bits define the byte in the block (32b words).
Q: Where in the cache is the memory block?
Use next 2 low-order memory address bits – the index – to determine which cache block (i.e., modulo the number of blocks in the cache)
Index
Notes: For class handout

## Slide 50: Caching: A Simple First Example
00
01
10
11
Cache
Main Memory
Q: Where in the cache is the mem block?
Use next 2 low-order memory address bits – the index – to determine which cache block (i.e., modulo the number of blocks in the cache)
Tag
Data
Q: Is the memory block in cache?
Compare the cache tag to the high-order 2 memory address bits to tell if the memory block is in the cache (provided valid bit is set)
Valid
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
One word blocks
Two low order bits (xx) define the byte in the block (32b words)
Index
Notes: For lecture
Valid bit indicates whether an entry contains valid information – if the bit is not set, there cannot be a match for this block

## Slide 51: Multiword-Block Direct-Mapped Cache
Four words/block, cache size = 1K words
8
Index
Data
Index
Tag
Valid
0
1
2
.
.
.
253
254
255
31 30 . . . 13 12 11 . . . 4 3 2 1 0
Byte offset
20
20
Tag
Hit
Data
32
Block offset
What kind of locality are we taking advantage of?
Notes: to take advantage for spatial locality want a cache block that is larger than word word in size.

## Slide 52: Cache Names for Each Organization
“Fully Associative”: Block can go anywhere
  First design in lecture
  Note: No Index field, but 1 comparator/block
“Direct Mapped”: Block goes one place
  Note: Only 1 comparator
  Number of sets = number blocks
“N-way Set Associative”: N places for a block
  Number of sets = number of blocks / N
  Fully Associative: N = number of blocks
  Direct Mapped: N = 1

## Slide 53: Range of Set-Associative Caches
For a fixed-size cache, each increase by a factor of 2 in associativity doubles the number of blocks per set (i.e., the number of “ways”) and halves the number of sets –
  decreases the size of the index by 1 bit and increases the size of the tag by 1 bit
Block offset
Index
Tag
More Associativity (more ways)
Note: IBM persists in calling sets “ways” and ways “sets”.
They’re wrong.
Notes: For class handout

## Slide 54
A and B only
A, B, and C only
All four statements are true
A only
☐
☐
☐
☐
For S sets, N ways, B blocks, which statements hold?
The cache has B tags
The cache needs N comparators
B = N x S
Size of Index = Log2(S)

## Slide 55
A and B only
A, B, and C only
All four statements are true
A only
☐
☐
☐
☐
For S sets, N ways, B blocks, which statements hold?
The cache has B tags
The cache needs N comparators
B = N x S
Size of Index = Log2(S)

## Slide 56: Typical Memory Hierarchy
Second
Level
Cache
(SRAM)
Control
Datapath
Secondary
Memory
(Disk
Or Flash)
On-Chip Components
RegFile
Main
Memory
(DRAM)
Data
Cache
Instr
Cache
Speed (cycles): ½’s 1’s 10’s 100’s 1,000,000’s
Size (bytes): 100’s 10K’s M’s G’s T’s
Principle of locality + memory hierarchy presents programmer with ≈ as much memory as is available in the cheapest technology at the ≈ speed offered by the fastest technology
Cost/bit: highest lowest
Notes: Instead, the memory system of a modern computer consists of a series of black boxes ranging from the fastest to the slowest.
Besides variation in speed, these boxes also varies in size (smallest to biggest) and cost.
What makes this kind of arrangement work is one of the most important principle in computer design. The principle of locality. The principle of locality states that programs access a relatively small portion of the address space at any instant of time.
The design goal is to present the user with as much memory as is available in the cheapest technology (points to the disk).
While by taking advantage of the principle of locality, we like to provide the user an average access speed that is very close to the speed that is offered by the fastest technology.
(We will go over this slide in detail in the next lectures on caches).

## Slide 57: And In Conclusion, …
Time (seconds/program) is measure of performance Instructions Clock cycles Seconds Program Instruction Clock Cycle
Principle of Locality for Libraries /Computer Memory
Hierarchy of Memories (speed/size/cost per bit) to Exploit Locality
Cache – copy of data lower level in memory hierarchy
Direct Mapped to find block in cache using Tag field and Valid bit for Hit
Larger caches reduce Miss rate via Temporal and Spatial Locality, but can increase Hit time
Multilevel caches help Miss penalty
AMAT helps balance Hit time, Miss rate, Miss penalty
×
×
=