## Slide 1: CS 61C: Great Ideas in Computer Architecture Caches
Instructors:
Randy H. Katz
http://inst.eecs.Berkeley.edu/~cs61c/fa13

## Slide 2: New-School Machine Structures (It’s a bit more complicated!)
Parallel Requests
  Assigned to computer
  e.g., Search “Katz”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates @ one time
Programming Languages
Smart Phone
Warehouse Scale Computer
Software Hardware
Harness Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory (Cache)
Input/Output
Computer
Cache Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0
Today’s
Lecture

## Slide 3: Agenda
Review
Direct Mapped Cache
Administrivia
Write Policy and AMAT
Technology Break
Multiple Cache Levels
And in Conclusion, …

## Slide 4: Agenda
Review
Direct Mapped Cache
Administrivia
Write Policy and AMAT
Technology Break
Multilevel Caches
And in Conclusion, …

## Slide 5: Review: Memory Hierarchy
Processor
Size of memory at each level
Increasing distance from processor, decreasing speed
Level 1
Level 2
Level n
Level 3
. . .
Inner
Outer
Levels in memory hierarchy
As we move to outer levels the latency goes up and price per bit goes down. Why?

## Slide 6: Review: Cache Philosophy
Principle of Locality: Programs access small portion of address space at any instant of time
  Temporal Locality (locality in time)
  Spatial Locality (locality in space)
Programmer-invisible hardware mechanism to give illusion of speed of fastest memory with size of largest memory

## Slide 7: Common Cache Optimizations
Reduce tag overhead by having larger blocks
  E.g., 2 words, 4 words, 8 words
Separate caches for instructions and data
  Double bandwidth, don’t interfere with each other
Bigger caches (but access time could get bigger than one clock cycle if too big)
Divide cache into multiple sets, only search inside one set => saves comparators, energy
  If as many sets as blocks, then only 1 comparator (aka Direct-Mapped Cache)
  But may increase Miss Rate

## Slide 8: Anatomy of a 16 Byte Cache, 4 Byte Block
Operations:
  Cache Hit
  Cache Miss
  Refill cache from memory
Cache needs Address Tags to decide if Processor Address is a Cache Hit or Cache Miss
  Compares all 4 tags
Processor
32-bit
Address
32-bit
Data
Cache
32-bit
Address
32-bit
Data
Memory
1022
99
252
7
20
12
131
2041

## Slide 9: Anatomy of a 32B Cache, 8B Block
Blocks must be aligned in pairs, otherwise could get same word twice in cache
Tags only have even-numbered words
Last 3 bits of address always 000two
Tags, comparators can be narrower
Can get hit for either word in block
Processor
32-bit
Address
32-bit
Data
Cache
32-bit
Address
32-bit
Data
Memory
1022
99
252
42
1947
12
130
2040
1000
7
20
-10

## Slide 10: Hardware Cost of Cache
Need to compare every tag to the Processor address
Comparators are expensive
Optimization: 2 sets => ½ comparators
1 Address bit selects which set
10
Processor
32-bit
Address
Tag
Data
32-bit
Data
Cache
32-bit
Address
32-bit
Data
Memory
Tag
Data
Set 0
Set 1
Notes: 2 sets, n/2 places where a block can be placed, n/2 comparators
E.g, even vs. odd blocks …

## Slide 11: Processor Address Fields used by Cache Controller
Block Offset: Byte address within block
Set Index: Selects which set
Tag: Remaining portion of processor address
Size of Index = log2 (number of sets)
Size of Tag = Address size – Size of Index – log2 (number of bytes/block)
Block offset
Set Index
Tag
Processor Address (32-bits total)
Notes: For class handout

## Slide 12: What is Limit to # of Sets?
Can save more comparators if have more than 2 sets
Limit: As Many Sets as Cache Blocks – only needs one comparator!
Called “Direct-Mapped” Design
Block offset
Index
Tag

## Slide 13: One More Detail: Valid Bit
When start a new program, cache does not have valid information for this program
Need an indicator whether this tag entry is valid for this program
Add a “valid bit” to the cache tag entry
  0 => cache miss, even if by chance, address = tag
  1 => cache hit, if processor address = tag

## Slide 14: Agenda
Review
Direct Mapped Cache
Administrivia
Write Policy and AMAT
Technology Break
Multilevel Caches
And in Conclusion, …

## Slide 15: Direct-Mapped Cache Example
One word blocks, cache size = 1K words (or 4KB)
20
Tag
10
Index
Data
Index
Tag
Valid
0
1
2
.
.
.
1021
1022
1023
31 30 . . . 13 12 11 . . . 2 1 0
Block offset
What kind of locality are we taking advantage of?
20
Data
32
Hit
Valid bit ensures something useful in cache for this index
Compare Tag with upper part of Address to see if a Hit
Read data from cache instead of memory if a Hit
Comparator
Notes: Let’s use a specific example with realistic numbers: assume we have a 1 K word (4Kbyte) direct mapped cache with block size equals to 4 bytes (1 word).
In other words, each block associated with the cache tag will have 4 bytes in it (Row 1).
With Block Size equals to 4 bytes, the 2 least significant bits of the address will be used as byte select within the cache block.
Since the cache size is 1K word, the upper 32 minus 10+2 bits, or 20 bits of the address will be stored as cache tag.
The rest of the (10) address bits in the middle, that is bit 2 through 11, will be used as Cache Index to select the proper cache entry
Temporal!

## Slide 16: Cache Terms
Hit rate: fraction of access that hit in the cache
Miss rate: 1 – Hit rate
Miss penalty: time to replace a block from lower level in memory hierarchy to cache
Hit time: time to access cache memory (including tag comparison)
Abbreviation: “$” = cache (A Berkeley innovation!)

## Slide 17: Mapping a 6-bit Memory Address
In example, block size is 4 bytes/1 word (it could be multi-word)
Memory and cache blocks are the same size, unit of transfer between memory and cache
# Memory blocks >> # Cache blocks
  16 Memory blocks/16 words/64 bytes/6 bits to address all bytes
  4 Cache blocks, 4 bytes (1 word) per block
  4 Memory blocks map to each cache block
Byte within block: low order two bits, ignore! (nothing smaller than a block)
Memory block to cache block, aka index: middle two bits
Which memory block is in a given cache block, aka tag: top two bits
0
5
1
Byte Offset Within Block (e.g., Word)
2
3
Block Within $
Index
4
Mem Block Within $ Block
Tag

## Slide 18: Caching: A Simple First Example
00
01
10
11
Cache
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
Main Memory
Tag
Data
Q: Is the mem block in cache?
Compare the cache tag to the high-order 2 memory address bits to tell if the memory block is in the cache (provided valid bit is set)
Valid
One word blocks.
Two low-order bits define the byte in the block (32b words).
Q: Where in the cache is the memory block?
Use next 2 low-order memory address bits – the index – to determine which cache block (i.e., modulo the number of blocks in the cache)
Index
Notes: For class handout

## Slide 19: Caching: A Simple First Example
00
01
10
11
Cache
Main Memory
Q: Where in the cache is the mem block?
Use next 2 low-order memory address bits – the index – to determine which cache block (i.e., modulo the number of blocks in the cache)
Tag
Data
Q: Is the memory block in cache?
Compare the cache tag to the high-order 2 memory address bits to tell if the memory block is in the cache (provided valid bit is set)
Valid
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
One word blocks
Two low order bits (xx) define the byte in the block (32b words)
Index
Notes: For lecture
Valid bit indicates whether an entry contains valid information – if the bit is not set, there cannot be a match for this block

## Slide 20: Multiword-Block Direct-Mapped Cache
Four words/block, cache size = 1K words
8
Index
Data
Index
Tag
Valid
0
1
2
.
.
.
253
254
255
31 30 . . . 13 12 11 . . . 4 3 2 1 0
Byte offset
20
20
Tag
Hit
Data
32
Block offset
What kind of locality are we taking advantage of?
Notes: to take advantage for spatial locality want a cache block that is larger than word word in size.

## Slide 21: Cache Names for Each Organization
“Fully Associative”: Block can go anywhere
  First design in lecture
  Note: No Index field, but 1 comparator/block
“Direct Mapped”: Block goes one place
  Note: Only 1 comparator
  Number of sets = number blocks
“N-way Set Associative”: N places for a block
  Number of sets = number of blocks / N
  Fully Associative: N = number of blocks
  Direct Mapped: N = 1

## Slide 22: Range of Set-Associative Caches
For a fixed-size cache, each increase by a factor of 2 in associativity doubles the number of blocks per set (i.e., the number of “ways”) and halves the number of sets –
  Decreases the size of the index by 1 bit and increases the size of the tag by 1 bit
Block offset
Index
Tag
More Associativity (more ways)
Note: IBM persists in calling sets “ways” and ways “sets”.
They’re wrong.
Notes: For class handout

## Slide 23
A and B only
A, B, and C only
All four statements are true
A only
☐
☐
☐
☐
For S sets, N ways, B blocks, which statements hold?
The cache has B tags
The cache needs N comparators
B = N x S
Size of Index = Log2(S)

## Slide 24
A and B only
A, B, and C only
All four statements are true
A only
☐
☐
☐
☐
For S sets, N ways, B blocks, which statements hold?
The cache has B tags
The cache needs N comparators
B = N x S
Size of Index = Log2(S)

## Slide 25: Agenda
Review
Direct Mapped Cache
Administrivia
Write Policy and AMAT
Technology Break
Multilevel Caches
And in Conclusion, …

## Slide 26: Administrivia
Midterm One Week from Thursday (17 October)
  6-9 PM in three different rooms:
    1 Pimentel
    10 Evans
    155 Dwinelle
  TA-led review session Saturday, 2-5 PM, Room 155 Dwinelle
  (Additional HKN Review on Sunday)
Topics:
  Cloud Computing and Warehouse Scale Computers
  C Programming
  MIPS Assembly/Machine Language and Conventions
  Compilers and Loaders
  Number Representations
  Memory Hierarchy and Caches
  Parallelism (Request and Data-Level Parallelism)
  Labs and Projects

## Slide 27: CS61c in the News

## Slide 28: Agenda
Review
Direct Mapped Cache
Administrivia
Write Policy
Technology Break
AMAT
And in Conclusion, …

## Slide 29: Handling Stores with Write-Through
Store instructions write to memory, changing values
Need to make sure cache and memory have same values on writes: 2 policies
1) Write-Through Policy: write cache and write through the cache to memory
  Every write eventually gets to memory
  Too slow, so include Write Buffer to allow processor to continue once data in Buffer
  Buffer updates memory in parallel to processor

## Slide 30: Write-Through Cache
Write both values in cache and in memory
Write buffer stops CPU from stalling if memory cannot keep up
Write buffer may have multiple entries to absorb bursts of writes
What if store misses in cache?
Processor
32-bit
Address
32-bit
Data
Cache
32-bit
Address
32-bit
Data
Memory
1022
99
252
7
20
12
131
2041
Addr
Data
Write Buffer

## Slide 31: Handling Stores with Write-Back
2) Write-Back Policy: write only to cache and then write cache block back to memory when evict block from cache
  Writes collected in cache, only single write to memory per block
  Include bit to see if wrote to block or not, and then only write back if bit is set
    Called “Dirty” bit (writing makes it “dirty”)

## Slide 32: Write-Back Cache
Store/cache hit, write data in cache only & set dirty bit
  Memory has stale value
Store/cache miss, read data from memory, then update and set dirty bit
  “Write-allocate” policy
Load/cache hit, use value from cache
On any miss, write back evicted block, only if dirty. Update cache with new block and clear dirty bit.
Processor
32-bit
Address
32-bit
Data
Cache
32-bit
Address
32-bit
Data
Memory
1022
99
252
7
20
12
131
2041
D
D
D
D
Dirty Bits

## Slide 33: Write-Through vs. Write-Back
Write-Through:
  Simpler control logic
  More predictable timing simplifies processor control logic
  Easier to make reliable, since memory always has copy of data
Write-Back
  More complex control logic
  More variable timing (0,1,2 memory accesses per cache access)
  Usually reduces write traffic
  Harder to make reliable, sometimes cache has only copy of data

## Slide 34: Average Memory Access Time (AMAT)
Average Memory Access Time (AMAT) is the average to access memory considering both hits and misses in the cache
  AMAT = Time for a hit + Miss rate x Miss penalty
Notes: AMAT = 1 + 0.02x50 = 2

## Slide 35
400 psec
600 psec
≥ 800 psec
≤200 psec
☐
☐
☐
☐
Average Memory Access Time (AMAT) is the average to access memory considering both hits and misses
  AMAT = Time for a hit + Miss rate x Miss penalty
Given a 200 psec clock, a miss penalty of 50 clock cycles, a miss rate of 0.02 misses per instruction and a cache hit time of 1 clock cycle, what is AMAT?
Notes: VertLeftWhiteCheck1
B: Print It saves PC+4 …because ints in this system are 4-bytes long and the actual address increments by 4 even though it appears to only incrememt 1.

## Slide 36
400 psec
600 psec
≥ 800 psec
≤200 psec
☐
☐
☐
☐
Average Memory Access Time (AMAT) is the average to access memory considering both hits and misses
  AMAT = Time for a hit + Miss rate x Miss penalty
Given a 200 psec clock, a miss penalty of 50 clock cycles, a miss rate of 0.02 misses per instruction and a cache hit time of 1 clock cycle, what is AMAT?
Notes: 1* 200 + 0.02 * 50 * 200 = 400

## Slide 37: Average Memory Access Time (AMAT)
Average Memory Access Time (AMAT) is the average to access memory considering both hits and misses
  AMAT = Time for a hit + Miss rate x Miss penalty
What is the AMAT for a processor with a 200 psec clock, a miss penalty of 50 clock cycles, a miss rate of 0.02 misses per instruction and a cache access time of 1 clock cycle?
1 + 0.02 x 50 = 2 clock cycles
Or 2 x 200 = 400 psecs
Notes: AMAT = 1 + 0.02x50 = 2

## Slide 38: Average Memory Access Time (AMAT)
Average Memory Access Time (AMAT) is the average to access memory considering both hits and misses
  AMAT = Time for a hit + Miss rate x Miss penalty
How calculate if separate instruction and data caches?
Notes: AMAT = 1 + 0.02x50 = 2

## Slide 39: Impact of Cache on CPI
Assume cache hit time included in normal CPU execution time, then
  CPU time = Instruction Count (IC) × Cycles Per Instruction (CPI) × Cycle Time (CT)
  = IC × (CPIideal + CPImiss) × CT
CPIstalls
A simple model for cache miss impact on CPI
CPImiss= accesses/instruction × miss rate × miss penalty
Notes: Reasonable write buffer depth (e.g., four or more words) and a memory capable of accepting writes at a rate that significantly exceeds the average write frequency means write buffer stalls are small

## Slide 40: Impacts of Cache Performance
Relative $ penalty increases as processor performance improves (faster clock rate and/or lower CPI)
  When calculating CPIstalls, cache miss penalty is measured in processor clock cycles needed to handle a miss
  Lower the CPIideal, more pronounced impact of stalls
Processor with a CPIideal of 2, a 100-cycle miss penalty, 36% load/store instr’s, and 2% I$ and 4% D$ miss rates
  CPImiss= 2% × 100 + 36% × 4% × 100 = 3.44
  So CPIstalls = 2 + 3.44 = 5.44
  More than twice the CPIideal !
What if the CPIideal is reduced to 1?
What if the D$ miss rate went up by 1%?
Notes: For ideal CPI = 1, then CPIstall = 4.44 and the amount of execution time spent on memory stalls would have risen from 3.44/5.44 = 63% to 3.44/4.44 = 77%
For miss penalty of 200, memory stall cycles = 2% 200 + 36% x 4% x 200 = 6.88 so that CPIstall = 8.88
This assumes that hit time (so hit time is 1 cycle) is not a factor in determining cache performance. A larger cache would have a longer access time (if a lower miss rate), meaning either a slower clock cycle or more stages in the pipeline for memory access.

## Slide 41: Impact of Larger Cache on AMAT?
1) Lower Miss rate
2) Longer Access time (Hit time): smaller is faster
  Increase in hit time will likely add another stage to the pipeline
At some point, increase in hit time for a larger cache may overcome the improvement in hit rate, yielding a decrease in performance
Computer architects expend considerable effort optimizing organization of cache hierarchy – big impact on performance and power!
Notes: AMAT = 1 + 0.02x50 = 2

## Slide 42: How to Reduce Miss Penalty?
Could there be locality on misses from a cache?
Use multiple cache levels!
With Moore’s Law, more room on die for bigger L1 caches and for second-level (L2) cache
And in some cases even an L3 cache!
IBM mainframes have ~1GB L4 cache off-chip.

## Slide 43: Agenda
Review
Direct Mapped Cache
Administrivia
Write Policy and AMT
Technology Break
Multilevel Caches
And in Conclusion, …

## Slide 44: Agenda
Review
Direct Mapped Cache
Administrivia
Write Policy and AMAT
Technology Break
Multilevel Caches
And in Conclusion, …

## Slide 45: Multiple Cache Levels
E.g., CPIideal of 2, 100 cycle miss penalty (to main memory), 25 cycle miss penalty (to L2$), 36% load/stores, a 2% (4%) L1 I$ (D$) miss rate, add a 0.5% L2$ miss rate
  CPIstalls = 2 + 0.02×25 + 0.36×0.04×25 + 0.005×100 + 0.36×0.005×100
  = 3.54 (vs. 5.44 with no L2$)
Notes: Also reduces cache miss penalty

## Slide 46: Local vs. Global Miss Rates
Local miss rate – the fraction of references to one level of a cache that miss
  Local Miss rate L2$ = $L2 Misses / L1$ Misses
Global miss rate – the fraction of references that miss in all levels of a multilevel cache
    L2$ local miss rate >> than the global miss rate
    Often as high as 50% local miss rate – still useful?

## Slide 47
Time for L1 hit + L1 Miss rate x L2 Miss rate x Miss penalty
Time for L1 hit + L1 Miss rate x (Time for L2 hit + L2 Miss rate x Miss Penalty)
Time for L1 hit + L1 Miss rate x Miss penalty + Time for L2 hit + L2 Miss rate x Miss penalty
Time for L2 hit + L2 Miss rate x L2 Miss penalty
☐
☐
☐
☐
For L1 cache
  AMAT = Time for a hit + Miss rate x Miss penalty
What is AMAT for system with L1 and L2 cache (L2 miss rate is local miss rate)?
Notes: VertLeftWhiteCheck1
B: Print It saves PC+4 …because ints in this system are 4-bytes long and the actual address increments by 4 even though it appears to only incrememt 1.

## Slide 48
Time for L1 hit + L1 Miss rate x L2 Miss rate x Miss penalty
Time for L1 hit + L1 Miss rate x (Time for L2 hit + L2 Miss rate x Miss Penalty)
Time for L1 hit + L1 Miss rate x Miss penalty + Time for L2 hit + L2 Miss rate x Miss penalty
Time for L2 hit + L2 Miss rate x L2 Miss penalty
☐
☐
☐
☐
For L1 cache
  AMAT = Time for a hit + Miss rate x Miss penalty
What is AMAT for system with L1 and L2 cache (L2 miss rate is local miss rate)?
Notes: VertLeftWhiteCheck1
B: Print It saves PC+4 …because ints in this system are 4-bytes long and the actual address increments by 4 even though it appears to only incrememt 1.

## Slide 49: Local vs. Global Miss Rates
Local miss rate – the fraction of references to one level of a cache that miss
  Local Miss rate L2$ = $L2 Misses / L1$ Misses
Global miss rate – the fraction of references that miss in all levels of a multilevel cache
    L2$ local miss rate >> than the global miss rate
  Global Miss rate = L2$ Misses / Total Accesses
  = L2$ Misses / L1$ Misses x L1$ Misses / Total Accesses
  = Local Miss rate L2$ x Local Miss rate L1$
  AMAT = Time for a hit + Miss rate x Miss penalty
  AMAT = Time for a L1$ hit + (local) Miss rateL1$ x (Time for a L2$ hit + (local) Miss rate L2$ x L2$ Miss penalty)

## Slide 50: Improving Cache Performance (1 of 3)
  AMAT = Hit Time + Miss rate x Miss penalty
1. Reduce the time to hit in the cache
  Smaller cache
2. Reduce the miss rate
  Bigger cache
  Larger blocks (16 to 64 bytes typical)
  (Later in semester: More flexible placement by increasing associativity)

## Slide 51: Improving Cache Performance (2 of 3)
3. Reduce the miss penalty
  Smaller blocks
  Use multiple cache levels
    L2 cache size not tied to processor clock rate
  Higher DRAM memory bandwidth (faster DRAMs)
  Use a write buffer to hold dirty blocks being replaced so don’t have to wait for the write to complete before reading

## Slide 52: The Cache Design Space (3 of 3)
Several interacting dimensions
  Cache size
  Block size
  Write-through vs. write-back
  Write allocation
  (Later Associativity)
  (Later Replacement policy)
Optimal choice is a compromise
  Depends on access characteristics
    Workload
    Use (I-cache, D-cache)
  Depends on technology / cost
Simplicity often wins
(Associativity)
Cache Size
Block Size
Bad
Good
Less
More
Factor A
Factor B
Notes: No fancy replacement policy is needed for the direct mapped cache.
As a matter of fact, that is what cause direct mapped trouble to begin with: only one place to go in the cache--causes conflict misses.
No fancy replacement policy is needed for the direct mapped cache.
As a matter of fact, that is what cause direct mapped trouble to begin with: only one place to go in the cache--causes conflict misses.
Besides working at Sun, I also teach people how to fly whenever I have time.
Statistic have shown that if a pilot crashed after an engine failure, he or she is more likely to get killed in a multi-engine light airplane than a single engine airplane.
The joke among us flight instructors is that: sure, when the engine quit in a single engine stops, you have one option: sooner or later, you land. Probably sooner.
But in a multi-engine airplane with one engine stops, you have a lot of options. It is the need to make a decision that kills those people.

## Slide 53: Multilevel Cache Design Considerations
Different design considerations for L1$ and L2$
  L1$ focuses on minimizing hit time for shorter clock cycle: Smaller $ with smaller block sizes
  L2$(s) focus on reducing miss rate to reduce penalty of long main memory access times: Larger $ with larger block sizes
Miss penalty of L1$ is significantly reduced by presence of L2$, so can be smaller/faster but with higher miss rate
For the L2$, hit time is less important than miss rate
  L2$ hit time determines L1$’s miss penalty
Notes: Global miss rate – the fraction of references that miss in all levels of a multilevel cache. The global miss rate dictates how often we must access the main memory.
Local miss rate – the fraction of references to one level of a cache that miss

## Slide 55: CPI/Miss Rates/DRAM Access SpecInt2006
Instructions and Data
Data Only
Data Only

## Slide 56: Typical Memory Hierarchy
Second
Level
Cache
(SRAM)
Control
Datapath
Secondary
Memory
(Disk
Or Flash)
On-Chip Components
RegFile
Main
Memory
(DRAM)
Data
Cache
Instr
Cache
Speed (cycles): ½’s 1’s 10’s 100’s 1,000,000’s
Size (bytes): 100’s 10K’s M’s G’s T’s
Principle of locality + memory hierarchy presents programmer with ≈ as much memory as is available in the cheapest technology at the ≈ speed offered by the fastest technology
Cost/bit: highest lowest
Notes: Instead, the memory system of a modern computer consists of a series of black boxes ranging from the fastest to the slowest.
Besides variation in speed, these boxes also varies in size (smallest to biggest) and cost.
What makes this kind of arrangement work is one of the most important principle in computer design. The principle of locality. The principle of locality states that programs access a relatively small portion of the address space at any instant of time.
The design goal is to present the user with as much memory as is available in the cheapest technology (points to the disk).
While by taking advantage of the principle of locality, we like to provide the user an average access speed that is very close to the speed that is offered by the fastest technology.
(We will go over this slide in detail in the next lectures on caches).

## Slide 57: And in Conclusion, …
Great Ideas: Principle of Locality and Memory Hierarchy
Cache – copy of data lower level in memory hierarchy
Direct Mapped to find block in cache using Tag field and Valid bit for Hit
AMAT balances Hit time, Miss rate, Miss penalty
Larger caches reduce Miss rate via Temporal and Spatial Locality, but can increase Hit time
Multilevel caches reduce the Miss penalty
Write-through versus write-back caches