## Slide 1: CS 61C: Great Ideas in Computer Architecture VM2: Virtual Memory and Machines
Instructor:
Randy H. Katz
http://inst.eecs.Berkeley.edu/~cs61c/fa13

## Slide 2: Part I: You Are Here!
Parallel Requests
  Assigned to computer
  e.g., Search “Katz”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates @ one time
Programming Languages
Smart Phone
Warehouse Scale Computer
Software Hardware
Harness Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory (Cache)
Input/Output
Computer
Main Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0
Today’s
Lecture

## Slide 3: Agenda
Virtual Memory
Administrivia
Virtual Machines
And, in Conclusion …

## Slide 4: Agenda
Virtual Memory
Administrivia
Virtual Machines
And, in Conclusion …

## Slide 5: Not Enough Memory
A problems from the 1960s
There were many applications whose data could not fit in the main memory, e.g., payroll
  Paged memory system reduced fragmentation but still required the whole program to be resident in the main memory

## Slide 6: Manual Overlays
Ferranti Mercury
1956
40k bits
main
640k bits
drum
Central Store
Assume an instruction can address all the storage on the drum
Method 1: programmer keeps track of addresses in the main memory and initiates an I/O transfer when required
  Difficult, error-prone!
Method 2: automatic initiation of I/O transfers by software address translation
  Brooker’s interpretive coding, 1960
  Inefficient!
Not just an ancient black art, e.g., IBM Cell microprocessor used in Playstation-3 has explicitly managed local store!
Notes: British Firm Ferranti, did Mercury and then Atlas
Method 1 too difficult for users
Method 2 too slow.

## Slide 7: Modern Virtual Memory Systems Illusion of a large, private, uniform store
Protection & Privacy
  several users, each with their private address space and one or more shared address spaces
page table  name space
Demand Paging
  Provides the ability to run programs larger than the primary memory
  Hides differences in machine configurations
The price is address translation on
each memory reference
OS
useri
Primary
Memory
Swapping
Store
VA
PA
mapping
TLB
Notes: Portability on machines with different memory configurations.

## Slide 8: “Bare” 5-Stage Pipeline
In a bare machine, the only kind of address is a physical address
PC
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Main Memory (DRAM)
Memory Controller
Physical Address
Physical Address
Physical Address
Physical Address
Physical Address

## Slide 9: Dynamic Address Translation
Motivation
  In early machines, I/O operations were slow and each word transferred involved the CPU
  Higher throughput if CPU and I/O of 2 or more programs were overlapped.
  How?multiprogramming with DMA I/O devices, interrupts
Location-independent programs
  Programming and storage management ease
 need for a base register
Protection
  Independent programs should not affect
  each other inadvertently
 need for a bound register
Multiprogramming drives requirement for resident supervisor software to manage context switches between multiple programs
prog1
prog2
Physical Memory
OS

## Slide 10: Simple Base and Bound Translation
Load X
Program
Address
Space
Bound
Register
Bounds
Violation?
Physical Memory
current
segment
Base
Register
+
Physical
Address
Logical
Address
Base and bounds registers are visible/accessible only when processor is running in kernel mode
Base Physical Address
Segment Length
≤

## Slide 11: Separate Areas for Program and Data
Physical Address
Physical Address
Load X
Program
Address
Space
Main Memory
data
segment
Data Bound Register
Mem. Address Register
Data Base Register
≤
+
Bounds
Violation?
Program Bound Register
Program Counter
Program Base Register
≤
+
Bounds
Violation?
program
segment
Logical Address
Logical Address
What is an advantage of this separation?
(Scheme used on all Cray vector supercomputers prior to X1, 2002)
Notes: Permits sharing of program segments.

## Slide 12: Base and Bound Machine
PC
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Main Memory (DRAM)
Memory Controller
Physical Address
Physical Address
Physical Address
Physical Address
Data Bound Register
Data Base Register
≤
+
[ Can fold addition of base register into (register+immediate) address calculation using a carry-save adder (sums three numbers with only a few gate delays more than adding two numbers) ]
Logical Address
Bounds Violation?
Physical Address
Prog. Bound Register
Program Base Register
≤
+
Logical Address
Bounds Violation?

## Slide 13: Memory Fragmentation
As users come and go, the storage is “fragmented”.
Therefore, at some stage programs have to be moved
around to compact the storage.
OS
Space
16K
24K
24K
32K
24K
user 1
user 2
user 3
OS
Space
16K
24K
16K
32K
24K
user 1
user 2
user 3
user 5
user 4
8K
Users 4 & 5
arrive
Users 2 & 5
leave
OS
Space
16K
24K
16K
32K
24K
user 1
user 4
8K
user 3
free
Notes: Called Burping the memory.

## Slide 14: Paged Memory Systems
Processor-generated address can be split into:
Page tables make it possible to store the pages of a program non-contiguously.
0
1
2
3
0
1
2
3
Address Space
of User-1
Page Table
of User-1
1
0
2
3
page number offset
Physical Memory
A page table contains the physical address of the base of each page
Notes: Relaxes the contiguous allocation requirement.

## Slide 15: Private Address Space per User
Each user has a page table
Page table contains an entry for each user page
VA1
User 1
Page Table
VA1
User 2
Page Table
VA1
User 3
Page Table
Physical Memory
free
OS
pages
Notes: OS ensures that the page tables are disjoint.

## Slide 16: Where Should Page Tables Reside?
Space required by the page tables (PT) is proportional to the address space, number of users, ...
    Too large to keep in registers
Idea: Keep PTs in the main memory
  Needs one reference to retrieve the page base address and another to access the data word
   doubles the number of memory references!

## Slide 17: Page Tables in Physical Memory
VA1
User 1 Virtual Address Space
User 2 Virtual Address Space
PT User 1
PT User 2
VA1
Physical Memory

## Slide 18: Demand Paging in Atlas (1962)
Secondary
(Drum)
32x6 pages
Primary
32 Pages
512 words/page
Central
Memory
User sees 32 x 6 x 512 words
of storage
“A page from secondary
storage is brought into the primary storage whenever it is (implicitly) demanded by the processor.”
Tom Kilburn
Primary memory as a cache
for secondary memory
Notes: Single-level Store

## Slide 19: Hardware Organization of Atlas
Initial
Address
Decode
16 ROM pages
0.4 ~1 sec
2 subsidiary pages-1.4 sec
Main
32 pages
1.4 sec
Drum (4)
192 pages
8 Tape decks
88 sec/word
48-bit words
512-word pages
1 Page Address Register (PAR) per page frame
Compare the effective page address against all 32 PARs
match  normal access
no match  page fault
save the state of the partially executed
instruction
Effective
Address
system code
(not swapped)
system data
(not swapped)
0
31
PARs
<effective PN , status>

## Slide 20: Atlas Demand Paging Scheme
On a page fault:
  Input transfer into a free page is initiated
  Page Address Register (PAR) is updated
  If no free page is left, a page is selected to be replaced (based on usage)
  Replaced page is written on the drum
    To minimize drum latency effect, the first empty page on the drum was selected
  Page table is updated to point to the new location of the page on the drum

## Slide 21: Agenda
Virtual Memory
Administrivia
Virtual Machines
And, in Conclusion …

## Slide 22: Administrivia
Verify all HW, Lab, Midterm, and Project Grades by Friday, 12/6!
Final Exam
  Friday, December 20, 8:00-11:00 RSF Fieldhouse!
  Short answer, fill in the blank, multiple choice, mix and match: 100 points/minutes
  Comprehensive, but concentrated on material since midterm examination
  Closed book/note, open crib sheet as before, MIPS Green Card provided
  Review Session, Monday, 12/9, 3-6 PM, Room TBD
  Special consideration students, please contact

## Slide 23: Administrivia
Topics for Final Exam
  Cache Aware Programming/Cache Blocking
  Data Level Parallelism: Intel SIMD SSE instructions and programming
  Thread Parallelism: Cache Coherency + Synchronization concepts
  OpenMP Programming
  Hardware: Transistors to Gates
  Hardware: Truth Tables to Boolean Algebra
  Hardware: Synchronous System Timing and Timing Diagrams
  Finite State Machines: State Diagrams and Implementation
  CPU Design: Data Path Design (ALUs, Shifters, Register Files, Muxes)
  CPU Design: Controller Design (FSMs for processor implementation)
  Instruction Level Parallelism/Instruction Pipelining
  Set Associative Caches
  Dependability: ECC + RAID
  Virtual Memory
  X-semester issues: Great Ideas in Computer Architecture

## Slide 24: Linear Page Table
VPN
Offset
Virtual address
PT Base Register
VPN
Data word
Data Pages
Offset
PPN
PPN
DPN
PPN
PPN
PPN
Page Table
DPN
PPN
DPN
DPN
DPN
PPN
Page Table Entry (PTE) contains:
  Bit to indicate if a page exists
  PPN (physical page number) for a memory-resident page
  DPN (disk page number) for a page on the disk
  Status bits for protection and usage
OS sets the Page Table Base Register whenever active user process changes

## Slide 25: Size of Linear Page Table
With 32-bit addresses, 4-KB pages & 4-byte PTEs:
  220 PTEs, i.e, 4 MB page table per user
  4 GB of swap needed to back up full virtual address space
Larger pages?
  Internal fragmentation (Not all memory in page is used)
  Larger page fault penalty (more time to read from disk)
What about 64-bit virtual address space???
  Even 1MB pages would require 244 8-byte PTEs (35 TB!)
What is the “saving grace” ?
Notes: Virtual address space is large but only a small fraction of the
pages are populated. So we can use a sparse representation
of the table.

## Slide 26: Hierarchical Page Table
Level 1
Page Table
Level 2
Page Tables
Data Pages
page in primary memory
page in secondary memory
Root of the Current
Page Table
p1
offset
p2
Virtual Address
(Processor
Register)
PTE of a nonexistent page
p1 p2 offset
0
11
12
21
22
31
10-bit
L1 index
10-bit
L2 index
Physical Memory

## Slide 27: Two-Level Page Tables in Physical Memory
VA1
User 1
User1/VA1
User2/VA1
Level 1 PT User 1
Level 1 PT User 2
VA1
User 2
Level 2 PT User 2
Virtual Address Spaces
Physical Memory

## Slide 28: Address Translation & Protection
Every instruction and data access needs address
translation and protection checks
A good VM design needs to be fast (~ one cycle) and space efficient
Physical Address
Virtual Address
Address
Translation
Virtual Page No. (VPN)
offset
Physical Page No. (PPN)
offset
Protection
Check
Exception?
Kernel/User Mode
Read/Write

## Slide 29: Protection via Page Table
Access Rights checked on every access to see if allowed
  Read: can read, but not write page
  Read/Write: read or write data on page
  Execute: Can fetch instructions from page
Valid = Valid page table entry
  Invalid means it’s on the disk, not in physical memory

## Slide 30: More Depth on Page Tables
Virtual Address:
page no.
offset
Page Table
Base Reg
Page Table located in physical memory
index
into
page
table
+
Physical
Memory
Address
Page Table
Val
-id
Access
Rights
Physical
Page
Address
.
V
A.R.
P. P. A.
...
...
20 bits
12 bits

## Slide 31: Translation Lookaside Buffers (TLB)
Address translation is very expensive!
  In a two-level page table, each reference becomes several memory accesses
Solution: Cache translations in TLB
TLB hit  Single-Cycle Translation
TLB miss  Page-Table Walk to refill
VPN offset
V R W D tag PPN
physical address
PPN offset
virtual address
hit?
(VPN = virtual page number)
(PPN = physical page number)
Notes: 3 memory references
2 page faults (disk accesses) + ..
Actually used in IBM before paged memory.

## Slide 32: TLB Designs
Typically 32-128 entries, usually fully associative
  Each entry maps a large page, hence less spatial locality across pages  more likely that two entries conflict
  Sometimes larger TLBs (256-512 entries) are 4-8 way set-associative
  Larger systems sometimes have multi-level (L1 and L2) TLBs
Random or FIFO replacement policy
No process information in TLB?
TLB Reach: Size of largest virtual address space that can be simultaneously mapped by TLB
  Example: 64 TLB entries, 4KB pages, one page per entry
  TLB Reach = _____________________________________________?

## Slide 33: TLB Designs
Typically 32-128 entries, usually fully associative
  Each entry maps a large page, hence less spatial locality across pages  more likely that two entries conflict
  Sometimes larger TLBs (256-512 entries) are 4-8 way set-associative
  Larger systems sometimes have multi-level (L1 and L2) TLBs
Random or FIFO replacement policy
No process information in TLB?
TLB Reach: Size of largest virtual address space that can be simultaneously mapped by TLB
  Example: 64 TLB entries, 4KB pages, one page per entry
  TLB Reach = _____________________________________________?
64 entries * 4 KB = 256 KB (if contiguous)

## Slide 34: Handling a TLB Miss
Software (MIPS, Alpha)
  TLB miss causes an exception and the operating system walks the page tables and reloads TLB. A privileged “untranslated” addressing mode used for walk
Hardware (SPARC v8, x86, PowerPC, RISC-V)
  A memory management unit (MMU) walks the page tables and reloads the TLB
  If a missing (data or PT) page is encountered during the TLB reloading, MMU gives up and signals a Page-Fault exception for the original instruction

## Slide 35: Flashcard Quiz: Which statement is false?
TLB miss is much faster than page fault
TLB exploits spatial locality
TLB hardware grows with larger page size
TLB exploits temporal locality

## Slide 36: Flashcard Quiz: Which statement is false?
TLB miss is much faster than page fault
TLB exploits spatial locality
TLB hardware grows with larger page size
TLB exploits temporal locality

## Slide 37: Hierarchical Page Table Walk: SPARC v8
31 11 0
Virtual Address
Index 1 Index 2 Index 3 Offset
31 23 17 11 0
Context
Table
Register
Context
Register
root ptr
PTP
PTP
PTE
Context Table
L1 Table
L2 Table
L3 Table
Physical Address
PPN Offset
MMU does this table walk in hardware on a TLB miss

## Slide 38: Page-Based Virtual-Memory Machine (Hardware Page-Table Walk)
PC
Inst. TLB
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Page Fault?
Protection violation?
Page Fault?
Protection violation?
Assumes page tables held in untranslated physical memory
Data TLB
Main Memory (DRAM)
Memory Controller
Physical Address
Physical Address
Physical Address
Physical Address
Page-Table Base Register
Virtual Address
Physical Address
Virtual Address
Hardware Page Table Walker
Miss?
Miss?

## Slide 39: Address Translation: Putting it All Together
Virtual Address
TLB
Lookup
Page Table
Walk
Update TLB
Page Fault
(OS loads page)
Protection
Check
Physical
Address
(to cache)
miss
hit
the page is
Ï memory Î memory
denied
permitted
Protection
Fault
hardware
hardware or software
software
SEGFAULT
Where?
Notes: Need to restart instruction.
Soft and hard page faults.

## Slide 40: Handling VM-Related Traps
Handling a TLB miss needs a hardware or software mechanism to refill TLB
Handling a page fault (e.g., page is on disk) needs a restartable trap so software handler can resume after retrieving page
  Precise exceptions are easy to restart
  Can be imprecise but restartable, but this complicates OS software
Handling protection violation may abort process
PC
Inst TLB
Inst. Cache
D
Decode
E
M
Data TLB
Data Cache
W
+
TLB miss? Page Fault?
Protection violation?
TLB miss? Page Fault?
Protection violation?

## Slide 41: Address Translation in CPU Pipeline
Need to cope with additional latency of TLB:
  slow down the clock?
  pipeline the TLB and cache access?
  virtual address caches (see CS152)
  parallel TLB/cache access
PC
Inst TLB
Inst. Cache
D
Decode
E
M
Data TLB
Data Cache
W
+
TLB miss? Page Fault?
Protection violation?
TLB miss? Page Fault?
Protection violation?

## Slide 42: Concurrent Access to TLB & Cache (Virtual Index/Physical Tag)
Index L is available without consulting the TLB
  cache and TLB accesses can begin simultaneously!
Tag comparison is made after both accesses are completed
Cases: L + b = k, L + b < k, L + b > k
VPN L b
TLB
Direct-map Cache
2L blocks
2b-byte block
PPN Page Offset
=
hit?
Data
Physical Tag
Tag
VA
PA
Virtual
Index
k

## Slide 43: Virtual-Index Physical-Tag Caches: Associative Organization
How does this scheme scale to larger caches?
VPN a L = k-b b
TLB
Direct-map
2L blocks
PPN Page Offset
=
hit?
Data
Phy.
Tag
Tag
VA
PA
Virtual
Index
k
Direct-map
2L blocks
2a
=
2a
After the PPN is known, 2a physical tags are compared
Notes:   Consider 4-Kbyte pages and caches with 32-byte blocks
  32-Kbyte cache  2a = 8
    4-Mbyte cache  2a =1024 No !

## Slide 44: Agenda
Virtual Memory
Administrivia
Virtual Machines
And, in Conclusion …

## Slide 45: Safely Sharing a Machine
Amazon Web Services allows independent tasks run on same computer
  Can sell each “instance”
Can a “small” operating system (~10,000 LOC) simulate the hardware of some machine, so that
  Another operating system can run in that simulated hardware?
  More than one instance of that operating system run on the same hardware at the same time?
  More than one different operating system can share the same hardware at the same time?
  And none can access each others’ data?
Answer: Yes

## Slide 46: Solution – Virtual Machine
A virtual machine provides interface identical to underlying bare hardware
  I.e., all devices, interrupts, memory, etc.
Examples
  IBM VM/370 (1970s technology!)
  VMWare (founded by Mendel & Diane Rosenblum)
  Xen (used by AWS)
  Microsoft Virtual PC
Called “System Virtual Machines” vs. language interpreters (e.g., Java Virtual Machine)
Virtualization has some performance impact
  Feasible with modern high-performance computers

## Slide 47: Virtual Machines
Host Operating System:
  OS actually running on the hardware
  Together with virtualization layer, it simulates environment for …
Guest Operating System:
  OS running in the simulated environment
  Runs identical as if on native hardware (except performance)
  Cannot change access of real system resources
  Guest OS code runs in native machine ISA
The resources of the physical computer are shared to create the virtual machines
Processor scheduling by OS can create the appearance that each user has own processor

## Slide 48: Virtual Machine Monitor (a.k.a. Hypervisor)
Maps virtual resources to physical resources
  Memory, I/O devices, processors
VMM handles real I/O devices
  Emulates generic virtual I/O devices for guest OS
Host OS must intercept attempts by Guest OS to access real I/O devices, allocate resources

## Slide 49: Why Virtual Machines Popular (Again)?
Increased importance of isolation and security
Failures in security and reliability of modern OS’s
Sharing of single computer between many unrelated users
  E.g., Cloud computing
Dramatic increase in performance of processors makes VM overhead acceptable

## Slide 50: 5 Reasons Amazon Web Services uses Virtual Machines
(Uses x86 ISA, Linux Host OS, and Xen VMM)
Allow AWS protect users from each other
Simplified SW distribution within WSC
  Customers install image, AWS distributes to all instances
Can reliably “kill” a VM => control resource usage
VMs hide identity of HW => can keep selling old HW AND can introduce new more efficient HW
  VM Performance not need be integer multiple of real HW
VM limiting rate of processing, network, and disk space => AWS offers many price points

## Slide 51: Peer Instruction: True or False
Which statements is True about Virtual Machines?
Multiple Virtual Machines can run on one computer
Multiple Virtual Machine Monitors can run on one computer
III. The Guest OS must be the same as the Host OS
A) I only
B) II only
C) III only
D) I and II
Notes: I is true

## Slide 52: Peer Instruction: True or False
Which statements is True about Virtual Machines?
Multiple Virtual Machines can run on one computer
Multiple Virtual Machine Monitors can run on one computer
III. The Guest OS must be the same as the Host OS
A) I only
B) II only
C) III only
D) I and II
Notes: D) 1c, 2a, 3b

## Slide 53: Virtual Machine/Memory Instruction Set Support
2 modes in hardware: User and System modes
  Some instruction only run in System mode
Page Table Base Register (PTBR): Page Table addr
Privileged instructions only available in system mode
  Trap to system (and VMM) if executed in user mode
All physical resources only accessible using privileged instructions
  Including interrupt controls, I/O registers
Renaissance of virtualization support in ISAs
  Current ISAs (e.g., x86) adapting, following IBM’s path

## Slide 54: Example: Timer Virtualization
In native machine (no VMM), on timer interrupt
  OS suspends current process, handles interrupt, selects and resumes next process
With Virtual Machine Monitor
  VMM suspends current VM, handles interrupt, selects and resumes next VM
If a VM requires timer interrupts
  VMM emulates a virtual timer
  Emulates interrupt for VM when physical timer interrupt occurs

## Slide 55: Virtual Machine Monitor (a.k.a. Hypervisor)
Maps virtual resources to physical resources
  Memory, I/O devices, processors
Guest OS code runs on native machine ISA in user mode
  Traps to VMM on privileged instructions and access to protected resources
Guest OS may be different from host OS
VMM handles real I/O devices
  Emulates generic virtual I/O devices for guest

## Slide 56: Performance Impact of Virtual Machines?
No impact on computation bound program, since they spend ≈0 time in OS
  E.g., matrix multiply
Big impact on I/O-intensive programs, since spend lots of time in OS and execute many systems calls and many privileged instructions
  Although if I/O-bound => spend most time waiting for I/O device, then can hide VM overhead

## Slide 57: Virtual Machines and Cores
Host OS can also limit amount of time a virtual machine uses a processor (core)
Hence, at cost of swapping registers, it can run multiple virtual machines on a single core
AWS cheapest VM was originally 2 VMs per core
Now, with faster processors, can install more VMs per core and deliver same performance or have multiple speeds of cores

## Slide 58: Agenda
Virtual Memory
Administrivia
Virtual Machines
And, in Conclusion …

## Slide 59: And in Conclusion, …
Virtual Memory, Paging for Isolation and Protection, help Virtual Machines share memory
  Can think of as another level of memory hierarchy, but not really used like caches are today
  Not really routinely paging to disk today
Virtual Machines as even greater level of protection to allow greater level of sharing
  Enables fine control, allocation, software distribution, multiple price points for Cloud Computing