## Slide 1: At a recent fireside chat…
CS10 The Beauty and Joy of Computing Lecture #8 : Concurrency
2010-09-29
Nvidia CEO Jen-Hsun Huang said: “whatever capability you think you have today, it’s nothing compared to what you’re going to have in a couple of years … due to supercomputers in the cloud”. Now, cloud computing does what you could do on your PC. Imagine 40,000 times that!
UC Berkeley EECS Lecturer SOE Dan Garcia
www.theregister.co.uk/2010/09/24/huang_muses_at_gtc/

## Slide 2: Happy Confucius Day!
Knowledge is recognizing what you know and what you don't.
I hear and I forget. I see and I remember. I do and I understand.

## Slide 3: Concurrency & Parallelism, 10 mi up…
Intra-computer
Today’s lecture
Multiple computing “helpers” are cores within one machine
Aka “multi-core”
  Although GPU parallism is also “intra-computer”
Inter-computer
Week 12’s lectures
Multiple computing “helpers” are different machines
Aka “distributed computing”
  Grid & cluster computing

## Slide 4: Anatomy: 5 components of any Computer

## Slide 5: Anatomy: 5 components of any Computer
Computer
Memory
Devices
Input
Output
John von Neumann invented this
architecture
Processor
Control
(“brain”)
Datapath (“brawn”)
What causes the most headaches for SW and HW designers with multi-core computing?
Control
Datapath
Memory
Input
Output
Notes: That is, any computer, no matter how primitive or advance, can be divided into five parts:
1. The input devices bring the data from the outside world into the computer.
2. These data are kept in the computer’s memory until ...
3. The datapath request and process them.
4. The operation of the datapath is controlled by the computer’s controller.
All the work done by the computer will NOT do us any good unless we can get the data back to the outside world.
5. Getting the data back to the outside world is the job of the output devices.
The most COMMON way to connect these 5 components together is to use a network of busses.

## Slide 6: But what is INSIDE a Processor?
Processor
Control
(“brain”)
Datapath (“brawn”)
Notes: That is, any computer, no matter how primitive or advance, can be divided into five parts:
1. The input devices bring the data from the outside world into the computer.
2. These data are kept in the computer’s memory until ...
3. The datapath request and process them.
4. The operation of the datapath is controlled by the computer’s controller.
All the work done by the computer will NOT do us any good unless we can get the data back to the outside world.
5. Getting the data back to the outside world is the job of the output devices.
The most COMMON way to connect these 5 components together is to use a network of busses.

## Slide 7: But what is INSIDE a Processor?
Primarily Crystalline Silicon
1 mm – 25 mm on a side
2009 “feature size” (aka process) ~ 45 nm = 45 x 10-9 m (then 32, 22, and 16 [by yr 2013])
100 - 1000M transistors
3 - 10 conductive layers
“CMOS” (complementary metal oxide semiconductor) - most common
Package provides:
  spreading of chip-level signal paths to board-level
  heat dissipation.
Ceramic or plastic with gold wires.
Chip in Package
Bare Processor Die
Processor
Control
(“brain”)
Datapath (“brawn”)

## Slide 8: Moore’s Law
Predicts: 2X Transistors / chip every 2 years
Gordon Moore Intel Cofounder B.S. Cal 1950!
Year
# of transistors on an integrated circuit (IC)
en.wikipedia.org/wiki/Moore's_law
What is this “curve”?
Constant
Linear
Quadratic
Cubic
Exponential

## Slide 9: Moore’s Law and related curves

## Slide 10: Moore’s Law and related curves

## Slide 11: Power Density Prediction circa 2000
4004
8008
8080
8085
8086
286
386
486
Pentium® proc
P6
1
10
100
1000
10000
1970
1980
1990
2000
2010
Year
Power Density (W/cm2)
Hot Plate
Nuclear Reactor
Rocket Nozzle
Source: S. Borkar (Intel)
Sun’s Surface
Core 2

## Slide 12: Going Multi-core Helps Energy Efficiency
Power of typical integrated circuit ~ C V2 f
  C = Capacitance, how well it “stores” a charge
  V = Voltage
  f = frequency. I.e., how fast clock is (e.g., 3 GHz)
William Holt, HOT Chips 2005
Activity Monitor
(on the lab Macs) shows how active your cores are

## Slide 13: Energy & Power Considerations
Courtesy: Chris Batten

## Slide 14: Parallelism again? What’s different this time?
“This shift toward increasing parallelism is not a triumphant stride forward based on breakthroughs in novel software and architectures for parallelism; instead, this plunge into parallelism is actually a retreat from even greater challenges that thwart efficient silicon implementation of traditional uniprocessor architectures.”
– Berkeley View, December 2006
HW/SW Industry bet its future that breakthroughs will appear before it’s too late
view.eecs.berkeley.edu

## Slide 15: Background: Threads
A Thread stands for “thread of execution”, is a single stream of instructions
  A program / process can split, or fork itself into separate threads, which can (in theory) execute simultaneously.
  An easy way to describe/think about parallelism
A single CPU can execute many threads by Time Division Multipexing
Multithreading is running multiple threads through the same hardware
CPU
Time
Thread0
Thread1
Thread2

## Slide 16: Speedup Issues : Amdahl’s Law
Applications can almost never be completely parallelized; some serial code remains
s is serial fraction of program, P is # of cores (was processors)
Amdahl’s law:
Speedup(P) = Time(1) / Time(P)
≤ 1 / ( s + [ (1-s) / P) ], and as P  ∞
≤ 1 / s
Even if the parallel portion of your application speeds up perfectly, your performance may be limited by the sequential portion
Time
Number of Cores
Parallel portion
Serial portion
1
2
3
4
5
en.wikipedia.org/wiki/Amdahl's_law

## Slide 17: Speedup Issues : Overhead
Even assuming no sequential portion, there’s…
  Time to think how to divide the problem up
  Time to hand out small “work units” to workers
  All workers may not work equally fast
  Some workers may fail
  There may be contention for shared resources
  Workers could overwriting each others’ answers
  You may have to wait until the last worker returns to proceed (the slowest / weakest link problem)
  There’s time to put the data back together in a way that looks as if it were done by one

## Slide 18: Life in a multi-core world…
This “sea change” to multi-core parallelism means that the computing community has to rethink:
  Languages
  Architectures
  Algorithms
  Data Structures
  All of the above

## Slide 19: But parallel programming is hard!
What if two people were calling withdraw at the same time?
  E.g., balance=100 and two withdraw 75 each
  Can anyone see what the problem could be?
  This is a race condition
In most languages, this is a problem.
  In Scratch, the system doesn’t let two of these run at once.
en.wikipedia.org/wiki/Concurrent_computing

## Slide 20: Another concurrency problem … deadlock!
Two people need to draw a graph but there is only one pencil and one ruler.
  One grabs the pencil
  One grabs the ruler
  Neither release what they hold, waiting for the other to release
Livelock also possible
  Movement, no progress
  Dan and Luke demo
en.wikipedia.org/wiki/Deadlock

## Slide 21: Summary
“Sea change” of computing because of inability to cool CPUs means we’re now in multi-core world
This brave new world offers lots of potential for innovation by computing professionals, but challenges persist