University of California at Berkeley

College of Engineering

Department of Electrical Engineering and Computer Science

EECS 150									R. H. Katz

Fall 2000

Problem Set # 7 (Assigned 19 October, Due 27 October)

- In lecture 06-SeqImpl, slides 34-35, we presented a Moore Machine and Mealy Machine description for a simple sequence detector that would output a 1 whenever the bit sequence 01 or 10 has been seen in the input bit stream. Assume positive edge-triggered state flipflops and that the input changes on the falling edge of the clock.

- Draw timing diagrams for how these two state machines behave for the input stream 001011010.

- If the Mealy Machine is implemented as a SYNCHRONOUS MEALY MACHINE, draw the timing diagram for this sequence.

- If the timing behaviors are different for the MOORE, MEALY, and SYNCHRONOUS MEALY machines, explain the reason why.

- Design a MEALY MACHINE sequence detector state machine that outputs a 1 whenever its input stream is a 4-bit bit serial palindrome, i.e., the last two bits are mirror images of the first two bits in the 4-bit sequence. An example of the machine’s correct behavior is shown below:

Input: 	0000 0110 1010 0011 1001 …

Output:	0001 0001 0000 0000 0001 …

- Given the following MOORE MACHINE State Transition Table, use the Implication Chart method to minimize the number of states. Draw the resulting minimized state diagram.

- Given the following MEALY MACHINE State Transition Table, perform three different state assignments and develop the minimized Next State and Output Boolean functions according the following specifications:

- Assign states sequentially: A=00, B=01, C=10, D=11

- Assign states using 1 Hot Encoding: A=1000, B=0100, C=0010, D=0001 (6 Variable K-maps!)

- Assign states using the heuristics presented in 06-SeqImpl, Slide #69

- Which yields the best implementation and why?

# Text boxes

11

C

C

C

C

10

D

B

D

B

01

B

A

D
B

00

A

B

A

A

Current State

A

B

C

D

Next State

Output

00

0

0

0

0

0

1

1

0

1

0

11

5

1

3

2

1

2

10

0

3

4

0

5

0

01

2

2

2

1

2

4

00

1

0

5

5

0

5

Output

Next State

Current State

0

1

2

3

4

5

01

1

0

0

0

10

0

0

0

0

11

1

1

1

1