Problem set #1: (5pts)

Note:   Grading is based on effort on every single problem. Points will be deducted from

not attempted questions.

1a) Combinational – We can make a truth table with the two 2-bit quantities as inputs and

generate a 4-bit output. Then all we need to do is writing boolean

expressions for each of the 4 output bits and building combinational

logics for those expressions.

b) Sequential – FSM is used to remember the states after checking each bit in a

continuous stream of bits. The easiest way is having one state per

pre-specified pattern of bits, and one state for error.

c) Combinational – The only information needed is the given specified year, which will

go through a bunch of combinational logics result from a formula

checking it’s leap year or not. No memory of past inputs is needed.

d) Sequential – A simple solution will be using a FSM with 5 cents for each state,

resulting 11 states (5, 10, 15 …, 55) and a start state. Each insertion of

quarters, dimes and nickels will deliver to the corresponding state. Get

the product if you get to the last state. Many other possible solutions

exist.

e) Combinational – We can make a truth table using those two binary control bits and the

single data as inputs with four output bits. Then all we need to know

is the inputs and it will match to the outputs, no extra memory is

needed.

f) Combinational –  It’s easy to write down boolean expressions for those three outputs.

The first output is NOR of the two inputs, the second is XOR and the

third is AND. Then build a circuit using those gates. No memory of

past input is needed.

2a)

b) d4 = d8 = d16 = 1

d2 = (m8 + m4 + m2’ + m1 + L’)*(m8 + m4 + m2’ + m1 + L)

= (m8 + m4 + m2’ + m1)

d1 = (m8’ * m4’ * m2’ * m1) + (m8’ * m4’ * m2 * m1’ * L) +

(m8’ * m4’ * m2 * m1)  + (m8’ * m4 * m2’ * m1) +

(m8’ * m4 * m2 * m1) + (m8 * m4’ * m2’ * m1’) +

(m8 * m4’* m2 * m1’) + (m8 * m4 * m2’ * m1’)

c) d4, d8, d16: none

d2: 	1  OR4

1  INV

d1: 	7  AND4

1  AND5

1  OR8

18 INV

3a)

b) d4 = d8 = d16 = 1

d2 = (d28’ * d29’ * d30 * d31’) + (d28’ * d29’ * d30’ * d31)

d1 = (d28’ * d29 * d30’ * d31’) + (d28’ * d29’ * d30’ * d31)

c) d4, d8, d16: none

d2: 	2 AND4

1 OR2

6 INV

d1: 	2 AND4

1 OR2

6 INV

d) The one presented in class uses more gates than the design in Problem 2. Using the

subsystem in this problem will only add to the complexity if the original design.

4a) d4 = d8 = d16 = 1

d2 = d30 + d31

d1 = d29 + d31

b) d4, d8, d16: none

d2: 	1 OR2

d1: 	1 OR2

5a)

not new		 not new

new &		      new &

new  &                          equal 		      equal

reset 		     equal

not new       new &

not equal	                    new		        new

not new		not new

b) 7 states:

5c)

States: 4 bits

Mux: 3 bits

Open/closed: 1 bit

5d)

Original implementation: open/closed = (reset’*new*equal*S3) + (reset’*Open)

New implementation:       open/closed = (reset’*new*equal*S3) + (reset’*Open)

Therefore, same complexity.

# Text boxes

closed

c1

S1

closed

c2

# S2

closed

c3

# S3

# Open

closed

c2

## E1

closed

c3

## E2

## Err