# University of California at Berkeley

## College of Engineering

Department of Electrical Engineering and Computer Sciences

### EECS150								J. Wawrzynek

# Fall 2002

#### Homework #6

This homework is due on Friday October 18th by 2pm.  Homework will be accepted in the EECS150 box outside 125 Cory.  Late homework will be penalized by 50%.  No late homework will be accepted after the solution is posted.  Please write your lab section number on your homework.

- Suppose you asked to sum the following list of 4-bit unsigned numbers (1,5,3,2,3,1), as quickly as possible using a set of carry-save adders (CSAs) and a single carry-propagate adder (CPA).  You may use as many CSAs as you would like.  Draw a diagram depicting the circuit you would construct.  Draw each CSA and CPA as a block.  Label each set of wires in-to and out-of blocks with the base 10 value of the number on that set of wires.

- In class we discussed two different major classes of multiplier circuits, the shift-and-add multiplier, that multiplies n pairs of bits at a time, and the array multiplier, that multiplies n2 pairs of bits at a time.  These two represent different tradeoffs between cost and delay.  A third class of multiplier, bit-serial, represents yet another tradeoff between cost and delay; it forms the product by multiplying only one pair of bits at a time.  Devise and draw a circuit for a bit-serial multiplier.  You may assume the presence of an external controller circuit, but need to write out the control algorithm (similar to what we did in class for the bit-serial adder).  Make sure to include all necessary shift-registers in your circuit.

- Make a table comparing array, shift-and-add, and bit-serial multipliers with respect to cost in terms of FA cells, cost in terms of FFs, and delay, all as a function of n, the number of bits in the inputs.  Use “big O” notation.

- From PHY datasheet and class notes:

- The chip supports “auto-negotiate”.  What is the main purpose of this operation?

- The device supports 100baseFX.  What does the FX stand for?

- When operating at 100Mbps,  what is the bit pattern the PHY sends out on the network when not sending Ethernet frames?

- On a 100Mbps Ethernet how long does it take to send a maximum sized packet, including the preamble?

- For the encapsulation scheme used for eTV (RTP directly in MAC), what would be the maximum size in bytes of a the payload of the RTP payload