University of California at Berkeley

College of Engineering

Department of Electrical Engineering and Computer Science

EECS 150									R. H. Katz

Fall 2005

Problem Set #2: Programmable Logic

Assigned 7 September 2005, Due 16 September at 2 PM

- Consider the following multilevel schematic constructed from AND-OR gates.

  - What is the Boolean algebra equation derived from this schematic?

  - What is the minimized AND-OR schematic that is equivalent to this schematic? Show your work using a K-map.

  - Suppose that the schematic is restricted to only using NAND, NOR, and NOT gates. Convert the original schematic to a similar one making use of these gates only.

  - Suppose that the schematic is restricted to only using NAND gates. Convert the original schematic to a similar one using only NAND gates. NOTE: You may have to add some gates to make the mapping work!

  - Suppose that the schematic is restricted to only using NOR gates. Convert the original schematic to a similar one using only NOR gates. NOTE: You may have to add some gates to make the mapping work!

- Consider the following four functions to be implemented in Programmable Logic Arrays:

F(A,B,C,D) = m(1,4,5,7,9,12,13,15)

G(A,B,C,D) = m(1,3,5,6,7,13,14,15)

H(A,B,C,D) = m(4,6,12,13,14,15)

I(A,B,C,D) = m(1,3,13,15)

  - Use K-maps to minimize in sum of products form each of the four functions independently. Write down the Boolean expressions that result.

  - How many unique product terms span the four functions?

  - Now minimize the four functions, seeking to find the minimum number of product terms across all four functions simultaneously.

  - How many unique terms does your solution require? Is it a savings compared with your answer to part b?

  - Show how you would program the AND-OR array to implement the four functions using your solution to part c.

- Programmable logic arrays as presented in class are based on AND-OR two-level logic. It is also possible to implement logic arrays in OR-AND logic. Repeat parts (a) through (d) except where the target is product of sums expressions for the functions F. G. H. I described above.

e.	Which solution is better and why, 2(d) versus 3(d)?

- Given the function F(A,B,C) = m(1,3,4,6,7):

  - Show how to implement F with an 8:1 multiplexer.

  - Show how to implement F with a 4:1 multiplexer (HINT: put A and B on the selection inputs).

- Given the function G(A,B,C,D) = M(0,1,3,4,5,10,11):

  - Show how to implement G with a 16:1 multiplexer.

  - Show how to implement G with an 8:1 multiplexer (HINT: put A, B, and C on the selection inputs).

- Given the function H(A,B,C,D) = m(1,3,5,7,12,13,14,15), show how to implement H with a single 4:1 multiplexer and no other logic.

- Given the same function from problem 6:

  - Implement H using a 4:16 decoder as a function generator along with a single large fan-in OR gate.

  - Implement H using a 3:8 decoder as a function generator along with a single 4-input OR gate.

- Given the functions F, G, H, I of Problem 2:

  - How many Xilinx CLBs would it take to implement your answer to Problem 2(a) for all four functions together?

  - How many Xilinx CLBs would it take to implement your answer to Problem 2(c) for all four functions together?

  - Considering just the truth tables for the four functions, how many Xilinx CLBs would it take to implement them together?