University of California at Berkeley

College of Engineering

Department of Electrical Engineering and Computer Science

SOLUTIONS

EECS 150									R. H. Katz

Fall 2005

Problem Set #2: Programmable Logic

Assigned 7 September 2005, Due 16 September at 2 PM

- Consider the following multilevel schematic constructed from AND-OR gates.

  - What is the Boolean algebra equation derived from this schematic?

F=(AB)(C+D)+C’

=ABC + ABD + C’

  - What is the minimized AND-OR schematic that is equivalent to this schematic? Show your work using a K-map.

| CD \ AB | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| 00 | 1 | 1 | 1 | 1 |
| 01 | 1 | 1 | 1 | 1 |
| 11 |  |  | 1 |  |
| 10 |  |  | 1 |  |

= C’ + AB

  - Suppose that the schematic is restricted to only using NAND, NOR, and NOT gates. Convert the original schematic to a similar one making use of these gates only.

  - Suppose that the schematic is restricted to only using NAND gates. Convert the original schematic to a similar one using only NAND gates. NOTE: You may have to add some gates to make the mapping work!

  - Suppose that the schematic is restricted to only using NOR gates. Convert the original schematic to a similar one using only NOR gates. NOTE: You may have to add some gates to make the mapping work!

- Consider the following four functions to be implemented in Programmable Logic Arrays:

F(A,B,C,D) = m(1,4,5,7,9,12,13,15)

G(A,B,C,D) = m(1,3,5,6,7,13,14,15)

H(A,B,C,D) = m(4,6,12,13,14,15)

I(A,B,C,D) = m(1,3,13,15)

  - Use K-maps to minimize in sum of products form each of the four functions independently. Write down the Boolean expressions that result.

| CD/AB | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| 00 |  | 1 | 1 |  |
| 01 | 1 | 1 | 1 | 1 |
| 11 |  | 1 | 1 |  |
| 11 |  |  |  |  |

F = C’D + BC’ + BD

| CD/AB | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| 00 |  |  |  |  |
| 01 | 1 | 1 | 1 |  |
| 11 | 1 | 1 | 1 |  |
| 11 |  | 1 | 1 |  |

G = A’D + BD + BC

| CD/AB | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| 00 |  | 1 | 1 |  |
| 01 |  |  | 1 |  |
| 11 |  |  | 1 |  |
| 11 |  | 1 | 1 |  |

H = AB + BD’

| CD/AB | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| 00 |  |  |  |  |
| 01 | 1 |  | 1 |  |
| 11 | 1 |  | 1 |  |
| 11 |  |  |  |  |

  - How many unique product terms span the four functions?

9 Unique Terms

  - Now minimize the four functions, seeking to find the minimum number of product terms across all four functions simultaneously.

Minimize Form

F = BD + C’D + BC’D’

G=BD + A’B’D + BCD’

H= BC’D’ + BCD’ + ABD

I = ABD + A’B’D

  - How many unique terms does your solution require? Is it a savings compared with your answer to part b?

ABD +BCD’ + BC’D’ + A’B’D + BD + C’D

6 Unique Terms

  - Show how you would program the AND-OR array to implement the four functions using your solution to part c.

- Programmable logic arrays as presented in class are based on AND-OR two-level logic. It is also possible to implement logic arrays in OR-AND logic. Repeat parts (a) through (d) except where the target is product of sums expressions for the functions F. G. H. I described above.

Product of Sums

| CD/AB | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| 00 | 0 |  |  | 0 |
| 01 |  |  |  |  |
| 11 | 0 |  |  | 0 |
| 11 | 0 | 0 | 0 | 0 |

F = (B+D)(C’+D)(B+C’)

| CD/AB | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| 00 | 0 | 0 | 0 | 0 |
| 01 |  |  |  | 0 |
| 11 |  |  |  | 0 |
| 11 | 0 |  |  | 0 |

G = (C+D)(A’+B)(B+D)

| CD/AB | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| 00 | 0 |  |  | 0 |
| 01 | 0 | 0 |  | 0 |
| 11 | 0 | 0 |  | 0 |
| 11 | 0 |  |  | 0 |

H = B(D’+A)

| CD/AB | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| 00 | 0 | 0 | 0 | 0 |
| 01 |  | 0 |  | 0 |
| 11 |  | 0 |  | 0 |
| 11 | 0 | 0 | 0 | 0 |

I=D(A+B’)(A’+B)

9 Unique Terms

Minimize Product

F= (B+C’)(C’+D)(B+D)

G=(A’+B)(B+D)(C+D)

H=(B+D)(A’+B)(A+D’)

I=(C+D)(C’+D)(A’+B)(A+B’+D’)

7 Unique Terms

e.	Which solution is better and why, 2(d) versus 3(d)?

2d is better as it has less unique terms.

- Given the function F(A,B,C) = m(1,3,4,6,7):

  - Show how to implement F with an 8:1 multiplexer.

| 0 | - | 0 |  |
| --- | --- | --- | --- |
| 1 | - | 1 |  |
| 0 | - | 2 |  |
| 1 | - | 3 | 8:1 Mux |
| 1 | - | 4 |  |
| 0 | - | 5 |  |
| 1 | - | 6 |  |
| 1 | - | 7 |  |
|  |  |  | ABC |

  - Show how to implement F with a 4:1 multiplexer (HINT: put A and B on the selection inputs).

| C | - | 0 |  |
| --- | --- | --- | --- |
| C | - | 1 |  |
| C’ | - | 2 | 4:1 Mux |
| 1 | - | 3 |  |
|  | - |  | AB |

- Given the function G(A,B,C,D) = M(0,1,3,4,5,10,11):

  - Show how to implement G with a 16:1 multiplexer.

| 0 | - | 0 |  |
| --- | --- | --- | --- |
| 0 | - | 1 |  |
| 1 | - | 2 |  |
| 0 | - | 3 |  |
| 0 | - | 4 |  |
| 0 | - | 5 |  |
| 1 |  | 6 |  |
| 1 | - | 7 |  |
| 1 | - | 8 | 16:1 Mux |
| 1 | - | 9 |  |
| 0 | - | 10 |  |
| 0 | - | 11 |  |
| 1 | - | 12 |  |
| 1 | - | 13 |  |
| 1 | - | 14 |  |
| 1 | - | 15 |  |
|  |  |  | ABCD |

  - Show how to implement G with an 8:1 multiplexer (HINT: put A, B, and C on the selection inputs).

| 0 | - | 0 |  |
| --- | --- | --- | --- |
| D’ | - | 1 |  |
| 0 | - | 2 |  |
| 1 | - | 3 | 8:1 Mux |
| 1 | - | 4 |  |
| 0 | - | 5 |  |
| 1 | - | 6 |  |
| 1 | - | 7 |  |
|  |  |  | ABC |

- Given the function H(A,B,C,D) = m(1,3,5,7,12,13,14,15), show how to implement H with a single 4:1 multiplexer and no other logic.

| D | - | 0 |  |
| --- | --- | --- | --- |
| D | - | 1 |  |
| 0 | - | 2 | 4:1 Mux |
| 1 | - | 3 |  |
|  | - |  | AB |

- Given the same function from problem 6:

  - Implement H using a 4:16 decoder as a function generator along with a single large fan-in OR gate.

AB+BD+A’B’D

  - Implement H using a 3:8 decoder as a function generator along with a single 4-input OR gate.

ABD + ABD’ + A’BD + A’B’D

- Given the functions F, G, H, I of Problem 2:

  - How many Xilinx CLBs would it take to implement your answer to Problem 2(a) for all four functions together?

2 CLBs

  - How many Xilinx CLBs would it take to implement your answer to Problem 2(c) for all four functions together?

2 CLBs

  - Considering just the truth tables for the four functions, how many Xilinx CLBs would it take to implement them together?

2 CLBs