# Professor Fearing	EECS 150/Problem Set 10	Fall 1997

Solutions by Chris Eng, cje@cory.eecs.berkeley.edu

Problem 1 (30 pts)

We want to emulate a 2-bit counter using the provided microprogrammed control unit.  Important things to notice about the MCU: 1) The top bit of the instruction word enables either the input mux or the clock enable of the output register, 2) Bits 5 and 6 of the instruction word specify which control signal(s) are selected by the mux, 3) The bottom two bits of the instruction word specify the two counter bits.  Based on the given specifications regarding the control signals CEN and UP, we can get a rough idea of how the microcode should work.

After each counter transition, the program must first latch a value into Q1 and Q0.  Then, it should check to see whether or not the counter is actually enabled – if not, it should remain in its current state until CEN is asserted.  Assuming the counter is on, it should increment if the CEN&UP signal is asserted or decrement if it is deasserted.  One possible implementation of the microcode is shown below.  The notation jmp(x) means to jump to the specified label if signal x is asserted.

| Label | ROM Address | Mnemonic Form | Numeric Form (O[7:0]) | Hex Data |
| --- | --- | --- | --- | --- |
| Start00 | 00000 | 00 ( Output Register | 0xxxxx00 | 00 |
| Hold00 | 00001 | jmp(CEN/) Hold00 | 10100001 | A1 |
|  | 00010 | jmp(CEN&UP) Start01 | 10000100 | 84 |
|  | 00011 | jmp Start11 | 11101100 | EC |
| Start01 | 00100 | 01 ( Output Register | 0xxxxx01 | 01 |
| Hold01 | 00101 | jmp(CEN/) Hold01 | 10100101 | A5 |
|  | 00110 | jmp(CEN&UP) Start10 | 10001000 | 88 |
|  | 00111 | jmp Start00 | 11100000 | E0 |
| Start10 | 01000 | 10 ( Output Register | 0xxxxx10 | 02 |
| Hold10 | 01001 | jmp(CEN/) Hold10 | 10101001 | A9 |
|  | 01010 | jmp(CEN&UP) Start11 | 10001100 | 8C |
|  | 01011 | jmp Start01 | 11100100 | E4 |
| Start11 | 01100 | 11 ( Output Register | 0xxxxx11 | 03 |
| Hold11 | 01101 | jmp(CEN/) Hold11 | 10101101 | AD |
|  | 01110 | jmp(CEN&UP) Start00 | 10000000 | 80 |
|  | 01111 | jmp Start10 | 11101000 | E8 |

The numeric form of each instruction is easily realized once the mnemonic instructions have been determined.  We can simplify the task by breaking it up into several parts.  First, we consider the top bit.  If a value is being loaded into the output register, we know that O7 must be 0; otherwise, since the rest of the instructions are jumps (possibly requiring an explicit load into the ROM Address counter), we must set O7 to 1.  The next two bits, O6 and O5, select the signal coming out of the 4-input mux.  All we need to do is select the control signal which corresponds to the jump being performed.  For example, the instruction “jmp(CEN/) Hold00” uses CEN/ as its jump criteria; thus, we would set O6 and O5 to 0 and 1, respectively.  This way, if CEN=0, the jump is carried out and a new value is loaded into the ROM Address counter.  If CEN=1, the jump does not happen and the Address counter simply increments by one.  Finally, the last five bits of each instruction word correspond to jump locations, which are easily extracted from the chart.  The exception to this is when the output register is being written, in which case we only care that the bottom two bits are written correctly to Q1 and Q0.  The corresponding ROM data (hex) is also shown in the table.  In this case, we have replaced the don’t-care values (x) with 0’s.

A timing diagram for this microcode is shown on the following page.  We start out in the initial state in which Q1 and Q0 are both set to 0.  We count up to Q1Q0=10, then deassert the UP signal so that the counter will count down.  When we reach  Q1Q0=01, we deassert CEN, causing the counter to hold in the current state.  After a few more cycles, we assert CEN again, allowing the counter to continue decrementing.  It counts down to Q1Q0=10, at which point we assert UP, telling the counter to count upward once again.  The microprogram counter (ROM Address) is also shown on the timing diagram, in decimal form.

| CLK |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| UP |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| CEN |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Q1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Q0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Address |  | 0 | 1 | 2 | 4 | 5 | 6 | 8 | 9 | 10 | 11... |

| CLK |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| UP |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| CEN |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Q1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Q0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Address | ...11 | 4 | 5 | 5 | 5 | 6 | 7 | 0 | 1 | 2 | 3... |

| CLK |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| UP |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| CEN |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Q1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Q0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Address | ...3 | 12 | 13 | 14 | 15 | 8 | 9 | 10 | 12 | 13 | 14... |

You may have noticed that the timing of the counter exhibits some asymmetry due to the structure of the microprogram.  That is, when UP is asserted, the counter value is incremented every three clock cycles, but when UP is deasserted, the counter value is decremented every four clock cycles.  This happens because of the extra “jmp” instruction that has to be processed when the counter is counting down.  If for some reason we needed the timing to be the same for counting up and down, we could insert extra states in the microcode in order to lengthen up-counting to four clock cycles.  This could be implemented something like this:

| Label | ROM Address | Mnemonic Form |
| --- | --- | --- |
| Nop00 | 00000 | no-op [jmp Start00] |
| Start00 | 00001 | 00 ( Output Register |
| Hold00 | 00010 | jmp(CEN/) Hold00 |
|  | 00011 | jmp(CEN&UP) Nop01 |
|  | 00100 | jmp Start11 |
| Nop01 | 00101 | no-op [jmp Start01] |
| Start01 | 00110 | 01 ( Output Register |
| Hold01 | 00111 | jmp(CEN/) Hold01 |
|  | 01000 | jmp(CEN&UP) Nop10 |
|  | 01001 | jmp Start00 |
| Nop10 | 01010 | no-op [jmp Start10] |
| (etc...) |  |  |

Using this implementation of the microprogram, we see that instead of jumping directly to a given “Start” state during a counter increment, the program jumps to a no-op state, where it basically wastes a clock cycle before continuing as before.  This change would fit easily into the ROM, since it only requires one extra microinstruction per counter state.

Problem 2 (30 pts)

Now we will modify the MCU used in Problem 1.  We are given a single 8Kx8 ROM which we will use to create an MCU with 15 output bits, 1024 microinstruction addresses, and 16 branch conditions.  Since the ROM is only 8 bits wide, we now that each instruction now occupies 2 consecutive memory addresses.  The MSB of the contents of the second address determines whether or not the instruction is a jump (jumps should always be to even addresses).  On a jump, the contents of the first address and the bottom 2 bits of the second address contain the target address.  Bits 6 through 3 determine which condition to use for branching.  The instruction format is shown on the next page.

|  | O15 | O14 | O13 | O12 | O11 | O10 | O9 | O8 | O7 | O6 | O5 | O4 | O3 | O2 | O1 | O0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| DO | 1 | Control Signals |
| JMP | 0 | Branch Variable |  | Branch Address |

Problem 3 (35 pts)

Given the datapath in Figure Ex11.13, we want to create an MCU that could control the processor.  We know, first of all, that there are two types of instruction that we should consider – branch instructions, in which the program counter jumps to a given location, and register transfer instructions, which operate sequentially.  Looking at the datapath, we see that in each register transfer instruction, we will need to specify two source signals plus a destination register (if any).  We will also need to select the function of the ALU.  For branch instructions, we need to specify the branch condition as well as a target address.

First, we will figure out how many bits will be needed for a register transfer microinstruction.  For the first output source, we can select between [R0, R1, R2, R3](ABus.  For the second output, we will select from [R0, R1, R2, R3, IR, PC, MBR](BBus, as well as MAR(M.  For the destination register, we will choose from CBus([R0, R1, R2, R3, IR, MAR, MBR], BBus([SHFT, PC, MAR], and M(MBR.  Finally, we will assume that we have a very basic ALU that only performs the functions ADD, SUB, PASS A, and PASS B.  The resulting register transfer instruction format is shown below.

| Type | Source A | Source B | Destination | ALU Function |
| --- | --- | --- | --- | --- |
| 1 | 2 | 3 | 4 | 2 |

The “Type” field will be set to 1, designating that this is a register transfer instruction.  For the remaining fields, we will use the following encoding:

| Source A | Source B | Destination | ALU Function |
| --- | --- | --- | --- |
| 00: R0(BusA | 000: R0(BusB | 0000: CBus(R0 | 00: A+B |
| 01: R1(BusA | 001: R1(BusB | 0001: CBus(R1 | 01: A–B |
| 10: R2(BusA | 010: R2(BusB | 0010: CBus(R2 | 10: Pass A |
| 11: R3(BusA | 011: R3(BusB | 0011: CBus(R3 | 11: Pass B |
|  | 100: IR(BusB | 0100: CBus(IR |  |
|  | 101: PC(BusB | 0101: CBus(MAR |  |
|  | 110: MBR(BusB | 0110: CBus(MBR |  |
|  | 111: MAR(M | 0111: BBus(SHIFT |  |
|  |  | 1000: BBus(PC |  |
|  |  | 1001: BBus(MAR |  |
|  |  | 1010: M(MBR |  |
|  |  | 1011: MBR(M |  |
|  |  | 1100: NOP |  |
|  |  | 1101: NOP |  |
|  |  | 1110: NOP |  |
|  |  | 1111: NOP |  |

Now, we will figure out the encoding for branch instructions.  First, we know that we need one bit set to 0 at the top of the instruction (the “Type” field).  Assuming that we have 256 possible microinstructions, we will need 8 bits to specify the jump address.  This leaves 3 bits, which we will use for the branch condition.  The resulting branch instruction format is shown below.

| Type | Branch Condition | Branch Destination |
| --- | --- | --- |
| 1 | 3 | 8 |

The final MCU is shown below.  Basically, it consists of an 8-bit counter to hold the program counter, a 256x12 ROM in which the microcode is stored, a 12-bit register to latch the controller outputs, and several decoders to interpret each of the control fields.  There is also an 8-input mux which selects the branch condition.  Note that the controller outputs are latched on the falling edge of the clock while the program counter is latched on the rising edge.  The combinational logic for the memory controller is not shown; however, “Read” would be asserted when “MAR to M” and “M to MBR” were both true, while “Write” would be asserted when “MAR to M” and “MBR to M” were both true.

Thus, the microcode we would use to implement the instruction “ADD Ra, (Rb)offset” is shown here.  For simplicity, we will make the assumption that Ra=R0 and Rb=R1.  Also note that the specified offset would be contained in the instruction register.  X’s, as usual, represent a “don’t care”.

| Microinstruction | Numeric Format |
| --- | --- |
| DO R1+Offset(MAR | 1 01 100 0101 00 |
| DO M[MAR](MBR | 1 xx 111 1011 xx |
| DO R0+MBR(R0 | 1 00 110 0000 00 |
| JMP Fetch |  |