CS150

Week 5, lecture 1

Covers:

- Various Flip-flops and what they’re good for ( and a bit of glitch stuff )

- Various counters

- Glitches. Glitches and Kmaps

- Self starting FSM

- Design flow chart

- Various Flip-flops and what they’re good for ( and a bit of glitch stuff )

3-state up/down counter:

Specifications:    	If   I=1, count up 1 ( 2 ( 3 ( 1

If  I=0, count down 3 ( 2 ( 1 ( 3

Output = state.

Did you want don’t cares in this table?

D1			            D0			 T1			     T0

__              __      __     __            __

D1 = Q1 + I Q1 Q0 = (Q0 + Q1 ) ( I + Q1 )

__                _ __       __     __           __

D0 = Q0 + I Q1 + I Q1 = (Q0 + Q1 + I ) ( I + Q1 )

S1			            R1			 S0			     R0

__

S1 = Q1

_

R1 =I Q1 + Q0 Q1

J1			            K1			 J0			     K0

J1 = 1

__

K1 = Q1 + I

Comments:

1.  “Don’t cares” in state diagram (  “X” in every k-map.

2.  Why do: 		rather than:		     ?   Answer: Glitches.

Two ways to write R1:

_

a)  R1 = Q1 I + Q0 Q1

__  _

b)  R1 = Q0 I + Q0 Q1

a)							b)

Especially makes a difference with “1” catching latch.  b) will have “glitches”.

GLITCH!

(A value that you don’t expect and probably don’t want.)

Good/Bad stuff about different kinds of flip-flops …

Fewer wires	Fewer Gates

Toggles good if lots of bits changing each transition.

Ds good in VLSI.

- Various counters

Offset counter: Counts X to 15 (To 15 for 4 bit counter… to 7 for 3 bit counter etc…)

Limit counter: Counts o to X

Offset and Limit Counter: Counts from X to Y.

Skipped state transition diagram on pages with counters.

3)	Glitches. Glitches and Kmaps

Glitch: Unwanted pulse.

Hazard: Circuit with the potential to have a glitch.

Use K-maps to find single bit transition hazards:

- Each implicant corresponds to a gate:

AND for SOP

OR for POS

(   Moving around inside an implicant corresponds to no change on inputs to implicant.

(   Moving between implicants causes hazards.

Implicant: Circled group in K-map.

Prime implicant: A circled group that can’t be contained in another group. As big as it can be.

Essential implicant: Covers something not covered somewhere else.

Essential

Implicant: All circled groups

Prime implicant

Not prime ( Can be put inside group of 4 )

4)	Self starting FSM

With ?????? in state transition diagrams, you need to figure out what you actually implemented.

T

⁂

⁂

5)	Design flow chart

# Text boxes

I Q1

Q0

X     0     X    X

1      0      0     1

I Q1

Q0

X     1      0    X

0      1      1     0

00     01      11      10

0

1

I Q1

Q0

X     1      1    X

X     0      X    0

00     01      11      10

0

1

I Q1

Q0

X     0      0    X

0      1      0     1

00     01      11      10

0

1

__

T1 = Q0 + I

__    _             __       __     __    _

T0 = Q0 + I Q1 + I Q1 = (Q0 + Q1 + I ) ( I + Q1 )

00     01      11      10

0

1

00     01      11      10

0

1

X     1      1    X

0      1      0     1

I Q1

Q0

00     01      11      10

0

1

X     1      0    X

1      1      1     1

I Q1

Q0

00     01      11      10

0

1

X     1      1    X

1      0      1     0

00     01      11      10

0

1

X     0      1    X

1      0      0     1

I Q1

Q0

I  Q1 Q0   Q1+  Q0+   T1 T0    S1 R1 S0 R0   J1 K1 J0 K0

0   0   0      X    X      X   X      X  X   X   X    X  X  X  X

0   0   1       1     1       1    0       1   0    1   0     1  X  X   0

0   1   0       0     1       1    1       0   1    1   0    X   1   1  X

0   1   1       0     0       1    1       0   1    0   1    X   1  X   1

1   0   0      X    X      X   X      X  X   X   X    X  X  X  X

1   0   1       1     0       1    1       1   0    0   1     1  X  X   1

1   1   0       1     1       0    1      X   0    1   0    X   0   1  X

1   1   1       0     1       1    0       0   1    1   0    X   1  X   0

0

0

0

1

1

1

3

2

1

I Q1

Q0

__

S0 = Q0

__     __

R0 = I Q1 +  I  Q1 Q0

00     01      11      10

0

1

X     0      0    X

0      1      0     1

I Q1

Q0

00     01      11      10

0

1

X     1      1    X

X     0      X    0

I Q1

Q0

00     01      11      10

0

1

X     1      0    X

0      1      1     0

I Q1

Q0

00     01      11      10

0

1

X     0     X    X

1      0      0     1

I Q1

Q0

J0 = 1

__     __

K0 = I Q1 +  I  Q1

_

I

Q1

Q1

Q0

_

I

Q1

Q0

R1

R1

Q  Q+      D(Q+)    T	S R	J K

0   0        0     	0	0 X	0 X

0   1        1     	1	1 0	1 X

1   0        0     	1	0 1	X 1

1   1        1     	0	X 0	X 0

W

X

Y

Z

D	QD

C	QC

B	QB

A	QA

LD

CLR

Q0    1

0

Q1    1

0

W     1

0

X      1

0

R1a)  1

0

Y      1

0

Z       1

0

R1b) 1

0

# X

Note: Synchronous LOAD (LD)

and CLEAR (CLR)

# =X?

D	QD

C	QC

B	QB

A	QA

LD

CLR

# X

# =Y?

D	QD

C	QC

B	QB

A	QA

LD

CLR

A:  1 ( 0

Output glitches to 0

1

A

1

B:  0 ( 1

Output glitches to 1

0

B

0

A

C

__

C

D

00     01      11      10

00

01

11

10

1      1      1     1

AB

CD

1    1

1     1

0      0      0     0

0      0

0     0

AB

CD

_

A

D

__

C

A

00     01      11      10

00

01

11

10

1      1      1     1

1

1     1

AB

CD

I  Q1 Q0   Q1+  Q0+   T1 T0    Q1+ Q0+

0   0   0       1     1       1    1       1   1

0   0   1       1     1       1    0       1   1

0   1   0       0     1       1    1       0   1

0   1   1       0     0       1    1       0   0

1   0   0       1     1       0    1       0   1

1   0   1       1     0       1    1       1   0

1   1   0       1     1       0    1       1   1

1   1   1       0     1       1    0       0   1

00     01      11      10

00

01

11

10

0

0

0

1

1

1

3

2

1

0

0,1

Problem stated

State transition diagram (Graph ?)

Implement logic

K-map

Excitation table

Truth table

Check “don’t cares” (sometimes)

Choose flip-flops