CS150

Week 9, lecture 1

Covers:

- Multiplication

- Shifters

- Floating point numbers

- Multiplication

How do you multiply a number?

a3 a2 a1 a0

b3 b2 b1 b0

b0 (a3 a2 a1 a0)

b1 (a3 a2 a1 a0)

b2 (a3 a2 a1 a0)

b2 (a3 a2 a1 a0)

Binary multiplication is the same.

Note: The bn in bn (a3 a2 a1 a0) is just bn ( which equals 1 or 0) ANDed with a3 a2 a1 a0.

a3 a2 a1 a0 is a 4-bit number. (For example: 1011 ( a3 = 1, a2 = 0, a1 = 1, and a0 = 1).

b2   b2		b1 (a3 a2 a1 a0)   b0 (a3 a2 a1 a0)

?

Sequential Adder:

Pipelined:

Sequential multiplier:

Worst case N/2 odds:	a3 a2 a1 a0 = 0111

7 (a3 a2 a1 a0) = 8 (a3 a2 a1 a0) - (a3 a2 a1 a0)

2)	Shifters

Multiple bit shifts – a lot of hardware!

(Barrel shifter)

Shifting just one bit is more efficient:

Shifters:

3)	Floating point

Sign, significand (N), exponent (K+1):	( n2K+1-N

1-2K < K < 2 K,	-2 N < ( n < 2 N

|  | Bytes | K+1 | N | MIN? | Min (Norm) | Max | 2-N |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Single | 4 | 8 | 24 | 1.4x10-45 | 1.2x10-38 | 3.4x1038 | 6x10-8 |
| Double | 8 | 11 | 53 | 5x10-324 | 2x10-308 | 2x10308 | 10-16 |
| Quad | 16 |  |  |  | E-4932 | E4932 |  |

Normalization: minimize exponent

2	2x20, 	2x21, 	½ x22, 	¼ x23

10,0	1,1	0.1,2	0.01,3

5.75	101.11x20,	1.0111x23,	0.10111x23

Write	2K+1-N n = ( 2K(1+f)	0<f<1

Don’t need to store this.

Problems:						     __

How do you represent ( and NaN (Not a number: 0/1,  (-1   )?

S?? normals:

K(most negative), f=0	2Kmin(1+0)	Min normalized number

Next smallest normal:	2Kmin(1+0.000…001)

- 1111

0	2Kmin

2Kmin(1.000…001)

2-N

Would like S?? normals.

Encodings of ( 2K+1-N n

|  | Sign | Exponent | Nth bit | Significand |
| --- | --- | --- | --- | --- |
| NaN | ? | 11…11 | 1 | 1xxxx |
| Infinity | ( | 11…11 | 1 | 0 |
| Normals | ( |  | 1 |  |
| Subnormals | ( | 0 | 0 | N < 2 N-1 |
| Zero | ( | 0 | 0 | 0 |

(	K+1		N

S             e                      f

K = e + 1 - 2 K	Reserved:	     0, 111…111

Min    1 – 2 K    0000…001+	(Sorry. Looks like the page got cut off)

Max    111…110 + 1 – 2 K  =  0111…111 = 2 K-???

K + 1

( 2 K + 1 – N

OR

( 2 K( 1 + f ) N		K = 0 ( e = 0111…110

# Text boxes

4

4

4

Full adders

b3

b2

b1

Register

Register

b0

ACC

FSM

Full adders

a3 a2 a1 a0

B

Cin

Cout

S

Q    D

Full

Adder

B

S8

S7-4

S3-0

A

2

3

5

5

5

+

+

5

D  Q

_

L/R

SH

EN

D  Q

_

L/R

SH

LD

SH_L

LD

SH_R

CLR

LD

ACC

ALU

5

Qn+3

Qn+2

Qn+1

Qn

Qn-1

A

+

1

2

4

8

16

32

64

ACC

CLR

LD

SHIFTER

Qi

i(