10/5 & 10/7

CS150

Section week 6

Timing and your Xilinx chip

( Synchronization, Chart lookups, timing estimates, Tristate with level sensitive latch. )

1.	So what’s all this timing stuff have to do with your Xilinx chip?

What are some problems you can have when you use a circuit that you’ve downloaded to your Xilinx chip?

- Transmission lines

The theory behind transmission lines is that long wires are not ideal; they actually create a complex system of resistance, capacitance and inductance and we call a long wire that has these traits a transmission line. Unlike signals travelling through very short wires ( for which we don’t need to consider propogation time ), signals on transmission lines take a finite time period to travel from one end to the other. The duration is fundamentally limited by the speed of light through the medium which, in the case of wires, is generally given as about ____________ which means a signal travels _______ meters in a ns.

Rs = Source resistance

Zo = Characteristic impedance

RL = Load resistance

How long would it take for a signal to propogate through this transmission line?

The standard equation for the calculating reflection coefficient is ( =

Travelling from left to right on this line, ( =

( Reflection from load )

Travelling from right to left on this line, ( =

( Reflection from source )

Draw the voltage values at time 2.5ns, 7.5ns, 12.5ns when:

RL = 2 Ohm

RS = 18 Ohms

Zo = 6 Ohms

V0 = 0V

Vwave = +10V

- Asynchronous inputs

Example: Given this FSM, fill in the STT and STD. Assume

That tsetup for both flip-flops is 5 ns and TXNOR is 10ns.

J0 =  ____________          K0  =  ___________

J1 = ____________           K1 =  ____________

#### Q1	Q0	IN	J1K1	J0K0	Q1+	Q0+

0	0	0

0	0	1

0	1	0

0	1	1

1	0	0

1	0	1

1	1	0

1	1	1

What happens if IN is an asynchronous input? That is, it can change at any time, not just after rising clock edges. Fill in the following diagram.

We would expect a transition

from state 01 to state _____,

instead we get a transition from

state 01 to state _______.

If the period was T=50ns, what

would the probability of a setup

time violation such as this to

occur?

What’s a simple fix for most asynchronous inputs?

Moral:

- Timing through a CLB

Page 4-97 & 4-98 in the Xilinx manual gives you important information about some of the chip’s internal delays.

Example: What is the TCKO for one of the CLB flip-flops in our Xilinx chip?

Look at rows for “Sequential Delays”, find “Clock K to output” then look in column for “-4” ( the speed grade ).

For our logic that we’ll use in this class, we’ll look for input into the F/G inputs and outputs to the X/Y outputs.

- Routing delays

How do you figure out what the delay through the lines are?

6. 	Delays due to capacitive loading on outputs

Page 13-16 to page 13-18.

# Text boxes

IN

J1        Q1

K1

CLR

R – Zo

R + Zo

RL

L=1m

9ns

2.5ns

7.5ns

12.5ns

-5V

Rs

5V

0V

10V

-5V

Q0

Q1

IN

CLK

5V

0V

10V

-5V

5V

FJKC

RESET

CLK

0V

10V

J0        Q0

K0

CLR

FJKC

Zo

V