9/28 & 9/30

CS150

Section week 5

- 3 Bit Up Counter ( Moore FSM Design, Setup/Hold Time, Logic Simplification )

1a)  Build a 3 bit up counter Moore machine using only AND, OR, NOT, and XOR gates. Simplify all logic. ( In other words use the fewest number of gates possible. )

1b)  Will this circuit have any problems if:

2ns < TpINV < 4ns

3ns < TpAND < 6ns

3ns < TpOR < 5ns

3ns < TpXOR < 4ns

3ns < Tcko < 8ns

Tsetup = 4ns

Thold = 6ns

CLK = 40 MHz

- Clock divider (FSM Design, Counters, Clocks and Glitches )

Design a clock divider which runs on a 200MHz clock and produces a 1MHz clock. Make the duty cycle of the 1MHz clock 50%. Should you design this to be a Moore or a Mealy machine?

- FSM Analysis

What does this circuit do? ( Is it a Mealy or Moore? Where are the NSD, OD & State FFs. )

- STD & STT

Draw a Moore STD for a circuit that does the same thing as the circuit in problem 3 and then make it’s STT.

- Gate Delay Timing Diagram ( Cross Coupled Gates, Gate Delays )

It’s too much to try create a problem like the one on last year’s MT. Try to do last year’s ( and if you can get it, the year before’s timing problem might be good practice ).

- Toggle Flip Flops ( FSM Design )

Design a 2 Bit Down Counter that is implemented with T FFs.

- JK Flip Flops ( FSM Design )

Design a 2 Bit Down Counter that is implemented with JK FFs.

- What’s the fastest way to fill in a table for:  F = ABC + ABD + ABC + ABD   ?

- If you want more... ( FSM Design, again )

Use counters from HW4 and output logic only to build same counter. ( And you’ll need to produce one control signal someplace ).

Solutions:

- a) STT:

b) Equations:

NS0 = PS0

NS1 = PS1      PS0

NS2 = PS2 PS0 + PS2 PS1 + PS2 PS1 PS0

c) Any problems?

Check for hold time violations ( Can value from flip flop output propogate back to the flip flop input so quickly that the hold time is violated? ):

>  Find the shortest propogation path: Looks like NS0 ( XOR gates have bigger delay

than inverters ).

Tckpmin + Tinvmin > Thold

3ns        + 2ns        > 6ns		This isn’t true ( hold time violation possible.

Check for setup time violations ( Can value from flip flop output propogate back to the flip flop input so slowly that the next clock’s setup time is violated? )

>  Find the longest propogation path: Looks like NS2.

Tckomax + Tinvmax + Tandmax + Tormax + Tsetup < Period ( 1/40MHz = 25ns )

8ns         +  4ns       + 6ns         +  5ns     + 4ns      < 25ns     False ( setup time

violation possible.

- This should be a Moore machine with two states and no logic on the output – the output should come directly from the state bits. Because... any combinational logic, no matter how simple may cause glitches. It should change states when a counter counts up to 100. Since the output of this circuit is a clock, we have to make especially sure that there aren’t glitches on the output. Moore is safer than a Maely in this case. Why?

- It’s a Mealy pattern detector ( 1011 ).

Equations:

NS1 = R ( PS0 Z + PS1 PS0 Z )

NS0 = Z R

OUT = Z PS1 PS0

STT:

STD:

- The Moore STD has 5 states. 1 is output in the 5th state.

On the STT, make sure that the output is the same for the same PS even though the input changes.

- ------

- STT:						Equations found for T1 and T0:

7.	STT:						Equations:

J1 = PS0

K1 = PS0

J0 = PS0

K0 = PS0

X means “don’t care”.

# Text boxes

Bookkeeping

PS1	PS0	J1K1	J0K0	NS1	NS0

0	0	0X	1X	0	1

0	1	1X	X1	1	0

1	0	X0	1X	1	1

1	1	X1	X1	0	0

OUT1

OUT0

1

T1        Q1

T0       Q0

Bookkeeping

PS1	PS0	T1	T0	NS1	NS0

0	0	0	1	0	1

0	1	1	1	1	0

1	0	0	1	1	1

1	1	1	1	0	0

00	           01	       10	                 11

0/0		1/0			     0/0

0/0		1/1

RESET	          1/0	        0/0	                 1/0

RESET	PS1	PS0	Z	NS1	NS0	OUT

0	0	0	0	0	0	0

0	0	0	1	0	1	0

0	0	1	0	1	0	0

0	0	1	1	0	1	0

0	1	0	0	0	0	0

0	1	0	1	1	1	0

0	1	1	0	1	0	0

0	1	1	1	0	1	1

1	0	0	0	0	0	0

1	0	0	1	0	0	0

1	0	1	0	0	0	0

1	0	1	1	0	0	0

1	1	0	0	0	0	0

1	1	0	1	0	0	0

1	1	1	0	0	0	0

1	1	1	1	0	0	1

S0

S1

?

?

?

?

PS2 	PS1 	PS0  	NS2 	NS1 	NS0

0	0	0	0	0	1

0	0	1	0	1	0

0	1	0	0	1	1

0	1	1	1	0	0

1	0	0	1	0	1

1	0	1	1	1	0

1	1	0	1	1	1

1	1	1	0	0	0

Z

RESET

OUT