CS150

Week 1, lecture 1

Covers:

- What’s a digital system?

- Logic gate introduction: An inverter

- Logic gate introduction: An AND gate

- What’s covered in cs150

- Sequential vs. combinatorial logic

- Logic gates

- What’s a digital system?

Digital systems use two discrete values or levels to represent information: { 0, 1 }

In other words, information is represented in binary form.

Boolean algebra is the basis for digital logic. Input to a system is either 0 or 1 and the results will also be either a 0 or a 1.

- Logic gate introduction: An inverter

Logic symbol for an inverter:

Input to a logic gate is one of two values: { 0, 1 }

For an inverter, output, F,  is 1 if input, X,  is 0.

For an inverter, output, F,  is 0 if input, X,  is 1.

A convenient and easy-to-understand form to express the rules for the output of a logic gate is the truth table. For the inverter it would look like:

X     F(X)

- 1

- 0

When writing this as an equation:

F(X) = NOT X = X

Implementation of an inverter (low level):

X ( [ 0, 5 ] Volts

F(X) ( [ 0, 5 ] Volts

3)	Logic gate introduction: An AND gate

Logic symbol for an AND gate:

F is true IFF ( A is true ) AND ( B is true )

The truth table for an AND gate would look like:

A  B     F(X)

0  0      0

0  1      0

1  0      0

1  1      1

When writing this as an equation:

F(X) = AB

4)	What’s covered in cs150

Speakers

Displays

Keyboards

Mouse

Sensors

Etc……

Teach you:

Glue logic

Single microprocessors

Transistors to microprocessors in one semester.

5)	Sequential vs. conbinatorial logic

Combinatorial logic: Takes one or more inputs and produces one or more outputs as a function of those inputs.

Mathematically speaking: OUTPUT = F(A, B, C, …)

No feedback, no memory. Output will always be the same for same input.

Sequential network: Some outputs are fed back as inputs.

Mathematically speaking: OUTPUT = F(A, B, C, F(X, Y, Z…), …)

Examples:

Combinatorial network		Sequential network

Adders				Clocks

AND gates			people

Inverters				most interesting things…

Note: Ideally, output changes instantaneously with input…

Types of sequential circuits:

- Synchronous

All feedback happens at the same time ( the state of the circuit changes at the same time). For example, on command of a special input called the clock.

- Asynchronous

State may change when any input changes. Asynchronous designs are dangerous but can be beautiful.

Synchronous example:

Asynchronous example:

6)	Logic gates

You’ve already seen the inverter and the AND gates:

Here are three more kinds of gates:

OR:					NAND:					NOR

Logic symbol:

The truth table for an OR gate:	          The truth table for an NAND gate:	 The truth table for an NOR gate:

A  B     F(X)			A   B   F(X)				A   B   F(X)

0  0      0			0    0    1					0    0     1

0  1      1			0    1    1					0    1     0

1  0      1			1    0    1					1    0     0

1  1      1  			1    1    0  				1    1     0

When writing this as an equation:           When writing this as an equation:         When writing this as an

equation:

F(X) = A + B			F(X) = AB				F(X) = A+B

# Text boxes

{ 0, 1 }

{ 0, 1 }

Output: F

Input: X

X

__

X

Vdd

Switch open when X == 1.

(Connection between Vdd and X cut).

Switch closed when X == 0.

(Connection created between Vdd and X).

Switch closed when X == 1.

(Connection created between GND and X).

Switch open when X == 0.

(Connection between GND and X cut).

Vdd

X

F(X)

F(X)

Input: A

Input: B

Output: F

Glue logic

(-processor

=

Digital camera

CDs

( wave  ovens

PDAs – palm pilot…

F

F

A ring oscillator (don’t you’ll find out about these a little later on). And an asynchronous circuit…

Combinational Block

A buffer that holds on to the previous value until clock comes…

Output: F

Input: A

Input: B

Input: X

Output: F

Input: A

Input: B

Output: F

Input: A

Input: B

Output: F

Input: A

Input: B

Output: F