11/8 & 11/10

CS150

Section week 11

This week: Karnaugh maps (HW 9, Q4), µ-programming (HW 9, Q3)

- K-maps

Making K-maps.

Terms:

Minterm: SOP (Sum Of Products). Equation you get when you circle 1s in a K-Map.

Implicant: Anything you can circle in a K-Map. Can be single 1. Can be the biggest group, too.

Prime implicant: The biggest circle drawable around an implicant.

Essential implicant: A prime implicant that has at least one implicant that isn’t contained in another circle.

Maxterm…: POS (Product Of Sums). Equation you get when you circle 0s in a K-Map.

Simplify:           _  _  _     _ _               _         _ _        _

OUT = XYZ + XYZ + XYZ + XYZ + XYZ ( ________________________

using K-maps.

_

- Glitches and K-maps:		K-map simplified equation:  OUT = B C + A C

Equation drawn in gates:

Can a glitch occur on the 110 ( 111 transition? Yes.

Timing: (A=B=1 and delays are gate delays)

C

A’

C’

OUT

How can you fix it using a K-map? Add a circle which contains the transition path.

- Microprogramming

Microprogram the control unit below to implement a rising edge detector. Emulate a Moore type FSM. The clock to the control unit is twice the clock of IN ( IN clock and the controller clock are synchronized. )

Some questions before we start:

Where is the (-program located? In the ROM

Can this be reused for different (-programs? It’s in a ROM. It can’t be re-written. In other words, the micro-controller will run a fixed program and can’t be re-programmed ( easily anyways… ).

What are the instructions for this microcode control unit?

Instruction			Bit:   7   6   5   4   3   2   1   0

DO  OUTPUT  OUT		         0  X  X  X  X  X  X  OUT

LOAD(IN) Address		         1   0  X  X  X    Address

LOAD(IN) Address		         1   1  X  X  X    Address

Remember the decode stage in the STD for the computer datapath we did in class. It branches 5 ways. How many directions can this controller branch on one instruction?   Only 2

What would it need to do if it had to go to multiple destinations on one instruction?

Can’t. You have to use multiple (-instructions to take care of multiple branches.

Write the microcode:

STD

| Address | Mnemonic form | O7 | O6 | O[5:0] |
| --- | --- | --- | --- | --- |
| 0 | DO OUTPUT 0 | 0 | X | XXXXX0 |
| 1 | JMP(IN) 0 | 1 | 1 | XXX000 |
| 2 | DO OUTPUT 1 | 0 | X | XXXXX1 |
| 3 | JMP(IN) 0 | 1 | 1 | XXX000 |
| 4 | DO OUTPUT 0 | 0 | X | XXXXX0 |
| 5 | JMP(IN) 0 | 1 | 1 | XXX000 |
| 6 | DO OUTPUT 0 | 0 | X | XXXXX0 |
| 7 | JMP(IN) 6 | 1 | 0 | XXX110 |

Possible problems with this program:

OUT will be asserted after one

(-controller clock cycle. Maybe not

a problem but something to notice.

The problems that I presented it with

in section are all solved by adding a

forth state. I don’t see any problems

with the 4 state based program.

# Text boxes

CLK

CLK

Micro

Program

counter

C

OUT

State 00

State 00      State 11

State 01

State 11     State 00

0       1

0       1

1

1

11

“1”

[0]

10

“11”

[0]

0

0

1

State 00

State 01

State 10

State 11

0

1

0

00

“0”

[0]

01

“01”

[1]

RESET

BRNtaken   BRNnot taken

STORE

LOAD

ADD

0

1

Output Register

CE

O0                  D0     Q0               OUT

A’

C’

Step 3: Equation

__          __

OUT = Y + X Z

Step 2: K-Map

XYZ 	OUT

000	1

001	1

010	0

011	0

100	1

101	1

110	1

111	0

Step 1:

Truth table

XY

Z       00       01        11        10

0        1           0         1          1

1        1           0         0          1

RESET

A

1    0    0   1    1    0    0   1

0    0    1   1    0    0    1   1

1    1    1   1    1    1    1   1

1    1    0   1    1    1    0   1

1    0    0   1    1    0    0   1

0    0    1   1    0    0    1   1

1    1    1   1    1    1    1   1

1    1    0   1    1    1    0   1

ABCD	OUT

0000	1

0001	0

0010	1

0011	1

0100	0

0101	0

0110	1

0111	1

1000	1

1001	1

1010	1

1011	1

1100	0

1101	1

1110	0

1111	1

AB

CD

8x8 ROM

A2      O7

A1

O[6:0]

A0

LOAD

O2            D2      Q2

O1            D1      Q1

O0            D0      Q0

O6

00

01

11

10

00

01

11

10

00	01	11	10          00          01          11           10

IN

__

IN

EN

State 00

State 00      State 10

B

AB

C       00       01        11        10

0        0           1         1          0

1        0           0         1          1

0       1

1       0

Branch diagram:

Left child is branch. Right child is natural path when counter counts up without branch.