9/7 & 9/8

Solutions are boxed…						CS150

Section week 2

- Cross coupled NOR gates

Equations:

Q'+ =    S + Q

Q+  =   R + Q’

- Generic steps for designing an FSM

- Backwards FSM design example: Meaningless random circuit

Circuit description:

Given an FSM consisting of two D flip-flops and an input X, generate the corresponding STT & STD. The next state equations are:

___            __                  ___

NS1 = X PS1 PS0 + X PS1 + PS1 PS0

__

NS0 = X

STT							STD

## PS1	PS0	X	NS1	NS0

0	0	0

0	0	1

0	1	0

0	1	1

1	0	0

1	0	1

1	1	0

1	1	1

- FSMs ( Finite State Machines )

Moore machine				      Mealy machine

Diagram:

See class notes…				  See class notes…

Outputs depend on:

Outputs change:

FSM Example: A rising edge detector

1) Design a finite state machine which takes a bitstream as input, outputting a single high pulse when the input changes from low to high.

Mealy						Moore

2)							2)

3) 							3)

4) Mealy						4) Moore

5) 							5)

Mealy						Moore

5)							5)

6)							6)

# Text boxes

CLK

IN

RE

CLK

IN

RE

Outputs depend on: Only present state

Outputs depend: On input and present state

IN

CLK

RE

Same as Mealy

State	    IN0       IN0        IN1       IN1       IN0       IN1       IN0

State   IN0       IN0    IN0->1    IN1       IN0     IN0->1      IN0       IN0

IN0

0

IN1

1

IN / RE

___

IN / RE

__   __

IN / RE

__   __

IN / RE

Internal state name

IN0

00

0

IN0->1

01

1

IN1

10

0

Illegal

11

0

Output

IN

IN

__

IN + IN

__

IN

IN

__

IN

__

IN

PS	IN	OUT	NS

0 (IN0)	0	0	0 (IN0)

0 (IN0)	1	1	1 (IN1)

1 (IN1)	0	0	0 (IN0)

1 (IN1)	1	0	1 (IN1)

PS		  	 	        NS

PS1	PS0	IN	OUT	NS1	NS0

0	0	0	0	0	0

0	0	1	0	0	1

0	1	0	1	0	0

0	1	1	1	1	0

1	0	0	0	0	0

1	0	1	0	1	0

1	1	0	0	0	0

1	1	1	0	0	0

NSD:

NS = IN

OD:        __

OUT = PS IN

NSD:

NS1 = PS1 PS0 IN + PS1 PS0 IN

NS0 = PS1 PS0 IN

OD:

OUT = PS1 PS0

Q'

Q

R

# S

1

0

1

0

1

0

1

0

Unit Time:      0	          1            2             3            4            5             6             7            8            9            10           11          12

# S

R

Q'

Q

- Understand problem

- Identify inputs and outputs

- Timing diagrams – to help understand problem

- Decide FSM type, Mealy or Moore

- State Transition Diagram – STD

- State Transition Table – STT

- Equations from table

- Draw Circuit

X

_

X

_

X

X

X

0	1

0	0

0	1

1	0

1	1

1	0

1	1

0	0

_

X

X

_

X

Outputs change: On the clock or when inputs change

Outputs change: Only on the clock