10/4 & 10/6

CS150

Section week 6

Timing.

1.	So what’s all this timing stuff have to do with your Xilinx chip?

What are some problems you can have when you use a circuit that you’ve downloaded to your Xilinx chip?

- Asynchronous inputs

Example: Given this FSM, fill in the STT and STD. Assume

That tsetup for both flip-flops is 5 ns and TXNOR (propogation time

Through the XNOR gate ) is 10ns.

J0 =  __IN(Q1_____          K0  =  ___J0______

J1 = ____Q0______           K1 =  ____IN______

#### Q1	Q0	IN	J1K1	J0K0	Q1+	Q0+

0	0	0

0	0	1

0	1	0

0	1	1

1	0	0

1	0	1

1	1	0

1	1	1

What happens if IN is an asynchronous input? That is, it can change at any time, not just after rising clock edges. Fill in the following diagram.

We would expect a transition

from state 01 to state _11__,

instead we get a transition from

state 01 to state __10___.

If the period was T=50ns, what

would the probability of a setup

time violation such as this to

occur?

What’s a simple fix for most asynchronous inputs?

Moral:

# Text boxes

IN

J1        Q1

K1

CLR

If IN changes any time between 5ns before the clock and the clock there will be a setup time violation on FF1. If IN changes changes between 15ns before the clock and 10ns before the clock, there will be a setup time violation on FF0. For a total of 10ns where a change in IN can cause a SU violation. So the probability of a SU violation is: 10ns/50ns=20%

Simple fix: Put flip-flops on asynchronous inputs.

Moral: Don’t use asynchronous inputs.

00	11	0	1

01	00	0	0

10	11	1	0

11	00	1	1

00	00	1	0

01	11	0	1

10	00	1	1

11	11	0	0

- Asynchronous inputs

- Delays

- Delays through CLBs ( Tcko for flip-flops, Tp for LUTs ( Look Up Tables )).

- Delays through wires & switches

wire ( propagation delay

switch ( introduces capacitance

fanout ( multiplies capacitance

- IOB ( Same type of delays as CLB )

- Driving outputs ( As in HW #6 )

Answers in red

9ns

Q0

Q1

IN

CLK

FJKC

RESET

CLK

J0        Q0

K0

CLR

FJKC