# University of California at Berkeley

## College of Engineering

Department of Electrical Engineering and Computer Sciences

### EECS150								J. Wawrzynek

# Spring 2000								E. Caspi

#### Homework #1 – Solution

- Recall, in a performance-cost tradeoff, we typically seek to maximize performance and/or minimize cost.

- Region I:	The system is optimized for low cost.  The high slope indicates that reducing cost incrementally further requires a big loss in performance

- Region II:	The system is balanced.  Cost and performance trade off well.

- Region III:	The system is optimized for high performance.  The low slope indicates that increasing performance incrementally further requires a large additional cost.

- Describe an object hierarchically.  This is fairly open ended.  Be creative.

- There are 12 3-bit gray codes.

Recall that an n-bit gray-code is a cyclic sequencing of all n-bit numbers such that successive numbers differ by exactly one bit. You should be able to list and count all such sequences for n=3.

There is a nice geometric interpretation for gray codes.  For a given bit width n, the set of all n-bit numbers corresponds to the corners of an n-dimensional hypercube (e.g. 2-bit numbers are the corners of a 2D square; 3-bit numbers are the corners of a 3D cube).  Each axis of the cube represents one bit, with coordinates valued 0 or 1.









An n-bit gray code is a cyclic sequence of all n-bit numbers such that successive numbers differ in exactly 1 bit.  Geometrically, such a sequence is a path along the legs of the hypercube, visiting every corner, and ultimately returning to the starting point (such a path is called a “Hamilton cycle”).  The number of unique n-bit gray codes is the number of unique paths around an n-bit hypercube.  Keep in mind that rotations, mirror images, and direction reversal may transform a path into a multitude of unique paths.

There are twelve (12) unique paths which cover the 3D cube.  The basic topology is the same for all paths.  The twelve-fold multiplicity arises from rotating about the 000-111 axis (3x), mirroring about the vertical 000-101 plane (2x), and reversing the path direction (2x).

- 125 decimal is “1111101” in binary, or padded to 8 bits: “01111101”.
25 decimal is “11001” in binary, or padded to 8 bits:  “00011001”.
In all examples, we assume that a wire carries a value “1” when not in use.

- The “bit-parallel” waveform transmits
one bit on each of 8 wires.

- The “bit-serial” waveform transmits each bit in sequence on 1 wire, LSB first, MSB last, in 1 second intervals.

- With parity and start/stop bits, each byte transmission look like:
{start (0), LSB … MSB, parity, stop (0)}.

- Convert the following numbers from base ten to two’s complement, one’s complement and sign magnitude (use 16 bits for each number). -1011, -32752, 1500

- Decimal -1011

- Positive decimal 1011 = binary “1111110011”

- To negate into one’s complement, pad with a “0” sign bit, then invert all bits:  binary “10000001100”.

- Two’s complement = one’s complement +1:  binary “10000001101”.

- Sign magnitude = sign bit adjoined to positive value:  binary “11111110011”.

- Decimal –32752

- Positive decimal 32752 = binary “111111111101111”

- To negate into one’s complement, pad with a “0” sign bit, then invert all bits:  binary “1000000000010000”.

- Two’s complement = one’s complement +1:  binary “1000000000010001”.

- Sign magnitude = sign bit adjoined to positive value:  binary “1111111111101111”.

- Decimal 1500

- Positive decimal 1500 = binary “100011001010”.

- For one’s complement representation of a positive number, simply pad with a “0” sign bit:  binary “0100011001010”.

- For two’s complement representation of a positive number, do same:
binary “0100011001010”.

- For sign-magnitude representation of a positive number, do same:
binary “0100011001010”.

# Text boxes

II

I

performance

cost

III

00

10

11

01

000

010

011

001

101

100

110

111

2-bit numbers

3-bit numbers

011

111

Bit-serial transmission of 125

25

125

1

0

Bit-parallel transmission of 125

0

1

1

1

1

1

0

1

LSB

MSB

110

100

101

001

010

000

1

0

start

par stop start

par stop

time

time