# University of California at Berkeley

## College of Engineering

Department of Electrical Engineering and Computer Sciences

### EECS150								J. Wawrzynek

# Spring 2000								E. Caspi

Quiz #9 – Solution

- The 1-bit subtractor computes:  d = x – y – bin, passing a borrow bout to the right.  The truth table for d and bout follows:

| x | y | bin | d | bout |
| --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | 0 |
| 0 | 0 | 1 | 1 | 1 |
| 0 | 1 | 0 | 1 | 1 |
| 0 | 1 | 1 | 0 | 1 |
| 1 | 0 | 0 | 1 | 0 |
| 1 | 0 | 1 | 0 | 0 |
| 1 | 1 | 0 | 0 | 0 |
| 1 | 1 | 1 | 1 | 1 |

The difference output d is identical to the sum output of a full adder.  It is expressed most simply using XORs:  d = x ( y ( bin.

The borrow output bout is not so familiar.  We derive its reduced expression using a Karnaugh map:  bout = x’bin + x’y + ybin.

| bin x y | 0 | 1 |
| --- | --- | --- |
| 00 | 0 | 1 |
| 01 | 1 | 1 |
| 11 | 0 | 1 |
| 10 | 0 | 0 |

- A ripple subtractor can be formed by cascading several 1-bit subtractors with a borrow-chain.  This construction is similar to a ripple adder with a carry-chain.

# Text boxes

x3

d3

Sub

y2

bout

y3

bin

bin

d2

x2

bout

Sub

y1

bin

d1

x1

bout

Sub

y0

bin

d0

x0

bout

Sub

bout

bin