# Here is the solution to homework #2 part 2

#4

A	     B            C	          D	 X               Y             Z

| 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| --- | --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 1 | 0 | 0 | 1 |
| 0 | 0 | 1 | 0 | 0 | 0 | 1 |
| 0 | 1 | 0 | 0 | 0 | 0 | 1 |
| 1 | 0 | 0 | 0 | 0 | 0 | 1 |
| 0 | 0 | 1 | 1 | 0 | 1 | 0 |
| 0 | 1 | 1 | 0 | 0 | 1 | 0 |
| 1 | 1 | 0 | 0 | 0 | 1 | 0 |
| 0 | 1 | 1 | 1 | 0 | 1 | 1 |
| 1 | 1 | 1 | 0 | 0 | 1 | 1 |
| 1 | 1 | 1 | 1 | 1 | 0 | 0 |

X = ABCD

Y:

AB

00	     01	      11	          10

| 00 | 0 | 0 | 0 | 0 |
| --- | --- | --- | --- | --- |
| 01 | 0 | 1 | 1 | 1 |
| 11 | 1 | 1 | 1 | 1 |
| 10 | 0 | 1 | 1 | 1 |

Z:

00	    01	      11	          10

| 00 | 0 | 1 | 0 | 1 |
| --- | --- | --- | --- | --- |
| 01 | 1 | 1 | 1 | 1 |
| 11 | 0 | 1 | 0 | 1 |
| 10 | 1 | 0 | 1 | 1 |

Y = CD + BD + AD + AC

_	        _ 	   ___  _     _   	_     _                _

Z = CD + AB + ABCD + ABC + ABD + ACD

Product of sum form:

X = ABCD	                     _             _              _             _                   _   _   _   _

Y = (A+B+C+D)(A+B+C+D)(A+B+C+D)(A+B+C+D)(A+B+C+D)(A+B+C+D)

_   _                   _   _        _   _              _   _   _  _

Z = (A+B+C+D)(A+B+C+D)(A+B+C+D)(A+B+C+D)(A+B+C+D)

# 5

a1                  a0                 b1                  b0	      s2	 	   s1		s0

| 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 0 | 0 | 0 | 0 | 1 |
| 0 | 1 | 0 | 1 | 0 | 1 | 0 |
| 1 | 0 | 0 | 0 | 0 | 1 | 0 |
| 1 | 0 | 0 | 1 | 0 | 1 | 1 |
| 1 | 0 | 1 | 0 | 1 | 0 | 0 |
| 1 | 1 | 0 | 0 | 0 | 1 | 1 |
| 1 | 1 | 0 | 1 | 1 | 0 | 0 |
| 1 | 1 | 1 | 1 | 1 | 1 | 0 |
| 1 | 1 | 1 | 0 | 1 | 0 | 1 |

S2 =

|  | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| 00 |  |  |  |  |
| 01 |  |  | 1 |  |
| 11 |  |  | 1 |  |
| 10 |  |  | 1 | 1 |

S1 =

|  | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| 00 |  |  |  | 1 |
| 01 |  | 1 |  | 1 |
| 11 | 1 |  | 1 |  |
| 10 |  |  |  |  |

S0 =

|  | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| 00 |  | 1 | 1 |  |
| 01 |  |  |  | 1 |
| 11 |  |  |  |  |
| 10 |  |  | 1 |  |

__

S2 = a1a0b0 + a1a0b1 + a1b1b0

__   __         ___

S1 = a1a0 + a1a0b1b0 + a1a0b1b0 + a1a0b1b0

____        ____                   __

S0 = a0b0b1 + a1a0b1b0 + a1a0b1b0

S0 = A0 xor B0

C1 = A0B0

S1 = A1 xor B1 xor C1

S2 = A1B1 + A1C1 + B1C1

I would say the above circuit is better because there are only two gate levels. But the adder circuit can be used to build adder circuit of more bits. I can’t imagine doing a K-map to construct a adder circuit of 64 bits using the method above.