1. This is the state diagram:

| C | B | A | C+ | B+ | A+ |
| --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | 0 | 1 |
| 1 | 1 | 1 | 0 | 0 | 1 |
| 0 | 0 | 1 | 0 | 1 | 0 |
| 0 | 1 | 1 | 1 | 0 | 0 |
| 1 | 0 | 0 | 1 | 0 | 1 |
| 1 | 0 | 1 | 1 | 1 | 0 |
| 1 | 1 | 0 | 0 | 0 | 1 |

_             __         _

C+ = CBA + CBA + CBA

B+ = CBA + CBA       __           _

A+ = CBA + CBA + CBA + CBA

4.

- Inputs: Externally, any of the drying options, such as cotton fabrics, permanent press fabrics, timed drying, etc. and their settings. Internally, information from temperature and humidity sensors, timer.

Output: Lights indicating which stage it is in, i.e. drying, cool down, stop

States: Different drying options, cool down and stop states.

Here is the state diagram: (only the state transition for cotton fabrics is given. The rest will be the same)

(Assume it’s a moore machine. Output of “drying” when drying is proceeding, whether it be cotton fabrics, press or timed drying.)

wet: input from the sensor. Assume that for different drying mode, the humidity requirement is different.