Problem #4

One of the many possible solutions:

- States: S0, S1, S2, S3 (stuck), S4

Inputs:

  - Reset

  - Left to the first correct number

  - Right past zero to the second correct number

  - Left to the third correct number

  - Close the lock

  - Right past zero a few times (t urn the dial right past zero a few times)

  - Else

Outputs:

  - Closed

  - Open

Assumptions:

At state S0, once the dial is turned to the left and the number entered matches the first number in memory, advance to S1.  At states S1 and S2, assume the user only dials to the right direction and stops at the correct number or he does, there are no intermediate stops. 	So the lock can only advance to the next state or it gets stuck at S3 until it is reset.

(b)

Problem #5

One of the many possible solutions, depending on the level of abstraction:

- In order to make the lock combination “programmable”, add two more input buttons. Input “program” is used to set the lock to program mode, and input “set” is used to save the number just entered into memory.

- Assumption:

For safety and security purpose, the lock combination can only be programmed when the lock is open and is set to program mode.  Once it is set to program mode, the old combo is cleared.  A number (0-39) can be saved to memory only when the set button is pressed regardless of the dialing direction.  After three numbers are saved and the lock is closed, the new combo is set.

# Text boxes

S0

S1

S2

S3

S4

Else / Closed

Else / Closed

Left to the first correct number / Closed

Reset

Else / Closed

Else  / Closed

Right past zero to the second correct number / Closed

Left to the third correct number / Open

Right past zero a few times / Closed

Close the lock / Closed

S4

S3

S2

S1

Close the lock / Closed

Right past zero a few times / Closed

Left to the third correct number / Open

Right past zero to the second correct number / Closed

Left to the first correct number / Closed

Reset

Else / Closed

Else  / Closed

Else / Closed

Else / Closed

S0

Program / Open

Enter a number (0-39) & set / Open

Enter a number (0-39) & set / Open

Enter a number (0-39) & set / Open

Close the lock / Closed

Else / Open

Else / Open

Else / Open

Else / Open

S5

S6

S7

S8