University of California at Berkeley

College of Engineering

Department of Electrical Engineering and Computer Science

EECS 150									R. H. Katz

Spring 2001

Homework Quiz # 4 (16 February)

## Name: __________________________________________      SID:________________

You are to design a simple combinational subsystem to the following specification. The system has the ability to pass its inputs directly to its outputs when a control input, S, is not asserted. It interchanges its inputs when the control input S is asserted. For example, given four inputs A, B, C, D and four outputs W, X, Y, Z, when S=0, WXYZ=ABCD and when S=1, WXYZ=BCDA.

Show how to implement this functionality using building blocks that are restricted to be 2:1 multiplexers and 2:1 demultiplexers. Draw your solution below, using black boxes for the mux/demux blocks.

# Text boxes

S

W

X

Y

Z

A

B

C

D