CS 150 Homework Quiz #5 Solution					Prepared by Wen Hui Guan

Solution:

Given an input D,

- output from D-latch changes as D changes regardless of the clock.

- output from clocked D-latch changes as D does only when the clock is high.

- output from D M/S FF are the samples taken from the input at the falling edge of the clock.

- output from positive edge FF changes relative to D at the rising edge of the clock.

- output form negative edge FF are the samples taken from the input at the falling edge of the clock (same as part 3).

Grading:

2 points-----miss at most one

1 points-----miss two or three

0 points-----miss 4 or more

# Text boxes

# Clk

# D

# D-latch

# Clocked

# D-latch

# D M/S

Flip-flop

# Positive

Edge FF

# Negative

Edge FF