# Datapath – Integration of Checkpoints

### Chkpt 1 – Controller Interface

The controller block acts as an independent subsystem.  It continually updates the button data so that it may be read by the FSM.

### Chkpt 2 – Audio Interface

The audio block is an independent module.  It receives requests from the FSM to play a certain sound.  The sounds are stored in the EPROM (erasable programmable ROM) as raw audio data, which can be directly sent out to the DAC (digital to analog converter).

The DAC will be directly connected (in hardware) to an amplifier, which in turn will be connected to the headphone jack.

### Chkpt 3 – Video Interface

The UART will be used to serially send out data to the RS232 line, which is driven by a MAXIM233 chip (hardware component).  This RS232 line will connect to the computer in order to use the monitor as a video display.  The video encoder interprets the current state of the game and translates it into data that can be read by the video decoder program running on the computer.

This checkpoint will also include the construction of the RAM game state component.  This will be needed to generate the data to test the video encoder and UART.

### The Rest

The controller interpreter is very closely tied with the FSM, so that is why it is done as an extension of the FSM and not part of checkpoint 1.

The FSM will control the overall behavior of the game, which includes game logic, game state interpreter, event handler, etc.

# FSM State Diagram

### idle

The FSM merely waits until the next cycle begins.  The rate at which the FSM loops depends on your implementation.

### read controller data

Grabs button information from the controller block so that we can process the player’s actions.

### update game state

Based on the button information grabbed in the previous state, the game state can be updated properly.  This is where all of the game logic gets processed.

The previous game state must be read from the RAM.  Then after the next state has been determined, the new state must be written back to the RAM.

This state will generate events, if any occur, such as a score increase or end-of-game.

### process events

This state will process events such as updating score, or updating mana points.  Also this is where sounds will be played if any need to be played.

### video output

This state outputs the game state to the RS232 line through the video encoder and UART.  It may or may not get executed on each loop, depending on how the FSM is implemented.  Nevertheless, it should be executed at a consistent rate, probably at around four times per second.

# Timeline

week	extra credit	normal

Mar 5 – Mar 9	Week 8	chkpt 1 extra credit

Mar 12 – Mar 16	Week 9	chkpt 2 extra credit	chkpt 1 normal credit

Mar 19 – Mar 23	Week 10	chkpt 3 extra credit	chkpt 2 normal credit

-  s  p  r  i  n  g          b  r  e  a  k  -

Apr 2 – Apr 6	Week 11		chkpt 3 normal credit

Apr 9 – Apr 13	Week 12

Apr 16 – Apr 20	Week 13	early demo week

Apr 23 – Apr 27	Week 14		demo week

Apr 30 – May 4	Week 15	reports due

# Text boxes

read controller data

update game state

controller block

controller interpreter

## FSM

RAM / game state

UART

audio block

controller

DAC

RS232

EPROM

video encoder

process events

video output

idle