# UC Berkeley

## College of Engineering

EECS Department

### EECS150								J. Wawrzynek

# Spring 2002								Prepared by Wen Hui Guan

#### Quiz #5

##### Name: ________________________Solution________________________

SID: ____________________________________Lab section number: _____________

For this problem assume that your complete library of logic components comprises 2-input AND, OR, and XOR gates and inverters.  Assume that inverters have cost of one unit and delay of one unit, and all other logic gates have cost of 2 units and delay of 2 units (ignore fanout and wire delay).  With these assumptions, a 2-input mux could be implemented with two AND gates, one OR gate, and one inverter, and would cost 7 and have delay 5 from the select input to output and a delay of 4 from data input to output.

Consider the structure of a 12-bit carry-select adder with inputs a[11:0], b[11:0], cin, and outputs s[11:0], cout.  It has the blocks sizes, 3,4,5, starting from the least significant side (the right).  All “sub-adders” are carry-ripple adders.  Assume that each ripple adders is made up only of full-adder cells (one-bit adders).

Full adder (FA):

Cost: 4 units					Cost: 8 units

Delay a/b ( S = 4				Delay a/b ( Cout = 6

Delay Cin ( S =2				Delay Cin ( Cout = 4

Total Cost: 12 units

a) Calculate the total cost for the 12-bit carry-select adder:

Total Cost  	= (11 Muxes x 7) + (21 FA x 12)

= 77 + 252

= 329 units

b) Calculate the delay from Cin to Cout:

Delay from Cin to Cout 	= 12 + 5 + 5

= 22 units

c) In words, describe the path with the worst case delay from any of the inputs to any of the

outputs:

Note that all blocks run in parallel.  The carry out of the 4-bit ripple adder comes at time of 18 units (a4/b4 ( Cout5 = 6 units, then 3 stages of Cin( Cout), is delayed by 4 by the first carry mux, and is then used by select of final carry mux, which adds 5 delay units.  So the total delay is 27 units.