University of California at Berkeley

College of Engineering

Department of Electrical Engineering and Computer Science

EECS 150									R. H. Katz

Spring 2007

Problem Set #1: Combinational Logic forms

Assigned 16 January 2007, Due 26 January at 2 PM

- Use Boolean algebra to simplify into two-level sum of products form the following Boolean expressions. Show your intermediate steps of applying Boolean algebra axioms and theorems!

  - F(A,B,C) = A’ B’ C’ + A B C’ + A B’ C’

  - F(A, B, C, D) = A’ B’ C’ D’ + A’ B’ C’ D + A’ B’ C D + A’ B C D + 
A B’ C’ D’ + A B’ C’ D + A B C’ D + A B C D

- Given the following minimized two-level sum of products expressions, describe the functions in “little m” notation:

  - F(A,B,C) = A’ B’ + A B

  - F(A,B,C,D) = C + A B  + A’ B C

- Given the following minimized two-level product of sums expressions, describe the functions in “big M” notation:

  - F(A, B, C) = (A’ + C) (B + C’)

  - F(A, B, C, D) = (A’ + B’) (A’ + C’) (B + D’)

- Use K-maps to simplify the following logical expressions into minimized two-level forms. Show how you have used K-maps to obtain your answers!

  - F(A, B, C) = A C + A B C’ + A B’ C’ + A’ B’ C’ (answer in sum of products form)

  - F(A, B, C) = M(2, 4, 6)  (answer in product of sums form)

  - F(A, B, C, D) = m(0, 4, 5, 8, 11, 12, 13) (answer in sum of products form)

  - F(A, B, C, D) = (A + C + D’) (A + B + D) (A’ + C + D’) (B’ + C + D’) (answer in product of sums form)

- Given that the Boolean function F(A, B, C) = A C’ + A’ B, answer the following questions. Show the intermediate work to arrive at the answer!

  - What is the corresponding expression in minimized product of sums form?

  - What is the corresponding expression for the complement of F in minimized sum of products form?

  - What is the corresponding expression for the complement of F in minimized product of sums form?

- F(A,B,C,D) = B(C’ + D’) in minimized product of sums form. Answer the following questions, showing your intermediate steps:

  - Show a K-map for F.

  - What is F in Big M notation?

  - What is F in Little M notation?

  - What is F in minimized two-level sum of products form?

  - Apply DeMorgan’s Law to derive the complement of F, starting with the original product of sums expression.

  - Apply DeMorgan’s Law to derive the complement of F given your answer to part d.

  - Using the K-map you filled in for part a, show how to derive the minimized complement of F in product of sums form. Is your answer the same as in part f? If not, why not?

  - Using the K-map you filled in for part a, show how to derive the minimized complement of F in sum of products form. Is your answer the same as in part e? If not, why not?