University of California at Berkeley

College of Engineering

Department of Electrical Engineering and Computer Science

EECS 150									R. H. Katz

Spring 2007

Problem Set # 8 (Assigned 20 March, Due 6 April)

- Derive a table to show the coverage of various stuck-at-0 and stuck-at-1 faults by the eight possible input combinations. What is the minimum test set for this circuit?

2.	In the following circuit, are all single stuck-at-0 and stuck-at-1 faults in the circuit detectable? If not, explain why?

3.  Given the following MEALY MACHINE State Transition Table, use the Implication Chart method to minimize the number of states. Draw the resulting minimized state diagram.

- Given your minimized state diagram for Problem 3, perform three alternative state assignments:

- Assign your states sequentially (e.g., A=0, B=1, C=2, …);

- Assign your states using a 1 Hot Encoding (e.g., A=001, B=010, C=100);

- Assign states using the heuristics presented in lecture.

- Implement your three assignments using K-maps. Which yields the best implementation and why?