University of California at Berkeley

College of Engineering

Department of Electrical Engineering and Computer Science

EECS 150									R. H. Katz

Spring 2007								   25 January 2007

Quiz #1: Combinational Logic Design

Closed Book!

### K-Maps and Canonical Forms

F(A,B,C,D) = Sm(0,2,4,6,8,9,11,12,13,15).

Fill in the K-map for this function:

Using the K-map, calculate F in minimized sum of products form:

#### F(A,B,C,D) = A’ D’ + A D + C’ D’ or A’ D’ + A D + A C’ (6 literals)

Using the K-map, calculate F in minimized PRODUCTS OF SUMS form:

#### F(A,B,C,D) = (A + D’) (A’ + C’ + D)  (5 literals)

In terms of literal count, which is the SIMPLEST implementation, sum of products or product of sums, and why?

PoS, fewer literals (5 versus 6)

# Text boxes

1      1      1      1

0      0      1      1

0      0      1      1

1      1      0      0

C

B

A

D