## Slide 1: CS 152 Computer Architecture and Engineering Lecture 1 - Introduction
Krste Asanovic
Electrical Engineering and Computer Sciences
University of California at Berkeley
http://www.eecs.berkeley.edu/~krste
http://inst.eecs.berkeley.edu/~cs152

## Slide 2: What is Computer Architecture?
Application
Physics
Gap too large to bridge in one step
In its broadest definition, computer architecture is the design of the abstraction layers that allow us to implement information processing applications efficiently using available manufacturing technologies.
(but there are exceptions, e.g. magnetic compass)

## Slide 3: Abstraction Layers in Modern Systems
Algorithm
Gates/Register-Transfer Level (RTL)
Application
Instruction Set Architecture (ISA)
Operating System/Virtual Machines
Microarchitecture
Devices
Programming Language
Circuits
Physics
EE141
CS150
CS162
CS170
CS164
EE143
CS152
UCB EECS Courses

## Slide 4: Architecture continually changing
Compatibility
Cost of software development makes compatibility a major force in market
Applications
Technology
Applications suggest how to improve technology, provide revenue to fund development
Improved technologies make new applications possible

## Slide 5: Computing Devices Then…
EDSAC, University of Cambridge, UK, 1949

## Slide 6: Computing Devices Now
Robots
Supercomputers
Automobiles
Laptops
Set-top boxes
Smart phones
Servers
Media Players
Sensor Nets
Routers
Cameras
Games

## Slide 7: Uniprocessor Performance
VAX : 25%/year 1978 to 1986
RISC + x86: 52%/year 1986 to 2002
RISC + x86: ??%/year 2002 to present
From Hennessy and Patterson, Computer Architecture: A Quantitative Approach, 4th edition, October, 2006
What happened????

## Slide 8
[from Kurzweil]
Major Technology Generations
Bipolar
nMOS
CMOS
pMOS
Relays
Vacuum Tubes
Electromechanical
?

## Slide 9: The End of the Uniprocessor Era
Single biggest change in the history of computing systems

## Slide 10: This Year’s CS252
CS152 focuses on interaction of software and hardware
  more architecture and less digital engineering
  more useful for OS developers, compiler writers, performance programmers
Much of the material you’ll learn this term was previously in CS252
  Some of the current CS61C, I first saw in CS252 over 20 years ago!
  Maybe every 10 years, shift CS252->CS152->CS61C?
Class contains labs based on various different machine designs
  Experiment with how architectural mechanisms work in practice on real software.
  Designs written in Chisel hardware description language
  Get to see (and modify) all the working parts of a modern microprocessor
  Hopefully FPGA versions later in course!

## Slide 11: Related Courses
CS61C
CS 152
CS 150
Basic computer organization, first look at pipelines + caches
Computer Architecture, First look at parallel architectures
Digital Logic Design, FPGAs
Strong
Prerequisite
CS 250
VLSI Systems Design
CS 252
Graduate Computer Architecture, Advanced Topics

## Slide 12: CS152 Executive Summary
The processor you built in CS61C
Plus, the technology behind chip-scale multiprocessors (CMPs) and graphics processing units (GPUs)
What you’ll understand and experiment with in CS152
Notes: Photo is of an Intel Conroe (Core 2 Duo Desktop processor). Photo taken from Intel web site.

## Slide 13: CS152 Administrivia
Instructor: Prof. Krste Asanovic, krste@eecs
Office: 579 Soda Hall (inside Par Lab)
Office Hours: Mon. 5:00-6:00PM (email to confirm), 579 Soda
T. A.: Yunsup Lee, yunsup@eecs
Office Hours: Tuesdays 1-2PM, 751 Soda
Lectures: Tu/Th, 2-3:30PM, 310 Soda (Possible room change!)
Section: F 10:30AM-12M, 9 Evans
Text: Computer Architecture: A Quantitative Approach,
Hennessey and Patterson, 5th Edition (2012)
Readings assigned from this edition, some readings available in older editions –see web page.
Web page: http://inst.eecs.berkeley.edu/~cs152
Lectures available online by noon before class
Piazzza: http://piazza.com/berkeley/spring2013/cs152
Notes: This slide is for the 3-min class administrative matters.
Make sure we update Handout #1 so it is consistent with this slide.

## Slide 14: CS152 Structure and Syllabus
Five modules
  Simple machine design (ISAs, microprogramming, unpipelined machines, Iron Law, simple pipelines)
  Memory hierarchy (DRAM, caches, optimizations) plus virtual memory systems, exceptions, interrupts
  Complex pipelining (score-boarding, out-of-order issue)
  Explicitly parallel processors (vector machines, VLIW machines, multithreaded machines)
  Multiprocessor architectures (memory models, cache coherence, synchronization)
Notes: This is the 1st slide of the “Course Structure and Course Philosophy” section of the lecture.
Need to emphasis that for exams, our goal is the test your knowledge. It is not our goal to test how well your perform under time pressure.

## Slide 15: CS152 Course Components
15% Problem Sets (one per module)
  Intended to help you learn the material. Feel free to discuss with other students and instructors, but must turn in your own solutions. Grading based mostly on effort, but quizzes assume that you have worked through all problems. Solutions released after PSs handed in.
35% Labs (one per module)
  Labs use advanced full system simulators (new Chisel simulators this year, no Simics)
  Directed plus open-ended sections to each lab
50% Quizzes (one per module)
  In-class, closed-book, no calculators, no smartphones, no laptops,...
  Based on lectures, readings, problem sets, and labs

## Slide 16: CS152 Labs
Each lab has directed plus open-ended assignments
Directed portion (2/7) is intended to ensure students learn main concepts behind lab
  Each student must perform own lab and hand in their own lab report
Open-ended assignment (5/7) is to allow you to show your creativity
  Roughly a one-day “mini-project”
    E.g., try an architectural idea and measure potential, negative results OK (if explainable!)
  Students can work individually or in groups of two or three
  Group open-ended lab reports must be handed in separately
  Students can work in different groups for different assignments
Lab reports must be readable English summaries – not dumps of log files!!!!!!

## Slide 17: RISC-V ISA
RISC-V is a new simple, clean, extensible ISA we developed at Berkeley for education and research
  RISC-I/II, first Berkeley RISC implementations
  Berkeley research machines SOAR/SPUR considered RISC-III/IV
Both of the dominant ISAs (x86 and ARM) are too complex to use for teaching
RISC-V ISA manual available on web page
Full GCC-based tool chain available

## Slide 18: Chisel simulators
Chisel is a new hardware description language we developed at Berkeley based on Scala
  Constructing Hardware in a Scala Embedded Language
Labs will use RISC-V processor simulators derived from Chisel processor designs
  Gives you much more detailed information than other simulators
  Can map to FPGA or real chip layout
You need to learn some minimal Chisel in CS152, but we’ll make Chisel RTL source available so you can see all the details of our processors
Can do lab projects based on modifying the Chisel RTL code if desired

## Slide 19: Chisel Design Flow
Chisel Design Description
C++ code
FPGA Verilog
ASIC Verilog
C++ Simulator
C++ Compiler
Chisel Compiler
FPGA Emulation
FPGA Tools
GDS Layout
ASIC Tools

## Slide 20: Computer Architecture: A Little History
Throughout the course we’ll use a historical narrative to help understand why certain ideas arose
Why worry about old ideas?
Helps to illustrate the design process, and explains why certain decisions were taken
Because future technologies might be as constrained as older ones
Those who ignore history are doomed to repeat it
  Every mistake made in mainframe design was also made in minicomputers, then microcomputers, where next?

## Slide 21: Charles Babbage 1791-1871 Lucasian Professor of Mathematics, Cambridge University, 1827-1839

## Slide 22: Charles Babbage
Difference Engine 1823
Analytic Engine 1833
  The forerunner of modern digital computer!
Application
  Mathematical Tables – Astronomy
  Nautical Tables – Navy
Background
  Any continuous function can be approximated by a polynomial --- Weierstrass
Technology
  mechanical - gears, Jacquard’s loom, simple calculators

## Slide 23: Difference Engine A machine to compute mathematical tables
Weierstrass:
  Any continuous function can be approximated by a polynomial
  Any polynomial can be computed from difference tables
An example
    f(n) = n2 + n + 41
    d1(n) = f(n) - f(n-1) = 2n
    d2(n) = d1(n) - d1(n-1) = 2
    f(n) = f(n-1) + d1(n) = f(n-1) + (d1(n-1) + 2)
all you need is an adder!
n
d2(n)
d1(n)
f(n)
0
41
1
2
2
2
3
2
4
2
4
6
8
43
47
53
61

## Slide 24: Difference Engine
1823
  Babbage’s paper is published
1834
  The paper is read by Scheutz & his son in Sweden
1842
  Babbage gives up the idea of building it; he is onto Analytic Engine!
1855
  Scheutz displays his machine at the Paris World Fare
  Can compute any 6th degree polynomial
  Speed: 33 to 44 32-digit numbers per minute!
Now the machine is at the Smithsonian

## Slide 25: Analytic Engine
1833: Babbage’s paper was published
  conceived during a hiatus in the development of the difference engine
Inspiration: Jacquard Looms
  looms were controlled by punched cards
    The set of cards with fixed punched holes dictated the pattern of weave  program
    The same set of cards could be used with different colored threads  numbers
1871: Babbage dies
  The machine remains unrealized.
It is not clear if the analytic engine could be built using the mechanical technology of the time

## Slide 26: Analytic Engine The first conception of a general-purpose computer
The store in which all variables to be operated upon, as well as all those quantities which have arisen from the results of the operations are placed.
The mill into which the quantities about to be operated upon are always brought.
The program
Operation variable1 variable2 variable3
An operation in the mill required feeding two punched cards and producing a new punched card for the store.
An operation to alter the sequence was also provided!

## Slide 27: The first programmer Ada Byron aka “Lady Lovelace” 1815-52
Ada’s tutor was Babbage himself!

## Slide 28: Babbage’s Influence
Babbage’s ideas had great influence later primarily because of
  Luigi Menabrea, who published notes of Babbage’s lectures in Italy
  Lady Lovelace, who translated Menabrea’s notes in English and thoroughly expanded them.
    “... Analytic Engine weaves algebraic patterns....”
In the early twentieth century - the focus shifted to analog computers but
  Harvard Mark I built in 1944 is very close in spirit to the Analytic Engine.

## Slide 29: Harvard Mark I
Built in 1944 in IBM Endicott laboratories
  Howard Aiken – Professor of Physics at Harvard
  Essentially mechanical but had some electro-magnetically controlled relays and gears
  Weighed 5 tons and had 750,000 components
  A synchronizing clock that beat every 0.015 seconds (66Hz)
Performance:
0.3 seconds for addition
6 seconds for multiplication
1 minute for a sine calculation
Decimal arithmetic
No Conditional Branch!
Broke down once a week!

## Slide 30: Linear Equation Solver John Atanasoff, Iowa State University
1930’s:
  Atanasoff built the Linear Equation Solver.
  It had 300 tubes!
  Special-purpose binary digital calculator
  Dynamic RAM (stored values on refreshed capacitors)
Application:
  Linear and Integral differential equations
Background:
  Vannevar Bush’s Differential Analyzer
  --- an analog computer
Technology:
  Tubes and Electromechanical relays
Atanasoff decided that the correct mode of computation was using electronic binary digits.

## Slide 31: Electronic Numerical Integrator and Computer (ENIAC)
Inspired by Atanasoff and Berry, Eckert and Mauchly designed and built ENIAC (1943-45) at the University of Pennsylvania
The first, completely electronic, operational, general-purpose analytical calculator!
  30 tons, 72 square meters, 200KW
Performance
  Read in 120 cards per minute
  Addition took 200 ms, Division 6 ms
  1000 times faster than Mark I
Not very reliable!
Application: Ballistic calculations
angle = f (location, tail wind, cross wind,
air density, temperature, weight of shell,
propellant charge, ... )
WW-2 Effort
Notes: Designers were obliged to install a ventilation shaft and a cooling system in the room. Machine had 18,000 vacuum tubes.
The slogan was: The ENIAC is able to calculate the trajectory of a large-caliber naval shell in less time than the shell takes to reach its target!
To change a program, it was necessary to change the instructions, the connector panels, and the positions of the switches all at the same time.
The inventors of ENIAC themselves admitted that, after taking into account human error, the machine only got the correct result 20 times out of 100!

## Slide 32: Electronic Discrete Variable Automatic Computer (EDVAC)
ENIAC’s programming system was external
  Sequences of instructions were executed independently of the results of the calculation
  Human intervention required to take instructions “out of order”
Eckert, Mauchly, John von Neumann and others designed EDVAC (1944) to solve this problem
  Solution was the stored program computer
   “program can be manipulated as data”
First Draft of a report on EDVAC was published in 1945, but just had von Neumann’s signature!
  In 1973 the court of Minneapolis attributed the honor of inventing the computer to John Atanasoff
Notes: Von Neumann (1903-1957) was born in Budapest. Great quantities of work in set theory to quantum physics. Celebrated for his theory of games and its application to economics.
Report was the formal specification of EDVAC. Before that the documentation on ENIAC or EDVAC was non-existent. Von Neumann devised a mathematical logical notation which expressed fundamental ideas of the fetch-execute-decode loop.
Five major components: Arithmetic unit, control unit, the memory, input devices and output devices.

## Slide 33: Stored Program Computer
manual control calculators
automatic control
  external (paper tape) Harvard Mark I , 1944
Zuse’s Z1, WW2
  internal
    plug board ENIAC 1946
    read-only memory ENIAC 1948
    read-write memory EDVAC 1947 (concept )
      The same storage can be used to store program and data
Program = A sequence of instructions
How to control instruction sequencing?
EDSAC 1950 Maurice Wilkes

## Slide 34: Technology Issues
ENIAC  EDVAC
18,000 tubes 4,000 tubes
20 10-digit numbers 2000 word storage
mercury delay lines
ENIAC had many asynchronous parallel units
but only one was active at a time
BINAC : Two processors that checked each other
for reliability.
  Didn’t work well because processors never
  agreed

## Slide 35: Dominant Problem: Reliability
Mean time between failures (MTBF)
  MIT’s Whirlwind with an MTBF of 20 min. was perhaps the most reliable machine !
Reasons for unreliability:
1. Vacuum Tubes
2. Storage medium
  acoustic delay lines
  mercury delay lines
  Williams tubes
  Selections
Reliability solved by invention of Core memory by J. Forrester 1954 at MIT for Whirlwind project

## Slide 36: Commercial Activity: 1948-52
IBM’s SSEC (follow on from Harvard Mark I)
  Selective Sequence Electronic Calculator
  150 word store.
  Instructions, constraints, and tables of data were read from paper tapes.
  66 Tape reading stations!
  Tapes could be glued together to form a loop!
  Data could be output in one phase of computation and read in the next phase of computation.

## Slide 37: And then there was IBM 701
IBM 701 -- 30 machines were sold in 1953-54
used CRTs as main memory, 72 tubes of 32x32b each
IBM 650 -- a cheaper, drum based machine,
more than 120 were sold in 1954
and there were orders for 750 more!
Users stopped building their own machines.
Why was IBM late getting into computer technology?
IBM was making too much money!
    Even without computers, IBM revenues were doubling every 4 to 5 years in 40’s and 50’s.

## Slide 38: Computers in mid 50’s
Hardware was expensive
Stores were small (1000 words)
   No resident system software!
Memory access time was 10 to 50 times slower than the processor cycle
   Instruction execution time was totally dominated by the memory reference time.
The ability to design complex control circuits to execute an instruction was the central design concern as opposed to the speed of decoding or an ALU operation
Programmer’s view of the machine was inseparable from the actual hardware implementation

## Slide 39: The IBM 650 (1953-4)
[From 650 Manual, © IBM]
Magnetic Drum (1,000 or 2,000
10-digit decimal words)
20-digit accumulator
Active instruction (including next program counter)
Digit-serial ALU

## Slide 40: Programmer’s view of the IBM 650
A drum machine with 44 instructions
Instruction: 60 1234 1009
  “Load the contents of location 1234 into the distribution; put it also into the upper accumulator; set lower accumulator to zero; and then go to location 1009 for the next instruction.”
Good programmers optimized the placement of instructions on the drum to reduce latency!

## Slide 41: The Earliest Instruction Sets
Single Accumulator - A carry-over from the calculators.
LOAD x AC  M[x]
STORE x M[x]  (AC)
ADD x AC  (AC) + M[x]
SUB x
MUL x Involved a quotient register
DIV x
SHIFT LEFT AC  2  (AC) SHIFT RIGHT
JUMP x PC  x
JGE x if (AC) ³ 0 then PC  x
LOAD ADR x AC  Extract address field(M[x])
STORE ADR x
Typically less than 2 dozen instructions!

## Slide 42: Programming: Single Accumulator Machine
LOOP LOAD N
    JGE DONE
    ADD ONE
    STORE N
F1 LOAD A
F2 ADD B
F3 STORE C
    JUMP LOOP
DONE HLT
Ci Ai + Bi, 1  i  n
How to modify the addresses A, B and C ?
A
B
C
N
ONE
code
-n
1

## Slide 43: Self-Modifying Code
LOOP LOAD N
    JGE DONE
    ADD ONE
    STORE N
F1 LOAD A
F2 ADD B
F3 STORE C
    JUMP LOOP
DONE HLT
modify the
program
for the next
iteration
Each iteration involves
total book-
keeping
instruction
fetches
operand
fetches
stores
Ci Ai + Bi, 1  i  n
    LOAD ADR F1
    ADD ONE
    STORE ADR F1
    LOAD ADR F2
    ADD ONE
    STORE ADR F2
    LOAD ADR F3
    ADD ONE
    STORE ADR F3
    JUMP LOOP
DONE HLT
17
10
5
14
8
4

## Slide 44: Index Registers Tom Kilburn, Manchester University, mid 50’s
Modify existing instructions
  LOAD x, IX AC  M[x + (IX)]
  ADD x, IX AC  (AC) + M[x + (IX)]
  ...
Add new instructions to manipulate index registers
  JZi x, IX if (IX)=0 then PC  x
  else IX  (IX) + 1
  LOADi x, IX IX  M[x] (truncated to fit IX)
  ...
One or more specialized registers to simplify
address calculation
Index registers have accumulator-like characteristics

## Slide 45: Using Index Registers
LOADi -n, IX
LOOP JZi DONE, IX
    LOAD LASTA, IX
    ADD LASTB, IX
    STORE LASTC, IX
    JUMP LOOP
DONE HALT
Program does not modify itself
Efficiency has improved dramatically (ops / iter)
with index regs without index regs
  instruction fetch 17 (14)
  operand fetch 10 (8)
  store 5 (4)
Costs: Instructions are 1 to 2 bits longer
        Index registers with ALU-like circuitry
        Complex control
A
LASTA
Ci Ai + Bi, 1  i  n
5(2)
2
1

## Slide 46: Operations on Index Registers
To increment index register by k
    AC  (IX) new instruction
    AC  (AC) + k
    IX  (AC) new instruction
also the AC must be saved and restored.
It may be better to increment IX directly
    INCi k, IX IX  (IX) + k
More instructions to manipulate index register
    STOREi x, IX M[x]  (IX) (extended to fit a word)
    ...
IX begins to look like an accumulator
    several index registers
      several accumulators
        General Purpose Registers

## Slide 47: Evolution of Addressing Modes
1. Single accumulator, absolute address
        LOAD x
2. Single accumulator, index registers
        LOAD x, IX
3. Indirection
        LOAD (x)
4. Multiple accumulators, index registers, indirection
        LOAD R, IX, x
    or LOAD R, IX, (x) the meaning?
    R  M[M[x] + (IX)]
    or R  M[M[x + (IX)]]
5. Indirect through registers
        LOAD RI, (RJ)
6. The works
        LOAD RI, RJ, (RK) RJ = index, RK = base addr

## Slide 48: Variety of Instruction Formats
One address formats: Accumulator machines
  Accumulator is always other source and destination operand
Two address formats: the destination is same as one of the operand sources
  (Reg  Reg) to Reg RI  (RI) + (RJ)
  (Reg  Mem) to Reg RI  (RI) + M[x]
  x can be specified directly or via a register
  effective address calculation for x could include indexing, indirection, ...
Three address formats: One destination and up to two operand sources per instruction
  (Reg x Reg) to Reg RI  (RJ) + (RK)
  (Reg x Mem) to Reg RI  (RJ) + M[x]

## Slide 49: Zero Address Formats
Operands on a stack
  add M[sp-1]  M[sp] + M[sp-1]
  load M[sp]  M[M[sp]]
  Stack can be in registers or in memory (usually top of stack cached in registers)
C
B
A
SP
Register

## Slide 50: Burrough’s B5000 Stack Architecture: An ALGOL Machine, Robert Barton, 1960
Machine implementation can be completely hidden if the programmer is provided only a high-level language interface.
Stack machine organization because stacks are convenient for:
  expression evaluation;
  subroutine calls, recursion, nested interrupts;
  accessing variables in block-structured languages.
B6700, a later model, had many more innovative features
  tagged data
  virtual memory
  multiple processors and memories

## Slide 51: Evaluation of Expressions
a
b
c
(a + b * c) / (a + d * c - e)
/
+
*
+
a
e
-
a
c
d
c
*
b
Reverse Polish
a b c * + a d c * + e - /
push a
push b
push c
multiply
*
Evaluation Stack
b * c

## Slide 52: Evaluation of Expressions
a
(a + b * c) / (a + d * c - e)
/
+
*
+
a
e
-
a
c
d
c
*
b
Reverse Polish
a b c * + a d c * + e - /
add
+
Evaluation Stack
b * c
a + b * c

## Slide 53: Hardware organization of the stack
Stack is part of the processor state
    stack must be bounded and small
    number of Registers,
    not the size of main memory
Conceptually stack is unbounded
    a part of the stack is included in the
    processor state; the rest is kept in the
    main memory

## Slide 54: Stack Operations and Implicit Memory References
Suppose the top 2 elements of the stack are kept in registers and the rest is kept in the memory.
  Each push operation 1 memory reference
  pop operation  1 memory reference
No Good!
Better performance by keeping the top N elements in registers, and memory references are made only when register stack overflows or underflows.
Issue - when to Load/Unload registers ?

## Slide 55: Stack Size and Memory References
program stack (size = 2) memory refs
push a R0 a
push b R0 R1 b
push c R0 R1 R2 c, ss(a)
* R0 R1 sf(a)
+ R0
push a R0 R1 a
push d R0 R1 R2 d, ss(a+b*c)
push c R0 R1 R2 R3 c, ss(a)
* R0 R1 R2 sf(a)
+ R0 R1 sf(a+b*c)
push e R0 R1 R2 e,ss(a+b*c)
- R0 R1 sf(a+b*c)
/ R0
a b c * + a d c * + e - /
4 stores, 4 fetches (implicit)

## Slide 56: Stack Size and Expression Evaluation
program stack (size = 4)
push a R0
push b R0 R1
push c R0 R1 R2
* R0 R1
+ R0
push a R0 R1
push d R0 R1 R2
push c R0 R1 R2 R3
* R0 R1 R2
+ R0 R1
push e R0 R1 R2
- R0 R1
/ R0
a b c * + a d c * + e - /
a and c are
“loaded” twice

not the best
use of registers!

## Slide 57: Register Usage in a GPR Machine
More control over register usage since registers can be named explicitly
  Load Ri m
  Load Ri (Rj)
  Load Ri (Rj) (Rk)
  
  - eliminates unnecessary
  Loads and Stores
  - fewer Registers
but instructions may be longer!
Load R0 a
Load R1 c
Load R2 b
Mul R2 R1
(a + b * c) / (a + d * c - e)
Reuse
R2
Add R2 R0
Load R3 d
Mul R3 R1
Add R3 R0
Reuse
R3
Load R0 e
Sub R3 R0
Div R2 R3
Reuse
R0

## Slide 58: Stack Machines: Essential features
In addition to push, pop, + etc., the instruction set must provide the capability to
  refer to any element in the data area
  jump to any instruction in the code area
  move any element in the stack frame to the top
machinery to
carry out
+, -, etc.
stack
SP
DP
PC
data
.
.
.
a
b
c

push a
push b
push c
*
+
push e
/
code

## Slide 59: Stack versus GPR Organization Amdahl, Blaauw and Brooks, 1964
1. The performance advantage of push down stack organization is derived from the presence of fast registers and not the way they are used.
2.“Surfacing” of data in stack which are “profitable” is approximately 50% because of constants and common subexpressions.
3. Advantage of instruction density because of implicit addresses is equaled if short addresses to specify registers are allowed.
4. Management of finite depth stack causes complexity.
5. Recursive subroutine advantage can be realized only with the help of an independent stack for addressing.
6. Fitting variable-length fields into fixed-width word is awkward.

## Slide 60: Stack Machines (Mostly) Died by 1980
1. Stack programs are not smaller if short (Register) addresses are permitted.
2. Modern compilers can manage fast register space better than the stack discipline.
GPR’s and caches are better than stack and displays
Early language-directed architectures often did not
take into account the role of compilers!
B5000, B6700, HP 3000, ICL 2900, Symbolics 3600
Some would claim that an echo of this mistake is visible in the SPARC architecture register windows - more later…

## Slide 61: Stacks post-1980
Inmos Transputers (1985-2000)
  Designed to support many parallel processes in Occam language
  Fixed-height stack design simplified implementation
  Stack trashed on context swap (fast context switches)
  Inmos T800 was world’s fastest microprocessor in late 80’s
Forth machines
  Direct support for Forth execution in small embedded real-time environments
  Several manufacturers (Rockwell, Patriot Scientific)
Java Virtual Machine
  Designed for software emulation, not direct hardware execution
  Sun PicoJava implementation + others
Intel x87 floating-point unit
  Severely broken stack model for FP arithmetic
  Deprecated in Pentium-4, replaced with SSE2 FP registers

## Slide 62: Software Developments
up to 1955 Libraries of numerical routines
        - Floating point operations
        - Transcendental functions
        - Matrix manipulation, equation solvers, . . .
1955-60 High level Languages - Fortran 1956
        Operating Systems -
        - Assemblers, Loaders, Linkers, Compilers
        - Accounting programs to keep track of
        usage and charges
Machines required experienced operators
 Most users could not be expected to understand
these programs, much less write them
   Machines had to be sold with a lot of resident
    software

## Slide 63: Compatibility Problem at IBM
By early 60’s, IBM had 4 incompatible lines of computers!
        701  7094
        650  7074
        702  7080
        1401   7010
Each system had its own
      Instruction set
      I/O system and Secondary Storage:
      magnetic tapes, drums and disks
      assemblers, compilers, libraries,...
      market niche
      business, scientific, real time, ...
 IBM 360

## Slide 64: IBM 360 : Design Premises Amdahl, Blaauw and Brooks, 1964
The design must lend itself to growth and successor machines
General method for connecting I/O devices
Total performance - answers per month rather than bits per microsecond  programming aids
Machine must be capable of supervising itself without manual intervention
Built-in hardware fault checking and locating aids to reduce down time
Simple to assemble systems with redundant I/O devices, memories etc. for fault tolerance
Some problems required floating-point larger than 36 bits

## Slide 65: IBM 360: A General-Purpose Register (GPR) Machine
Processor State
  16 General-Purpose 32-bit Registers
    may be used as index and base register
    Register 0 has some special properties
  4 Floating Point 64-bit Registers
  A Program Status Word (PSW)
    PC, Condition codes, Control flags
A 32-bit machine with 24-bit addresses
  But no instruction contains a 24-bit address!
Data Formats
  8-bit bytes, 16-bit half-words, 32-bit words, 64-bit double-words
The IBM 360 is why bytes are 8-bits long today!

## Slide 66: IBM 360: Initial Implementations
        Model 30 . . . Model 70
Storage 8K - 64 KB 256K - 512 KB
Datapath 8-bit 64-bit
Circuit Delay 30 nsec/level 5 nsec/level
Local Store Main Store Transistor Registers
Control Store Read only 1sec Conventional circuits
IBM 360 instruction set architecture (ISA) completely hid the underlying technological differences between various models.
Milestone: The first true ISA designed as portable hardware-software interface!
With minor modifications it still survives today!

## Slide 67: IBM 360: 47 years later… The zSeries z11 Microprocessor
5.2 GHz in IBM 45nm PD-SOI CMOS technology
1.4 billion transistors in 512 mm2
64-bit virtual addressing
  original S/360 was 24-bit, and S/370 was 31-bit extension
Quad-core design
Three-issue out-of-order superscalar pipeline
Out-of-order memory accesses
Redundant datapaths
  every instruction performed in two parallel datapaths and results compared
64KB L1 I-cache, 128KB L1 D-cache on-chip
1.5MB private L2 unified cache per core, on-chip
On-Chip 24MB eDRAM L3 cache
Scales to 96-core multiprocessor with 768MB of shared L4 eDRAM
[ IBM, HotChips, 2010]

## Slide 68: And in conclusion …
Computer Architecture >> ISAs and RTL
CS152 is about interaction of hardware and software, and design of appropriate abstraction layers
Computer architecture is shaped by technology and applications
  History provides lessons for the future
Computer Science at the crossroads from sequential to parallel computing
  Salvation requires innovation in many fields, including computer architecture
Read Chapter 1 & Appendix A for next time!

## Slide 69: Acknowledgements
These slides contain material developed and copyright by:
  Arvind (MIT)
  Krste Asanovic (MIT/UCB)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)
MIT material derived from course 6.823
UCB material derived from course CS252