## Slide 1: CS 152 Computer Architecture and Engineering Lecture 10 - Complex Pipelines, Out-of-Order Issue, Register Renaming
Krste Asanovic
Electrical Engineering and Computer Sciences
University of California at Berkeley
http://www.eecs.berkeley.edu/~krste
http://inst.eecs.berkeley.edu/~cs152

## Slide 2: Last time in Lecture 9
Modern page-based virtual memory systems provide:
  Translation, Protection, Virtual memory.
Translation and protection information stored in page tables, held in main memory
Translation and protection information cached in “translation-lookaside buffer” (TLB) to provide single-cycle translation+protection check in common case
Virtual memory interacts with cache design
  Physical cache tags require address translation before tag lookup, or use untranslated offset bits to index cache.
  Virtual tags do not require translation before cache hit/miss determination, but need to be flushed or extended with ASID to cope with context swaps. Also, must deal with virtual address aliases (usually by disallowing copies in cache).

## Slide 3: Complex Pipelining: Motivation
Pipelining becomes complex when we want high performance in the presence of:
Long latency or partially pipelined floating-point units
Memory systems with variable access time
Multiple arithmetic and memory units

## Slide 4: Floating-Point Unit (FPU)
Much more hardware than an integer unit
  Single-cycle FPU is a bad idea – why?
Common to have several FPU’s
Common to have different types of FPU’s: Fadd, Fmul, Fdiv, …
An FPU may be pipelined, partially pipelined or not pipelined
To operate several FPU’s concurrently the FP register file needs to have more read and write ports

## Slide 5: Functional Unit Characteristics
fully
pipelined
partially
pipelined
Functional units have internal pipeline registers
   operands are latched when an instruction
    enters a functional unit
   following instructions are able to write register file during a long-latency operation
1cyc
1cyc
1cyc
2 cyc
2 cyc

## Slide 6: Floating-Point ISA
Interaction between floating-point datapath and integer datapath is determined by ISA
RISC-V ISA
  separate register files for FP and Integer instructions
    the only interaction is via a set of move/convert instructions (some ISA’s don’t even permit this)
  separate load/store for FPR’s and GPR’s but both use GPR’s for address calculation
  FP compares write integer registers, then use integer branch
Notes: Why not have a transfer between FP and GPR? Why have it?

## Slide 7: Realistic Memory Systems
Common approaches to improving memory performance:
Caches - single cycle except in case of a miss
stall
Banked memory - multiple memory accesses
 bank conflicts
split-phase memory operations (separate memory request from response), many in flight
 out-of-order responses
Latency of access to the main memory is usually much greater than one cycle and often unpredictable
  Solving this problem is a central issue in computer architecture

## Slide 8: Issues in Complex Pipeline Control
IF
ID
WB
ALU
Mem
Fadd
Fmul
Fdiv
Issue
GPRs
FPRs
Structural conflicts at the execution stage if some FPU or memory unit is not pipelined and takes more than one cycle
Structural conflicts at the write-back stage due to variable latencies of different functional units
Out-of-order write hazards due to variable latencies of different functional units
How to handle exceptions?

## Slide 9: Complex In-Order Pipeline
Delay writeback so all operations have same latency to W stage
  Write ports never oversubscribed (one inst. in & one inst. out every cycle)
  Stall pipeline on long latency operations, e.g., divides, cache misses
  Handle exceptions in-order at commit point
Commit Point
PC
Inst. Mem
D
Decode
X1
X2
Data Mem
W
+
GPRs
X2
W
FAdd
X3
X3
FPRs
X1
X2
FMul
X3
X2
FDiv
X3
Unpipelined divider
How to prevent increased writeback latency from slowing down single cycle integer operations?
Bypassing

## Slide 10: In-Order Superscalar Pipeline
Fetch two instructions per cycle; issue both simultaneously if one is integer/memory and other is floating point
Inexpensive way of increasing throughput, examples include Alpha 21064 (1992) & MIPS R5000 series (1996)
Same idea can be extended to wider issue by duplicating functional units (e.g. 4-issue UltraSPARC & Alpha 21164) but regfile ports and bypassing costs grow quickly
Commit Point
2
PC
Inst. Mem
D
Dual
Decode
X1
X2
Data Mem
W
+
GPRs
X2
W
FAdd
X3
X3
FPRs
X1
X2
FMul
X3
X2
FDiv
X3
Unpipelined divider

## Slide 11: Types of Data Hazards
Consider executing a sequence of
rk ri op rj
type of instructions
Data-dependence
      r3  r1 op r2 Read-after-Write
      r5  r3 op r4 (RAW) hazard
Anti-dependence
      r3  r1 op r2 Write-after-Read
      r1  r4 op r5 (WAR) hazard
Output-dependence
      r3  r1 op r2 Write-after-Write
      r3  r6 op r7 (WAW) hazard

## Slide 12: Register vs. Memory Dependence
Data hazards due to register operands can be determined at the decode stage, but data hazards due to memory operands can be determined only after computing the effective address
Store: M[r1 + disp1]  r2
Load: r3  M[r4 + disp2]
Does (r1 + disp1) = (r4 + disp2) ?

## Slide 13: Data Hazards: An Example
I1 FDIV.D f6, f6, f4
I2 FLD f2, 45(x3)
I3 FMUL.D f0, f2, f4
I4 FDIV.D f8, f6, f2
I5 FSUB.D f10, f0, f6
I6 FADD.D f6, f8, f2
RAW Hazards
WAR Hazards
WAW Hazards

## Slide 14: Instruction Scheduling
I6
I2
I4
I1
I5
I3
Valid orderings:
in-order I1 I2 I3 I4 I5 I6
out-of-order
out-of-order
I1 FDIV.D f6, f6, f4
I2 FLD f2, 45(x3)
I3 FMULT.D f0, f2, f4
I4 FDIV.D f8, f6, f2
I5 FSUB.D f10, f0, f6
I6 FADD.D f6, f8, f2
I2 I1 I3 I4 I5 I6
I1 I2 I3 I5 I4 I6

## Slide 15: Out-of-order Completion In-order Issue
Latency
I1 FDIV.D f6, f6, f4 4
I2 FLD f2, 45(x3) 1
I3 FMULT.D f0, f2, f4 3
I4 FDIV.D f8, f6, f2 4
I5 FSUB.D f10, f0, f6 1
I6 FADD.D f6, f8, f2 1
in-order comp 1 2
out-of-order comp 1 2
1 2 3 4 3 5 4 6 5 6
2 3 1 4 3 5 5 4 6 6

## Slide 16: Complex Pipeline
IF
ID
WB
ALU
Mem
Fadd
Fmul
Fdiv
Issue
GPR’s
FPR’s
Can we solve write hazards without equalizing all pipeline depths and without bypassing?

## Slide 17: When is it Safe to Issue an Instruction?
Suppose a data structure keeps track of all the instructions in all the functional units
The following checks need to be made before the Issue stage can dispatch an instruction
Is the required function unit available?
Is the input data available?  RAW?
Is it safe to write the destination? WAR? WAW?
Is there a structural conflict at the WB stage?

## Slide 18: A Data Structure for Correct Issues Keeps track of the status of Functional Units
The instruction i at the Issue stage consults this table
  FU available? check the busy column
  RAW? search the dest column for i’s sources
  WAR? search the source columns for i’s destination
  WAW? search the dest column for i’s destination
An entry is added to the table if no hazard is detected;
An entry is removed from the table after Write-Back
Name Busy Op Dest Src1 Src2
  Int
  Mem
  Add1
  Add2
  Add3
  Mult1
  Mult2
  Div

## Slide 19: Simplifying the Data Structure Assuming In-order Issue
Suppose the instruction is not dispatched by the Issue stage if a RAW hazard exists or the required FU is busy, and that operands are latched by functional unit on issue:
  Can the dispatched instruction cause a
    WAR hazard ?
    WAW hazard ?
NO: Operands read at issue
YES: Out-of-order completion
Notes:   Can the dispatched instruction cause a
    WAR hazard ? NO: Operands read at issue
    WAW hazard ? YES: Out-of-order completion

## Slide 20: Simplifying the Data Structure ...
No WAR hazard
   no need to keep src1 and src2
The Issue stage does not dispatch an instruction in
case of a WAW hazard
  a register name can occur at most once in the dest column
WP[reg#] : a bit-vector to record the registers for which writes are pending
  These bits are set by the Issue stage and cleared by the WB stage
   Each pipeline stage in the FU's must carry the dest field and a flag to indicate if it is valid “the (we, ws) pair”

## Slide 21: Scoreboard for In-order Issues
Busy[FU#] : a bit-vector to indicate FU’s availability.
        (FU = Int, Add, Mult, Div)
  These bits are hardwired to FU's.
WP[reg#] : a bit-vector to record the registers for which writes are pending.
  These bits are set by Issue stage and cleared by WB stage
Issue checks the instruction (opcode dest src1 src2)
against the scoreboard (Busy & WP) to dispatch
    FU available?
    RAW?
    WAR?
    WAW?
Busy[FU#]
WP[src1] or WP[src2]
cannot arise
WP[dest]

## Slide 22: Scoreboard Dynamics
I1 FDIV.D f6, f6, f4
I2 FLD f2, 45(x3)
I3 FMULT.D f0, f2, f4
I4 FDIV.D f8, f6, f2
I5 FSUB.D f10, f0, f6
I6 FADD.D f6, f8, f2
  Functional Unit Status Registers Reserved
  Int(1) Add(1) Mult(3) Div(4) WB for Writes
t0 I1 f6 f6
t1 I2 f2 f6 f6, f2
t2 f6 f2 f6, f2 I2
t3 I3 f0 f6 f6, f0
t4 f0 f6 f6, f0 I1
t5 I4 f0 f8 f0, f8
t6 f8 f0 f0, f8 I3
t7 I5 f10 f8 f8, f10
t8 f8 f10 f8, f10 I5
t9 f8 f8 I4
t10 I6 f6 f6
t11 f6 f6 I6

## Slide 23: In-Order Issue Limitations: an example
latency
1 FLD f2, 34(x2) 1
2 FLD f4, 45(x3) long
3 FMULT.D f6, f4, f2 3
4 FSUB.D f8, f2, f2 1
5 FDIV.D f4, f2, f8 4
6 FADD.D f10, f6, f4 1
In-order: 1 (2,1) . . . . . . 2 3 4 4 3 5 . . . 5 6 6
1
2
3
4
5
6
In-order issue restriction prevents instruction 4 from being dispatched

## Slide 24: CS152 Administrivia
Quiz 2, Tuesday March 5
  Caches and Virtual memory L6 – L9, PS 2, Lab 2, readings

## Slide 25: Out-of-Order Issue
Issue stage buffer holds multiple instructions waiting to issue.
Decode adds next instruction to buffer if there is space and the instruction does not cause a WAR or WAW hazard.
  Note: WAR possible again because issue is out-of-order (WAR not possible with in-order issue and latching of input operands at functional unit)
Any instruction in buffer whose RAW hazards are satisfied can be issued (for now at most one dispatch per cycle). On a write back (WB), new instructions may get enabled.
IF
ID
WB
ALU
Mem
Fadd
Fmul
Issue

## Slide 26: Issue Limitations: In-Order and Out-of-Order
latency
1 FLD f2, 34(x2) 1
2 FLD f4, 45(x3) long
3 FMULT.D f6, f4, f2 3
4 FSUB.D f8, f2, f2 1
5 FDIV.D f4, f2, f8 4
6 FADD.D f10, f6, f4 1
In-order: 1 (2,1) . . . . . . 2 3 4 4 3 5 . . . 5 6 6
1
2
3
4
5
6
Out-of-order: 1 (2,1) 4 4 . . . . 2 3 . . 3 5 . . . 5 6 6
Out-of-order execution did not allow any significant improvement!

## Slide 27: How many instructions can be in the pipeline?
Which features of an ISA limit the number of
instructions in the pipeline?
Out-of-order dispatch by itself does not provide any significant performance improvement!
Number of Registers
Notes: Ilustrates how one feature alone may not help – happens today when people study single new idea in a very detailed model.

## Slide 28: Overcoming the Lack of Register Names
Floating Point pipelines often cannot be kept filled with small number of registers.
IBM 360 had only 4 floating-point registers
Can a microarchitecture use more registers than
specified by the ISA without loss of ISA compatibility ?
    Robert Tomasulo of IBM suggested an ingenious solution in 1967 using on-the-fly register renaming

## Slide 29: Issue Limitations: In-Order and Out-of-Order
latency
1 FLD f2, 34(x2) 1
2 FLD f4, 45(x3) long
3 FMULT.D f6, f4, f2 3
4 FSUB.D f8, f2, f2 1
5 FDIV.D f4’, f2, f8 4
6 FADD.D f10, f6, f4’ 1
1
2
3
4
5
6
Any antidependence can be eliminated by renaming.
    (renaming  additional storage)
    Can it be done in hardware?
yes!
X
In-order: 1 (2,1) . . . . . . 2 3 4 4 3 5 . . . 5 6 6
Out-of-order: 1 (2,1) 4 4 5 . . . 2 (3,5) 3 6 6

## Slide 30: Register Renaming
Decode does register renaming and adds instructions to the issue-stage instruction reorder buffer (ROB)
 renaming makes WAR or WAW hazards impossible
Any instruction in ROB whose RAW hazards have been satisfied can be dispatched.
 Out-of-order or dataflow execution
IF
ID
WB
ALU
Mem
Fadd
Fmul
Issue

## Slide 31: Renaming Structures
Renaming
table &
regfile
Reorder
buffer
Load
Unit
FU
FU
Store
Unit
< t, result >
Ins# use exec op p1 src1 p2 src2
t1
t2
.
.
tn
Instruction template (i.e., tag t) is allocated by the Decode stage, which also associates tag with register in regfile
When an instruction completes, its tag is deallocated
Replacing the
tag by its value
is an expensive
operation

## Slide 32: Reorder Buffer Management
Instruction slot is candidate for execution when:
  It holds a valid instruction (“use” bit is set)
  It has not already started execution (“exec” bit is clear)
  Both operands are available (p1 and p2 are set)
t1
t2
.
.
.
tn
ptr2
next to
deallocate
ptr1
next
available
Ins# use exec op p1 src1 p2 src2
Destination registers are renamed to the instruction’s slot tag
ROB managed circularly
  “exec” bit is set when instruction begins execution
  When an instruction completes its “use” bit is marked free
  ptr2 is incremented only if the “use” bit is marked free

## Slide 33: Renaming & Out-of-order Issue An example
When are tags in sources
replaced by data?
When can a name be reused?
1 FLD f2, 34(x2)
2 FLD f4, 45(x3)
3 FMULT.D f6, f4, f2
4 FSUB.D f8, f2, f2
5 FDIV.D f4, f2, f8
6 FADD.D f10, f6, f4
Renaming table
Reorder buffer
Ins# use exec op p1 src1 p2 src2
t1
t2
t3
t4
t5
.
.
data / ti
p data
f1
f2
f3
f4
f5
f6
f7
f8
Whenever an FU produces data
Whenever an instruction completes
t1
1 1 0 LD
t2
2 1 0 LD
5 1 0 DIV 1 v1 0 t4
4 1 0 SUB 1 v1 1 v1
t4
3 1 0 MUL 0 t2 1 v1
t3
t5
v1
v1
1 1 1 LD
0
4 1 1 SUB 1 v1 1 v1
4 0
v4
5 1 0 DIV 1 v1 1 v4
2 1 1 LD
2 0
3 1 0 MUL 1 v2 1 v1

## Slide 34: IBM 360/91 Floating-Point Unit R. M. Tomasulo, 1967
Mult
1
1
2
3
4
5
6
load
buffers
(from
memory)
1
2
3
4
Adder
1
2
3
Floating-Point
Regfile
store buffers
(to memory)
...
instructions
Common bus ensures that data is made available immediately to all the instructions waiting for it.
Match tag, if equal, copy value & set presence “p”.
Distribute
instruction
templates
by
functional
units
< tag, result >
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
2
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data

## Slide 35: Effectiveness?
Renaming and Out-of-order execution was first
implemented in 1969 in IBM 360/91 but did not show up in the subsequent models until mid-Nineties.
Why ?
Reasons
    1. Effective on a very small class of programs
    2. Memory latency a much bigger problem
    3. Exceptions not precise!
    One more problem needed to be solved
Control transfers

## Slide 36: Acknowledgements
These slides contain material developed and copyright by:
  Arvind (MIT)
  Krste Asanovic (MIT/UCB)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)
MIT material derived from course 6.823
UCB material derived from course CS252