## Slide 1: CS 152 Computer Architecture and Engineering Lecture 1 - Introduction
Dr. George Michelogiannakis
EECS, University of California at Berkeley
CRD, Lawrence Berkeley National Laboratory
http://inst.eecs.berkeley.edu/~cs152

## Slide 2: Pronunciation
Miheloyannakis
(optional)

## Slide 3: What is Computer Architecture?
Application
Physics
Gap too large to bridge in one step
In its broadest definition, computer architecture is the design of the abstraction layers that allow us to implement information processing applications efficiently using available manufacturing technologies.
(but there are exceptions, e.g. magnetic compass)

## Slide 4: What is Computer Architecture?
A set of rules and methods that describe the functionality, organization and implementation of computer systems.
Computer Architecture is the science and art of selecting and interconnecting hardware components to create computers that meet functional, performance and cost goals.
Computer architecture acts as the intermediate between programmers and devices (e.g., VLSI).
What are you here to learn?

## Slide 5: Abstraction Layers in Modern Systems
Algorithm
Gates/Register-Transfer Level (RTL)
Application
Instruction Set Architecture (ISA)
Operating System/Virtual Machines
Microarchitecture
Devices
Programming Language
Circuits
Physics
EE141
CS150
CS162
CS170
CS164
EE143
CS152
UCB EECS Courses

## Slide 6: Architecture Continually Changing
Compatibility
Cost of software development makes compatibility a major force in market
Applications
Technology
Applications suggest how to improve technology, provide revenue to fund development
Improved technologies make new applications possible

## Slide 7: Example: x86 Backwards Compatibility
Intel’s 8086 was released in 1978 with ~50 instructions
Today, x86 has ~650 with all extensions
  Most are rarely emitted by compilers

## Slide 8: Computing Devices Then…
EDSAC, University of Cambridge, UK, 1949

## Slide 9: Computing Devices Now
Robots
Supercomputers
Automobiles
Laptops
Set-top boxes
Smart phones
Servers
Media Players
Sensor Nets
Routers
Cameras
Games

## Slide 10: Moore’s Law
The observation that, over the history of computing hardware, the number of transistors in a dense integrated circuit (chip) has doubled approximately every two years.

## Slide 11: Design Complexity

## Slide 12: Design Capacity
In 1978, Intel could design a chip (8086) with 29,000 transistors
In 2012, 2,104 million (Ivy Bridge)
Rocket (RISC-V) which you’ll be using has 75+ million transistors
Does humanity get smarter with time?

## Slide 13: Computer Architects Then

## Slide 14: Computer Architects Now

## Slide 15: Technology Trends

## Slide 16: Power Dissipation

## Slide 17: Power Wall in Modern Processors
While at the same time chips keep getting larger.
Therefore, not all of the chip can be powered on at the same time

## Slide 18: The End of the Uniprocessor Era
Single biggest change in the history of computing systems

## Slide 19: We Went From This
Cray-1
Single processor

## Slide 20: To This
Titan, an XK7 supercomputer at Oak Ridge National Laboratory (Cray XT3) (299,008 AMD Opteron cores)

## Slide 21: Result: Simple Cores
J. Huh, D.C. Burger, and S.W. Keckler. Exploring the Design Space of Future CMPs.
In International Conference on Parallel Architectures and Compilation Techniques (PACT), September, 2001

## Slide 22: Result: Simple Cores

## Slide 23: Result: Specialization

## Slide 24: Before That: Dennard Scaling
Power = A x C x F x V2
  A: Activity factor
  C: Capacitance
  F: Frequency
  V: Voltage
Capacitance is related to area
  So, as the size of the transistors shrunk, and the voltage was reduced, circuits could operate at higher frequencies at the same power
But leakage current and threshold voltage of transistors set a lower bound for voltage
Transistors get smaller, their power is the same -> Power density increases

## Slide 25: A Little History
Learn from the mistakes of others

## Slide 26: Antikythera Mechanism
Found in a Greek ship believed to have sank around 80 B.C.
It accurately predicted lunar and solar eclipses, as well as solar, lunar and planetary positions
  Size: 8 inches across

## Slide 27: Difference Engine
1855. Can compute any 6th degree polynomial by calculating the difference between 2D matrix elements
Speed: 33 to 44 32-digit numbers per minute!
Now the machine is
at the Smithsonian
n
d2(n)
d1(n)
f(n)
0
41
1
2
2
2
3
2
4
2
4
6
8
43
47
53
61

## Slide 28: Harvard Mark I
Built in 1944 in IBM Endicott laboratories
  Howard Aiken – Professor of Physics at Harvard
  Essentially mechanical but had some electro-magnetically controlled relays and gears
  Weighed 5 tons and had 750,000 components
  A synchronizing clock that beat every 0.015 seconds (66Hz)
  Inspired by Charles Babbage’s analytic engine
Performance:
0.3 seconds for addition
6 seconds for multiplication
1 minute for a sine calculation
Decimal arithmetic
No Conditional Branch!
Broke down once a week!

## Slide 29: Electronic Numerical Integrator and Computer (ENIAC)
Inspired by Atanasoff and Berry, Eckert and Mauchly designed and built ENIAC (1943-45) at the University of Pennsylvania
The first, completely electronic, operational, general-purpose analytical calculator!
  30 tons, 72 square meters, 200KW
Performance
  Read in 120 cards per minute
  Addition took 200 ms, Division 6 ms
  1000 times faster than Mark I
Not very reliable!
Application: Ballistic calculations
angle = f (location, tail wind, cross wind,
air density, temperature, weight of shell,
propellant charge, ... )
WW-2 Effort
Notes: Designers were obliged to install a ventilation shaft and a cooling system in the room. Machine had 18,000 vacuum tubes.
The slogan was: The ENIAC is able to calculate the trajectory of a large-caliber naval shell in less time than the shell takes to reach its target!
To change a program, it was necessary to change the instructions, the connector panels, and the positions of the switches all at the same time.
The inventors of ENIAC themselves admitted that, after taking into account human error, the machine only got the correct result 20 times out of 100!

## Slide 30: Computers in mid 50’s
Hardware was expensive
Store instructions were small (1000 words)
   No resident system software!
Memory access time was 10 to 50 times slower than the processor cycle
   Instruction execution time was totally dominated by the memory reference time.
The ability to design complex control circuits to execute an instruction was the central design concern as opposed to the speed of decoding or an ALU operation
Programmer’s view of the machine was inseparable from the actual hardware implementation
MTBF 20 minutes was state of the art

## Slide 31: Compatibility Problem at IBM
By early 60’s, IBM had 4 incompatible lines of computers!
        701  7094
        650  7074
        702  7080
        1401  7010
Each system had its own
      Instruction set
      I/O system and Secondary Storage:
      magnetic tapes, drums and disks
      assemblers, compilers, libraries,...
      market niche
      business, scientific, real time, ...
 IBM 360

## Slide 32: IBM 360 : Design Premises Amdahl, Blaauw and Brooks, 1964
The design must lend itself to growth and successor machines
General method for connecting I/O devices
Total performance - answers per month rather than bits per microsecond  programming aids
Machine must be capable of supervising itself without manual intervention
Built-in hardware fault checking and locating aids to reduce down time
Simple to assemble systems with redundant I/O devices, memories etc. for fault tolerance
Some problems required floating-point larger than 36 bits

## Slide 33: IBM 360: A General-Purpose Register (GPR) Machine
Processor State
  16 General-Purpose 32-bit Registers
    may be used as index and base register
    Register 0 has some special properties
  4 Floating Point 64-bit Registers
  A Program Status Word (PSW)
    PC, Condition codes, Control flags
A 32-bit machine with 24-bit addresses
  But no instruction contains a 24-bit address!
Data Formats
  8-bit bytes, 16-bit half-words, 32-bit words, 64-bit double-words
The IBM 360 is why bytes are 8-bits long today!

## Slide 34: IBM 360: Initial Implementations
        Model 30 . . . Model 70
Storage 8K - 64 KB 256K - 512 KB
Datapath 8-bit 64-bit
Circuit Delay 30 nsec/level 5 nsec/level
Local Store Main Store Transistor Registers
Control Store Read only 1sec Conventional circuits
IBM 360 instruction set architecture (ISA) completely hid the underlying technological differences between various models.
Milestone: The first true ISA designed as portable hardware-software interface!
With minor modifications it still survives today!

## Slide 35: IBM 360: 47 years later… The zSeries z11 Microprocessor
5.2 GHz in IBM 45nm PD-SOI CMOS technology
1.4 billion transistors in 512 mm2
64-bit virtual addressing
  original S/360 was 24-bit, and S/370 was 31-bit extension
Quad-core design
Three-issue out-of-order superscalar pipeline
Out-of-order memory accesses
Redundant datapaths
  every instruction performed in two parallel datapaths and results compared
64KB L1 I-cache, 128KB L1 D-cache on-chip
1.5MB private L2 unified cache per core, on-chip
On-Chip 24MB eDRAM L3 cache
Scales to 96-core multiprocessor with 768MB of shared L4 eDRAM
[ IBM, HotChips, 2010]

## Slide 36: Storage Devices Also Progressed

## Slide 37: Magnetic Storage Devices
7.25 MB

## Slide 38: Logistics

## Slide 39: Related Courses
CS61C
CS 152
CS 150
Basic computer organization, first look at pipelines + caches
Computer Architecture, First look at parallel architectures
Digital Logic Design, FPGAs
Strong
Prerequisite
CS 250
VLSI Systems Design
CS 252
Graduate Computer Architecture, Advanced Topics

## Slide 40: CS61C vs CS152 vs CS252
CS152 focuses on interaction of software and hardware
  more architecture and less digital engineering
  more useful for OS developers, compiler writers, performance programmers
Much of the material you’ll learn this term was previously in CS252
  Some of the current CS61C was in CS252 over 20 years ago!
  Maybe every 10 years, shift CS252->CS152->CS61C?
CS152 begins where CS61C left off (with overlap)
CS252 delves into more detail and has a research project

## Slide 41: CS152 Executive Summary
The processor you built in CS61C
Plus, the technology behind chip-scale multiprocessors (CMPs) and graphics processing units (GPUs)
What you’ll understand and experiment with in CS152
Notes: Photo is of an Intel Conroe (Core 2 Duo Desktop processor). Photo taken from Intel web site.

## Slide 42: CS152 Structure and Syllabus
Five modules
  Simple machine design (ISAs, microprogramming, unpipelined machines, Iron Law, simple pipelines)
  Memory hierarchy (DRAM, caches, optimizations) plus virtual memory systems, exceptions, interrupts
  Complex pipelining (score-boarding, out-of-order issue)
  Explicitly parallel processors (vector machines, VLIW machines, multithreaded machines)
  Multiprocessor architectures (memory models, cache coherence, synchronization)
Notes: This is the 1st slide of the “Course Structure and Course Philosophy” section of the lecture.
Need to emphasis that for exams, our goal is the test your knowledge. It is not our goal to test how well your perform under time pressure.

## Slide 43: CS152 Administrivia
Instructor: George Michelogiannakis, mihelog@eecs
Office Hours: After lectures, Wednesdays 11-12:30pm 341A Soda
T. A.: Colin Schmidt, colins@eecs
Office Hours: Tuesday 2-4pm 651 Soda
Lectures: M/W, 9-10:30AM, 306 Soda
Section: Th 2PM-4PM, 9 105 Latimer
Text: Computer Architecture: A Quantitative Approach,
Hennessey and Patterson, 5th Edition (2012)
Readings assigned from this edition, some readings available in older editions –see web page.
Web page: http://inst.eecs.berkeley.edu/~cs152
Lectures available online
Piazzza: http://piazza.com/berkeley/spring2016/cs152
Notes: This slide is for the 3-min class administrative matters.
Make sure we update Handout #1 so it is consistent with this slide.

## Slide 44: CS152 Course Components
15% Problem sets (one per module)
  Intended to help you learn the material. Feel free to discuss with other students and instructors, but must turn in your own solutions. Grading based mostly on effort, but quizzes assume that you have worked through all problems. Solutions released after PSs handed in
45% Quizzes (one per module)
  In-class, closed-book, no calculators, no smartphones, no laptops,...
  Based on lectures, readings, problem sets, and labs
40% Labs (one per module)
  Labs use advanced processor and system simulators
  Directed plus open-ended sections to each lab
Sections will review each of the above
Check the website for deadlines!
Sign up for Piazza!

## Slide 45: CS152 Labs
Each lab has directed plus open-ended assignments
Directed portion (2/7) is intended to ensure students learn main concepts behind lab
  Each student must perform own lab and hand in their own lab report
Open-ended assignment (5/7) is to allow you to show your creativity
  Roughly a “mini-project”
    E.g., try an architectural idea and measure potential, or try to improve a design. Negative results OK (if explainable!)
  Students can work individually or in groups of two
  Group open-ended lab reports must be handed in separately (but state who you worked with)
  Students can work in different groups for different assignments
Lab reports must be readable English summaries
Two free two-day extensions per student
You may have to learn scripting languages

## Slide 46: RISC-V ISA
RISC-V is a new simple, clean, extensible ISA we developed at Berkeley for education and research
  RISC-I/II, first Berkeley RISC implementations
  Berkeley research machines SOAR/SPUR considered RISC-III/IV
Both of the dominant ISAs (x86 and ARM) are too complex to use for teaching
RISC-V ISA manual available on web page
  See “resources” on class website
Full GCC-based tool chain available

## Slide 47: Chisel simulators
Chisel is a new hardware description language we developed at Berkeley based on Scala
  Constructing Hardware in a Scala Embedded Language
Labs will use RISC-V processor simulators derived from Chisel processor designs
  Gives you much more detailed information than other simulators
  Can map to FPGA or real chip layout
You need to learn some minimal Chisel in CS152, but we’ll make Chisel RTL source available so you can see all the details of our processors
Can do lab projects based on modifying the Chisel RTL code if desired

## Slide 48: Chisel Design Flow
Chisel Design Description
C++ code
FPGA Verilog
ASIC Verilog
C++ Simulator
C++ Compiler
Chisel Compiler
FPGA Emulation
FPGA Tools
GDS Layout
ASIC Tools

## Slide 49: Familiarity QUIZ

## Slide 50: Pipelined Processor

## Slide 51: Virtual Addresses

## Slide 52: Caches

## Slide 53: Birds Cache (hoard) too!
Same idea. Bring valuable objects close
Acorn Woodpeckers store their food in holes drilled in trees

## Slide 54: In Conclusion
Computer Architecture >> ISAs and RTL
CS152 is about interaction of hardware and software, and design of appropriate abstraction layers
Computer architecture is shaped by technology and applications
  History provides lessons for the future
Computer Science at the crossroads from sequential to parallel computing
  Salvation requires innovation in many fields, including computer architecture
Read Chapter 1 & Appendix A for next time!

## Slide 55: Acknowledgements
These slides contain material developed and copyright by:
  Arvind (MIT)
  Krste Asanovic (MIT/UCB)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)
  Various websites and papers
MIT material derived from course 6.823
UCB material derived from course CS252