## Slide 1: CS 152 Computer Architecture and Engineering Lecture 2 - Simple Machine Implementations, Microcode
Dr. George Michelogiannakis
EECS, University of California at Berkeley
CRD, Lawrence Berkeley National Laboratory
http://inst.eecs.berkeley.edu/~cs152

## Slide 2: Last Time in Lecture 1
Computer Architecture >> ISAs and RTL
  CS152 is about interaction of hardware and software, and design of appropriate abstraction layers
The end of the uniprocessor era
  With simple and specialized cores due to power constraints
Cost of software development becomes a large constraint on architecture (need compatibility)
IBM 360 introduces notion of “family of machines” running same ISA but very different implementations
  Six different machines released on same day (April 7, 1964)
  “Future-proofing” for subsequent generations of machine

## Slide 3: Question of the Day
What purpose does microcode serve today?
  Would we have it if designing ISAs from scatch?
  Why would we want a complex ISA?
  Why do you think motivated CISC and RISC?

## Slide 4: Instruction Set Architecture (ISA)
The contract between software and hardware
Typically described by giving all the programmer-visible state (registers + memory) plus the semantics of the instructions that operate on that state
IBM 360 was first line of machines to separate ISA from implementation (aka. microarchitecture)
Many implementations possible for a given ISA
  E.g., the Soviets build code-compatible clones of the IBM360, as did Amdahl after he left IBM.
  E.g.2., today you can buy AMD or Intel processors that run the x86-64 ISA.
  E.g.3: many cellphones use the ARM ISA with implementations from many different companies including TI, Qualcomm, Samsung, Marvell, etc.

## Slide 5: Name a Famous ISA!
Intel’s x86 was initially deployed in 1978
Is alive and well today, though larger
Reference manual has 3883 pages!

## Slide 6: Implementations of the x86
Hundreds of different processors implement x86
  Not just by Intel
Some have extensions that compilers can use if available
  But software still compatible if not
More than just intel develop x86
  X86-64 was first specified by AMD in 2000

## Slide 7: ISA to Microarchitecture Mapping
ISA often designed with particular microarchitectural style in mind, e.g.,
    Accumulator  hardwired, unpipelined
    CISC  microcoded
    RISC  hardwired, pipelined
    VLIW  fixed-latency in-order parallel pipelines
    JVM  software interpretation
But can be implemented with any microarchitectural style
    Intel Ivy Bridge: hardwired pipelined CISC (x86) machine (with some microcode support)
    Simics: Software-interpreted SPARC RISC machine
    ARM Jazelle: A hardware JVM processor
    This lecture: a microcoded RISC-V machine

## Slide 8: Today, Microprogramming
To show how to build very small processors with complex ISAs
To help you understand where CISC* machines came from
Because still used in common machines (IBM360, x86, PowerPC)
As a gentle introduction into machine structures
To help understand how technology drove the move to RISC*
  * “CISC”/”RISC” names much newer than style of machines they refer to.

## Slide 9: Problem Microprogramming Solves
Complex ISA to ease programmer and assembler’s life
  With instructions that have multiple steps
Simple processors such as in order to meet power constraints
  (refer to previous lecture)
Turn complex architecture into simple microarchitecture with programmable control
Can also patch microcode

## Slide 10: The Idea
An ISA (assembly) instruction, is not what drives the processor’s datapath directly
Instead, instructions are broken down to FSM states
Each state is a microinstruction and outputs control signals

## Slide 11: Microarchitecture: Bus-Based Implementation of ISA
Structure: How components are connected.
Static
Behavior: How data moves between components
Dynamic
Controller
Data
path
Control
Points
Status
lines

## Slide 12: Microcontrol Unit Maurice Wilkes, 1954
Embed the control logic state table in a memory array
First used in EDSAC-2, completed 1958
Matrix A
Matrix B
Decoder
Next state
op conditional
code flip-flop
µaddress
Control lines to
ALU, MUXs, Registers
Memory

## Slide 13: Microcoded Microarchitecture
Memory
(RAM)
Datapath
mcontroller
(ROM)
Addr
Data
zero?
busy?
opcode
enMem
MemWrt
holds fixed
microcode instructions
holds user program written in macrocode instructions (e.g., x86, RISC-V, etc.)

## Slide 14: RISC-V ISA
RISC design from UC Berkeley
Realistic & complete ISA, but open & simple
Not over-architected for a certain implementation style
Both 32-bit and 64-bit address space variants
  RV32 and RV64
Easy to subset/extend for education/research
  RV32IM, RV32IMA, RV32IMAFD, RV32G
Techreport with RISC-V spec available on class website or riscv.org
We’ll be using 32-bit and 64-bit RISC-V this semester in lectures and labs. Similar to MIPS you saw in CS61C

## Slide 15: RV32 Processor State
Program counter (pc)
32x32-bit integer registers (x0-x31)
x0 always contains a 0
32 floating-point (FP) registers (f0-f31)
each can contain a single- or double-precision FP value (32-bit or 64-bit IEEE FP)
Is an extension
FP status register (fsr), used for FP rounding mode & exception reporting
Notes: There is no hardwired subroutine return address link register, but the standard software calling convention
uses register x1 to hold the return address on a call.

## Slide 16: RISC-V Instruction Encoding
Base instruction set (RV32) always has fixed 32-bit instructions lowest two bits = 112
All branches and jumps have targets at 16-bit granularity (even in base ISA where all instructions are fixed 32 bits)
  Still will cause a fault if fetching a 32-bit instruction

## Slide 17: Four Core RISC-V Instruction Formats
Destination Reg.
Reg. Source 1
Reg. Source 2
7-bit opcode field (but low 2 bits =112)
Additional opcode bits/immediate
Aligned on a four-byte boundary in memory. There are variants!
Sign bit of immediates always on bit 31 of instruction. Register fields never move

## Slide 18: With Variants

## Slide 19: Integer Computational Instructions
I-type
ADDI: adds sign extended 12-bit immediate to rs1
  Actually, all immediates in all instructions are sign extended
SLTI(U): set less than immediate
Shift instructions, etc…
Notes: SLTIU: Same as SLTI but compares immediate as unsigned.

## Slide 20: Integer Computational Instructions
R-type
Rs1 and rs2 are the source registers. Rd the destination
SLT, SLTU: set less than
SRL, SLL, SRA: shift logical or arithmetic left or right
Notes: SLTIU: Same as SLTI but compares immediate as unsigned.

## Slide 21: S-Type
12-bit signed immediate split across two fields
Branches, compare two registers, PC+(immediate<<1) target
(Signed offset in multiples of two).Branches do not have delay slot

## Slide 22: UJ-Type
“J” Unconditional jump, PC+offset target
“JAL” Jump and link, also writes PC+4 to x1
Offset scaled by 1-bit left shift – can jump to 16-bit instruction boundary (Same for branches)
Also “JALR” where Imm (12 bits) + rd1 = target

## Slide 23: L-Type
Writes 20-bit immediate to top of destination register.
Used to build large immediates.
12-bit immediates are signed, so have to account for sign when building 32-bit immediates in 2-instruction sequence (LUI high-20b, ADDI low-12b)

## Slide 24: Loads and Stores
Store instructions (S-type). Loads (I-type).
(rs1 + immediate) addressing
Store only uses rs1 and rs2. Rd is only present when being written to

## Slide 25: Where is NOP?
addi x0, x0, 0

## Slide 26: Data Formats and Memory Addresses
Data formats:
8-b Bytes, 16-b Half words, 32-b words and 64-b double words
Some issues
Byte addressing
Word alignment
  Suppose the memory is organized in 32-bit words.
  Can a word address begin only at 0, 4, 8, .... ?
0 1 2 3 4 5 6 7
Most Significant Byte
Least Significant Byte
Byte Addresses
3
2
1
0
0
1
2
3
Big Endian
Little Endian (RISC-V)
Notes: Memory is addressed in words (32 bits).

## Slide 27: Back to MICROCODING

## Slide 28: A Bus-based Datapath for RISC-V
Microinstruction: register to register transfer (17 control signals)
MA <= PC means RegSel = PC; enReg=yes; ldMA= yes
  B <= Reg[rs2] means
enMem
MA
addr
data
ldMA
Memory
busy
MemWrt
Bus
32
zero?
A
B
ALUOp
ldA
ldB
ALU
enALU
RegWrt
enReg
addr
data
rs1
rs2
rd
32(PC)
RegSel
32 GPRs
+ PC ...
32-bit Reg
3
rs1
rs2
rd
ImmSel
IR
Opcode
ldIR
Immed
Select
enImm
3
RegSel = rs2; enReg=yes; ldB = yes

## Slide 29: Memory Module
Assumption: Memory operates independently
and is slow as compared to Reg-to-Reg transfers (multiple CPU clock cycles per access)
Enable
Write(1)/Read(0)
RAM
din
dout
we
addr
busy
bus

## Slide 30: Instruction Execution
Execution of a RISC-V instruction involves:
    1. instruction fetch
    2. decode and register fetch
    3. ALU operation
    4. memory operation (optional)
    5. write back to register file (optional)
    + the computation of the
    next instruction address

## Slide 31: Microprogram Fragments
instr fetch: MA, A <= PC
      PC <= A + 4
      IR <= Memory
      dispatch on Opcode
can be
treated as
a macro
ALU: A <= Reg[rs1]
      B <= Reg[rs2]
      Reg[rd] <= func(A,B)
      do instruction fetch
ALUi: A <= Reg[rs1]
      B <= Imm sign extension
      Reg[rd] <= Opcode(A,B)
      do instruction fetch

## Slide 32: Microprogram Fragments (cont.)
A <= Reg[rs1]
      B <= Imm
      MA <= A + B
      Reg[rd] <= Memory
      do instruction fetch
A <= A - 4 Get original PC back in A
      B <= IR
      PC <= JumpTarg(A,B)
      do instruction fetch
A <= Reg[rs1]
B <= Reg[rs2]
If A==B then go to bz-taken
do instruction fetch
A <= PC
A <= A - 4 Get original PC back in A
      B <= BImm << 1 BImm = IR[31:27,16:10]
      PC <= A + B
      do instruction fetch
JumpTarg(A,B) =
{A + (B[31:7]<<1)}
LW:
J: (JAL with rd=x0)
beq:
bz-taken:

## Slide 33: RISC-V Microcontroller: first attempt pure ROM implementation
next state
PC (state)
Opcode
zero?
Busy (memory)
Control Signals (17)
s
s
7
Program ROM
addr
data
= 2(opcode+sbits) words
How big is “s”?
ROM size ?
Word size ?
= control+s bits

## Slide 34: Microprogram in the ROM worksheet
State Op zero? busy Control points next-state
fetch0 * * * MA,A <= PC fetch1
fetch1 * * yes .... fetch1
fetch1 * * no IR <= Memory fetch2
fetch2 * * * PC <= A + 4 ?
ALU0 * * * A <= Reg[rs1] ALU1
ALU1 * * * B <= Reg[rs2] ALU2
ALU2 * * * Reg[rd] <= func(A,B) fetch0
fetch2 ALU * * PC <= A + 4 ALU0
Notes: Why the one cycle stall during fetch 1? Why ALU0 and ALU1 are separate states (load registers in separate cycles)?

## Slide 35: Microprogram in the ROM
State Op zero? busy Control points next-state
fetch0 * * * MA,A <= PC fetch1
fetch1 * * yes .... fetch1
fetch1 * * no IR <= Memory fetch2
fetch2 ALU * * PC <= A + 4 ALU0
fetch2 ALUi * * PC <= A + 4 ALUi0
fetch2 LW * * PC <= A + 4 LW0
fetch2 SW * * PC <= A + 4 SW0
fetch2 J * * PC <= A + 4 J0
fetch2 JAL * * PC <= A + 4 JAL0
fetch2 JR * * PC <= A + 4 JR0
fetch2 JALR * * PC <= A + 4 JALR0
fetch2 beq * * PC <= A + 4 beq0
...
ALU0 * * * A <= Reg[rs1] ALU1
ALU1 * * * B <= Reg[rs2] ALU2
ALU2 * * * Reg[rd] <= func(A,B) fetch0

## Slide 36: Microprogram in the ROM Cont.
State Op zero? busy Control points next-state
ALUi0 * * * A <= Reg[rs1] ALUi1
ALUi1 * * * B <= Imm ALUi2
ALUi2 * * * Reg[rd]<= Op(A,B) fetch0
...
J0 * * * A <= A - 4 J1
J1 * * * B <= IR J2
J2 * * * PC <= JumpTarg(A,B) fetch0
...
beq0 * * * A <= Reg[rs1] beq1
beq1 * * * B <= Reg[rs2] beq2
beq2 * yes * A <= PC beq3
beq2 * no * .... fetch0
beq3 * * * A <= A - 4 beq4
beq4 * * * B <= BImm beq5
beq5 * * * PC <= A+B fetch0
...

## Slide 37: Size of Control Store
RISC-V: w = 5+2 c = 17 s = ?
  no. of steps per opcode = 4 to 6 + fetch-sequence
  no. of states ~= (4 steps per op-group ) x op-groups
  + common sequences
  = 4 x 8 + 10 states = 42 states => s = 6
Control ROM = 2(5+6) x 23 bits approx. 24 Kbytes
size = 2(w+s) x (c + s)
Control ROM
data
status & opcode
addr
next μPC
Control signals
μPC
/
w
/ s
/ c

## Slide 38: Reducing Control Store Size
Reduce the ROM height (= address bits)
    reduce inputs by extra external logic
        each input bit doubles the size of the
        control store
    reduce states by grouping opcodes
        find common sequences of actions
    condense input status bits
        combine all exceptions into one, i.e.,
        exception/no-exception
Reduce the ROM width
    restrict the next-state encoding
        Next, Dispatch on opcode, Wait for memory, ...
    encode control signals (vertical microcode)
Control store has to be fast => expensive

## Slide 39: RISC-V Controller V2
μJumpType =
next | spin
| fetch | dispatch
| ftrue | ffalse
Control Signals (17)
Control ROM
address
data
+1
Opcode
ext
μPC (state)
jump
logic
zero
μPC
μPC+1
absolute
op-group
busy
μPCSrc
input encoding reduces ROM height
next-state encoding reduces ROM width

## Slide 40: Jump Logic
μPCSrc = Case μJumpTypes
  next => μPC+1
  spin => if (busy) then μPC else μPC+1
  fetch => absolute
  dispatch => op-group
  ftrue => if (zero) then absolute else μPC+1
  ffalse => if (zero) then μPC+1 else absolute

## Slide 41: Instruction Fetch & ALU: RISC-V-Controller-2
State Control points next-state
fetch0 MA,A <= PC
fetch1 IR <= Memory
fetch2 PC <= A + 4
...
ALU0 A <= Reg[rs1]
ALU1 B <= Reg[rs2]
ALU2 Reg[rd]<=func(A,B)
ALUi0 A <= Reg[rs1]
ALUi1 B <= Imm
ALUi2 Reg[rd]<= Op(A,B)
next
spin
dispatch
next
next
fetch
next
next
fetch

## Slide 42: Load & Store: RISC-V-Controller-2
State Control points next-state
LW0 A <= Reg[rs1] next
LW1 B <= Imm next
LW2 MA <= A+B next
LW3 Reg[rd] <= Memory spin
LW4 fetch
SW0 A <= Reg[rs1] next
SW1 B <= BImm next
SW2 MA <= A+B next
SW3 Memory <= Reg[rs2] spin
SW4 fetch

## Slide 43: Branches: RISC-V-Controller-2
State Control points next-state
beq0 A <= Reg[rs1] next
beq1 B <= Reg[rs2] next
beq2 A <= PC ffalse
beq3 A <= A- 4 next
beq3 B <= BImm<<1 next
beq4 PC <= A+B fetch

## Slide 44: Jumps: RISC-V-Controller-2
State Control points next-state
JALR0 A <= Reg[rs1] next
JALR1 Reg[1] <= A next
JALR2 PC <= A fetch
JAL0 A <= PC next
JAL1 Reg[1] <= A next
JAL2 A <= A-4 next
JAL3 B <= IR next
JAL4 PC <= JumpTarg(A,B) fetch
J and JR are special cases with rd = x0

## Slide 45: VAX 11-780 Microcode

## Slide 46: Implementing Complex Instructions
enMem
MA
addr
data
ldMA
Memory
busy
MemWrt
Bus
32
zero?
A
B
ALUOp
ldA
ldB
ALU
enALU
RegWrt
enReg
addr
data
rs1
rs2
rd
32(PC)
RegSel
32 GPRs
+ PC ...
32-bit Reg
3
rs1
rs2
rd
ImmSel
IR
Opcode
ldIR
Immed
Select
enImm
3
rd <= M[(rs1)] op (rs2) Reg-Memory-src ALU op
M[(rd)] <= (rs1) op (rs2) Reg-Memory-dst ALU op
M[(rd)] <= M[(rs1)] op M[(rs2)] Mem-Mem ALU op

## Slide 47: Mem-Mem ALU Instructions: RISC-V-Controller-2
Mem-Mem ALU op M[(rd)] <= M[(rs1)] op M[(rs2)]
  ALUMM0 MA <= Reg[rs1] next
  ALUMM1 A <= Memory spin
  ALUMM2 MA <= Reg[rs2] next
  ALUMM3 B <= Memory spin
  ALUMM4 MA <=Reg[rd] next
  ALUMM5 Memory <= func(A,B) spin
  ALUMM6 fetch
Complex instructions usually do not require datapath modifications in a microprogrammed implementation
-- only extra space for the control program
Implementing these instructions using a hardwired controller is difficult without datapath modifications

## Slide 48: Performance Issues
Microprogrammed control
=> multiple cycles per instruction
Cycle time ?
  tC > max(treg-reg, tALU, tROM)
Suppose 10 * tμROM < tRAM
  Good performance, relative to a single-cycle
  hardwired implementation, can be achieved
  even with a CPI of 10

## Slide 49: Horizontal vs Vertical mCode
Horizontal mcode has wider minstructions
  Multiple parallel operations per minstruction
  Fewer microcode steps per macroinstruction
  Sparser encoding  more bits
Vertical mcode has narrower minstructions
  Typically a single datapath operation per minstruction
      separate minstruction for branches
  More microcode steps per macroinstruction
  More compact  less bits
Nanocoding
  Tries to combine best of horizontal and vertical mcode
# µInstructions
Bits per µInstruction

## Slide 50: Nanocoding
MC68000 had 17-bit µcode containing either 10-bit µjump or 9-bit nanoinstruction pointer
  Nanoinstructions were 68 bits wide, decoded to give 196 control signals
µcode ROM
nanoaddress
µcode
next-state
µaddress
μPC (state)
nanoinstruction ROM
data
Exploits recurring control signal patterns in µcode, e.g.,
ALU0 A <= Reg[rs1]
...
ALUi0 A <= Reg[rs1]
...

## Slide 51: Microprogramming in IBM 360
Only the fastest models (75 and 95) were hardwired
 | M30 | M40 | M50 | M65
Datapath width (bits) | 8 | 16 | 32 | 64
µinst width (bits) | 50 | 52 | 85 | 87
µcode size (K µinsts) | 4 | 4 | 2.75 | 2.75
µstore technology | CCROS | TCROS | BCROS | BCROS
µstore cycle (ns) | 750 | 625 | 500 | 200
memory cycle (ns) | 1500 | 2500 | 2000 | 750
Rental fee ($K/month) | 4 | 7 | 15 | 35

## Slide 52: IBM Card Capacitor Read-Only Storage
[ IBM Journal, January 1961]
Punched Card with metal film
Fixed sensing plates

## Slide 53: Microcode Emulation
IBM initially miscalculated the importance of software compatibility with earlier models when introducing the 360 series
Honeywell stole some IBM 1401 customers by offering translation software (“Liberator”) for Honeywell H200 series machine
IBM retaliated with optional additional microcode for 360 series that could emulate IBM 1401 ISA, later extended for IBM 7000 series
  one popular program on 1401 was a 650 simulator, so some customers ran many 650 programs on emulated 1401s
  (650 simulated on 1401 emulated on 360)

## Slide 54: Microprogramming thrived in the Seventies
Significantly faster ROMs than DRAMs were available
For complex instruction sets, datapath and controller were cheaper and simpler
New instructions , e.g., floating point, could be supported without datapath modifications
Fixing bugs in the controller was easier
ISA compatibility across various models could be achieved easily and cheaply
Except for the cheapest and fastest machines, all computers were microprogrammed

## Slide 55: Writable Control Store (WCS)
Implement control store in RAM not ROM
  MOS SRAM memories now almost as fast as control store (core memories/DRAMs were 2-10x slower)
  Bug-free microprograms difficult to write
User-WCS provided as option on several minicomputers
  Allowed users to change microcode for each processor
User-WCS failed
  Little or no programming tools support
  Difficult to fit software into small space
  Microcode control tailored to original ISA, less useful for others
  Large WCS part of processor state - expensive context switches
  Protection difficult if user can change microcode
  Virtual memory required restartable microcode

## Slide 56: Microprogramming is far from extinct
Played a crucial role in micros of the Eighties
    DEC uVAX, Motorola 68K series, Intel 286/386
Plays an assisting role in most modern micros
  e.g., AMD Bulldozer, Intel Ivy Bridge, Intel Atom, IBM PowerPC, …
  Most instructions executed directly, i.e., with hard-wired control
  Infrequently-used and/or complicated instructions invoke microcode
Patchable microcode common for post-fabrication bug fixes, e.g. Intel processors load µcode patches at bootup
  Intel released microcode updates in 2014 and 2015

## Slide 57: Question of the Day
What purpose does microcode serve today?
  Would we have it if designing ISAs from scatch?
  Why would we want a complex ISA?
  Why do you think motivated CISC and RISC?