## Slide 1: CS 152 Computer Architecture and Engineering Lecture 7 - Memory Hierarchy-II
Dr. George Michelogiannakis
EECS, University of California at Berkeley
CRD, Lawrence Berkeley National Laboratory
http://inst.eecs.berkeley.edu/~cs152

## Slide 2: Logistics
PS 1 is due NOW
Lab 1 also due now unless you are using one of your two extensions
PS 2 is out
Lab 2 will be out
Quiz Wednesday next week this room and time
  SHOW UP ON TIME

## Slide 3: Last time in Lecture 6
Dynamic RAM (DRAM) is main form of main memory storage in use today
  Holds values on small capacitors, need refreshing (hence dynamic)
  Slow multi-step access: precharge, read row, read column
Static RAM (SRAM) is faster but more expensive
  Used to build on-chip memory for caches
Cache holds small set of values in fast memory (SRAM) close to processor
  Need to develop search scheme to find values in cache, and replacement policy to make space for newly accessed locations
Caches exploit two forms of predictability in memory reference streams
  Temporal locality, same location likely to be accessed again soon
  Spatial locality, neighboring location likely to be accessed soon
Miss rate1 x Miss penalty1

## Slide 4: Question of the Day
If you had a limited area/power budget, would you invest it in larger caches or a prefetcher?

## Slide 5: Line Size and Spatial Locality
Word3
Word0
Word1
Word2
Larger line size has distinct hardware advantages
  less tag overhead
  exploit fast burst transfers from DRAM
  exploit fast burst transfers over wide busses
What are the disadvantages of increasing line size?
Line Address
2b = line size a.k.a line size (in bytes)
Split CPU address
b bits
32-b bits
Tag
A line is unit of transfer between the cache and memory
4 word line, b=2
Fewer lines => more conflicts. Can waste bandwidth.
Offset
Notes: Larger line size will reduce compulsory misses (first miss to a line).
Larger lines may increase conflict misses since the number of lines
is smaller.

## Slide 6: Direct-Mapped Cache
Tag
Data
V
=
Offset
Tag
Index
t
k
b
t
HIT
Data Word or Byte
2k
lines

## Slide 7: 2-Way Set-Associative Cache
Tag
Data
V
=
Offset
Tag
Index
t
k
b
HIT
Tag
Data
V
Data
Word
or Byte
=
t
Notes: Compare latency to direct mapped case? (jse)

## Slide 8: Fully Associative Cache
Tag
Data
V
=
Offset
Tag
t
b
HIT
Data
Word
or Byte
=
=
t

## Slide 9: Replacement Policy
In an associative cache, which line from a set should be evicted when the set becomes full?
Random
Least-Recently Used (LRU)
  LRU cache state must be updated on every access
  True implementation only feasible for small sets (2-way)
  Pseudo-LRU binary tree often used for 4-8 way
First-In, First-Out (FIFO) a.k.a. Round-Robin
  Used in highly associative caches
Not-Most-Recently Used (NMRU)
  FIFO with exception for most-recently used line or lines
Notes: NLRU used in Alpha TLBs (jse)

## Slide 10: CPU-Cache Interaction Caches instead of memory blocks (5-stage pipeline)
PC
addr
inst
Primary
Instruction
Cache
0x4
Add
IR
D
bubble
hit?
  PCen
Decode,
Register
Fetch
wdata
R
addr
wdata
rdata
Primary
Data
Cache
we
A
B
Y
Y
ALU
MD1
MD2
Cache Refill Data from Lower Levels of Memory Hierarchy
hit?
Stall entire CPU on data cache miss
To Memory Control
M
E
Notes: How are writes to istream handled?

## Slide 11: AMAT
Average memory access time (AMAT) =
Hit time + Miss rate x Miss penalty
Average memory access time (AMAT) =
Hit time + Miss rate1 x Miss penalty1 +
Miss rate2 x Miss penalty2
Notes: Design the largest primary cache without slowing down the clock
Or adding pipeline stages.

## Slide 12: Improving Cache Performance
Average memory access time (AMAT) =
Hit time + Miss rate x Miss penalty
To improve performance:
  reduce the hit time
  reduce the miss rate
  reduce the miss penalty
What is best cache design for 5-stage pipeline?
Biggest cache that doesn’t increase hit time past 1 cycle (approx 8-32KB in modern technology)
[ design issues more complex with deeper pipelines and/or out-of-order superscalar processors]
Notes: Design the largest primary cache without slowing down the clock
Or adding pipeline stages.

## Slide 13: Causes of Cache Misses: The 3 C’s
Compulsory:
first reference to a line (a.k.a. cold start misses)
  misses that would occur even with infinite cache
Capacity:
cache is too small to hold all data needed by the program
  misses that would occur even under perfect replacement policy
Conflict:
misses that occur because of collisions due to line-placement strategy
  misses that would not occur with ideal full associativity

## Slide 14: Effect of Cache Parameters on Performance
Larger cache size
  reduces capacity and conflict misses
  hit time will increase
Higher associativity
  reduces conflict misses
  may increase hit time
Larger line size
  reduces compulsory and capacity (reload) misses
  increases conflict misses and miss penalty
Notes: Requested line first….
The following could be in the slide…
spatial locality reduces compulsory misses and capacity reload misses
  fewer lines may increase conflict miss rate
  larger lines may increase miss penalty

## Slide 15: What About Writes?
If a write enters the cache, what happens if
  There is a cache miss
    Does the cache need to bring in the cache line?
  There is a cache hit
    Does the cache need to write back to memory?

## Slide 16: Write Policy Choices
Cache hit:
  write through: write both cache & memory
    Generally higher traffic but simpler pipeline & cache design
  write back: write cache only, memory is written only when the entry is evicted
    A dirty bit per line further reduces write-back traffic
    Must handle 0, 1, or 2 accesses to memory for each load/store
Cache miss:
  no write allocate: only write to main memory
  write allocate (aka fetch on write): fetch into cache
Common combinations:
  write through and no write allocate
  write back with write allocate

## Slide 17: Write Performance
Tag
Data
V
=
Offset
Tag
Index
t
k
b
t
HIT
Data Word or Byte
2k
lines
WE
When is the result of the tag check known?
Notes: Completely serial (jse)

## Slide 18: Reducing Write Hit Time
Problem: Writes take two cycles in memory stage, one cycle for tag check plus one cycle for data write if hit
Solutions:
Design data RAM that can perform read and write in one cycle, restore old value after tag miss
Fully-associative (CAM Tag) caches: Word line only enabled if hit
Pipelined writes: Hold write data for store in single buffer ahead of cache, write cache data during next store’s tag check
Notes: Need to bypass from write buffer if read address matches write buffer tag!

## Slide 19: Pipelining Cache Writes
Tags
Data
Tag
Index
Store Data
Address and Store Data From CPU
Delayed Write Data
Delayed Write Addr.
=?
=?
Load Data to CPU
Load/Store
L
S
1
0
Hit?
Data from a store hit written into data portion of cache during tag access of subsequent store
Notes: The load path shown is to cover the case that a store is followed by a load.

## Slide 20: Write Buffer to Reduce Read Miss Penalty
Processor is not stalled on writes, and read misses can go ahead of write to main memory
Problem: Write buffer may hold updated value of location needed by a read miss
Simple solution: on a read miss, wait for the write buffer to go empty
Faster solution: Check write buffer addresses against read miss addresses, if no match, allow read miss to go ahead of writes, else, return value in write buffer
Data Cache
Unified L2 Cache
RF
CPU
Write
buffer
Evicted dirty lines for writeback cache
OR
All writes in writethrough cache
Notes: Deisgners of the MIPS M/1000 estimated that waiting for a four-word buffer to empty
increased the read miss penalty by a factor of 1.5.

## Slide 21: Reducing Tag Overhead with Sub-Blocks
Problem: Tags are too large, i.e., too much overhead
  Simple solution: Larger lines, but miss penalty could be large.
Solution: Sub-block placement (aka sector cache)
  A valid bit added to units smaller than full line, called sub-blocks
  Only read a sub-block on a miss
  If a tag matches, is the word in the cache?
100
300
204
1 1 1 1
1 0 0
0 1 0 1
Notes: Main reason for subblock placement is to reduce tag overhead.
Sector cache (jse)

## Slide 22: Multilevel Caches
Problem: A memory cannot be large and fast
Solution: Increasing sizes of cache at each level
CPU
L1$
L2$
DRAM
Local miss rate = misses in cache / accesses to cache
Global miss rate = misses in cache / CPU memory accesses
Misses per instruction = misses in cache / number of instructions
Notes: MPI makes it easier to compute overall performance (jse)

## Slide 23: Presence of L2 influences L1 design
Size?
Use smaller L1 if there is also L2
  Trade increased L1 miss rate for reduced L1 hit time
  Backup L2 reduces L1 miss penalty
  Reduces average access energy
Write through versus write back?
Use simpler write-through L1 with on-chip L2
  Write-back L2 cache absorbs write traffic, doesn’t go off-chip
  At most one L1 miss request per L1 access (no dirty victim write back) simplifies pipeline control
  Simplifies coherence issues
  Simplifies error recovery in L1 (can use just parity bits in L1 and reload from L2 when parity error detected on L1 read)

## Slide 24: Inclusion Policy
Inclusive multilevel cache:
  Inner cache can only hold lines also present in outer cache
  External coherence snoop access need only check outer cache
Exclusive multilevel caches:
  Inner cache may hold lines not in outer cache
  Swap lines between inner/outer caches on miss
  Used in AMD Athlon with 64KB primary and 256KB secondary cache
Why choose one type or the other?
Notes: New slide (jse)

## Slide 25: Itanium-2 On-Chip Caches (Intel/HP, 2002)
Level 1: 16KB, 4-way s.a., 64B line, quad-port (2 load+2 store), single cycle latency
Level 2: 256KB, 4-way s.a, 128B line, quad-port (4 load or 4 store), five cycle latency
Level 3: 3MB, 12-way s.a., 128B line, single 32B port, twelve cycle latency
Notes: If two is good, then three must be better (jse)

## Slide 26: Power 7 On-Chip Caches [IBM 2009]
32KB L1 I$/core
32KB L1 D$/core
3-cycle latency
256KB Unified L2$/core
8-cycle latency
32MB Unified Shared L3$
Embedded DRAM (eDRAM)
25-cycle latency to local slice

## Slide 27: IBM z196 Mainframe Caches 2010
96 cores (4 cores/chip, 24 chips/system)
  Out-of-order, 3-way superscalar @ 5.2GHz
L1: 64KB I-$/core + 128KB D-$/core
L2: 1.5MB private/core (144MB total)
L3: 24MB shared/chip (eDRAM) (576MB total)
L4: 768MB shared/system (eDRAM)

## Slide 28: Prefetching
Speculate on future instruction and data accesses and fetch them into cache(s)
  Instruction accesses easier to predict than data accesses
Varieties of prefetching
  Hardware prefetching
  Software prefetching
  Mixed schemes
What types of misses does prefetching affect?
Notes: Reduces compulsory misses, can increase conflict and
capacity misses.

## Slide 29: Issues in Prefetching
Usefulness – should produce hits (i.e., what data)
Timeliness – not late and not too early (i.e., when)
Cache and bandwidth pollution
L1 Data
L1 Instruction
Unified L2 Cache
RF
CPU
Prefetched data

## Slide 30: Hardware Instruction Prefetching
Notes: Need to check the stream buffer if the requested line is in there.
Never more than one 32-byte line in the stream buffer.

## Slide 31: Hardware Instruction Prefetching
Instruction prefetch in Alpha AXP 21064
  Fetch two lines on a miss; the requested line (i) and the next consecutive line (i+1)
  Requested line placed in cache, and next line in instruction stream buffer
  If miss in cache but hit in stream buffer, move stream buffer line into cache and prefetch next line (i+2)
L1 Instruction
Unified L2 Cache
RF
CPU
Stream
Buffer
Prefetched
instruction line
Req
line
Req
line
Notes: Need to check the stream buffer if the requested line is in there.
Never more than one 32-byte line in the stream buffer.

## Slide 32: Hardware Data Prefetching
Prefetch-on-miss:
  Prefetch b + 1 upon miss on b
One-Block Lookahead (OBL) scheme
  Initiate prefetch for block b + 1 when block b is accessed
  Why is this different from doubling block size?
  Can extend to N-block lookahead
Strided prefetch
  If observe sequence of accesses to line b, b+N, b+2N, then prefetch b+3N etc.
Probablistic prefetching (Markov prefetching)
Example: IBM Power 5 [2003] supports eight independent streams of strided prefetch per processor, prefetching 12 lines ahead of current access
Notes: HP PA 7200 uses OBL prefetching
Tag prefetching is twice as effective as prefetch-on-miss in
reducing miss rates.

## Slide 33: Where to Put Prefetched Data
Inside the cache, or in a separate prefetch buffer
Why would we want to do this?
Also, what about interaction of prefetching and replacement policy?

## Slide 34: Software Prefetching
  for(i=0; i < N; i++) { prefetch( &a[i + 1] ); prefetch( &b[i + 1] ); SUM = SUM + a[i] * b[i]; }
Notes: Cache should be non-blocking or lockup-free.
By that we mean that the processor can proceed while the prefetched
Data is being fetched; and the caches continue to supply instructions
And data while waiting for the prefetched data to return.

## Slide 35: Software Prefetching Issues
Timing is the biggest issue, not predictability
  If you prefetch very close to when the data is required, you might be too late
  Prefetch too early, cause pollution
  Estimate how long it will take for the data to come into L1, so we can set P appropriately
  Why is this hard to do?
  for(i=0; i < N; i++) { prefetch( &a[i + P] ); prefetch( &b[i + P] ); SUM = SUM + a[i] * b[i]; }
Must consider cost of prefetch instructions

## Slide 36: Compiler Optimizations
Restructuring code affects the data access sequence
  Group data accesses together to improve spatial locality
  Re-order data accesses to improve temporal locality
Prevent data from entering the cache
  Useful for variables that will only be accessed once before being replaced
  Needs mechanism for software to tell hardware not to cache data (“no-allocate” instruction hints or page table bits)
Kill data that will never be used again
  Streaming data exploits spatial locality but not temporal locality
  Replace into dead cache locations
Notes: Miss-rate reduction without any hardware changes.
Hardware designer’s favorite solution.

## Slide 37: Loop Interchange
  for(j=0; j < N; j++) { for(i=0; i < M; i++) { x[i][j] = 2 * x[i][j]; } }
  for(i=0; i < M; i++) { for(j=0; j < N; j++) { x[i][j] = 2 * x[i][j]; } }
What type of locality does this improve?
Notes: Spatial

## Slide 38: Loop Fusion
  for(i=0; i < N; i++) a[i] = b[i] * c[i];
  for(i=0; i < N; i++)
  d[i] = a[i] * c[i];
  for(i=0; i < N; i++) { a[i] = b[i] * c[i]; d[i] = a[i] * c[i];
  }
What type of locality does this improve?
Notes: Temporal

## Slide 39: Matrix Multiply, Naïve Code
  for(i=0; i < N; i++) for(j=0; j < N; j++) { r = 0; for(k=0; k < N; k++) r = r + y[i][k] * z[k][j]; x[i][j] = r; }
Not touched
Old access
New access
x
j
i
y
k
i
z
j
k

## Slide 40: Matrix Multiply with Cache Tiling
  for(jj=0; jj < N; jj=jj+B) for(kk=0; kk < N; kk=kk+B) for(i=0; i < N; i++) for(j=jj; j < min(jj+B,N); j++) { r = 0; for(k=kk; k < min(kk+B,N); k++) r = r + y[i][k] * z[k][j]; x[i][j] = x[i][j] + r; }
What type of locality does this improve?
Assuming row-major order
y
k
i
z
j
k
x
j
i
Notes: Y benefits from spatial locality
z benefits from temporal locality
For a given loop break it up into multiple loops. So instead loop into the first tile and then do the second tile.
B is the blocking factor. N/2. For each block, the inner loop sweeps over that block.
With the loop inversion it changes the access order to get better locality.
Reduce the working set.

## Slide 41: Question of the Day
If you had a limited area/power budget, would you invest it in larger caches or a prefetcher?

## Slide 42: Acknowledgements
These slides contain material developed and copyright by:
  Arvind (MIT)
  Krste Asanovic (MIT/UCB)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)
MIT material derived from course 6.823
UCB material derived from course CS252