## Slide 1: CS 152 Computer Architecture and Engineering Lecture 8 - Address Translation
Dr. George Michelogiannakis
EECS, University of California at Berkeley
CRD, Lawrence Berkeley National Laboratory
http://inst.eecs.berkeley.edu/~cs152

## Slide 2: Last time in Lecture 7
3 C’s of cache misses
  Compulsory, Capacity, Conflict
Write policies
  Write back, write-through, write-allocate, no write allocate
Multi-level cache hierarchies reduce miss penalty
  3 levels common in modern systems (some have 4!)
  Can change design tradeoffs of L1 cache if known to have L2
Prefetching: retrieve memory data before CPU request
  Prefetching can waste bandwidth and cause cache pollution
  Software vs hardware prefetching
Software memory hierarchy optimizations
  Loop interchange, loop fusion, cache tiling

## Slide 3: Question of the Day
After talking about virtual addresses, what challenge does this mean for caches (especially L1)?
  And what to do about it?

## Slide 4: Bare Machine
In a bare machine, the only kind of address is a physical address
PC
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Main Memory (DRAM)
Memory Controller
Physical Address
Physical Address
Physical Address
Physical Address
Physical Address

## Slide 5: Absolute Addresses
Only one program ran at a time, with unrestricted access to entire machine (RAM + I/O devices)
Addresses in a program depended upon where the program was to be loaded in memory
But it was more convenient for programmers to write location-independent subroutines
EDSAC, early 50’s
How could location independence be achieved?
Linker and/or loader modify addresses of subroutines and callers when building a program memory image
Notes: Location independence:
Load time rewriting
PC relative branches
PC relative data access or base pointer on entry to routine.

## Slide 6: Dynamic Address Translation
Motivation
  In early machines, I/O was slow and each I/O transfer involved the CPU (programmed I/O)
  Higher throughput possible if CPU and I/O of 2 or more programs were overlapped, how?
  =>multiprogramming with DMA I/O devices, interrupts
Location-independent programs
  Programming and storage management ease
  => need for a base register
Protection
  Independent programs should not affect each other inadvertently
  => need for a bound register
Multiprogramming drives requirement for resident supervisor software to manage context switches between multiple programs
Physical Memory
Program 1
Program 2
OS

## Slide 7: Simple Base and Bound Translation
Load X
Program Address Space
Bound
Register
Bounds
Violation?
Physical Memory
Current
Segment
Base
Register
+
Physical
Address
Logical
Address
Base and bounds registers are visible/accessible only when processor is running in the supervisor mode
Base Physical Address
Segment Length
≥

## Slide 8: Separate Areas for Program and Data
Physical Address
Physical Address
Load X
Program Address Space
Main Memory
Data Segment
Data Bound Register
Mem. Address Register
Data Base Register
+
Bounds Violation?
Program Bound Register
Program Counter
Program Base Register
+
Program Segment
Logical Address
Logical Address
What is an advantage of this separation?
(Scheme used on all Cray vector supercomputers prior to X1, 2002)
≥
≥
Bounds Violation?
Notes: Permits sharing of program segments.

## Slide 9: Base and Bound Machine
Can fold addition of base register into (register+immediate) address calculation using a carry-save adder (sums three numbers with only a few gate delays more than adding two numbers)
PC
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Main Memory (DRAM)
Memory Controller
Physical Address
Physical Address
Physical Address
Physical Address
Data Bound Register
Data Base Register
+
Logical Address
Bounds Violation?
Physical Address
Program Bound Register
Program Base Register
+
Logical Address
Bounds Violation?
≥
≥

## Slide 10: Question
How much memory to allocate to each program?
  I.e., How to set the upper bound?
What if we allocate not enough?
What if we allocate too much?

## Slide 11: Memory Fragmentation
What if the next request is for 32K?
At some stage programs have to be moved
around to compact the storage.
OS
Space
16K
24K
24K
32K
24K
user 1
user 2
user 3
OS
Space
16K
24K
16K
32K
24K
user 1
user 2
user 3
user 5
user 4
8K
Users 4 & 5
arrive
Users 2 & 5
leave
OS
Space
16K
24K
16K
32K
24K
user 1
user 4
8K
user 3
free
Notes: Called Burping the memory.

## Slide 12: Paged Memory Systems
Processor-generated address can be split into:
Page tables make it possible to store the pages of a program non-contiguously.
0
1
2
3
0
1
2
3
Address Space
of User-1
Page Table
of User-1
1
0
2
3
A Page Table contains the physical address at the start of each page
Physical Memory
Page Number
Offset
Notes: Relaxes the contiguous allocation requirement.

## Slide 13: Private Address Space per Process (User)
Each user (process) has a page table
Page table contains an entry for each user page
VA1
User 1
Page Table
VA1
User 2
Page Table
VA1
User 3
Page Table
Physical Memory
free
OS
pages
Notes: OS ensures that the page tables are disjoint.

## Slide 14: Question (2)
How large do we make pages?
  Why make them large?
  Why make them small?

## Slide 15: Where Should Page Tables Reside?
Space required by the page tables (PT) is proportional to the address space, number of users, ...
    Too large to keep in registers
Idea: Keep PTs in the main memory
  needs one reference to retrieve the page base address and another to access the data word
   doubles the number of memory references!

## Slide 16: Page Tables in Physical Memory
VA1
User 1 Virtual Address Space
User 2 Virtual Address Space
PT User 1
PT User 2
VA1
Physical Memory
Did we just increase memory access latency?

## Slide 17: A Problem in the Early Sixties
There were many applications whose data could not fit in the main memory, e.g., payroll
  Paged memory system reduced fragmentation but still required the whole program to be resident in the main memory

## Slide 18: Manual Overlays
Assume an instruction can address all the storage on the drum
Method 1: programmer keeps track of addresses in the main memory and initiates an I/O transfer when required
  Difficult, error-prone!
Method 2: automatic initiation of I/O transfers by software address translation
  Brooker’s interpretive coding, 1960
  Inefficient!
Ferranti Mercury
1956
40k bits
main
640k bits
drum
Central Store
Not just an ancient black art, e.g., IBM Cell microprocessor using in Playstation-3 has explicitly managed local store!
Notes: British Firm Ferranti, did Mercury and then Atlas
Method 1 too difficult for users
Method 2 too slow.

## Slide 19: Demand Paging in Atlas (1962)
Secondary
(Drum)
32x6 pages
Primary
32 Pages
512 words/page
Central
Memory
User sees 32 x 6 x 512 words
of storage
“A page from secondary
storage is brought into the primary storage whenever it is (implicitly) demanded by the processor.”
Tom Kilburn
Primary memory as a cache
for secondary memory
Notes: Single-level Store

## Slide 20: Hardware Organization of Atlas
Initial
Address
Decode
16 ROM pages
0.4-1 sec
2 subsidiary pages
1.4 sec
Main
32 pages
1.4 sec
Drum (4)
192 pages
8 Tape decks
88 sec/word
48-bit words
512-word pages
1 Page Address Register (PAR) per page frame
Compare the effective page address against all 32 PARs
match  normal access
no match  page fault
save the state of the partially executed instruction
Effective
Address
system code
(not swapped)
system data
(not swapped)
0
31
PARs
<effective PN , status>

## Slide 21: Atlas Demand Paging Scheme
On a page fault:
Input transfer into a free page is initiated
The Page Address Register (PAR) is updated
If no free page is left, a page is selected to be replaced (based on usage)
The replaced page is written on the drum
  to minimize drum latency effect, the first empty page on the drum was selected
The page table is updated to point to the new location of the page on the drum

## Slide 22: Linear Page Table
Page Table Entry (PTE) contains:
  A bit to indicate if a page exists
  PPN (physical page number) for a memory-resident page
  DPN (disk page number) for a page on the disk
  Status bits for protection and usage
OS sets the Page Table Base Register whenever active user process changes
VPN
Offset
Virtual address from CPU Execute Stage
PT Base Register
VPN
Data word
Data Pages
Offset
PPN
PPN
DPN
PPN
PPN
PPN
Page Table
DPN
PPN
DPN
DPN
DPN
PPN
Supervisor Accessible Control Register inside CPU

## Slide 23: Size of Linear Page Table
With 32-bit addresses, 4-KB pages & 4-byte PTEs:
  220 PTEs, i.e, 4 MB page table per user
  4 GB of swap needed to back up full virtual address space
Larger pages?
  Internal fragmentation (Not all memory in page is used)
  Larger page fault penalty (more time to read from disk)
What about 64-bit virtual address space???
  How many page table entries (PTEs)?
What is the “saving grace” ?
Notes: Virtual address space is large but only a small fraction of the
pages are populated. So we can use a sparse representation
of the table.

## Slide 24: Hierarchical Page Table
Level 1
Page Table
Level 2
Page Tables
Data Pages
page in primary memory
page in secondary memory
Root of the Current
Page Table
p1
offset
p2
Virtual Address from CPU
(Processor
Register)
PTE of a nonexistent page
p1 p2 offset
0
11
12
21
22
31
10-bit
L1 index
10-bit
L2 index
Physical Memory
What is the downside?

## Slide 25: Two-Level Page Tables in Physical Memory
VA1
User 1
User1/VA1
User2/VA1
Level 1 PT User 1
Level 1 PT User 2
VA1
User 2
Level 2 PT User 2
Virtual Address Spaces
Physical Memory
Level 2 PT User 1

## Slide 26: Address Translation & Protection
Every instruction and data access needs address
translation and protection checks
A good VM design needs to be fast (~ one cycle) and space efficient
Physical Address
Virtual Address
Address
Translation
Virtual Page No. (VPN)
offset
Physical Page No. (PPN)
offset
Exception?
Kernel/User Mode
Read/Write
Protection Check

## Slide 27: Translation Lookaside Buffers (TLB)
Address translation is very expensive!
  In a two-level page table, each reference becomes several memory accesses
Solution: Cache translations in TLB
TLB hit  Single-Cycle Translation
TLB miss  Page-Table Walk to refill
VPN offset
V R W D tag PPN
physical address
PPN offset
virtual address
hit?
W, R: Read and write
permission bits
D: Dirty
V: Valid
(PPN = physical page number)
Notes: 3 memory references
2 page faults (disk accesses) + ..
Actually used in IBM before paged memory.

## Slide 28: How Would You Design the TLB?
Associativity?
Replacement policy?

## Slide 29: TLB Designs
Typically 32-128 entries, usually fully associative
  Each entry maps a large page, hence less spatial locality across pages  more likely that two entries conflict
  Sometimes larger TLBs (256-512 entries) are 4-8 way set-associative
  Larger systems sometimes have multi-level (L1 and L2) TLBs
Random or FIFO replacement policy
No process information in TLB?
TLB Reach: Size of largest virtual address space that can be simultaneously mapped by TLB
  How much of the physical address space is the TLB mapping to?
  Example: 64 TLB entries, 4KB pages, one page per entry
  TLB Reach = _____________________________________________?
64 entries * 4 KB = 256 KB (if contiguous)

## Slide 30: Handling a TLB Miss
Software (MIPS, Alpha)
  TLB miss causes an exception and the operating system walks the page tables and reloads TLB. A privileged “untranslated” addressing mode used for walk.
Hardware (SPARC v8, x86, PowerPC, RISC-V)
  A memory management unit (MMU) walks the page tables and reloads the TLB.
  If a missing (data or PT) page is encountered during the TLB reloading, MMU gives up and signals a Page Fault exception for the original instruction.
Tradeoffs?
  The hardware needs to know the structure of the page table for hardware handling.

## Slide 31: Hierarchical H/W Page Table Walk: SPARC v8
31 11 0
Virtual Address
Index 1 Index 2 Index 3 Offset
31 23 17 11 0
Context
Table
Register
Context
Register
root ptr
PTP
PTP
PTE
Context Table
L1 Table
L2 Table
L3 Table
Physical Address
PPN Offset
MMU does this table walk in hardware on a TLB miss

## Slide 32: Page-Based Virtual-Memory Machine (Hardware Page-Table Walk)
Assumes page tables held in untranslated physical memory
PC
Inst. TLB
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Page Fault?
Protection violation?
Page Fault?
Protection violation?
Data TLB
Main Memory (DRAM)
Memory Controller
Physical Address
Physical Address
Physical Address
Physical Address
Page-Table Base Register
Virtual Address
Physical Address
Virtual Address
Hardware Page Table Walker
Miss?
Miss?

## Slide 33: Address Translation: putting it all together
Virtual Address
TLB
Lookup
Page Table
Walk
Update TLB
Page Fault
(OS loads page)
Protection
Check
Physical
Address
(to cache)
miss
hit
the page is
Ï memory Î memory
denied
permitted
Protection
Fault
hardware
hardware or software
software
SEGFAULT
Where?
Notes: Need to restart instruction.
Soft and hard page faults.

## Slide 34: Question of the Day
After talking about virtual addresses, what challenge does this mean for caches (especially L1)?
  And what to do about it?

## Slide 35: Acknowledgements
These slides contain material developed and copyright by:
  Arvind (MIT)
  Krste Asanovic (MIT/UCB)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)
MIT material derived from course 6.823
UCB material derived from course CS252