## Slide 1: CS 152 Computer Architecture and Engineering Lecture 18: Snoopy Caches
Dr. George Michelogiannakis
EECS, University of California at Berkeley
CRD, Lawrence Berkeley National Laboratory
http://inst.eecs.berkeley.edu/~cs152

## Slide 2: Administrivia
Lab 4 due now
PS 5 due next week Wednesday (20th)
Lecture 20 will be on datacenters
Quiz 4 and PS 3 will be returned tomorrow

## Slide 3: Last time in Lecture 17
Two kinds of synchronization between processors:
Producer-Consumer
  Consumer must wait until producer has produced value
  Software version of a read-after-write hazard
Mutual Exclusion
  Only one processor can be in a critical section at a time
  Critical section guards shared data that can be written
Producer-consumer synchronization implementable with just loads and stores, but need to know ISA’s memory model!
Mutual-exclusion can also be implemented with loads and stores, but tricky and slow, so ISAs add atomic read-modify-write instructions to implement locks

## Slide 4: Sequential Consistency
Cost:
Prevents aggressive compiler reordering optimizations
Constrains hardware utilization (e.g., store buffer)

## Slide 5: Sequential Consistency
Sequential consistency imposes more memory ordering constraints than those imposed by uniprocessor program dependencies ( )
What are these in our example ?
T1: T2:
  Store (X), 1 (X = 1) Load R1, (Y)
  Store (Y), 11 (Y = 11) Store (Y’), R1 (Y’= Y)
  Load R2, (X)
  Store (X’), R2 (X’= X)
additional SC requirements

## Slide 6: Load-reserve & Store-conditional
Special register(s) to hold reservation flag and address,
and the outcome of store-conditional
try: Load-reserve Rhead, (head)
spin: Load Rtail, (tail)
if Rhead==Rtail goto spin
Load R, (Rhead)
Rhead = Rhead + 1
Store-conditional (head), Rhead
if (status==fail) goto try
process(R)
Load-reserve R, (m):
  <flag, adr>  <1, m>;
  R  M[m];
Store-conditional (m), R:
  if <flag, adr> == <1, m>
  then cancel other procs’
  reservation on m;
    M[m] R;
    status succeed;
  else status fail;

## Slide 7: Performance of Locks
Blocking atomic read-modify-write instructions
e.g., Test&Set, Fetch&Add, Swap
vs
Non-blocking atomic read-modify-write instructions
e.g., Compare&Swap,
Load-reserve/Store-conditional
vs
Protocols based on ordinary Loads and Stores
Performance depends on several interacting factors:
degree of contention,
caches,
out-of-order execution of Loads and Stores
later ...

## Slide 8: Amdahl’s Law
Begins with Simple Software Assumption (Limit Arg.)
  Fraction F of execution time perfectly parallelizable
  No Overhead for Scheduling Communication, Synchronization, etc.
  F is the Parallel Part
  Fraction 1 – F Completely Serial
Time on 1 core = (1 – F) / 1 + F / 1 = 1
Time on N cores = (1 – F) / 1 + F / N

## Slide 9: Strong Consistency
An execution is strongly consistent (linearizable) if the method calls can be correctly arranged retaining the mutual order of calls that do not overlap in time, regardless of what thread calls them.

## Slide 10: Quiescent Consistency
An execution is quiescently consistent if the method calls can be correctly arranged retaining the mutual order of calls separated by quiescence, a period of time where no method is being called in any thread.

## Slide 11: Relaxed Memory Models Need Fences
Producer posting Item x:
Load Rtail, (tail)
Store (Rtail), x
MembarSS
Rtail=Rtail+1
Store (tail), Rtail
Consumer:
Load Rhead, (head)
spin: Load Rtail, (tail)
if Rhead==Rtail goto spin
MembarLL
Load R, (Rhead)
Rhead=Rhead+1
Store (head), Rhead
process(R)
Producer
Consumer
tail
head
Rtail
Rtail
Rhead
R
ensures that tail ptr
is not updated before
x has been stored
ensures that R is
not loaded before
x has been stored

## Slide 12: Memory Coherence in SMPs
Suppose CPU-1 updates A to 200.
write-back: memory and cache-2 have stale values
write-through: cache-2 has a stale value
Do these stale values matter?
What is the view of shared memory for programming?
cache-1
A 100
CPU-Memory bus
CPU-1
CPU-2
cache-2
A 100
memory
A 100

## Slide 13: Write-back Caches & SC
T1 is executed
prog T2
LD Y, R1
ST Y’, R1
LD X, R2
ST X’,R2
prog T1
ST X, 1
ST Y,11
cache-2
cache-1
memory
X = 0
Y =10
X’=
Y’=
X= 1
Y=11
Y =
Y’=
X =
X’=
cache-1 writes back Y
X = 0
Y =11
X’=
Y’=
X= 1
Y=11
Y =
Y’=
X =
X’=
X = 1
Y =11
X’=
Y’=
X= 1
Y=11
Y = 11
Y’= 11
X = 0
X’= 0
cache-1 writes back X
X = 0
Y =11
X’=
Y’=
X= 1
Y=11
Y = 11
Y’= 11
X = 0
X’= 0
T2 executed
X = 1
Y =11
X’= 0
Y’=11
X= 1
Y=11
Y =11
Y’=11
X = 0
X’= 0
cache-2 writes back
X’ & Y’
inconsistent

## Slide 14: Write-through Caches & SC
cache-2
Y =
Y’=
X = 0
X’=
memory
X = 0
Y =10
X’=
Y’=
cache-1
X= 0
Y=10
prog T2
LD Y, R1
ST Y’, R1
LD X, R2
ST X’,R2
prog T1
ST X, 1
ST Y,11
Write-through caches don’t preserve sequential consistency either
T1 executed
Y =
Y’=
X = 0
X’=
X = 1
Y =11
X’=
Y’=
X= 1
Y=11
T2 executed
Y = 11
Y’= 11
X = 0
X’= 0
X = 1
Y =11
X’= 0
Y’=11
X= 1
Y=11

## Slide 15: Maintaining Cache Coherence
Hardware support is required such that
  only one processor at a time has write permission for a location
  no processor can load a stale copy of the location after a write
  -> cache coherence protocols

## Slide 16: Cache Coherence vs. Memory Consistency
A cache coherence protocol ensures that all writes by one processor are eventually visible to other processors, for one memory address
  i.e., updates are not lost
No guarantee of when an update should be seen
No guarantee of what order of updates (of different addresses) should be seen
A cache coherence protocol is not enough to ensure sequential consistency
  But if sequentially consistent, then caches must be coherent

## Slide 17: Cache Coherence vs. Memory Consistency
A memory consistency model gives the rules on when a write by one processor can be observed by a read on another, across different addresses
  As previously seen with examples
Combination of cache coherence protocol plus processor memory reorder buffer used to implement a given architecture’s memory consistency model

## Slide 18: Warmup: Parallel I/O
(DMA stands for “Direct Memory Access”, means the I/O device can read/write memory autonomous from the CPU)
Either Cache or DMA can
be the Bus Master and
effect transfers
DISK
DMA
Physical
Memory
Proc.
R/W
Data (D)
Cache
Address (A)
A
D
R/W
Page transfers
occur while the
Processor is running
Memory
Bus

## Slide 19: Problems with Parallel I/O
Memory Disk: Physical memory may be
stale if cache copy is dirty
Disk Memory: Cache may hold stale data and not see memory writes
DISK
DMA
Physical
Memory
Proc.
Cache
Memory
Bus
Cached portions
of page
DMA transfers

## Slide 20: Snoopy Cache, Goodman 1983
Idea: Have cache watch (or snoop upon) DMA transfers, and then “do the right thing”
Snoopy cache tags are dual-ported
Proc.
Cache
Snoopy read port
attached to Memory
Bus
Data
(lines)
Tags and
State
A
D
R/W
Used to drive Memory Bus
when Cache is Bus Master
A
R/W

## Slide 21: Snoopy Cache Actions for DMA
Observed Bus Cycle Cache State Cache Action
Address not cached
DMA Read Cached, unmodified
Memory Disk Cached, modified
Address not cached
DMA Write Cached, unmodified
Disk Memory Cached, modified
No action
No action
No action
Cache intervenes
Cache purges its copy
???

## Slide 22: Shared Memory Multiprocessor
Use snoopy mechanism to keep all processors’ view of memory coherent
M1
M2
M3
Snoopy
Cache
DMA
Physical
Memory
Memory
Bus
Snoopy
Cache
Snoopy
Cache
DISKS

## Slide 23: Snoopy Cache Coherence Protocols
write miss:
  the address is invalidated in all other
  caches before the write is performed
read miss:
  if a dirty copy is found in some cache, a write-back is performed before the memory is read
Notes: Update protocols, or write broadcast. Latency between writing a word in one processor
and reading it in another is usually smaller in a write update scheme.
But since bandwidth is more precious, most multiprocessors use a write invalidate scheme.

## Slide 24: Cache State Transition Diagram The MSI protocol
M
S
I
M: Modified
S: Shared
I: Invalid
Each cache line has state bits
Address tag
state
bits
Write miss
(P1 gets line from memory)
Other processor
intents to write (P1 writes back)
Read miss
(P1 gets line from memory)
P1 intent to write
Other processor
intents to write
Read by any
processor
P1 reads
or writes
Cache state in processor P1
Other processor reads
(P1 writes back)

## Slide 25: Two Processor Example (Reading and writing the same cache line)
M
S
I
Write miss
Read
miss
P1 intent to write
P2 intent to write
P2 reads,
P1 writes back
P1 reads
or writes
P2 intent to write
P1
M
S
I
Write miss
Read
miss
P2 intent to write
P1 intent to write
P1 reads,
P2 writes back
P2 reads
or writes
P1 intent to write
P2
P1 reads
P1 writes
P2 reads
P2 writes
P1 writes
P2 writes
P1 reads
P1 writes

## Slide 26: Observation
If a line is in the M state then no other cache can have a copy of the line!
Memory stays coherent, multiple differing copies cannot exist
M
S
I
Write miss
Other processor
intent to write
Read
miss
P1 intent to write
Other processor
intent to write
Read by any
processor
P1 reads
or writes
Other processor reads
P1 writes back

## Slide 27: MESI: An Enhanced MSI protocol increased performance for private data
M
E
S
I
M: Modified Exclusive
E: Exclusive but unmodified
S: Shared
I: Invalid
Each cache line has a tag
Address tag
state
bits
Write miss
Other processor
intent to write
Read miss,
shared
Other processor
intent to write
P1 write
Read by any
processor
Other processor reads
P1 writes back
P1 read
P1 write
or read
Cache state in processor P1
P1 intent to write
Read miss, not shared
Other processor
reads
Other processor intent to write, P1 writes back

## Slide 28: Optimized Snoop with Level-2 Caches
Snooper
Snooper
Snooper
Snooper
Processors often have two-level caches
  small L1, large L2 (on chip)
Inclusion property: entries in L1 must be in L2
invalidation in L2  invalidation in L1
Snooping on L2 does not affect CPU-L1 bandwidth
What problem could occur?
CPU
L1 $
L2 $
CPU
L1 $
L2 $
CPU
L1 $
L2 $
CPU
L1 $
L2 $
Notes: Interlocks are required when both CPU-L1 and L2-Bus interactions involve
the same address.

## Slide 29: Intervention
When a read-miss for A occurs in cache-2,
a read request for A is placed on the bus
  Cache-1 needs to supply & change its state to shared
  The memory may respond to the request also!
Does memory know it has stale data?
Cache-1 needs to intervene through memory controller to supply correct data to cache-2
cache-1
A 200
CPU-Memory bus
CPU-1
CPU-2
cache-2
memory (stale data)
A 100

## Slide 30: False Sharing
state line addr data0 data1 ... dataN
A cache line contains more than one word
Cache-coherence is done at the line-level and not word-level
Suppose M1 writes wordi and M2 writes wordk and
both words have the same line address.
What can happen?
Notes: The block may be invalidated many times unnecessarily because
the addresses share a common block.

## Slide 31: Synchronization and Caches: Performance Issues
Cache-coherence protocols will cause mutex to ping-pong between P1’s and P2’s caches.
Ping-ponging can be reduced by first reading the mutex location (non-atomically) and executing a swap only if it is found to be zero.
cache
Processor 1
R  1
L: swap (mutex), R;
if <R> then goto L;
<critical section>
M[mutex]  0;
Processor 2
R  1
L: swap (mutex), R;
if <R> then goto L;
<critical section>
M[mutex]  0;
Processor 3
R  1
L: swap (mutex), R;
if <R> then goto L;
<critical section>
M[mutex]  0;
CPU-Memory Bus
mutex=1
cache
cache

## Slide 32: Load-reserve & Store-conditional
If the snooper sees a store transaction to the address
in the reserve register, the reserve bit is set to 0
  Several processors may reserve ‘a’ simultaneously
  These instructions are like ordinary loads and stores
  with respect to the bus traffic
Special register(s) to hold reservation flag and address, and the outcome of store-conditional
Load-reserve R, (a):
  <flag, adr>  <1, a>;
  R  M[a];
Store-conditional (a), R:
  if <flag, adr> == <1, a>
  then cancel other procs’
  reservation on a;
    M[a] <R>;
    status succeed;
  else status fail;
Notes: Can implement reservation by using cache hit/miss, no additional hardware required (problems?)

## Slide 33: Out-of-Order Loads/Stores & CC
Blocking caches
  One request at a time + CC  SC
Non-blocking caches
  Multiple requests (different addresses) concurrently + CC
   Relaxed memory models
CC ensures that all processors observe the same order of loads and stores to an address
Cache
Memory
pushout (Wb-rep)
load/store
buffers
CPU
(S-req, E-req)
(S-rep, E-rep)
Wb-req, Inv-req, Inv-rep
snooper
(I/S/E)
CPU/Memory
Interface

## Slide 34: Acknowledgements
These slides contain material developed and copyright by:
  Arvind (MIT)
  Krste Asanovic (MIT/UCB)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)
MIT material derived from course 6.823
UCB material derived from course CS252
“New microprocessor claims 10x energy improvement”, from extremetech
“Exploring the diverse world of programming” by Pavel Shved
“Amdahl’s Law in the Multicore Era” b Mark D. Hill and Michael R. Marty