## Slide 1: CS 152 Computer Architecture and Engineering CS252 Graduate Computer Architecture Lecture 3 - Pipelining
Krste Asanovic
Electrical Engineering and Computer Sciences
University of California at Berkeley
http://www.eecs.berkeley.edu/~krste
http://inst.eecs.berkeley.edu/~cs152

## Slide 2: Last Time in Lecture 2
Microcoding, an effective technique to manage control unit complexity, invented in era when logic (tubes), main memory (magnetic core), and ROM (diodes) used different technologies
Difference between ROM and RAM speed motivated additional complex instructions
Technology advances leading to fast SRAM made technology assumptions invalid
Complex instructions sets impede parallel and pipelined implementations
Load/store, register-rich ISAs (pioneered by Cray, popularized by RISC) perform better in new VLSI technology

## Slide 3: “Iron Law” of Processor Performance
Instructions per program depends on source code, compiler technology, and ISA
Cycles per instructions (CPI) depends on ISA and µarchitecture
Time per cycle depends upon the µarchitecture and base technology
Time = Instructions Cycles Time
Program Program * Instruction * Cycle
Microarchitecture | CPI | cycle time
Microcoded | >1 | short
Single-cycle unpipelined | 1 | long
Pipelined | 1 | short

## Slide 4: Classic 5-Stage RISC Pipeline
Memory
EXecute
Decode
Fetch
Registers
ALU
B
A
Data Cache
PC
Instruction Cache
Store
Imm
Inst. Register
Writeback
This version designed for regfiles/memories with synchronous reads and writes.

## Slide 5: CPI Examples
Time
Inst 3
7 cycles
Inst 1
Inst 2
5 cycles
10 cycles
Microcoded machine
3 instructions, 22 cycles, CPI=7.33
Unpipelined machine
3 instructions, 3 cycles, CPI=1
Inst 1
Inst 2
Inst 3
Pipelined machine
3 instructions, 3 cycles, CPI=1
Inst 1
Inst 2
Inst 3
5-stage pipeline CPI≠5!!!

## Slide 6: Instructions interact with each other in pipeline
An instruction in the pipeline may need a resource being used by another instruction in the pipeline  structural hazard
An instruction may depend on something produced by an earlier instruction
  Dependence may be for a data value  data hazard
  Dependence may be for the next instruction’s address  control hazard (branches, exceptions)
Handling hazards generally introduces bubbles into pipeline and reduces ideal CPI > 1

## Slide 7: Pipeline CPI Examples
Time
3 instructions finish in 3 cycles
CPI = 3/3 =1
Inst 1
Inst 2
Inst 3
3 instructions finish in 4 cycles
CPI = 4/3 = 1.33
Inst 1
Inst 2
Inst 3
Bubble
Measure from when first instruction finishes to when last instruction in sequence finishes.
3 instructions finish in 5cycles
CPI = 5/3 = 1.67
Inst 1
Inst 2
Inst 3
Bubble 1
Bubble 2
Inst 3

## Slide 8: Resolving Structural Hazards
Structural hazard occurs when two instructions need same hardware resource at same time
  Can resolve in hardware by stalling newer instruction till older instruction finished with resource
A structural hazard can always be avoided by adding more hardware to design
  E.g., if two instructions both need a port to memory at same time, could avoid hazard by adding second port to memory
Classic RISC 5-stage integer pipeline has no structural hazards by design
  Many RISC implementations have structural hazards on multi-cycle units such as multipliers, dividers, floating-point units, etc., and can have on register writeback ports

## Slide 9: Types of Data Hazards
Consider executing a sequence of register-register instructions of type:
rk ri op rj
Data-dependence
      r3  r1 op r2 Read-after-Write
      r5  r3 op r4 (RAW) hazard
Anti-dependence
      r3  r1 op r2 Write-after-Read
      r1  r4 op r5 (WAR) hazard
Output-dependence
      r3  r1 op r2 Write-after-Write
      r3  r6 op r7 (WAW) hazard

## Slide 10: Three Strategies for Data Hazards
Interlock
  Wait for hazard to clear by holding dependent instruction in issue stage
Bypass
  Resolve hazard earlier by bypassing value as soon as available
Speculate
  Guess on value, correct if wrong

## Slide 11: Interlocking Versus Bypassing
add x1, x3, x5
sub x2, x1, x4
F
add x1, x3, x5
D
F
X
D
F
sub x2, x1, x4
W
M
X
bubble
F
D
W
X
M
W
M
W
W
M
D
X
bubble
M
X
bubble
D
F
Instruction interlocked in decode stage
F
D
X
M
W
add x1, x3, x5
F
D
X
M
W
sub x2, x1, x4
Bypass around ALU with no bubbles

## Slide 12: Example Bypass Path
Memory
EXecute
Decode
Fetch
Registers
ALU
B
A
Data Cache
PC
Instruction Cache
Store
Imm
Inst. Register
Writeback

## Slide 13: Fully Bypassed Data Path
Memory
EXecute
Decode
Fetch
Registers
ALU
B
A
Data Cache
PC
Instruction Cache
Store
Imm
Inst. Register
Writeback
F
D
X
M
W
F
D
X
M
W
F
D
X
M
W
F
D
X
M
W
[ Assumes data written to registers in a W cycle is readable in parallel D cycle (dotted line). Extra write data register and bypass paths required if this is not possible. ]

## Slide 14: Value Speculation for RAW Data Hazards
Rather than wait for value, can guess value!
So far, only effective in certain limited cases:
  Branch prediction
  Stack pointer updates
  Memory address disambiguation

## Slide 15: Control Hazards
What do we need to calculate next PC?
For Unconditional Jumps
  Opcode, PC, and offset
For Jump Register
  Opcode, Register value, and offset
For Conditional Branches
  Opcode, Register (for condition), PC and offset
For all other instructions
  Opcode and PC ( and have to know it’s not one of above )

## Slide 16: Control flow information in pipeline
Memory
EXecute
Decode
Fetch
Registers
B
A
Data Cache
PC
Instruction Cache
Store
Imm
Inst. Register
Writeback
PC known
Opcode,
offset known
Branch condition, Jump register value known
ALU

## Slide 17: RISC-V Unconditional PC-Relative Jumps
EXecute
Decode
Fetch
Registers
B
A
Instruction Cache
Imm
Inst. Register
ALU
PC_decode
Add
Jump?
PCJumpSel
PC_fetch
Kill
FKill
+4
[ Kill bit turns instruction into a bubble ]

## Slide 18: Pipelining for Unconditional PC-Relative Jumps
M
W
X
M
W
D
X
M
W
j target
F
D
F
target: add x1, x2, x3
X
D
F
bubble

## Slide 19: Branch Delay Slots
Early RISCs adopted idea from pipelined microcode engines, and changed ISA semantics so instruction after branch/jump is always executed before control flow change occurs:
  0x100 j target
  0x104 add x1, x2, x3 // Executed before target
  …
  0x205 target: xori x1, x1, 7
Software has to fill delay slot with useful work, or fill with explicit NOP instruction
M
W
X
M
W
D
X
M
W
j target
F
D
F
target: xori x1, x1, 7
X
D
F
add x1, x2, x3

## Slide 20: Post-1990 RISC ISAs don’t have delay slots
Encodes microarchitectural detail into ISA
  c.f. IBM 650 drum layout
Performance issues
  Increased I-cache misses from NOPs in unused delay slots
  I-cache miss on delay slot causes machine to wait, even if delay slot is a NOP
Complicates more advanced microarchitectures
  Consider 30-stage pipeline with four-instruction-per-cycle issue
Better branch prediction reduced need
  Branch prediction in later lecture

## Slide 21: RISC-V Conditional Branches
EXecute
Decode
Fetch
Registers
B
A
Instruction Cache
Inst.
Inst. Register
ALU
PC_decode
Add
Branch?
PCSel
PC_fetch
Kill
FKill
+4
Cond?
PC_execute
Add
Kill
DKill

## Slide 22: Pipelining for Conditional Branches
M
W
X
M
W
D
X
M
W
beq x1, x2, target
F
D
F
target: add x1, x2, x3
X
D
F
bubble
bubble
F
D
X
M
W

## Slide 23: Pipelining for Jump Register
Register value obtained in execute stage
M
W
X
M
W
D
X
M
W
jr x1
F
D
F
target: add x5, x6, x7
X
D
F
bubble
bubble
F
D
X
M
W

## Slide 24: Why instruction may not be dispatched every cycle in classic 5-stage pipeline (CPI>1)
Full bypassing may be too expensive to implement
  typically all frequently used paths are provided
  some infrequently used bypass paths may increase cycle time and counteract the benefit of reducing CPI
Loads have two-cycle latency
  Instruction after load cannot use load result
  MIPS-I ISA defined load delay slots, a software-visible pipeline hazard (compiler schedules independent instruction or inserts NOP to avoid hazard). Removed in MIPS-II (pipeline interlocks added in hardware)
    MIPS:“Microprocessor without Interlocked Pipeline Stages”
Jumps/Conditional branches may cause bubbles
  kill following instruction(s) if no delay slots
Machines with software-visible delay slots may execute significant number of NOP instructions inserted by the compiler.
NOPs reduce CPI, but increase instructions/program!

## Slide 25: CS152 Administrivia
PS 1 is posted
PS 1 is due at start of class on Monday Feb 5
Lab 1 out on Friday
Lab 1 overview in Section Friday 2-4pm,
  DIS 101 3113 Etcheverry
  DIS 102 310 Soda

## Slide 26: CS252 Administrivia
CS252 discussions grading policy
  We’ll ignore your two lowest scores in grading, which includes absences
  Send in summary even if you can’t attend discussion
CS252 Piazza class has been created
  Sign up for this as well as CS152 Piazza
Each CS252 paper has dedicated thread
  Post your response as private note to instructors
  Due 6AM Monday before Monday discussion section

## Slide 27: Traps and Interrupts
In class, we’ll use following terminology
Exception: An unusual internal event caused by program during execution
  E.g., page fault, arithmetic underflow
Trap: Forced transfer of control to supervisor caused by exception
  Not all exceptions cause traps (c.f. IEEE 754 floating-point standard)
Interrupt: An external event outside of running program, which causes transfer of control to supervisor
Traps and interrupts usually handled by same pipeline mechanism

## Slide 28: History of Exception Handling
(Analytical Engine had overflow exceptions)
First system with traps was Univac-I, 1951
  Arithmetic overflow would either
    1. trigger the execution a two-instruction fix-up routine at address 0, or
    2. at the programmer's option, cause the computer to stop
  Later Univac 1103, 1955, modified to add external interrupts
    Used to gather real-time wind tunnel data
First system with I/O interrupts was DYSEAC, 1954
  Had two program counters, and I/O signal caused switch between two PCs
  Also, first system with DMA (direct memory access by I/O device)
  And, first mobile computer (two tractor trailers, 12 tons + 8 tons)

## Slide 29: DYSEAC, first mobile computer!
Carried in two tractor trailers, 12 tons + 8 tons
Built for US Army Signal Corps
[Courtesy Mark Smotherman]

## Slide 30: Asynchronous Interrupts
An I/O device requests attention by asserting one of the prioritized interrupt request lines
When the processor decides to process the interrupt
  It stops the current program at instruction Ii , completing all the instructions up to Ii-1 (precise interrupt)
  It saves the PC of instruction Ii in a special register (EPC)
  It disables interrupts and transfers control to a designated interrupt handler running in supervisor mode

## Slide 31: Interrupts: altering the normal flow of control
Ii-1
HI1
HI2
HIn
Ii
Ii+1
program
interrupt
handler
An external or internal event that needs to be processed by another (system) program. The event is usually unexpected or rare from program’s point of view.

## Slide 32: Interrupt Handler
Saves EPC before enabling interrupts to allow nested interrupts 
  need an instruction to move EPC into GPRs
  need a way to mask further interrupts at least until EPC can be saved
Needs to read a status register that indicates the cause of the interrupt
Uses a special indirect jump instruction ERET (return-from-environment) which
  enables interrupts
  restores the processor to the user mode
  restores hardware status and control state

## Slide 33: Synchronous Trap
A synchronous trap is caused by an exception on a particular instruction
In general, the instruction cannot be completed and needs to be restarted after the exception has been handled
  requires undoing the effect of one or more partially executed instructions
In the case of a system call trap, the instruction is considered to have been completed
  a special jump instruction involving a change to a privileged mode

## Slide 34: Exception Handling 5-Stage Pipeline
How to handle multiple simultaneous exceptions in different pipeline stages?
How and where to handle external asynchronous interrupts?
PC
Inst. Mem
D
Decode
E
M
Data Mem
W
+
Illegal Opcode
Overflow
Data address Exceptions
PC address Exception
Asynchronous Interrupts

## Slide 35: Exception Handling 5-Stage Pipeline
PC
Inst. Mem
D
Decode
E
M
Data Mem
W
+
Illegal Opcode
Overflow
Data address Exceptions
PC address Exception
Asynchronous
Interrupts
Exc
D
PC
D
Exc
E
PC
E
Exc
M
PC
M
Cause
EPC
Kill D Stage
Kill F Stage
Kill E Stage
Select Handler PC
Kill Writeback
Commit Point

## Slide 36: Exception Handling 5-Stage Pipeline
Hold exception flags in pipeline until commit point (M stage)
Exceptions in earlier pipe stages override later exceptions for a given instruction
Inject external interrupts at commit point (override others)
If exception at commit: update Cause and EPC registers, kill all stages, inject handler PC into fetch stage

## Slide 37: Speculating on Exceptions
Prediction mechanism
  Exceptions are rare, so simply predicting no exceptions is very accurate!
Check prediction mechanism
  Exceptions detected at end of instruction execution pipeline, special hardware for various exception types
Recovery mechanism
  Only write architectural state at commit point, so can throw away partially executed instructions after exception
  Launch exception handler after flushing pipeline
Bypassing allows use of uncommitted instruction results by following instructions

## Slide 38: Acknowledgements
This course is partly inspired by previous MIT 6.823 and Berkeley CS252 computer architecture courses created by my collaborators and colleagues:
  Arvind (MIT)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)