## Slide 1: IO Performance Oriented Drivers
David E. Culler
CS162 – Operating Systems and Systems Programming
Lecture 22
October 20, 2014
Reading: A&D 7.5, 12.1c
HW 4 out
Proj 2 out

## Slide 2: I/O Performance
Response Time = Queue + I/O device service time
User
Thread
Queue
[OS Paths]
Controller
I/O
device
Performance of I/O subsystem
  Metrics: Response Time, Throughput
  Effective BW per op = transfer size / response time
    EffBW(n) = n / (S + n/B) = B / (1 + SB/n )
  Contributing factors to latency:
    Software paths (can be loosely modeled by a queue)
    Hardware controller
    I/O device service time
Queuing behavior:
  Can lead to big increases of latency as utilization increases
  Solutions?
100%
Response
Time (ms)
Throughput (Utilization)
(% total BW)
0
100
200
300
0%

## Slide 3: A Simple Deterministic World
Assume requests arrive at regular intervals, take a fixed time to process, with plenty of time between …
Service rate (μ = 1/T S) - operations per sec
Arrival rate: (λ = 1/T A) - requests per second
Utilization: U = λ/μ , where λ < μ
Average rate is the complete story
Queue
Server
arrivals
departures
T Q
T S
T A
T A
T A

## Slide 4: A Ideal Linear World
What does the queue wait time look like?
  Grows unbounded at a rate ~ (Ts/TA) till request rate subsides
Offered Load (TA/TS)
Delivered Throughput
0
1
1
time
Queue delay
time
Queue delay
Delivered Throughput
0
1
1
Offered Load (TA/TS)
Empty Queue
Saturation
Unbounded

## Slide 5: A Bursty World
Requests arrive in a burst, must queue up till served
Same average arrival time, but almost all of the requests experience large queue delays
Even though average utilization is low
Queue
Server
arrivals
departures
T Q
T S
Q depth
Server
Arrivals

## Slide 6: So how do we model the burstiness?
Elegant mathematical framework if you start with exponential distribution
  Probability density function of a continuous random variable with a mean of 1/λ
  f(x) = λe-λx
  “Memoryless”
Chart: 
| 0.001 | 0.01 | 0.02 | 0.04 | 0.08 | 0.16 | 0.32 | 0.64 | 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 10.0
f(x) | 0.999 | 0.99005 | 0.9802 | 0.96079 | 0.92312 | 0.85214 | 0.72615 | 0.52729 | 0.36788 | 0.13534 | 0.049787 | 0.018316 | 0.0067379 | 0.0024788 | 0.00091188 | 0.00033546 | 4.54e-05
mean arrival interval (1/λ)
Lots of short arrival intervals (i.e., high instantaneous rate)
Few long gaps (i.e., low instantaneous rate)
Likelihood of an event occuring is independent of how long we’ve been waiting
x (λ)

## Slide 7: How Long should we expect to wait?
RespTime = ServTime * 1/(1-U)
  Better if gaussian (spread around the mean)
Variance in R = S/(1-U)2
Response Time vs. Utilization

## Slide 8: Little’s Law
In any stable system
  Average arrival rate = Average departure rate
the average number of tasks in the system (N) is equal to the throughput (B) times the response time (L)
N (ops) = B (ops/s) x L (s)
Regardless of structure, bursts of requests, variation in service
  instantaneous variations, but it washes out in the average
  Overall requests match departures
arrivals
departures
N
B
L

## Slide 9: I/O Performance
Response Time = Queue + I/O device service time
User
Thread
Queue
[OS Paths]
Controller
I/O
device
Solutions?
  Make everything faster 
  More Decoupled (Parallelism) systems
    multiple independent buses or controllers
  Optimize the bottleneck to increase service rate
    Use the queue to optimize the service
  Do other useful work while waiting
Queues absorb bursts and smooth the flow
Admissions control (finite queues)
  Limits delays, but may introduce unfairness and livelock
100%
Response
Time (ms)
Throughput (Utilization)
(% total BW)
0
100
200
300
0%

## Slide 10: Ex: Disk Scheduling to Minimize Seek

## Slide 11: Disk Performance Examples
Assumptions:
  Ignoring queuing and controller times for now
  Avg seek time of 5ms,
  7200RPM  Time for one rotation: 60000ms/7200 ~= 8ms
  Transfer rate of 4MByte/s, sector size of 1 KByte
Read sector from random place on disk:
  Seek (5ms) + Rot. Delay (4ms) + Transfer (0.25ms)
  Approx 10ms to fetch/put data: 100 KByte/sec
Read sector from random place in same cylinder:
  Rot. Delay (4ms) + Transfer (0.25ms)
  Approx 5ms to fetch/put data: 200 KByte/sec
Read next sector on same track:
  Transfer (0.25ms): 4 MByte/sec
Key to using disk effectively (especially for file systems) is to minimize seek and rotational delays

## Slide 12: Disk Scheduling
Disk can do only one request at a time; What order do you choose to do queued requests?
  Request denoted by (track, sector)
Scheduling algorithms:
  First In First Out (FIFO)
  Shortest Seek Time First
  SCAN
  C-SCAN
In our examples we ignore the sector
  Consider only track #
2,3
2,1
3,10
7,2
5,2
2,2
Head
User
Requests
1
4
2
Disk Head
3

## Slide 13: FIFO: First In First Out
Schedule requests in the order they arrive in the queue
Example:
  Request queue: 2, 1, 3, 6, 2, 5
  Scheduling order: 2, 1, 3, 6, 2, 5
  16 tracks, 6 seeks
  Pros: Fair among requesters
  Cons: Order of arrival may be to random spots on the disk  Very long seeks
Disk Head
6
1
2
3
4
5

## Slide 14: SSTF: Shortest Seek Time First
Pick the request that’s closest to the head on the disk
  Although called SSTF, include rotational delay in calculation, as rotation can be as long as seek
Example:
  Request queue: 2, 1, 3, 6, 2, 5
  Scheduling order: 5, 6, 3, 2, 2, 1
  6 tracks, 4 seeks
Pros: reduce seeks
Cons: may lead to starvation
  Greedy. Not optimal
Disk Head
6
1
2
3
4
5

## Slide 15: SCAN
Implements an Elevator Algorithm: take the closest request in the direction of travel
Example:
  Request queue: 2, 1, 3, 6, 2, 5
  Head is moving towards center
  Scheduling order: 5, 3, 2, 2, 1, 6
  8 tracks, 4 seeks
Pros:
  No starvation
  Low seek
Cons: favors middle tracks
  May spend time on sparse tracks while dense requests elsewhere
Disk Head
6
1
2
3
4
5

## Slide 16: C-SCAN
Like SCAN but only serves request in only one direction
Example:
  Request queue: 2, 1, 3, 6, 2, 5
  Head only serves request on its way from center towards edge
  Scheduling order: 5, 6, 1, 2, 2, 3
  8 tracks, 5 seeks
Pros:
  Fairer than SCAN
  Accumulate work in remote region then go get it
Cons: longer seeks on the way back
Optimization: dither to pickup nearby requests as you go
Disk Head
6
1
2
3
4
5

## Slide 17: When is the disk performance highest
When there are big sequential reads, or
When there is so much work to do that they can be piggy backed (c-scan)
OK, to be inefficient when things are mostly idle
Bursts are both a threat and an opportunity
<your idea for optimization goes here>
  Waste space for speed?

## Slide 18: Ex: Concurrency to break the bottleneck
Busses provide a way of connecting many (N) different things with a single set of wires and standard connections and protocols
  N2 relationships with 1 set of wires (!!!)
But only one transaction can go on at a time
  The rest have to wait
  Queue up at “bus arbitration”

## Slide 19: PCI Bus evolution
PCI started life out as a bus
  32 physical bits double for address/data
But a parallel bus has many limitations
  Multiplexing address/data for many requests
  Slowest device must be able to tell what’s happening
   Bus speed is set to that of the slowest device

## Slide 20: PCI Express “Bus”
No longer a parallel bus
Really a collection of fast serial channels or “lanes”
Devices can use as many as they need to achieve a desired bandwidth
Slow devices don’t have to share with fast ones
Both motherboard slots and daughter cards are sized for the number of lanes, x4, x8, or x16
Speeds (in an x16 configuration):
  v1.x: 4 GB/s (40 GT/s)
  v2.x: 8 GB/s (80 GT/s)
  v3.0: 15.75 GB/s (128 GT/s)
  v4.0: 31.51 GB/s (256 GT/s)
  3.0+ Speeds are competitive with block memory-to-memory operations on the CPU

## Slide 21: PCI Express Interface (Linux)
One of the successes of device abstraction in Linux was the ability to migrate from PCI to PCI-Express
Although the physical interconnect changed completely, the old API still worked
Drivers written for older PCI devices still worked, because of the standardized API for both models of the interface
PCI register map:
Figure from “Linux Device Drivers,” 3rd Ed, Jonathan Corbet, Alessandro Rubini, Greg Kroah-Hartman
Notes: Up to size address regions, 4 GB addressable I/O memory

## Slide 22: PCI Express Bus
In practice PCI is used as the interface to many other interconnects on a PC:
Figure from “Linux Device Drivers,” 3rd Ed, Jonathan Corbet, Alessandro Rubini, Greg Kroah-Hartman

## Slide 23: OS Solutions
Reduce the impact of I/O delays by doing other useful work in the meantime.
Reduce overhead through user level drivers

## Slide 24: How do we hide I/O latency?
Blocking Interface: “Wait”
  When request data (e.g., read() system call), put process to sleep until data is ready
  When write data (e.g., write() system call), put process to sleep until device is ready for data
Non-blocking Interface: “Don’t Wait”
  Returns quickly from read or write request with count of bytes successfully transferred to kernel
  Read may return nothing, write may write nothing
Asynchronous Interface: “Tell Me Later”
  When requesting data, take pointer to user’s buffer, return immediately; later kernel fills buffer and notifies user
  When sending data, take pointer to user’s buffer, return immediately; later kernel takes data and notifies user

## Slide 25: Kernel vs User-level I/O
Both are popular/practical for different reasons:
  Kernel-level drivers for critical devices that must keep running, e.g. display drivers.
    Programming is a major effort, correct operation of the rest of the kernel depends on correct driver operation.
  User-level drivers for devices that are non-threatening, e.g USB devices in Linux (libusb).
    Provide higher-level primitives to the programmer, avoid every driver doing low-level I/O register tweaking.
    The multitude of USB devices can be supported by Less-Than-Wizard programmers.
    New drivers don’t have to be compiled for each version of the OS, and loaded into the kernel.

## Slide 26: Kernel vs User-level Programming Styles
Kernel-level drivers
  Have a much more limited set of resources available:
    Only a fraction of libc routines typically available.
    Memory allocation (e.g. Linux kmalloc) much more limited in capacity and required to be physically contiguous.
    Should avoid blocking calls.
    Can use asynchrony with other kernel functions but tricky with user code.
User-level drivers
  Similar to other application programs but:
    Will be called often – should do its work fast, or postpone it – or do it in the background.
    Can use threads, blocking operations (usually much simpler) or non-blocking or asynchronous.

## Slide 27: Summary
IO and data transfers often described by linear performance model and utilization model
  T(n) = S + n/B
  U = Service Rate / Request Rate
But for shared resources burstiness in request rate can introduce substantial delays
Subsystem design focuses on eliminating bottlenecks, e.g.,
  disk scheduling to minimize seek and latency overhead
  Multiple lanes to allow simultaneous transfers
  Non-blocking requests (or threads) to overlap IO and compute
  User level access to devices