## Slide 1: Towards the Internet of Everything…
David E. Culler
CS162 – Operating Systems and Systems Programming
http://cs162.eecs.berkeley.edu/
Lecture 41
December 5, 2014
8

## Slide 2: 1997 - The Internet of Every Computer

## Slide 3: 2007 - The Internet of Every Body

## Slide 4: 2017 - The Internet of Everyday Things

## Slide 5: Why “Real” Information is so Important
Improve Productivity
Protect Health
High-Confidence Transport
Enhance Safety & Security
Improve Food & H20
Save Resources
Preventing Failures
Increase
Comfort
Enable New Knowledge

## Slide 6: 2013

## Slide 7: 2014

## Slide 8: 2013

## Slide 9: 2014

## Slide 10: 2014

## Slide 12: Broad Technology Trends
Today: 1 million transistors per $
Moore’s Law: # transistors on cost-effective chip doubles every 18 months
Mote!
years
Computers
Per Person
103:1
1:106
Laptop
PDA
Mainframe
Mini
Workstation
PC
Cell
1:1
1:103
Bell’s Law: a new computer class emerges every 10 years
Same fabrication technology provides CMOS radios for communication and micro-sensors

## Slide 13: ‘Low-Tech’ Enabling Technology
Microcontroller
Radio
Communication
Flash
Storage
Sensors
IEEE 802.15.4
Network

## Slide 14: The Systems Challenge
applications
service
network
system
architecture
data
mgmt
Monitoring & Managing Spaces and Things
technology
sensing
Power
Comm.
actuate
Miniature, low-power connections to the physical world
Proc
Store
Notes: Now that we’ve set the context, here’s a picture of the rest of the presentation
I do
Kris does

## Slide 15: Leading Internet Research Perspective ~ 1999
“Resource constraints may cause us to give up the layered architecture.”
“Sheer numbers of devices, and their unattended deployment, will preclude reliance on broadcast communication or the configuration currently needed to deploy and operate networked devices.”
“There are significant robustness and scalability advantages to designing applications using localized algorithms.”
“Unlike traditional networks, a sensor node may not need an identity (e.g. address).”
“It is reasonable to assume that sensor networks can be tailored to the application at hand.”
We were wrong...

## Slide 16: Key WSN Research Developments
Event-Driven Component-Base Operating System
  Framework for building System & Network abstractions
  Low-Power Protocols
  Hardware and Application Specific
Idle listening
  All the energy is consumed by listening for a packet to receive
  => Turn radio on only when there is something to hear
Reliable routing on Low-Power & Lossy Links
  Power, Range, Obstructions => multi-hop
  Always at edge of SNR => loss is common
  => monitoring, retransmission, and local rerouting
Trickle – don’t flood (tx rate < 1/density, and < info change)
  Connectivity is determined by physical points of interest, not network designer.
  never naively respond to a broadcast
  re-broadcast very very politely

## Slide 17: Decade of Networking (sans Architecture)
Link
Network
Transport
Application
1999
2002
2003
2004
2005
2006
2007
SPIN
2000
2001
2008
Broadcast Storm
TinyOS 0.6
WooMAC
GAF
S-MAC
Aloha PS
PSFQ
GDI
CODA
MintRoute
T-MAC
RMST
B-MAC
MultihopLQI
Fusion
Deluge
FPS
WiseMAC
SP
Drip
Drain
BVR
Redwoods
North Sea
SCP-MAC
PEDAMACS
X-MAC
Volcano
CTP
Flush
Golden Gate Bridge
S4
Dip

## Slide 18: Internet of Every Thing – Realized 2008
Footprint, power, packet size, & bandwidth
Open version 27k / 4.6k
 | ROM | RAM
CC2420 Driver | 3149 | 272
802.15.4 Encryption | 1194 | 101
Media Access Control | 330 | 9
Media Management Control | 1348 | 20
6LoWPAN + IPv6 | 2550 | 0
Checksums | 134 | 0
SLAAC | 216 | 32
DHCPv6 Client | 212 | 3
DHCPv6 Proxy | 104 | 2
ICMPv6 | 522 | 0
Unicast Forwarder | 1158 | 451
Multicast Forwarder | 352 | 4
Message Buffers | 0 | 2048
Router | 2050 | 106
UDP | 450 | 6
TCP | 1674 | 50
(including runtime)
* Production implementation on TI msp430/cc2420
24038 | ROM
3598 | RAM

## Slide 19: Internet of Every Thing – standardized 2010

## Slide 20: Smart meter rollouts
http://www.edisonfoundation.net/iee/Documents/IEE_SmartMeterRollouts_0512.pdf
Proprietary / Zigbee
Open IPv6, …

## Slide 21: Hardware

## Slide 22: The Mote/TinyOS revolution…
SmartDust
WeC
Rene
Intel
rene’
99
98
00
01
03
02
04
06
05
07
SENSIT
Expedition
NEST
NETS/ NOSS
CENS STC
NSF
Cyber-Physical
Mica
Intel/UCB
dot
Intel
iMOTE
XBOW
cc-dot
XBOW
mica2
XBOW
rene2
Intel
cf-mica
Bosch
cc-mica
Dust Inc
blue cc-TI
digital sun
rain-mica
XBOW
mica
zeevo BT
Telos
XBOW
micaZ
Intel
MOTE2
Eyes
BTNode
trio
8 kB rom
½ kB ram
48 kB rom
10 kB ram
802.15.4
LoWPAN/IPv6
Epic
11
IETF RPL
10
Mote inside
uP => Arm Cortex
Radio => 802.15.4g narrow=band freq. hopper
TinyOS too
SOC from here

## Slide 23: Example 2004 Mote: TelosB
CC2420
IEEE 802.15.4 radio
PIFA Antenna
USB-serial
10 pin expansion
6 pin expansion
SHT11 humidity / temp
TI MSP430 F1611
reset button
user button
TSR photodiode
PAR photodiode
LEDs
(bottom)
ST M25P80 flash
reset support
jtag
serial ID

## Slide 24: Microcontrollers
48K ROM
10K RAM
250 kbps

## Slide 25: Mote Characteristics
Limited resources
  RAM, ROM, Computation, Energy
   Wakeup, do work as quickly as possible, sleep
Hardware modules operate concurrently
  No parallel execution of code (not Core 2 Duos!)
   Asynchronous operation is first class
Diverse application requirements
   Efficient modularity
Robust operation
  Numerous, unattended, critical
   Predictable operation

## Slide 26: What we mean by “Low Power”
2 AA => 1.5 amp hours (~4 watt hours)
Cell => 1 amp hour (3.5 watt hours)
Cell: 500 -1000 mW => few hours active
WiFi: 300 - 500 mW => several hours
GPS: 50 – 100 mW => couple days
WSN: 50 mW active, 20 uW passive
450 uW => one year
45 uW => ~10 years
Ave Power = fact * Pact + fsleep * Psleep + fwaking * Pwaking
* System design
* Leakage (~RAM)
* Nobody fools mother nature

## Slide 27: Storm 2014

## Slide 28: TinyOS – Framework for Innovation
Storage
Processing
Wireless
Sensors
WSN mote platform
Radio Serial
Flash
ADC, Sensor I/F
MCU, Timers, Bus,…
Link
Network
Protocols
Blocks, Logs, Files
Scheduling, Management
Streaming drivers
Over-the-air
Programming
Applications and Services
Communication Centric
Resource-Constrained
Event-driven Execution

## Slide 29: UCB => A worldwide community
Storage
Wireless
Processing
Sensors
SmartDust
NEST
Wireless Sensor Networks

## Slide 30: Low Power Networking in the Real World
Applications
system
Storage
Processing
Wireless
Sensors
Technology
architecture
Network
Notes: Now that we’ve set the context, here’s a picture of the rest of the presentation
I do
Kris does

## Slide 31: A Low-Power Standard Link
 | 802.15.4 | 802.15.1 | 802.15.3 | 802.11 | 802.3
Class | WPAN | WPAN | WPAN | WLAN | LAN
Lifetime (days) | 100-1000+ | 1-7 | Powered | 0.1-5 | Powered
Net Size | 65535 | 7 | 243 | 30 | 1024
BW (kbps) | 20-250 | 720 | 11,000+ | 11,000+ | 100,000+
Range (m) | 1-75+ | 1-10+ | 10 | 1-100 | 185 (wired)
Goals | Low Power, Large Scale, Low Cost | Cable Replacement | Cable Replacement | Throughput | Throughput
Low Transmit power, Low Signal-to-noise Ratio (SNR), modest BW, Little Frames
BTLE

## Slide 32: The “Idle Listening” Problem
The power consumption of “short range” (i.e., low-power) wireless communications is roughly the same when
  transmitting,
  receiving,
  or simply ON, “listening” for potential reception.
  IEEE 802.15.4, Zwave, Bluetooth, …, WiFi
Radio must be ON (listening) in order receive anything.
  Transmission is rare
  Listening happens all the time
Energy consumption dominated by idle listening
Do Nothing Well

## Slide 33: Communication Power – Passive Vigilance
Listen just when there is something to hear …
Sleep
~10 uA
Transmit
~20 mA x 1-5 ms
[20 - 100 uAs]
I
I
Time
Time
Listen
~20 mA x * ???
Receive
~20 mA x 2-6 ms

## Slide 34: 3 Basic Solution Techniques
Scheduled Listening
  Arrange a schedule of communication Time Slots
  Maintain coordinated clocks and schedule
  Listen during specific “slots”
  Many variants:
    Aloha, Token-Ring, TDMA, Beacons, Bluetooth piconets, …
    S-MAC, T-MAC, PEDAMACS, TSMP, FPS, …
Sampled Listening
  Listen for very short intervals to detect eminent transmissions
  On detection, listen actively to receive
  DARPA packet radio, LPL, BMAC, XMAC, …
  Maintain “always on” illusion, Robust
Listen after send (with powered infrastructure)
  After transmit to a receptive device, listen for a short time
  Many variants: 802.11 AMAT, Key fobs, remote modems, …
Many hybrids possible
802.15.4e

## Slide 35: Self-Organized Routing - nutshell
0
1
1
2
2
2
2
2
Receiver diversity through dynamic rerouting
Retrans. rate < 1/density
Neighbor table exceeds RAM
Dissem. rate < change

## Slide 36: Key IPv6 Contributions
Large simple address
  Network ID + Interface ID
  Plenty of addresses, easy to allocate and manage
Autoconfiguration and Management
  ICMPv6
Integrated bootstrap and discovery
  Neighbors, routers, DHCP
Protocol options framework
  Plan for extensibility
Simplify for speed
  MTU discovery with min
6-to-4 translation for compatibility
Prefix
IID
ICMPv6
IPv6 Base
HbH Opt
Routing
Fragment
Dst Opt
128 bits

## Slide 37: 6LoWPAN – IPv6 over 802.15.4
Large IP Address & Header => 16 bit short address / 64 bit EUID
Minimum Transfer Unit => Fragmentation
Short range & Embedded => Multiple Hops
Link frame
ctrl
src UID
len
chk
dst UID
link payload
cls
flow
len
hops
src IP
dst IP
net payload
Network packet
UDP datagram or
TCP stream segment
transport header
application payload
…, modbus, BacNET/IP, … , HTML, XML, …, ZCL
16 B
128 Bytes MAX
1280 Bytes MIN
16 B
40 B + options
NH
?

## Slide 38: 6LoWPAN adaptation layer
802.5
Token Ring
802.3
Ethernet
802.11
WiFi
802.3a
Ethernet
10b2
802.3i
Ethernet
10bT
802.3y
Ethernet
100bT
802.3ab
Ethernet
1000bT
802.3an
Ethernet
1G bT
802.11a
WiFi
802.11b
WiFi
802.11g
WiFi
802.11n
WiFi
X3T9.5
FDDI
Serial
Modem
GPRS
ISDN
DSL
Sonet
Transport (UDP/IP, TCP/IP)
Application (Telnet, FTP, SMTP, SNMP, HTTP)
Diverse Object and Data Models (HTML, XML, …, BacNet, …)
802.15.4
LoWPAN
Network (IP)
Link
2: link
3: net
4: xport
7: app
1: phy
6LoWPAN

## Slide 39: 6LoWPAN – IP Header Optimization
Eliminate all fields in the IPv6 header that can be derived from the 802.15.4 header in the common case
  Source address : derived from link address
  Destination address : derived from link address
  Length : derived from link frame length
  Traffic Class & Flow Label : zero
  Next header : UDP, TCP, or ICMP
Additional IPv6 options follow as options
Link frame
ctrl
src UID
len
chk
dst UID
Network packet
40 B
6LoWPAN adaptation header
hops
3 B
cls
flow
len
hops
src IP
dst IP
net payload
NH

## Slide 40: Internet – WSN assimilated
802.5
Token Ring
802.3
Ethernet
802.11
WiFi
802.3a
Ethernet
10b2
802.3i
Ethernet
10bT
802.3y
Ethernet
100bT
802.3ab
Ethernet
1000bT
802.3an
Ethernet
1G bT
802.11a
WiFi
802.11b
WiFi
802.11g
WiFi
802.11n
WiFi
X3T9.5
FDDI
Serial
Modem
GPRS
ISDN
DSL
Sonet
Transport (UDP/IP, TCP/IP)
Application (Telnet, FTP, SMTP, SNMP, HTTP)
Diverse Object and Data Models (HTML, XML, …, BacNet, …)
802.15.4
LoWPAN
Network (IP)
Link
2: link
3: net
4: xport
7: app
1: phy
802.15.4e
802.15.4g
P1901.2
6LoWPAN RFC6282
RPL RFC6550
COAP

## Slide 41: Complete Embedded IPv6 Stack
Link
Net
Tran
App
Media Management Control
Remote Media
Link Stats
Neighbor Table |  |  |  |  | 
Addr | Period | Phase | Pending | RSSI | PRR
Local Media
Sample Period
Sample Phase
Router
Routing Protocol
Routing Table
Prefix | Next
Stateless
Autoconf
Autoconf
DHCPv6
UDP
TCP
6LoWPAN Adaptation
ICMPv6
Data
Ack
HTTP
Telnet
SNMP
DNS
…
Forwarder
Multicast
Send Manager
Buffer
Unicast
Queue
Forwarding Table
Send Manager
Prefix | Next
Default | 

## Slide 42: Adding up the pieces
 | ROM | RAM
CC2420 Driver | 3149 | 272
802.15.4 Encryption | 1194 | 101
Media Access Control | 330 | 9
Media Management Control | 1348 | 20
6LoWPAN + IPv6 | 2550 | 0
Checksums | 134 | 0
SLAAC | 216 | 32
DHCPv6 Client | 212 | 3
DHCPv6 Proxy | 104 | 2
ICMPv6 | 522 | 0
Unicast Forwarder | 1158 | 451
Multicast Forwarder | 352 | 4
Message Buffers | 0 | 2048
Router | 2050 | 106
UDP | 450 | 6
TCP | 1674 | 50
(including runtime)
* Production implementation on TI msp430/cc2420
24038 | ROM
3598 | RAM

## Slide 43: Real World – “Signals” and “Information”
What is the bandwidth of the weather?
What is the nyquist of the soil?
What is the placement noise?
What is the sampling jitter error?
How do you classify it?
How do you search it?

## Slide 44: The Macroscope - Keck HydroWatch
Sagehen wireless
data infrastructure
Colored digital vegetation and topography from a lidar survey

## Slide 45: Networking the Physical World
Bi-directional
Patch Antenna
Mote + Accelerometer Board)
Battery

## Slide 46: Ambient Vibration
8 nodes
51 nodes
1125 ft
4200 ft
500 ft
246 ft
SF
(south)
Sausalito
(north)
Vertical Sensor at Quarter-span 365m North of the South Tower
Vertical Sensor at Quarter-span 335m South of the North Tower

## Slide 47: Bonus – Spectacular Views

## Slide 48: Real World …

## Slide 49: The “Killer App” for WSNs
Energy and the environmental impact of extraction, use, and disposal
THE problem of the Industrial Age
We need to find Information Age solutions to THE Industrial Age Problem
=> Fundamental transformation in the architecture of the electric grid

## Slide 50: Traditional Load-Following Grid
Baseline + Dispatchable Tiers
Oblivious Loads
Transmission
Generation
Demand
Distribution

## Slide 51: Towards an ‘Aware’ Energy Infrastructure
Baseline + Dispatchable Tiers
Oblivious Loads
Communication
Non-Dispatchable
Sources
Communication
Aware Interactive Loads
Transmission
Generation
Demand
Distribution

## Slide 52: How can we transform buildings into fundamentally more agile machines?
Programmable
Separation of the hardware capabilities (primitives)
from the universe of potential behaviors (applications)
allow them to be tailored to our desires
  To the full extent of the underlying capabilities
And become good citizens of the grid

## Slide 53: Software Defined Buildings
Building Application Programming Interface (BAS)
  Enable application portability and innovation
Building Operation System & Services (BOSS)
  Physical services and distributed device drivers
  Middle services: mapping, transactions, RAS
  Application services: baselining, ensemble, …
Innovate in Model-Driven Predictive Control
  objectives: efficiency, satisfaction, supply-following
Rich Human-Building Interaction
  Location, personal and ambient devices, gestures, …
Introduce meaningful security

## Slide 54: BOSS Architecture – first cut
sMAP
driver inst
sMAP
driver inst
sMAP
driver inst
sMAP
driver inst
6LoWPAN
XML/HTTP
BACnet/IP
…
Authorization Service
CPS Application Environment
Application Programming Interface & Runtime
Data feeds,
Calendar, …
Bldg Mgmt System
CO2/Motion/…
Physical Systems
OPC-DA
ModBus
RS-485
Hardware Presentation Layer
publish
command
Request/Auth Token
Stream Query
Advanced Control Apps
Model Training
prognostics/ diagnostics
External Interactions
Occupant displays & interaction
Submit/Callback
TimeSeries
metadata
Context & Historian
Deployment key, config & base metadata
System Services
Transaction Manager
Reliability
Fault-Tolerance
Security
Data Archiving
Hardware Independence
Authorization Manager
Driver
Driver
Driver
Driver
Driver
Bldg
Entity/Rel
Graph

## Slide 55: The Revolution
10M
1B
10B
1T
100B
1990
2010
2020
Computers
People
Everything
Connectivity
Community
Awareness
2000

## Slide 56: The Revolution
10M
1B
10B
1T
100B
1990
2000
2010
2020
Computers
People
Everything
Cost to Connect
Things Connected
$100
$1
1¢

## Slide 57: CS162: Spiral
intro
OS Concepts (3)
Concurrency (6)
Address Space (4)
File Systems (8)
Distributed Systems (8)
Reliability, Security, Cloud (8)