## Slide 1: CS162 Operating Systems and Systems Programming Lecture 3 Processes (con’t), Fork, Introduction to I/O
January 29th, 2019
Prof. John Kubiatowicz
http://cs162.eecs.Berkeley.edu

## Slide 2: Recall: Four fundamental OS concepts
Thread
  Single unique execution context
  Program Counter, Registers, Execution Flags, Stack
Address Space w/ translation
  Programs execute in an address space that is distinct from the memory space of the physical machine
Process
  An instance of an executing program is a process consisting of an address space and one or more threads of control
Dual Mode operation/protection
  Only the “system” has the ability to access certain resources
  The OS and the hardware are protected from user programs and user programs are isolated from one another by controlling the translation from program virtual addresses to machine physical addresses

## Slide 3: Recall: give the illusion of multiple processors?
vCPU3
vCPU2
vCPU1
Shared Memory
Assume a single processor. How do we provide the illusion of multiple processors?
  Multiplex in time!
  Multiple “virtual CPUs”
Each virtual “CPU” needs a structure to hold:
  Program Counter (PC), Stack Pointer (SP)
  Registers (Integer, Floating point, others…?)
How switch from one virtual CPU to the next?
  Save PC, SP, and registers in current state block
  Load PC, SP, and registers from new state block
What triggers switch?
  Timer, voluntary yield, I/O, other things
vCPU1
vCPU2
vCPU3
vCPU1
vCPU2
Time

## Slide 4: Recall: Single and Multithreaded Processes
Threads encapsulate concurrency: “Active” component
Address spaces encapsulate protection: “Passive” part
  Keeps buggy program from trashing the system
Why have multiple threads per address space?
Notes: Sometimes need parallelism for a single job, and processes are very expensive – to start, switch between, and to communicate between

## Slide 5: Recall: Simple address translation with Base and Bound
code
Static Data
heap
stack
code
Static Data
heap
stack
code
Static Data
heap
stack
0000…
FFFF…
1000…
0000…
Program
address
Base Address
Bound
<
1000…
1100…
0100…
Can the program touch OS?
Can it touch other programs?
0010…
0010…
Addresses translated on-the-fly
1010…
0100…

## Slide 6: Simple B&B: User => Kernel
OS
Proc 1
Proc 2
Proc n
…
code
Static Data
heap
stack
code
Static Data
heap
stack
code
Static Data
heap
stack
0000…
FFFF…
1000…
1100…
3000…
3080…
Base
1000 …
1100…
Bound
xxxx…
uPC
regs
sysmode
…
0
PC
0000…
FFFF…
00FF…
How to return to system?
0000 1234

## Slide 7: Simple B&B: Interrupt
OS
Proc 1
Proc 2
Proc n
…
code
Static Data
heap
stack
code
Static Data
heap
stack
code
Static Data
heap
stack
0000…
FFFF…
1000…
1100…
3000…
3080…
Base
1000 …
1100 …
Bound
0000 1234
uPC
regs
sysmode
…
1
PC
0000…
FFFF…
00FF…
How to save registers and set up system stack?
IntrpVector[i]

## Slide 8: Simple B&B: Switch User Process
OS
Proc 1
Proc 2
Proc n
…
code
Static Data
heap
stack
code
Static Data
heap
stack
code
Static Data
heap
stack
0000…
FFFF…
1000…
1100…
3000…
3080…
Base
3000 …
0080 …
Bound
0000 0248
uPC
regs
sysmode
…
1
PC
0000…
FFFF…
00D0…
How to save registers and set up system stack?
0001 0124
1000 …
1100 …
0000 1234
regs
00FF…
RTU

## Slide 9: Simple B&B: “resume”
OS
Proc 1
Proc 2
Proc n
…
code
Static Data
heap
stack
code
Static Data
heap
stack
code
Static Data
heap
stack
0000…
FFFF…
1000…
1100…
3000…
3080…
Base
3000 …
0080 …
Bound
xxxx xxxx
uPC
regs
sysmode
…
0
PC
0000…
FFFF…
00D0…
How to save registers and set up system stack?
000 0248
1000 …
1100 …
0000 1234
regs
00FF…
RTU

## Slide 10: Running Many Programs
We have the basic mechanism to
  switch between user processes and the kernel,
  the kernel can switch among user processes,
  Protect OS from user processes and processes from each other
Questions ???
  How do we represent user processes in the OS?
  How do we decide which user process to run?
  How do we pack up the process and set it aside?
  How do we get a stack and heap for the kernel?
  Aren’t we wasting are lot of memory?

## Slide 11: Process Control Block
Kernel represents each process as a process control block (PCB)
  Status (running, ready, blocked, …)
  Register state (when not ready)
  Process ID (PID), User, Executable, Priority, …
  Execution time, …
  Memory space, translation, …
Kernel Scheduler maintains a data structure containing the PCBs
Scheduling algorithm selects the next one to run

## Slide 12: Scheduler
Scheduling: Mechanism for deciding which processes/threads receive the CPU
Lots of different scheduling policies provide …
  Fairness or
  Realtime guarantees or
  Latency optimization or ..
if ( readyProcesses(PCBs) ) {
nextPCB = selectProcess(PCBs);
run( nextPCB );
} else {
run_idle_process();
}

## Slide 13: Simultaneous MultiThreading/Hyperthreading
Hardware scheduling technique
  Superscalar processors can execute multiple instructions that are independent.
  Hyperthreading duplicates register state to make a second “thread,” allowing more instructions to run.
Can schedule each thread as if were separate CPU
  But, sub-linear speedup!
Original technique called “Simultaneous Multithreading”
  http://www.cs.washington.edu/research/smt/index.html
  SPARC, Pentium 4/Xeon (“Hyperthreading”), Power 5
Colored blocks show
instructions executed
Notes: Intel seems to be discarding SMT in Silvermont because of power problems

## Slide 14: Also Recall: The World Is Parallel
Intel Skylake (2017)
  28 Cores
  Each core has two hyperthreads!
  So: 54 Program Counters(PCs)
Scheduling here means:
  Pick which core
  Pick which thread
Space of possible scheduling much more interesting
  Can afford to dedicate certain cores to housekeeping tasks
  Or, can devote cores to services (e.g. Filesystem)

## Slide 15: Is Branch and Bound a Good-Enough Protection Mechanism?
NO: Too simplistic for real systems
Inflexible/Wasteful:
  Must dedicate physical memory for potential future use
  (Think stack and heap!)
Fragmentation:
  Kernel has to somehow fit whole processes into contiguous block of memory
  After a while, memory becomes fragmented!
Sharing:
  Very hard to share any data between Processes or between Process and Kernel
  Need to communicate indirectly through the kernel…

## Slide 16: Better: x86 – segments and stacks
CS
EIP
SS
ESP
DS
ECX
ES
EDX
ESI
EDI
EAX
EBX
code
Static Data
heap
stack
code
Static Data
heap
stack
CS:
EIP:
SS:
ESP:
Processor Registers
Start address, length and access rights associated with each segment

## Slide 17: Alternative: Address Mapping
Prog 1
Virtual
Address
Space 1
Prog 2
Virtual
Address
Space 2
Code
Data
Heap
Stack
Code
Data
Heap
Stack
Data 2
Stack 1
Heap 1
OS heap &
Stacks
Code 1
Stack 2
Data 1
Heap 2
Code 2
OS code
OS data
Translation Map 1
Translation Map 2
Physical Address Space

## Slide 18: Administrivia: Getting started
Kubiatowicz Office Hours:
  1-2pm, Monday & Thursday
Homework 0 Due Today!
  Get familiar with the cs162 tools
  configure your VM, submit via git
  Practice finding out information:
    How to use GDB? How to understand output of unix tools?
    We don’t assume that you already know everything!
    Learn to use “man” (command line), “help” (in gdb, etc), google
Should be going to sections now – Important information there
  Any section will do until groups assigned
THIS Friday is Drop Deadline! HARD TO DROP LATER!
  If you know you are going to drop, please do so to leave room for others on waitlist!

## Slide 19: Administrivia (Con’t)
Group sign up via autograder form next week
  Get finding groups of 4 people ASAP
  Priority for same section; if cannot make this work, keep same TA
  Remember: Your TA needs to see you in section!
Midterm 1 conflicts
  We will handle these conflicts after have final class roster
  I know about one problem with Midterm 1 scheduling, and it can be dealt with. Have I missed any others?
  Watch for queries by HeadTA to collect information

## Slide 20: Recall: 3 types of Kernel Mode Transfer
Syscall
  Process requests a system service, e.g., exit
  Like a function call, but “outside” the process
  Does not have the address of the system function to call
  Like a Remote Procedure Call (RPC) – for later
  Marshall the syscall id and args in registers and exec syscall
Interrupt
  External asynchronous event triggers context switch
  eg. Timer, I/O device
  Independent of user process
Trap or Exception
  Internal synchronous event in process triggers context switch
  e.g., Protection violation (segmentation fault), Divide by zero, …

## Slide 21: Recall: User/Kernel (Privileged) Mode
User Mode
Kernel Mode
Full HW access
Limited HW access
exec
syscall
exit
rtn
interrupt
rfi
exception

## Slide 22: Implementing Safe Kernel Mode Transfers
Important aspects:
  Controlled transfer into kernel (e.g., syscall table)
  Separate kernel stack
Carefully constructed kernel code packs up the user process state and sets it aside
  Details depend on the machine architecture
Should be impossible for buggy or malicious user program to cause the kernel to corrupt itself

## Slide 23: Need for Separate Kernel Stacks
Kernel needs space to work
Cannot put anything on the user stack (Why?)
Two-stack model
  OS thread has interrupt stack (located in kernel memory) plus User stack (located in user memory)
  Syscall handler copies user args to kernel space before invoking specific function (e.g., open)
  Interrupts (???)

## Slide 24: Before

## Slide 25: During

## Slide 26: Kernel System Call Handler
Vector through well-defined syscall entry points!
  Table mapping system call number to handler
Locate arguments
  In registers or on user (!) stack
Copy arguments
  From user memory into kernel memory
  Protect kernel from malicious code evading checks
Validate arguments
  Protect kernel from errors in user code
Copy results back
  Into user memory

## Slide 27: Hardware support: Interrupt Control
Interrupt processing not visible to the user process:
  Occurs between instructions, restarted transparently
  No change to process state
  What can be observed even with perfect interrupt processing?
Interrupt Handler invoked with interrupts ‘disabled’
  Re-enabled upon completion
  Non-blocking (run to completion, no waits)
  Pack up in a queue and pass off to an OS thread for hard work
    wake up an existing OS thread

## Slide 28: Hardware support: Interrupt Control
OS kernel may enable/disable interrupts
  On x86: CLI (disable interrupts), STI (enable)
  Atomic section when select next process/thread to run
  Atomic return from interrupt or syscall
HW may have multiple levels of interrupts
  Mask off (disable) certain interrupts, eg., lower priority
  Certain Non-Maskable-Interrupts (NMI)
    e.g., kernel segmentation fault
    Also: Power about to fail!

## Slide 29: Interrupt Controller
Interrupts invoked with interrupt lines from devices
Interrupt controller chooses interrupt request to honor
  Interrupt identity specified with ID line
  Mask enables/disables interrupts
  Priority encoder picks highest enabled interrupt
  Software Interrupt Set/Cleared by Software
CPU can disable all interrupts with internal flag
Non-Maskable Interrupt line (NMI) can’t be disabled
Network
IntID
Interrupt
Interrupt Mask
Control
Software
Interrupt
NMI
CPU
Priority Encoder
Timer
Int Disable

## Slide 30: How do we take interrupts safely?
Interrupt vector
  Limited number of entry points into kernel
Kernel interrupt stack
  Handler works regardless of state of user code
Interrupt masking
  Handler is non-blocking
Atomic transfer of control
  “Single instruction”-like to change:
    Program counter
    Stack pointer
    Memory protection
    Kernel/user mode
Transparent restartable execution
  User program does not know interrupt occurred

## Slide 31: Putting it together: web server
Request
Reply
(retrieved by web server)
Client
Web Server

## Slide 32: Putting it together: web server
Server
Kernel
Hardware
request
buffer
reply
buffer
11. kernel copy
from user buffer
to network buffer
Network
interface
Disk interface
12. format outgoing
packet and DMA
6. disk
request
10. network
socket
write
network
socket
read
2. copy arriving
packet (DMA)
syscall
wait
interrupt
3. kernel
copy
RTU
5. file
read
syscall
8. kernel
copy
RTU
7. disk data
(DMA)
interrupt
4. parse request
9. format reply
Request
Reply

## Slide 33: Can a process create a process ?
Yes! Unique identity of process is the “process ID” (or PID)
fork() system call creates a copy of current process with a new PID
Return value from fork(): integer
  When > 0:
    Running in (original) Parent process
    return value is pid of new child
  When = 0:
    Running in new Child process
  When < 0:
    Error! Must handle somehow
    Running in original process
State of original process duplicated in both Parent and Child!
  Memory, File Descriptors (next topic), etc…

## Slide 34: Create Process: fork1.c
#include <stdlib.h>
#include <stdio.h>
#include <string.h>
#include <unistd.h>
#include <sys/types.h>
int main(int argc, char *argv[])
{
pid_t cpid, mypid;
pid_t pid = getpid(); /* get current processes PID */
printf("Parent pid: %d\n", pid);
cpid = fork();
if (cpid > 0) { /* Parent Process */
mypid = getpid();
printf("[%d] parent of [%d]\n", mypid, cpid);
} else if (cpid == 0) { /* Child Process */
mypid = getpid();
printf("[%d] child\n", mypid);
} else {
perror("Fork failed");
exit(1);
}
exit(0);
}

## Slide 35: UNIX Process Management
UNIX fork – system call to create a copy of the current process, and start it running
  No arguments!
UNIX exec – system call to change the program being run by the current process
UNIX wait – system call to wait for a process to finish
UNIX signal – system call to send a notification to another process
UNIX man pages: fork(2), exec(3), wait(2), signal(3)
Notes: UNIX splits creating a process into two steps, each of them a lot simpler.

## Slide 36: UNIX Process Management
Notes: How is this used – typically, fork a process, child and parent are now both running the same program. One sets up the child program, and runs exec – becoming the new program
The parent, usually, waits for the child to finish

## Slide 37: Parent wait for child: fork2.c
int status;
pid_t = tcpid;
…
cpid = fork();
if (cpid > 0) { /* Parent Process */
mypid = getpid();
printf("[%d] parent of [%d]\n", mypid, cpid);
tcpid = wait(&status);
printf("[%d] bye %d(%d)\n", mypid, tcpid, status);
} else if (cpid == 0) { /* Child Process */
mypid = getpid();
printf("[%d] child\n", mypid);
}
…

## Slide 38: Process Races: fork3.c
Question: What does this program print?
Does it change if you add in one of the sleep() statements?
int i;
cpid = fork();
if (cpid > 0) {
mypid = getpid();
printf("[%d] parent of [%d]\n", mypid, cpid);
for (i=0; i<10; i++) {
printf("[%d] parent: %d\n", mypid, i);
// sleep(1);
}
} else if (cpid == 0) {
mypid = getpid();
printf("[%d] child\n", mypid);
for (i=0; i>-10; i--) {
printf("[%d] child: %d\n", mypid, i);
// sleep(1);
}
}

## Slide 39: Shell
A shell is a job control system
  Allows programmer to create and manage a set of programs to do some task
  Windows, MacOS, Linux all have shells
Example: to compile a C program
  cc –c sourcefile1.c
  cc –c sourcefile2.c
  ln –o program sourcefile1.o sourcefile2.o
  ./program
HW1

## Slide 40: Signals – infloop.c
#include <stdlib.h>
#include <stdio.h>
#include <sys/types.h>
#include <unistd.h>
#include <signal.h>
void signal_callback_handler(int signum)
{
printf("Caught signal %d - phew!\n",signum);
exit(1);
}
int main() {
signal(SIGINT, signal_callback_handler);
while (1) {}
}

## Slide 41: How Does the Kernel Provide Services?
You said that applications request services from the operating system via syscall, but …
I’ve been writing all sort of useful applications and I never ever saw a “syscall” !!!
That’s right.
It was buried in the programming language runtime library (e.g., libc.a)
… Layering

## Slide 42: OS Run-Time Library
OS
Proc 1
Proc 2
Proc n
…
OS
Appln
login
Window Manager
…
OS library
OS library
OS library

## Slide 43: Recall: UNIX System Structure
User Mode
Kernel Mode
Hardware
Applications
Standard Libs

## Slide 44: A Kind of Narrow Waist
Compilers
Web Servers
Web Browsers
Databases
Email
Word Processing
Portable OS Library
System Call
Interface
Portable OS Kernel
Platform support, Device Drivers
x86
ARM
PowerPC
Ethernet (1Gbs/10Gbs)
802.11 a/g/n/ac
SCSI
Thunderbolt
Graphics
PCI
Hardware
Software
System
User
OS
Application / Service

## Slide 45: Summary
Process: execution environment with Restricted Rights
  Address Space with One or More Threads
  Owns memory (address space)
  Owns file descriptors, file system context, …
  Encapsulate one or more threads sharing process resources
Interrupts
  Hardware mechanism for regaining control from user
  Notification that events have occurred
  User-level equivalent: Signals
Native control of Process
  Fork, Exec, Wait, Signal