CS162:
Operating Systems and
Systems Programming
Lecture 22:
Storage Devices,
Performance + Queuing Theory (start)
28 July 2015
Charles Reiss
https://cs162.eecs.berkeley.edu/

---
How does the processor actually talk to the device?
Recall: How does the processor actually talk to the device?
1. Processor accesses registers in two ways:
  1. I/O instructions: in/out instructions
    1. Intel: out 0x21,AL
  2. Memory mapped I/O: load/store instructions
    1. Registers appear in physical address space
    2. I/O with load and store instructions
Device
Controller
read
write
control
status
Addressable
Memory
and/or
Queues
Registers
(port 0x20)
Hardware
Controller
Memory Mapped
Region: 0x8f008020
Bus
Interface
Address+
Data
Interrupt Request
Processor Memory Bus
CPU
Regular
Memory
Interrupt
Controller
Bus
Adaptor
Bus
Adaptor
Other Devices
or Buses

---
Recall: How does the processor actually talk to the device?
History: Seperate memory bus from I/O bus (usually much slower)
Or I/O "pin" on memory bus rather than normal address ranges
1. Processor accesses registers in two ways:
  1. I/O instructions: in/out instructions
    1. Intel: out 0x21,AL
  2. Memory mapped I/O: load/store instructions
    1. Registers appear in physical address space
    2. I/O with load and store instructions
Device
Controller
read
write
control
status
Addressable
Memory
and/or
Queues
Registers
(port 0x20)
Hardware
Controller
Memory Mapped
Region: 0x8f008020
Bus
Interface
Address+
Data
Interrupt Request
Processor Memory Bus
CPU
Regular
Memory
Interrupt
Controller
Bus
Adaptor
Bus
Adaptor
Other Devices
or Buses

---
Example: Memory-Mapped Display Controller
Recall: Memory-Mapped Display Controller
1. Hardware maps control registers and display memory into physical address space
  1. Addresses set by hardware jumpers or programming at boot time
2. Writing to display memory (“frame buffer”) changes image on screen
  1. Addr: 0x8000F000—0x8000FFFF
3. Writing graphics description to command-queue area
  1. Set of triangles to draw on graphics card
  2. Addr: 0x80010000—0x8001FFFF
4. Writing to the command register may cause on-board graphics hardware to do something
  1. Process current command queue
  2. Addr: 0x0007F004
5. Can protect with address translation
Display
Memory
0x8000F000
0x80010000
Physical Address
Space
Status
0x0007F000
Command
0x0007F004
Graphics
Command
Queue
0x80020000

---
Transferring Data To/From Controller
1. Programmed I/O:
  1. Processor reads/writes data from/to device registers
  2. Pro: Simple hardware (control + data interface the same)
  3. Con: I/O can take a lot of CPU time
  Direct Memory Access (DMA):
  1. I/O controller reads/writes from RAM without CPU
  2. OS specifies physical addresses with device registers
  3. Pro: CPU can do other things during large I/Os

---
Transferring Data To/From Controller
Sample interaction with DMA controller (from OSC):
addr
len

---
I/O Device Notifying the OS
1. The OS needs to know when:
  1. The I/O device has completed an operation
  2. The I/O operation has encountered an error
2. Two options: I/O Interrupts and Polling
[Speaker Notes: After the OS has issued a command to the I/O device either via a special I/O instruction or by writing to a location in the I/O address space, the OS needs to be notified when: (a) The I/O device has completed the operation. (b) Or when the I/O device has encountered an error. This can be accomplished in two different ways: Polling and I/O interrupt. +1 = 58 min. (Y:38)]

---
I/O Device Notifying the OS
I/O Device Notifying the OS
1. I/O Interrupts:
  1. Device generates an interrupt whenever it needs service
  2. Pro: handles unpredictable events well
  3. Con: handling each interrupt relatively high overhead
2. Polling:
  1. OS periodically checks a device-specific status register
  2. Pro: low overhead to check
  3. Con: may waste cycles checking for infrequent events
3. Actual devices combine both: High-bandwidth network adapter:
  1. Interrupt for first incoming packet
  2. Poll for following packets until hardware queues are empty
[Speaker Notes: After the OS has issued a command to the I/O device either via a special I/O instruction or by writing to a location in the I/O address space, the OS needs to be notified when: (a) The I/O device has completed the operation. (b) Or when the I/O device has encountered an error. This can be accomplished in two different ways: Polling and I/O interrupt. +1 = 58 min. (Y:38)]

---
Device Drivers
Device Drivers
1. Device Driver: Device-specific code in the kernel that interacts directly with the device hardware
  1. Supports a standard, internal interface
  2. Same kernel I/O system can interact easily with different device drivers
  3. Special device-specific configuration supported with the ioctl() system call

---
Device Drivers
1. Device Drivers typically divided into two pieces:
  1. Top half: accessed in call path from system calls
    1. implements a set of standard, cross-device calls like open(), close(), read(), write(), ioctl(), strategy()
    2. This is the kernel’s interface to the device driver
    3. Top half will start I/O to device, may put thread to sleep until finished
  2. Bottom half: run as interrupt routine
    1. Gets input or transfers next block of output
    2. May wake sleeping threads if I/O now complete

---
Basic Performance Concepts
1. Response Time or Latency: Time to perform an operation (s)
2. Bandwidth or Throughput: Rate at which operations are performed (op/s)
  1. Files: mB/s, Networks: mb/s, Arithmetic: GFLOP/s
3. Start up or “Overhead”: time to initiate an operation
4. Most I/O operations are roughly linear
  1. Latency (n) = Ovhd + n/Bandwidth

---
Example (fast network)
Example (fast network)
1. Consider a gpbs link (125 MB/s)
2. With a startup cost S = 1 ms
3. Theorem: half-power point occurs at n=S*B:
  1. When transfer time = startup T(S*B) = S + S*B/B

---
Example: at 10 ms startup (disk)
Example: at 10 ms startup (disk)

---
What determines peak BW for I/O ?
What determines peak BW for I/O ?
1. Bus Speed
  1. PCI-X: 1064 MB/s = 133 MHz x 64 bit (per lane)
  2. ULTRA WIDE SCSI: 40 MB/s
  3. Serial Attached SCSI & Serial ATA & IEEE 1394 (firewire) : 1.6 Gbps full duplex (200 MB/s)
  4. USB 1: 1.5 – 12 mb/s
2. Device Transfer Bandwidth
  1. Rotational speed of disk
  2. Write / Read rate of NAND flash
  3. Signaling rate of network link

---
Today
1. HDD architecture
2. SSD architecture
3. Introduction to Queuing Theory

---
Basic Performance Concepts
Recall: Basic Performance Concepts
1. Response Time or Latency: Time to perform an operation (s)
2. Bandwidth or Throughput: Rate at which operations are performed (op/s)
  1. Files: mB/s, Networks: mb/s, Arithmetic: GFLOP/s
3. Start up or “Overhead”: time to initiate an operation
4. Most I/O operations are roughly linear
  1. Latency (N bytes) = Overhead + N/Bandwidth

---
Storage Devices
Storage Devices
1. Magnetic disks
  1. Storage that rarely becomes corrupted
  2. Large capacity at low cost
  3. Block level random access
  4. Slow performance for random access
  5. Better performance for streaming access
2. Flash memory
  1. Storage that rarely becomes corrupted
  2. Capacity at intermediate cost (50x disk ???)
  3. Block level random access
  4. Good performance for reads; worse for random writes
  5. Erasure requirement in large blocks
  6. Wear patterns

---
Are we in an inflection point?
Are we in an inflection point?

---
Why do we care about HDDs?
1. History: Filesystems are designed to use HDDs efficiently
2. Still the cheapest online storage per byte
  1. Maybe the cheapest "cold" storage per byte

---
Hard Disk Drives (HDDs)
Hard Disk Drives (HDDs)
IBM Personal Computer/AT (1986)
30 MB hard disk - $500
30-40ms seek time
0.7-1 MB/s (est.)
IBM/Hitachi Microdrive
Western Digital Drive
http://www.storagereview.com/guide/
Read/Write Head
Side View
[Speaker Notes: Winchester disk drives developed by IBM: 1973 first drive Uses “sealed” assembly with heads floating on air bearings – Bernoulli effect]

---
The Amazing Magnetic Disk
1. Unit of Transfer: Sector
  1. Ring of sectors form a track
  2. Stack of tracks form a cylinder
  3. Heads position on cylinders
2. Disk Tracks ~ 1µm (micron) wide
  1. Wavelength of light is ~ 0.5µm
  2. Resolution of human eye: 50µm
  3. 100K on a typical 2.5” disk

---
The Amazing Magnetic Disk
The Amazing Magnetic Disk
1. Tracks separated by guard regions
  1. Reduces likelihood neighboring tracks are corrupted during writes (still a small non-zero chance)
  2. Erasure codes...
2. Track length varies across disk
  1. Outside: More sectors per track, higher bandwidth
  2. Disk is organized into regions of tracks with same # of sectors/track
  3. Only outer half of radius is used
    1. Most of the disk area in the outer regions of the disk

---
Magnetic Disk Characteristic
Magnetic Disk Geometry
1. Track: circular recording location on media
2. Cylinder: all the tracks under the
   head at a given point on all surfaces
3. Sector: minimal storage unit – 512-4096 bytes
Sector
Track
Platter
Cylinder
Head
[Speaker Notes: To read write information into a sector, a movable arm containing a read/write head is located over each surface. The term cylinder is used to refer to all the tracks under the read/write head at a given point on all surfaces. To access data, the operating system must direct the disk through a 3-stage process. (a) The first step is to position the arm over the proper track. This is the seek operation and the time to complete this operation is called the seek time. (b) Once the head has reached the correct track, we must wait for the desired sector to rotate under the read/write head. This is referred to as the rotational latency. (c) Finally, once the desired sector is under the read/write head, the data transfer can begin. The average seek time as reported by the manufacturer is in the range of 12 ms to 20ms and is calculated as the sum of the time for all possible seeks divided by the number of possible seeks. This number is usually on the pessimistic side because due to locality of disk reference, the actual average seek time may only be 25 to 33% of the number published. +2 = 34 min. (Y:14)]

---
Reading and Writing
1. 1. Seek time – move heads
   to the correct cylinder
3. 2. Rotational latency – wait for sector to come under heads
6. 3. Transfer time – time to actually read the sectors
Sector
Track
avg 5-10 ms
faster if reads adjacent
Platter
~4-8 ms (3600-7200 rpm, typical laptop/desktop)
~2-4 ms (15000 rpm; high-end server)
faster if reads adjacent
50-100 MB/sec
Cylinder
Head
[Speaker Notes: To read write information into a sector, a movable arm containing a read/write head is located over each surface. The term cylinder is used to refer to all the tracks under the read/write head at a given point on all surfaces. To access data, the operating system must direct the disk through a 3-stage process. (a) The first step is to position the arm over the proper track. This is the seek operation and the time to complete this operation is called the seek time. (b) Once the head has reached the correct track, we must wait for the desired sector to rotate under the read/write head. This is referred to as the rotational latency. (c) Finally, once the desired sector is under the read/write head, the data transfer can begin. The average seek time as reported by the manufacturer is in the range of 12 ms to 20ms and is calculated as the sum of the time for all possible seeks divided by the number of possible seeks. This number is usually on the pessimistic side because due to locality of disk reference, the actual average seek time may only be 25 to 33% of the number published. +2 = 34 min. (Y:14)]

---
Involvement of Controller (old view)
Latency = Queue time + Controller Time +
        Seek Time + Rotational latency +
    Transfer Time
Best bandwidth: large transfers of adjacent sectors from one track
(no seek time/rotational latency)
Software
Queue
(Device Driver)
Hardware
Controller
 Media Time
(Seek+Rot+Xfer)
Request
Result

---
HDD cost and density
1. Still cheaper than SSDs – <$0.03/Gbyte
2. Density >1 Terabit/square inch

---
Intelligence in the Controller (1)
1. Does OS know what cylinder it's using?
2. Used to address sectors with cylinder #, head #, track #
3. Not anymore – opaque sector #s
  1. Numerically close sector # are close to each other
4. Track skewing
  1. Different cylinders have different numbers of sectors

---
Intelligence in the Controller (2)
1. Error correcting codes –
  1. Hide corruptions from "leakage" from neighboring track writes
  2. Handle degrading hardware mostly invisibly
2. Sector sparing –
  1. Detect broken sectors, remap them
  2. Means OS doesn't really know where sectors are
3. Slip sparing –
  1. Remap more sectors to keep sequential behavior

---
Logistics
Project 3 Out – Initial Design before class Thursday

---
Break

---
Storage Devices
1. Magnetic disks
  1. Storage that rarely becomes corrupted
  2. Large capacity at low cost
  3. Block level random access
  4. Slow performance for random access
  5. Better performance for streaming access
2. Flash memory
  1. Storage that rarely becomes corrupted
  2. Capacity at intermediate cost (50x disk ???)
  3. Block level random access
  4. Good performance for reads; worse for random writes
  5. Erasure requirement in large blocks
  6. Wear patterns

---
Solid State Disks (SSDs)
Solid State Disks (SSDs)
1. NAND Multi-Level Cell (2 or 3-bit/cell) flash memory
  1. Sector (4 KB page) addressable, but stores 4-64 “pages” per memory block
2. Trapped electrons distinguish between 1 and 0
3. No moving parts
  1. No seek time / no rotational delay – 0.1-0.2ms access time
  2. Very low power and lightweight
4. Limited “write cycles”

---
SSD Architecture – Reads
SSD Architecture – Reads
Host
Buffer
Manager
(software
Queue)
Flash
Memory
Controller
SATA
DRAM
Read 4 KB Page: ~25 usec
  1. True random access: No seek or rotational latency
  2. Transfer time (SATA): ~10 microseconds
  3. Latency = Queuing Time + Controller time + Xfer Time
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND

---
SSD Architecture – Writes (I)
SSD Architecture – Writes (1)
https://en.wikipedia.org/wiki/Solid-state_drive

---
SSD Architecture – Writes (2)
1. SSDs provide same interface as disks to OS
2. … but can only overwrite 256 KB at a time
3. Controller can't just erase+rewrite 256 KB block?
  1. Slow
  2. Each block can only be erased ~10K times – some pages are likely to wear out
4. Solution: More intelligence in controller

---
SSD architecture – Block remapping
1. Controller maintains a mapping between page #s and actual locations in SSDs
  1. Spreads out erasures across entire media
  2. Avoid large erases for small amounts of new data
2. … but controller is much more complicated
4. Recall: Similar to disk controllers for bad blocks

---
Storage Performance & Price (jan 13)
Storage Performance & Price (2013)
	Bandwidth (Sequential R/W)	Cost/GB	Size
HDD2	50-100 MB/s	$0.03-0.07/GB	2-4 TB
SSD1,2	200-550 MB/s (SATA) / 6 GB/s (read PCI) / 4.4 GB/s (write PCI)	$0.87-1.13/GB	200GB-1TB
DRAM2	10-16 GB/s	$4-14*/GB / *SK Hynix 9/4/13 fire	64GB-256GB
1http://www.fastestssd.com/featured/ssd-rankings-the-fastest-solid-state-drives/
2http://www.extremetech.com/computing/164677-storage-pricewatch-hard-drive-and-ssd-prices-drop-making-for-a-good-time-to-buy
BW: SSD up to x10 than HDD, DRAM > x10 than SSD
Price: HDD x20 less than SSD, SSD x5 less than DRAM

---
SSD Summary
SSD Summary (1)
1. Pros (vs. hard disk drives):
  1. Low latency, high throughput (eliminate seek/rotational delay)
  2. No moving parts:
    1. Very light weight, low power, silent, very shock insensitive
  3. Read at memory speeds (limited by controller and I/O bus)

---
SSD Summary (2)
1. Cons
  1. Small storage (0.1-0.5x disk), expensive (20x disk ???)
    1. Hybrid alternative: combine small SSD with large HDD
  2. Asymmetric block write performance: read pg/erase/write pg
    1. Controller garbage collection (GC) algorithms have major effect on performance
  3. Limited drive lifetime
    1. 1-10K writes/page for MLC NAND
    2. Avg failure rate is 6 years, life expectancy is 9–11 years
2. These are changing rapidly

---
Recall: Basic Performance Concepts
1. Response Time or Latency: Time to perform an operation (s)
2. Bandwidth or Throughput: Rate at which operations are performed (op/s)
  1. Files: mB/s, Networks: mb/s, Arithmetic: GFLOP/s
3. Start up or “Overhead”: time to initiate an operation
4. Most I/O operations are roughly linear
  1. Latency (N bytes) = Overhead + N/Bandwidth

---
What goes into startup cost for I/O?
1. Syscall overhead
2. Operating system processing
3. Controller overhead
4. Device Startup
  1. Mechanical latency for a disk
  2. Media Access + Speed of light + Routing for network
5. Queuing (next topic)

---
I/O Performance
I/O Performance
1. Latency:
  1. Wait time – Software paths – model as queue
  2. Controller time – constant? queue?
  3. Actual service time
2. Queuing behavior:
  1. Can lead to big increases of latency as utilization increases
  2. Solutions?
Response Time = Queue + I/O device service time
User
Thread
Queue
[OS Paths]
Controller
I/O
device
100%
Response
Time (ms)
Throughput (Utilization)
(% total BW)
0
100
200
300
0%

---
I/O Performance
Long queues → more wait time
High throughput overall
Low effective throughput per operation
Effective BW = size / response time
Response Time = Queue + I/O device service time
User
Thread
Queue
[OS Paths]
Controller
I/O
device
100%
Response
Time (ms)
Throughput (Utilization)
(% total BW)
0
100
200
300
0%

---
A Simple Deterministic World
A Simple Deterministic World
Queue
Server
arrivals
departures
TQ
TS
TA
TA
TA
1. Requets arrive at fixed intervals and take constant amount of time to service
Service Rate	μ = 1/TS	operations per second
Arrival Rate	λ = 1/TA	requests per second
Utilization	U = λ/μ	%

---
A Simple Deterministic World
Queue
Server
arrivals
departures
Something that provides service
(not client/server)
TQ
TS
TA
TA
TA
1. Requets arrive at fixed intervals and take constant amount of time to service
Service Rate	μ = 1/TS	operations per second
Arrival Rate	λ = 1/TA	requests per second
Utilization	U = λ/μ	%
Offered Load	TA/TS	%

---
A Ideal Linear World
A Ideal Linear World
Offered Load < 100%
Offered Load > 100%
1
0
1
Offered Load (TA/TS)
Delivered Throughput
time
Response Time
time
Response Time
Delivered Throughput
0
1
1
Offered Load (TA/TS)
Empty Queue
Saturation
Unbounded

---
A Bursty World
A Bursty World
Queue
Server
arrivals
departures
T Q
T S
Arrivals
Q depth
Server
1. Same average arrival time, but almost all of the requests experience large queue delays
2. Even though average utilization is low

---
Modeling Uneven Arrivals
1. Simplest assumption: arrivals are equally likely at any time
  1. chance of 1 arrival between 1pm and 2pm =
     chance of 1 arrival between 2pm and 3pm
  2. chance of 1 arrival between 1:00pm and 1:01pm =
     chance of 1 arrival between 2:00pm and 2:01pm
2. Memoryless
  1. Doesn't matter when last arrival happened

---
Modeling Uneven Arrivals
1. Memoryless property implies time between arrivals follows exponential distribution
  1. probability distribution function f(x) = λe-λx
  2. mean 1/λ
x (λ)
Likelihood of an event occuring is independent of how long we’ve been waiting
Lots of short arrival intervals (i.e., high instantaneous rate)
Few long gaps (i.e., low instantaneous rate)
mean arrival interval (1/λ)

---
Background: General Use of random distributions
Other distribution
1. Generally, some probability distribution:
  1. Mean (Average) m1 = Σp(T)•T
  2. Variance σ2 = Σp(T)•(T-m1)2 = Σp(T)•(T2-m12)
  3. Squared coefficient of variance: C = σ2/m12
     Aggregate description of the distribution.
Important values of C:
  1. No variance or deterministic: C=0
  2. “memoryless” or exponential: C=1
  3. Disk response times C ≈ 1.5 (majority seeks < avg)
Mean
(m1)
mean
Memoryless
Distribution
of service times
σ

---
Introduction to Queuing Theory
Introduction to Queuing Theory
1. Queuing Theory: studies long term, steady state behavior of queuing systems
2. Based on queue behavior, and probability distributions of arrival, service times
Departures
Arrivals
Queuing System
Queue
Controller
Disk
[Speaker Notes: Old and New Testament by Kleirock Regret skipping as grad student]

---
Little’s Law
Little’s Law:
What goes in must come out (1)
1. Avg arrival rate = Avg departure rate = Throughput/Bandwidth B
  1. or queue is growing to infinity
2. Avg latency = L
arrivals
departures
N
B
L

---
Little’s Law:
What goes in must come out (2)
1. How many items are in the system?
  1. B items come in per unit time
  2. each averages L units in the system
2. → N (# requests in the system) = B (ops/s) x L (s)
arrivals
departures
N
B
L

---
Little’s Law:
What goes in must come out (3)
1. N (# requests in the system) = B (ops/s) x L (s)
2. Called Little's Law
3. About averages
4. Works regardless of arrival, service distribution
  1. (assuming system is stable)
arrivals
departures
N
B
L

---
Summary (1)
1. Devices have complex protocols for interaction and performance characteristics
  1. Response time (Latency) = Queue + Overhead + Transfer
    1. Effective BW = BW * T/(S+T)
  2. HDD: controller + seek + rotation + transfer
  3. SDD: controller + transfer (erasure & wear)
2. Bursts & High Utilization introduce queuing delays

---
Summary (2)
1. Systems (e.g., file system) designed to optimize performance and reliability
  1. Relative to performance characteristics of underlying device
2. Disk Performance:
  1. Queuing time + Controller + Seek + Rotational + Transfer
  2. Rotational latency: on average ½ rotation

---
Summary (3)
1. SSDs:
  1. Truly random reads
  2. Can only erase in large blocks a limited number of times (in hardware)
  3. Complex logic in controller to hide erase block limitation

---
Naming Queuing Systems
Distributions
M – memoryless (exponential)
G – general (anything)
D – deterministic
(constant)
X/X/N
# of requests serviced at a time
(usually 1)
Distribution of Service Times
Distribution of Arrival Times

---
Results for Memoryless Arrivals
General (anything)
Memoryless
M/G/1
λ	mean number of requests/second
Tser	mean time to service a customer (m1)
C	squared coeff. variance of service time (σ2/m12)
μ	service rate = 1/Tser
U	server utilization (0≤U≤1): U = λ/μ = λ x Tser
Tq	Time in queue = Tser x U/(1-U) x (1+C)/2
Lq	Length of queue = λ x Tq (from Little's Law)
Arrival Rate
λ
Queue
Server
Service Rate
μ=1/Tser

---
… for Memoryless Arrival + Service
Memoryless
Memoryless
M/M/1
λ	mean number of requests/second
Tser	mean time to service a customer (m1)
C	squared coeff. variance of service time (σ2/m12)
μ	service rate = 1/Tser
U	server utilization (0≤U≤1): U = λ/μ = λ x Tser
Tq	Time in queue = Tser x U/(1-U) x (1+C)/2
Lq	Length of queue = λ x Tq (from Little's Law)
= 1
Arrival Rate
λ
Queue
Server
Service Rate
μ=1/Tser

---
The Utilization Curve
Time in queue =
Tser x U/(1-U)
Cannot get 100% utilization

---
Queuing Theory Example
  1. Ten 8KB disk I/Os per second (λ = 10/s)
  2. Memoryless arrival + service (M/M/1 queue)
  3. Average service time = Tser= 20 ms (avg controller + seek + rotational delay + transfer time)
2. Questions
  1. Utilization?
    1. U = λTser = 10/s x 0.02 s = 20%
  2. Average time spent in queue?
    1. Tq= TserU/(1-U) = 0.02 s x 0.2 / 0.8 = 5 ms
  3. Average number waiting requests?
    1. Lq = λTq = 10/s x 0.005 s = 0.05 reqs
  4. Average response time?
    1. Tsys= Tq + Tser = 5 ms + 20 ms = 25 ms

---
Queuing Theory Resources
Queuing Theory Resources
1. Handouts page contains Queueing Theory Resources:
  1. Scanned pages from Patterson and Hennesey book that gives further discussion and simple proof for general eq.
  2. A complete website full of resources
2. Assume that Queueing theory is fair game for Final!

---
Optimize I/O Performance
1. Options to improve performance:
  1. Improve service time
  2. Multiple servers – e.g. use two disks instead of one
  3. Do more useful work while waiting
  4. Admission control: don't allow too many threads
    1. Response time over throughput
Response Time =
Queue + I/O device service time
User
Thread
Queue
[OS Paths]
Controller
I/O
device
100%
Response
Time (ms)
Throughput (Utilization)
(% total BW)
0
100
200
300
0%

---
Optimize I/O Performance
1. Options to improve performance:
  1. Improve service time
  2. Multiple servers – e.g. use two disks instead of one
  3. Do more useful work while waiting
  4. Admission control: don't allow too many threads
    1. Response time over throughput
Response Time =
Queue + I/O device service time
User
Thread
Queue
[OS Paths]
Controller
I/O
device
100%
Response
Time (ms)
Throughput (Utilization)
(% total BW)
0
100
200
300
0%

---
Recall: Reading and Writing
1. 1. Seek time – move heads
   to the correct cylinder
3. 2. Rotational latency – wait for sector to come under heads
6. 3. Transfer time – time to actually read the sectors
Sector
Track
avg 5-10 ms
faster if reads adjacent
Platter
~4-8 ms (3600-7200 rpm, typical laptop/desktop)
~2-4 ms (15000 rpm; high-end server)
faster if reads adjacent
50-100 MB/sec
Cylinder
Head
[Speaker Notes: To read write information into a sector, a movable arm containing a read/write head is located over each surface. The term cylinder is used to refer to all the tracks under the read/write head at a given point on all surfaces. To access data, the operating system must direct the disk through a 3-stage process. (a) The first step is to position the arm over the proper track. This is the seek operation and the time to complete this operation is called the seek time. (b) Once the head has reached the correct track, we must wait for the desired sector to rotate under the read/write head. This is referred to as the rotational latency. (c) Finally, once the desired sector is under the read/write head, the data transfer can begin. The average seek time as reported by the manufacturer is in the range of 12 ms to 20ms and is calculated as the sum of the time for all possible seeks divided by the number of possible seeks. This number is usually on the pessimistic side because due to locality of disk reference, the actual average seek time may only be 25 to 33% of the number published. +2 = 34 min. (Y:14)]

---
When does disk perform best?
1. Big sequential reads
2. Reads are in order so there's no "backtracking" when seeking/rotating
4. Idea: sort disk queue to minimize seek times
  1. Needs multiple independent reads

---
Disk Scheduling
Cylinder#
Sector#
1. How do we pick from the queue?
2. Go from cylinder 2 to cylinder 2?
  1. No seek time
3. Go from cylinder 3 to cylinder 7?
  1. Seek time
2
3
2
1
3
10
7
2
5
2
2
2
Head
User
Requests

---
Disk Scheduling
Cylinder#
Sector#
1. FIFO – First-In, First-Out
  1. Simplest, Fair, but encourages very long seeks
2. SSTF – Shortest Seek Time First
  1. Pick the closest request
  2. Problem: Starvation – never leaves
     "current" section of disk
2
3
2
1
3
10
7
2
5
2
2
2
Head
User
Requests
1
4
2
Disk Head
3

---
Disk Scheduling
Cylinder#
Sector#
1. SCAN – "Elevator" Algorithm
  1. Go from inside to outside and then back
  2. Cylinder #1 → #N → #1 → #N → ...
  3. Favors middle cylinders of disk
2. C-SCAN – Circular Scan
  1. Like SCAN, but only one direction
  2. Cylinder #1 → N; #1 → N; ...
  3. Fairer than SCAN
2
3
2
1
3
10
7
2
5
2
2
2
Head
User
Requests
1
4
2
Disk Head
3

---
Recall: Intelligence in the Controller
1. Does OS know what cylinder it's using?
2. Used to address sectors with cylinder #, head #, track #
3. Not anymore – opaque sector #s
  1. Numerically close sector # are close to each other
4. Track skewing
  1. Different cylinders have different numbers of sectors

---
Disk Scheduling
Also something controller does (disk controller has its own queue)
1. More criteria to optimize for, like process scheduling
  1. Fairness versus Throughput versus Response Time

---
Filesystems Preview

---
Building a File System
1. File System: Layer of OS that transforms block interface of disks (or other block devices) into Files, Directories, etc.
2. File System Components
  1. Disk Management: collecting disk blocks into files
  2. Naming: Interface to find files by name, not by blocks
  3. Protection: Layers to keep data secure
  4. Reliability/Durability: Keeping of files durable despite crashes, media failures, attacks, etc

---
Building a File System
Building a File System
1. User vs. System View of a File
  1. User’s view:
    1. Durable Data Structures
  2. System’s view (system call interface):
    1. Collection of Bytes (UNIX)
    2. Doesn’t matter to system what kind of data structures you want to store on disk!
  3. System’s view (inside OS):
    1. Collection of blocks (a block is a logical transfer unit, while a sector is the physical transfer unit)
    2. Block size may not be sector size; in UNIX, block size is 4KB

---
Translating from User to System View
File
System
1. What happens if user says: give me bytes 2—12?
  1. Fetch block corresponding to those bytes
  2. Return just the correct portion of the block
2. What about: write bytes 2—12?
  1. Fetch block
  2. Modify portion
  3. Write out block

---
Translating from User to System View
Translating from User to System View
File
System
1. Everything inside File System is in whole size blocks
  1. Actual disk I/O only happens in whole blocks
  2. read()/write() of less than blocks need to translate/buffer
2. From now on, file is a collection of blocks

---
Disk Management Policies
Disk Management Policies
1. Basic entities on a disk:
  1. File: user-visible group of blocks arranged sequentially in logical space
  2. Directory: user-visible index mapping names to files
2. Access disk as linear array of sectors. Two Options:
  1. Identify sectors as vectors [cylinder, surface, sector]. Sort in cylinder-major order. Not used much anymore.
  2. Logical Block Addressing (LBA). Every sector has integer address from zero up to max number of sectors.
  3. Controller translates from address = physical position
    1. First case: OS/BIOS must deal with bad sectors
    2. Second case: hardware shields OS from structure of disk

---
Things Our Filesystem Needs
1. Track free disk blocks
  1. Need to know where to put data that's written
2. Track blocks containing parts of files
  1. Need to know where to read a file from
3. Track files in a directory
  1. Need to find list of blocks given a name
4. Where do we track all of this?
  1. Somewhere on the disk

---
Summary (1)
1. Devices have complex protocols for interaction and performance characteristics
  1. Response time (Latency) = Queue + Overhead + Transfer
    1. Effective BW = BW * T/(S+T)
  2. HDD: controller + seek + rotation + transfer
  3. SDD: controller + transfer (erasure & wear)
2. Bursts & High Utilization introduce queuing delays

---
Summary (2)
1. Systems (e.g., file system) designed to optimize performance and reliability
  1. Relative to performance characteristics of underlying device
2. Disk Performance:
  1. Queuing time + Controller + Seek + Rotational + Transfer
  2. Rotational latency: on average ½ rotation
  3. Scheduling to minimize seek + rotational time

---
Summary (3)
1. Queuing Latency:
  1. M/M/1 and M/G/1 queues: simplest to analyze
  2. As utilization approaches 100%, latency → infinity
  3. time in queue = Tser x U/(1-U) x (1+C)/2