CS162:
Operating Systems and
Systems Programming
Lecture 23:
Queuing Theory /
Filesystems (Intro)
29 July 2015
Charles Reiss
https://cs162.eecs.berkeley.edu/

---
Recall: Storage Devices
1. Magnetic disks
  1. Storage that rarely becomes corrupted
  2. Large capacity at low cost
  3. Block level random access
  4. Slow performance for random access
  5. Better performance for streaming access
2. Flash memory
  1. Storage that rarely becomes corrupted
  2. Capacity at intermediate cost (50x disk ???)
  3. Block level random access
  4. Good performance for reads; worse for random writes
  5. Erasure requirement in large blocks
  6. Wear patterns

---
I/O Performance
Recall: I/O Performance
1. Latency:
  1. Wait time – Software paths – model as queue
  2. Controller time – constant? queue?
  3. Actual service time
2. Queuing behavior:
  1. Can lead to big increases of latency as utilization increases
  2. Solutions?
Response Time = Queue + I/O device service time
User
Thread
Queue
[OS Paths]
Controller
I/O
device
100%
Response
Time (ms)
Throughput (Utilization)
(% total BW)
0
100
200
300
0%

---
Recall: I/O Performance
Long queues → more wait time
High throughput overall
Low effective throughput per operation
Effective BW = size / response time
Response Time = Queue + I/O device service time
User
Thread
Queue
[OS Paths]
Controller
I/O
device
100%
Response
Time (ms)
Throughput (Utilization)
(% total BW)
0
100
200
300
0%

---
A Simple Deterministic World
A Simple Deterministic World
Queue
Server
arrivals
departures
TQ
TS
TA
TA
TA
1. Requets arrive at fixed intervals and take constant amount of time to service
Service Rate	μ = 1/TS	operations per second
Arrival Rate	λ = 1/TA	requests per second
Utilization	U = λ/μ	%

---
A Simple Deterministic World
Queue
Server
arrivals
departures
Something that provides service
(not client/server)
TQ
TS
TA
TA
TA
1. Requets arrive at fixed intervals and take constant amount of time to service
Service Rate	μ = 1/TS	operations per second
Arrival Rate	λ = 1/TA	requests per second
Utilization	U = λ/μ	%
Offered Load	TA/TS	%

---
A Ideal Linear World
A Ideal Linear World
Offered Load < 100%
Offered Load > 100%
1
0
1
Offered Load (TA/TS)
Delivered Throughput
time
Response Time
time
Response Time
Delivered Throughput
0
1
1
Offered Load (TA/TS)
Empty Queue
Saturation
Unbounded

---
A Bursty World
Queue
Server
arrivals
departures
T Q
T S
Arrivals
Q depth
Server
1. Same average arrival time, but almost all of the requests experience large queue delays
2. Even though average utilization is low

---
Modeling Uneven Arrivals
1. Simplest assumption: arrivals are equally likely at any time
  1. chance of 1 arrival between 1pm and 2pm =
     chance of 1 arrival between 2pm and 3pm
  2. chance of 1 arrival between 1:00pm and 1:01pm =
     chance of 1 arrival between 2:00pm and 2:01pm
2. Memoryless
  1. Doesn't matter when last arrival happened

---
Modeling Uneven Arrivals
1. Memoryless property implies time between arrivals follows exponential distribution
  1. probability distribution function f(x) = λe-λx
  2. mean 1/λ
x (λ)
Likelihood of an event occuring is independent of how long we’ve been waiting
Lots of short arrival intervals (i.e., high instantaneous rate)
Few long gaps (i.e., low instantaneous rate)
mean arrival interval (1/λ)

---
Background: General Use of random distributions
Other distribution
1. Generally, some probability distribution:
  1. Mean (Average) m1 = Σp(T)•T
  2. Variance σ2 = Σp(T)•(T-m1)2 = Σp(T)•(T2-m12)
  3. Squared coefficient of variance: C = σ2/m12
     Aggregate description of the distribution.
Important values of C:
  1. No variance or deterministic: C=0
  2. “memoryless” or exponential: C=1
  3. Disk response times C ≈ 1.5 (majority seeks < avg)
Mean
(m1)
mean
Memoryless
Distribution
of service times
σ

---
Queuing Theory
1. Queuing Theory: studies long term, steady state behavior of queuing systems
2. Based on queue behavior, and probability distributions of arrival, service times
Departures
Arrivals
Queuing System
Queue
Controller
Disk
[Speaker Notes: Old and New Testament by Kleirock Regret skipping as grad student]

---
Little’s Law
Little’s Law:
What goes in must come out (1)
1. Avg arrival rate = Avg departure rate = Throughput/Bandwidth B
  1. or queue is growing to infinity
2. Avg latency = L
arrivals
departures
N
B
L

---
Little’s Law:
What goes in must come out (2)
1. How many items are in the system?
  1. B items come in per unit time
  2. each averages L units in the system
2. → N (# requests in the system) = B (ops/s) x L (s)
arrivals
departures
N
B
L

---
Little’s Law:
What goes in must come out (3)
1. N (# requests in the system) = B (ops/s) x L (s)
2. Called Little's Law
3. About averages
4. Works regardless of arrival, service distribution
  1. (assuming system is stable)
arrivals
departures
N
B
L

---
Naming Queuing Systems
Distributions
M – memoryless (exponential)
G – general (anything)
D – deterministic
(constant)
X/X/N
# of requests serviced at a time
(usually 1)
Distribution of Service Times
Distribution of Arrival Times

---
Results for Memoryless Arrivals
General (anything)
Memoryless
M/G/1
λ	mean number of requests/second
Tser	mean time to service a customer (m1)
C	squared coeff. variance of service time (σ2/m12)
μ	service rate = 1/Tser
U	server utilization (0≤U≤1): U = λ/μ = λ x Tser
Tq	Time in queue = Tser x U/(1-U) x (1+C)/2
Lq	Length of queue = λ x Tq (from Little's Law)
Arrival Rate
λ
Queue
Server
Service Rate
μ=1/Tser

---
… for Memoryless Arrival + Service
Memoryless
Memoryless
M/M/1
λ	mean number of requests/second
Tser	mean time to service a customer (m1)
C	squared coeff. variance of service time (σ2/m12)
μ	service rate = 1/Tser
U	server utilization (0≤U≤1): U = λ/μ = λ x Tser
Tq	Time in queue = Tser x U/(1-U) x (1+C)/2
Lq	Length of queue = λ x Tq (from Little's Law)
= 1
Arrival Rate
λ
Queue
Server
Service Rate
μ=1/Tser

---
A Bursty World
Recall: A Bursty World
Queue
Server
arrivals
departures
T Q
T S
Arrivals
Q depth
Server
1. Same average arrival time, but almost all of the requests experience large queue delays
2. Even though average utilization is low

---
The Utilization Curve
Time in queue =
Tser x U/(1-U)
Cannot get 100% utilization

---
Queuing Theory Example
  1. Ten 8KB disk I/Os per second (λ = 10/s)
  2. Memoryless arrival + service (M/M/1 queue)
  3. Average service time = Tser= 20 ms (avg controller + seek + rotational delay + transfer time)
2. Questions
  1. Utilization?
    1. U = λTser = 10/s x 0.02 s = 20%
  2. Average time spent in queue?
    1. Tq= TserU/(1-U) = 0.02 s x 0.2 / 0.8 = 5 ms
  3. Average number waiting requests?
    1. Lq = λTq = 10/s x 0.005 s = 0.05 reqs
  4. Average response time?
    1. Tsys= Tq + Tser = 5 ms + 20 ms = 25 ms

---
Queuing Theory Resources
Queuing Theory Resources
1. Handouts page contains Queueing Theory Resources:
  1. Scanned pages from Patterson and Hennesey book that gives further discussion and simple proof for general eq.
  2. A complete website full of resources
2. Assume that Queueing theory is fair game for Final!

---
Optimize I/O Performance
1. Options to improve performance:
  1. Improve service time
  2. Multiple servers – e.g. use two disks instead of one
  3. Do more useful work while waiting
  4. Admission control: don't allow too many threads
    1. Response time over throughput
Response Time =
Queue + I/O device service time
User
Thread
Queue
[OS Paths]
Controller
I/O
device
100%
Response
Time (ms)
Throughput (Utilization)
(% total BW)
0
100
200
300
0%

---
Optimize I/O Performance
1. Options to improve performance:
  1. Improve service time
  2. Multiple servers – e.g. use two disks instead of one
  3. Do more useful work while waiting
  4. Admission control: don't allow too many threads
    1. Response time over throughput
Response Time =
Queue + I/O device service time
User
Thread
Queue
[OS Paths]
Controller
I/O
device
100%
Response
Time (ms)
Throughput (Utilization)
(% total BW)
0
100
200
300
0%

---
Recall: Reading and Writing
1. 1. Seek time – move heads
   to the correct cylinder
3. 2. Rotational latency – wait for sector to come under heads
6. 3. Transfer time – time to actually read the sectors
Sector
Track
avg 5-10 ms
faster if reads adjacent
Platter
~4-8 ms (3600-7200 rpm, typical laptop/desktop)
~2-4 ms (15000 rpm; high-end server)
faster if reads adjacent
50-100 MB/sec
Cylinder
Head
[Speaker Notes: To read write information into a sector, a movable arm containing a read/write head is located over each surface. The term cylinder is used to refer to all the tracks under the read/write head at a given point on all surfaces. To access data, the operating system must direct the disk through a 3-stage process. (a) The first step is to position the arm over the proper track. This is the seek operation and the time to complete this operation is called the seek time. (b) Once the head has reached the correct track, we must wait for the desired sector to rotate under the read/write head. This is referred to as the rotational latency. (c) Finally, once the desired sector is under the read/write head, the data transfer can begin. The average seek time as reported by the manufacturer is in the range of 12 ms to 20ms and is calculated as the sum of the time for all possible seeks divided by the number of possible seeks. This number is usually on the pessimistic side because due to locality of disk reference, the actual average seek time may only be 25 to 33% of the number published. +2 = 34 min. (Y:14)]

---
When does disk perform best?
1. Big sequential reads
2. Reads are in order so there's no "backtracking" when seeking/rotating
4. Idea: sort disk queue to minimize seek times
  1. Needs multiple independent reads

---
Disk Scheduling
Cylinder#
Sector#
1. How do we pick from the queue?
2. Go from cylinder 2 to cylinder 2?
  1. No seek time
3. Go from cylinder 3 to cylinder 7?
  1. Seek time
2
3
2
1
3
10
7
2
5
2
2
2
Head
User
Requests

---
Disk Scheduling
Cylinder#
Sector#
1. FIFO – First-In, First-Out
  1. Simplest, Fair, but encourages very long seeks
2. SSTF – Shortest Seek Time First
  1. Pick the closest request
  2. Problem: Starvation – never leaves
     "current" section of disk
2
3
2
1
3
10
7
2
5
2
2
2
Head
User
Requests
1
4
2
Disk Head
3

---
Disk Scheduling
Cylinder#
Sector#
1. SCAN – "Elevator" Algorithm
  1. Go from inside to outside and then back
  2. Cylinder #1 → #N → #1 → #N → ...
  3. Favors middle cylinders of disk
2. C-SCAN – Circular Scan
  1. Like SCAN, but only one direction
  2. Cylinder #1 → N; #1 → N; ...
  3. Fairer than SCAN
2
3
2
1
3
10
7
2
5
2
2
2
Head
User
Requests
1
4
2
Disk Head
3

---
Recall: Intelligence in the Controller
1. Does OS know what cylinder it's using?
2. Used to address sectors with cylinder #, head #, track #
3. Not anymore – opaque sector #s
  1. Numerically close sector # are close to each other
4. Track skewing
  1. Different cylinders have different numbers of sectors

---
Disk Scheduling
Also something controller does (disk controller has its own queue)
1. More criteria to optimize for, like process scheduling
  1. Fairness versus Throughput versus Response Time

---
Recall: When does disk perform best?
1. Big sequential reads
2. Reads are in order so there's no "backtracking" when seeking/rotating
4. Idea: sort disk queue to minimize seek times
  1. Needs multiple independent reads

---
Performance: multiple outstanding requests
Performance: multiple outstanding requests
Queue
Server
1. Suppose each read takes 10 ms to service.
2. If a process works for 100 ms after each read, what is the utilization of the disk?
  1. U = 10 ms / 110ms = 9%
3. What it there are two such processes?
  1. U = (10 ms + 10 ms) / 110ms = 18%
4. What if each of those processes have two such threads?

---
Logistics

---
Break

---
I/O & Storage Layers
I/O & Storage Layers
Operations, Entities and Interface
Application / Service
streams
High Level I/O
handles
Low Level I/O
registers
Syscall
file_open, file_read, … on struct file * & void *
we are here …
File System
descriptors
I/O Driver
Commands and Data Transfers
Disks, Flash, Controllers, DMA

---
Recall: C Low level I/O
Recall: C Low level I/O
1. Operations on File Descriptors – as OS object representing the state of a file
  1. User has a “handle” on the descriptor
#include <fcntl.h>
#include <unistd.h>
#include <sys/types.h>
int open (const char *filename, int flags [, mode_t mode])
int creat (const char *filename, mode_t mode)
int close (int filedes)
Bit vector of:
Access modes (Rd, Wr, …)
Open Flags (Create, …)
Operating modes (Appends, …)
Bit vector of Permission Bits:
User|Group|Other X R|W|X
http://www.gnu.org/software/libc/manual/html_node/Opening-and-Closing-Files.html

---
Recall: C Low Level Operations
Recall: C Low Level Operations
ssize_t read (int filedes, void *buffer, size_t maxsize)
 - returns bytes read, 0 => EOF, -1 => error
ssize_t write (int filedes, const void *buffer, size_t size)
 - returns bytes written
off_t lseek (int filedes, off_t offset, int whence)
int fsync (int fildes) – wait for i/o to finish
void sync (void) – wait for ALL to finish
When write returns, data is on its way to disk and can be read, but it may not actually be permanent!

---
Building a File System
1. User vs. System View of a File
  1. User’s view:
    1. Durable Data Structures
  2. System’s view (system call interface):
    1. Collection of Bytes (UNIX)
    2. Doesn’t matter to system what kind of data structures you want to store on disk!
  3. System’s view (inside OS):
    1. Collection of blocks (a block is a logical transfer unit, while a sector is the physical transfer unit)
    2. Block size may not be sector size; in UNIX, block size is 4KB

---
Translating from User to System View
File
System
1. What happens if user says: give me bytes 2—12?
  1. Fetch block corresponding to those bytes
  2. Return just the correct portion of the block
2. What about: write bytes 2—12?
  1. Fetch block
  2. Modify portion
  3. Write out block

---
Translating from User to System View
Translating from User to System View
File
System
1. Everything inside File System is in whole size blocks
  1. Actual disk I/O only happens in whole blocks
  2. read()/write() of less than blocks need to translate/buffer
2. From now on, file is a collection of blocks

---
Disk Management Policies
Disk Management Policies
1. Basic entities on a disk:
  1. File: user-visible group of blocks arranged sequentially in logical space
  2. Directory: user-visible index mapping names to files
2. Access disk as linear array of sectors
  1. Controller translates from address = physical position
    1. First case: OS/BIOS must deal with bad sectors
    2. Second case: hardware shields OS from structure of disk

---
Things Our Filesystem Needs
1. Track free disk blocks
  1. Need to know where to put data that's written
2. Track blocks containing parts of files
  1. Need to know where to read a file from
3. Track files in a directory
  1. Need to find list of blocks given a name
4. Where do we track all of this?
  1. Somewhere on the disk

---
Things Our Filesystem Needs
1. Track free disk blocks
  1. Need to know where to put data that's written
2. Track blocks containing parts of files
  1. Need to know where to read a file from
3. Track files in a directory
  1. Need to find list of blocks given a name
4. Where do we track all of this?
  1. Somewhere on the disk

---
Data Structures on Disk
1. Not quite like data structures in memory
2. Access in blocks:
  1. Can't efficiently read or write a single word – have to read or write the whole block containing it
  2. Ideally want to read/write blocks sequentially
  Durable:
  1. Need to make sure filesystem is in a sane state if power lost
  2. You may know that this doesn't always happen

---
Tracking Free Blocks: Option 1
Bitmap on disk (at well-known block #s)
  1. Bit #i is 0 if block #i is free, 1 otherwise
  2. Scan sequentially until 1
  3. Rewrite whole block to update
1. Isn't this slow?
  1. Make faster with caching
  2. Finding free block is sequential

---
Components of a File System
Components of a File System
File path
Directory
Structure
File Index
Structure
File number
Data blocks
…

---
Components of a file system
Components of a file system
file number
offset
file name
offset
Storage block
index structure
directory
Open performs name resolution
  1. Translates pathname into a “file number”
    1. Used as an “index” to locate the blocks
  2. Creates a open file description in PCB within kernel
  3. Returns a file descriptor (int) to user process
Read, Write, Seek, and Sync operate on handle
  1. Mapped to descriptor and to blocks

---
Directories
Directories

---
Directory
Possibly need slide on what links are
Directory
1. Basically a hierarchical structure
2. Each directory entry is a collection of
  1. Regular Files
  2. Directories
    1. A link to another entries
3. Each has a name and attributes
  1. Files have data
4. Links (hard links – tomorrow) make it a DAG, not just a tree
  1. Softlinks (aliases) are another name for an entry

---
File
File
Data blocks
1. Named permanent storage:
  1. Data
    1. Blocks on disk somewhere
  2. Metadata (Attributes)
    1. Owner, size, last opened, …
    2. Access rights
      1. R, W, X
      2. Owner, Group, Other (in Unix systems)
      3. Access control list in Windows system
File handle
File descriptor
File object (inode)
Attributes
Position
…

---
Performance Summary
1. Disk Performance:
  1. Queuing time + Controller + Seek + Rotational + Transfer
  2. Rotational latency: on average ½ rotation
  3. Scheduling to minimize seek + rotational time
2. Queuing Latency:
  1. M/M/1 and M/G/1 queues: simplest to analyze
  2. As utilization approaches 100%, latency → infinity
  3. time in queue = Tser x U/(1-U) x (1+C)/2

---
File System Intro
1. File System:
  1. Transforms blocks into Files and Directories
  2. Optimize for access and usage patterns
  3. Maximize sequential access, allow efficient random access

---
FAT (File Allocation Table)
FAT
Disk Blocks
0:
0:
1. Simple way to store blocks of a file: linked list
2. File number is the first block
3. FAT contains pointers to the next block for each block
  1. One entry for each data block
N-1:
N-1:
File 31, Block 0
File 31, Block 1
File 31, Block 2
31:
file number

---
FAT (File Allocation Table)
FAT
Disk Blocks
0:
0:
1. Assume (for now) we have a way to translate a path to a “file number”
2. Example: file_read 31, < 2, x>
  1. Index into FAT with file number
  2. Follow linked list to block 2 of the file
  3. Read the block from disk into mem
N-1:
N-1:
File 31, Block 0
File 31, Block 1
File 31, Block 2
31:
file number

---
FAT Properties
FAT
Disk Blocks
0:
0:
1. File is collection of disk blocks
2. FAT is linked list 1-1 with blocks
3. File Number is index of first block list for the file
4. File offset (o = B:x )
5. Follow list to get block #
6. Unused blocks = FAT free list
N-1:
N-1:
mem
File 31, Block 0
File 31, Block 1
File 31, Block 2
31:
file number
free

---
FAT Assessment
Storing the FAT
FAT
Disk Blocks
0:
0:
1. On disk when system is shutdown
  1. Fixed, well-known location
  Copied in memory when running
  1. Makes accesses, updates fast
  2. Otherwise lots of disk seeking
     to locate the blocks of a file
free
63:
N-1:
N-1:
mem
File 31, Block 3
File 31, Block 0
File 31, Block 1
File 31, Block 2
31:
file number
File 63, Block 1
File 63, Block 0
file descriptor 2 number

---
FAT Setup
FAT
Disk Blocks
0:
0:
1. Format a new FAT drive?
2. Link up the free list
free
.
.
.
N-1:
N-1:
File 31, Block 3
File 31, Block 0
File 31, Block 1
File 31, Block 2
File 63, Block 1
File 63, Block 0

---
FAT Assessment
FAT
Disk Blocks
0:
0:
1. Used all over the place
  1. DOS
  2. Windows (sometimes)
  3. Thumb Drives
2. Really simple
free
63:
N-1:
N-1:
mem
File 31, Block 3
File 31, Block 0
File 31, Block 1
File 31, Block 2
31:
file number
File 63, Block 1
File 63, Block 0
file descriptor 2 number

---
What about the Directory?
What about the Directory?
1. File containing	<file_name: file_number> mappings
2. Free space for new entries
3. In FAT: attributes kept in directory (!!!)
4. Each directory a linked list of entries
5. Where do you find root directory ( “/” )?

---
Directory Structure (Con’t)
Directory Structure (Con’t)
1. How many disk accesses to resolve “/my/book/count”?
  1. Read in file header for root (fixed spot on disk)
  2. Read in first data block for root
    1. Table of file name/index pairs. Search linearly – ok since directories typically very small
  3. Read in file header for “my”
  4. Read in first data block for “my”; search for “book”
  5. Read in file header for “book”
  6. Read in first data block for “book”; search for “count”
  7. Read in file header for “count”
2. Current working directory: Per-address-space pointer to a directory (file #) used for resolving file names
  1. Allows user to specify relative filename instead of absolute path (say CWD=“/my/book” can resolve “count”)

---
Big FAT security holes
Big FAT security holes
1. FAT has no access rights
2. FAT has no header in the file blocks
3. Just gives and index into the FAT
  1. (file number = block number)

---
Designing Better Filesystems
Question: What will they be used for?

---
Characteristics of Files
Empirical Characteristics of Files
1. Most files are small
2. Most of the space is occupied by the rare big ones

---
So what about a “real” file system
So what about a “real” file system
Meet the inode
file_number

---
So what about a “real” file system
Meet the inode
Array on disk
at well-known locations
Reserved when disk is "formatted"
(more later)
file_number

---
Unix Fast File System (Optimization on Unix Filesystem)
Unix Fast File System (Optimization on Unix Filesystem)
1. Original inode format appeared in BSD 4.1
  1. Berkeley Standard Distribution Unix
  2. Part of your heritage!
2. File Number is index into inode arrays
3. Multi-level index structure
  1. Great for little to large files
  2. Asymmetric tree with fixed sized blocks
4. Metadata associated with the file
  1. Rather than in the directory that points to it
5. UNIX FFS: BSD 4.2: Locality Heuristics
  1. Block group placement
  2. Reserve space
6. Scalable directory structure

---
BSD Fast File System (1)
1. Original inode format appeared in BSD 4.1
  1. Berkeley Standard Distribution Unix
2. File Number is index into inode arrays
3. Multi-level index structure
  1. Great for little to large files
  2. Asymmetric tree with fixed sized blocks

---
BSD Fast File System (2)
1. Metadata associated with the file
  1. Rather than in the directory that points to it
2. UNIX FFS: BSD 4.2: Locality Heuristics
  1. Attempt to allocate files contiguously
  2. Block group placement
  3. Reserve space
3. Scalable directory structure

---
An “almost real” file system
An “almost real” file system
Pintos: src/filesys/file.c, inode.c
file_number

---
FFS: File Attributes
FFS: File Attributes
Inode metadata – stored within inode
User
Group
9 basic access control bits
   - UGO x RWX
Setuid bit
    - execute at owner permissions
    - rather than user
Getgid bit
    - execute at group’s permissions

---
FFS: Data Storage
FFS: Data Storage
Small files: 12 pointers direct to data blocks
Direct pointers
4kB blocks: sufficient for files up to 48KB

---
Freespace Management
FFS: Freespace Management
1. Bit vector with a bit per storage block
2. Stored at a fixed location on disk

---
Where are inodes stored?
Where are inodes stored? (1)
1. In early UNIX and DOS/Windows’ FAT file system, headers/inodes stored in special array in outermost cylinders
  1. Outermost because fastest to read
  2. Fixed size, set when disk is formatted.

---
Where are inodes stored? (2)
1. In early UNIX and DOS/Windows’ FAT file system, headers/inodes stored in special array in outermost cylinders
2. Problem: How do you read a small file?
  1. Read its inode (outermost cylinders)
  2. Read its data – probably far away
  3. Lots of seek time

---
Locality: Block Groups
Locality: Block Groups
1. File system volume is divided into a set of block groups
  1. Close set of tracks
2. Idea: Low seek times between inode/directories for a file and blocks of a file

---
Locality: Block Groups
1. File data blocks, metadata, and free space are interleaved within block group
  1. No huge seeks
2. Put directory and its files in common block group

---
FFS First Fit Block Allocation
FFS First Fit Block Allocation
- Fills in the small holes at the start of block group
- Avoids fragmentation, leaves contiguous free space at end

---
Locality: Block Groups
1. First-free allocation of new file block
  1. Few little holes at start, big sequential runs at end of group
  2. Sequential layout for big files
2. Reserve space in the BG
  1. 10%
  2. Makes sure there's sequential holes for big files
  3. Lets "first fit" be fast – likely to find something quickly

---
Attack of the Rotational Delay
1. Problem: Missing blocks due to rotational delay
  1. Read one block, do processing, and read next block.
  2. In meantime, disk has continued turning: missed next block!
  3. Need 1 revolution/block!

---
Attack of the Rotational Delay
Attack of the Rotational Delay
1. Solution 1: Skip sector positioning (“interleaving”)
  1. Place the blocks from one file on every other block of a track: give time for processing to overlap rotation
  2. FFS did this
2. Solution 2: Read ahead: read next block right after first – speculate that it will be needed
  1. By OS (make larger request) – requires RAM to hold result of read
  2. By disk (track buffers) – requires RAM in the controller
  3. Most modern disk controllers do this
Skip Sector
Track Buffer
(Holds complete track)

---
FFS
BSD Fast File System
1. Pros
  1. Efficient storage for both small and large files
  2. Locality for both small and large files
  3. Locality for metadata and data
2. Cons
  1. Inefficient for tiny files (a 1 byte file requires both an inode and a data block)
  2. Inefficient encoding when file is mostly contiguous on disk (no way to say "blocks 1026-4085" – need to write out each block number)
  3. Need to reserve 10-20% of free space to prevent fragmentation

---
File System Summary
File System Summary
1. File System:
  1. Transforms blocks into Files and Directories
  2. Optimize for access and usage patterns
  3. Maximize sequential access, allow efficient random access
2. File (and directory) defined by header, called “inode”
3. Multilevel Indexed Scheme
  1. Inode contains file info, direct pointers to blocks,
  2. indirect blocks, doubly indirect, etc..
4. 4.2 BSD Multilevel index files
  1. Inode contains pointers to actual blocks, indirect blocks, double indirect blocks, etc.
  2. Optimizations for sequential access: start new files in open ranges of free blocks, rotational Optimization
5. Naming: act of translating from user-visible names to actual system resources
  1. Directories used for naming for local file systems