CS162:
Operating Systems and
Systems Programming
Lecture 29:
Conclusion
10 August 2015
Charles Reiss
https://cs162.eecs.berkeley.edu/

---
What happens when I press a key to advance a slide?

---
Reading from the Keyboard (1):
Making the System Call
1. Before hand:
  read(keyboard_fd, buffer, 1);
2. …
3. push SYS_READ ; put system call number on user stack
4. push keyboard_fd
5. push buffer
6. push 1
7. int $0x30

---
Pintos Interrupt Handling
interrupt.c
Intr_handler(*frame)
 - classify
 - dispatch
Wrapper for generic handler
stubs
***
0
intr_entry:
  save regs as frame
  set up kernel env.
  call intr_handler
intr_exit:
  restore regs
  iret
push 0x30 (int #)
jmp intr_entry
0x30
push 0x31 (int #)
jmp intr_entry
syscall_handler(*frame)
***
255
syscall.c
Hardware interrupt vector
stubs.S
0
Pintos intr_handlers
0x30

---
Reading from the Keyboard (2):
Handling the system call
1. Before hand:
  void syscall_handler(f) {
  1. read syscall # from f->esp
  2. dispatch read syscall
  3. extract remaining arguments
  4. lookup file descriptor in process control block
  5. actually call device driver: keyboard_read()

---
Reading from the keyboard (3):
Top half of the device driver
1. Before hand, after calling read
2. Somewhere deep within the kernel
  keyboard_read(...):
  1. Disable interrupts (why?)
  2. Check buffer for characters
  3. See none, block thread (e.g. on semaphore)...

---
What happens when I press a key to advance a slide?
1. Before hand, after calling read, thread is blocked in device driver top half...
2. Blocking thread calls scheduler
  1. Scheduler runs another thread
  2. (or the idle thread)

---
Recall: Juggling Stacks
proc A() {
  B();
}
proc B() {
   while(TRUE) {
 yield();
}
}
switch(curThread, newThread);
Thread S's switch returns to Thread T's
(and vice-versa)
Thread S
Stack growth
A
B(while)
yield
run_new_thread
switch
Thread T
A
B(while)
yield
run_new_thread
switch

---
Recall: The Context Switch Itself
switch(tCur,tNew) {
  /* Unload old thread */
  TCB[tCur].regs.r7 = CPU.r7;
…
  TCB[tCur].regs.r0 = CPU.r0;
     TCB[tCur].regs.sp = CPU.sp;
     /* store old thread's return address from switch() */
  TCB[tCur].regs.retpc = CPU.retpc;
  /* Load and execute new thread */
  CPU.r7 = TCB[tNew].regs.r7;
…
  CPU.r0 = TCB[tNew].regs.r0;
  CPU.sp = TCB[tNew].regs.sp;
  CPU.retpc = TCB[tNew].regs.retpc;
  return; /* Return to CPU.retpc */
}

---
What about address spaces switch?
switch(tCur,tNew) {
/* Unload old thread */
   TCB[tCur].regs.r7 = CPU.r7;
 …
   TCB[tCur].regs.r0 = CPU.r0;
   TCB[tCur].regs.sp = CPU.sp;
   /* store old thread's return address from switch() */
TCB[tCur].regs.retpc = CPU.retpc;
/* Load and execute new thread */
   CPU.r7 = TCB[tNew].regs.r7;
   …
   CPU.r0 = TCB[tNew].regs.r0;
   CPU.sp = TCB[tNew].regs.sp;
   CPU.page_table_base_register = …;
CPU.retpc = TCB[tNew].regs.retpc;
return; /* Return to CPU.retpc */
}

---
The keyboard acts
Memory Bus
PCI Bus
Adapter
DRAM
USB Bus
Adapter
SATA Bus
Adapter
CPU
$
Keyboard
Controller
interrupt controller

---
Pintos Interrupt Handling (Again)
interrupt.c
Intr_handler(*frame)
 - classify
 - dispatch
Wrapper for generic handler
stubs
***
0
intr_entry:
  save regs as frame
  set up kernel env.
  call intr_handler
intr_exit:
  restore regs
  iret
push 0x30 (int #)
jmp intr_entry
0x30
push 0x31 (int #)
jmp intr_entry
syscall_handler(*frame)
***
255
syscall.c
Hardware interrupt vector
stubs.S
0
Pintos intr_handlers
0x30

---
Keyboard Device Driver –
Bottom Half
Memory Bus
PCI Bus
Adapter
DRAM
USB Bus
Adapter
SATA Bus
Adapter
interrupt handler read from status register
CPU
$
Keyboard
Controller
interrupt controller

---
Move to ready queue

---
Move to ready queue

---
Keyboard driver: the top half (again)
1. Somewhere deep within the kernel (again)
  keyboard_read(...):
  1. Done waiting on semaphore
  2. Disable interrupts
  3. Check buffer for characters
  4. Copy into userspace buffer...

---
Changing what's displayed on the screen
1. Simplest mechanism:
  1. Memory-mapped "display memory"
  2. Mapped directly in user address
     space
Memory Bus
Graphics
Adapter
DRAM
CPU
$
0x8000F000
0x80010000
Physical Address
Space
Status
0x0007F000
Command
0x0007F004
Graphics
Command
Queue
0x80020000
Display
Memory

---
Two-level Page Table
1. Tree of page tables
2. Some system call sets up mapping to display memory
Physical
Address:
Offset
Physical
Page #
Display
Memory
Normal
Memory
4 bytes
PageTablePtr
4 bytes
10 bits
10 bits
12 bits
Virtual
Address:
Offset
Virtual
P2 index
Virtual
P1 index

---
Address Space Layout
Display Memory Mapping
VIRTUAL addresses

---
Click a link in the browser
Same procedure for getting the mouse click as the keyboard input...

---
Resolve name to address...
1. https://www.cs.berkeley.edu/ →
2. getaddrinfo(
    "www.cs.berkeley.edu",
    "443",
    …);

---
Recall: Domain Name System
Top-level
edu
com
MIT
berkeley.edu
berkeley
Mit.edu
www
calmail
eecs
1. Resolution by repeated queries:
  1. One server for each "domain" (<root>, edu, berkeley.edu)
  2. Plus backups: redundancy (available, not gaurenteed consistent)
169.229.131.81
128.32.61.103
128.32.139.48
eecs.berkeley.edu
www

---
Resolving www.cs.berkeley.edu
1. We ask our ISP's nameserver
  1. "What's an IP address for www.cs.berkeley.edu?"
2. Our ISP's nameserver asks:
  1. Root nameserver: "What's an IP address for …?"
    1. Root nameserver says "Try this .edu nameserver,
       IP = w.x.y.z"
  2. Edu nameserver: "What's an IP address for …?"
    1. Edu nameserver says "Try this berkeley.edu nameserver,
       IP = w.x.y.z"
  3. …

---
Resolving www.cs.berkeley.edu
1. We ask our ISP's nameserver
  1. "What's an IP address for www.cs.berkeley.edu?"
2. Our ISP's nameserver asks:
  1. Root nameserver: "What's an IP address for …?"
    1. Root nameserver says "Try this .edu nameserver,
       IP = w.x.y.z"
  2. Edu nameserver: "What's an IP address for …?"
    1. Edu nameserver says "Try this berkeley.edu nameserver,
       IP = w.x.y.z"
  3. …

---
Asking nameserver?
Form IP packet:
16-bit identification
ToS
4
13-bit frag off
Total length(16-bits)
protocol
TTL
16-bit header checksum
32-bit source IP address
32-bit destination IP address
IHL
flags
options (if any)
Data
0
15
16
31
IP Ver4
IP Header
Length
Size of datagram
(header+data)
Flags &
Fragmentation
to split large
messages
Time to
Live (hops)
Type of
transport
protocol
IP header
20 bytes
Destination machine

---
Asking nameserver?
Form IP packet:
16-bit identification
ToS
4
13-bit frag off
Total length(16-bits)
protocol
TTL
16-bit header checksum
32-bit source IP address
32-bit destination IP address
IHL
flags
options (if any)
Data
Link-Layer (Ethernet, WiFi, ...) Header
Transport Protocol (e.g. TCP) Header (part of data)

---
Sending IP packet
Form local network frame + send (WiFi/Ethernet/...):
Routers read packet, forward across one of their local networks...
subnet1
subnet2
Router
Other
subnets
Router
Router
Transcontinental
Link
subnet3
Other
subnets

---
Send request over TCP connection
Sequence Numbers
Sent
not acked
Sent
acked
Not yet
sent
Sender
Not yet
received
Received
Given to app
Received
Buffered
Receiver
B
A
Window size
ack#0
ack#4
pkt#0
pkt#4

---
Server: Process request
Client
Server
Create Server Socket
Bind it to an Address (host:port)
Create Client Socket
Listen for Connection
Connect it to server (host:port)
Accept connection
Child
Parent
Close Listen Socket
Close Connection Socket
write request
read request
read response
write response
Close Conn Socket
Close Client Socket

---
Request: Read from Disk
1. First check cache...
2. If not found...

---
Request: Finding the inode
1. Directory is file:
  1. Example above: Linked list: pointers are offsets in file
2. /home/tom/foo.txt → inode # is 66212871

---
… and send it back
subnet1
subnet2
Router
Other
subnets
Router
Router
Transcontinental
Link
subnet3
Other
subnets

---
… and read() it in the browser
read(sock_fd, buffer, ...)
foo.txt
…
…
…
…
… Lorum Ipsum …
Not yet
received
Received
Given to app
Received
Buffered
Receiver

---
Render and Write to Display
Graphics
Adapter
DRAM
CPU
$
0x8000F000
0x80010000
Physical Address
Space
Status
0x0007F000
Command
0x0007F004
Graphics
Command
Queue
0x80020000
Display
Memory

---
Misc logistics
1. HW3 Wednesday
2. Project 3 tonight

---
Final Logistics
1. Closed book, closed notes
2. 3 hour timeslot, aiming for 2 hour exam
3. Similar to midterm/past midterms, slightly longer
4. Review tomorrow – please have questions ready