## Slide 1: Packet Delay
CS168 and EE122 GSIs past and present

## Slide 2: What We’re Doing Today
Review of delays
Crash course on “virtual circuits”
Work through worksheet in pairs

## Slide 3: Nodal Delay
Processing delay
+
Queuing delay
+
Transmission delay
+
Propagation delay
Sum of several types of delay
(Diagram from Kurose & Ross)
Notes: Total Nodal Delay
Not going to talk about processing delay here

## Slide 4: Delays
(Diagram from Kurose & Ross)
Processing Delay
Processing on reception
Examine header and determine where to send
Error checking (maybe)
Notes: Not going to talk about this one much
Why not? (Sylvia probably said in lecture – we assume it’s trivially short)

## Slide 5: Delays
(Diagram from Kurose & Ross)
Queuing Delay
Time packet spends in buffer/queue
Only when arrival rate > service rate
Especially significant when packet arrivals are bursty

## Slide 6: Queuing Delay
A
B
C
Brown packet does not have to wait
BC’s transmission delay is twice that of AB
A
B
C
Brown packet waits for half the trans. delay of blue packet
Queuing delay
Queuing Delay: No
Queuing Delay: Yes
Notes: Review: What does the transmission delay say about the bandwidth? (It’s half.)
Q: Is there queuing delay at B?
What would look different here if B was a cut-through switch?

## Slide 7: Sidenote: Burstiness
Not Bursty
Bursty
Queue
Notes: Service rate and arrival rate
What happens to the extra packet? (drops)
Take a guess at which of these is bursty?

## Slide 8: Delays
(Diagram from Kurose & Ross)
Transmission Delay
Time taken to push data onto link
Measured…
  .. from when first bit of data pushed onto link
  .. until last bit of data is pushed onto the link
Limited by the link Bandwidth
Propagation Delay
Time taken by data to traverse link
Limited by the speed of light
Latency of a link is the propagation delay to traverse the link

## Slide 9: Transmission & Propagation
How fast is my speech?
  ~1000 ft/s (speed of sound)
  ~125 words/minute
What about Sean Shannon?
  ~1000 ft/s (speed of sound)
  ~655 words/minute
How long would it take:
  to hear me or Sean, if we shout “Help” (very loudly) from Stanford? (~40 miles [~200,000 feet] away)
  me or Sean to dictate War and Peace? (~600,000 words)
Notes: Which of these is transmission? Which is propagation?
~200 seconds, or 3min 20sec from Stanford
~1000 minutes or ~16 hours (Sean), ~4800 minutes or over 3 days (me)

## Slide 10: Transmission & Propagation
Propagation delay
Transmission delay
A
B
A
B
Packet

## Slide 11: Beyond Nodal Delays
End-to-End Delay
  Just the sum of the nodal delays along a path
Round Trip Time (RTT)
  Time for packet to reach destination
  .. and for response to return to source
A
B
Packet
Response

## Slide 12: TL;DR Delays
Propagation delay
Transmission delay
A
B
Size of transfer / Bandwidth of link
Physical distance / Speed of light
A
B

## Slide 13: Virtual Circuits
Covered more in section 4.2 of text
  which you may not have read yet!
With what you got in lecture and from section 1.3.2, here’s what you need to know for the worksheet…
Basic idea:
  Make a packet switched network a bit more like a circuit switched network
  How?

## Slide 14: Virtual Circuits
Information
time
(From lecture)
Circuit
Establishment
Transfer
Circuit
Teardown
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 15: Virtual Circuits
Circuit Establishment
  Source sends a setup packet to switches along path/circuit toward destination
  Switches along path set up connection
  At end of path, destination sends confirmation back
Transfer
  Data sent along path/circuit
  Note: Data sent along established circuit is cut-through!
  Question: What is the transmission rate of the circuit?
Circuit Teardown
  Source sends teardown packet along path
  Destination sends confirmation back

## Slide 16: Virtual Circuits
Circuit Establishment
  Source sends a setup packet to switches along path/circuit toward destination
  Switches along path set up connection
  At end of path, destination sends confirmation back
Transfer
  Data sent along path/circuit
  Note: Data sent along established circuit is cut-through!
  Question: What is the transmission rate of the circuit?
Circuit Teardown
  Source sends teardown packet along path
  Destination sends confirmation back
Notes: Answer: It’s the rate of the bottleneck link

## Slide 17: Virtual Circuits
Circuit Establishment
  Source sends a setup packet to switches along path/circuit toward destination
  Switches along path set up connection
  At end of path, destination sends confirmation back
Transfer
  Data sent along path/circuit
  Note: Data sent along established circuit is cut-through!
  Question: What is the transmission rate of the circuit?
Circuit Teardown
  Source sends teardown packet along path
  Destination sends confirmation back

## Slide 18: Worksheet!